| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de |
| Date:* | 2017-03-20 |
| Reason for Change/s:* | Add a “setColour” action to the “colour” ModuleClass to allow for a synchronized setting of colour data points. |
| CR against: Release* | Rel.3 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | 5.3.10 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new action “setColour” for the “colour” ModuleClass to allow the synchronized setting of colour values to a device. Setting the single “red”, “green”, “blue” data points might, depending on the implmentation, result in presenting wrong colours, even for a very short period.

### -----------------------Start of change 1-------------------------------------------

### 5.3.10	colour

This ModuleClass provides the capabilities to set the value of Red, Green, Blue for the colour device.

Table 5.3.10-1: Actions of colour ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | setColour | xs:integer, xs:integer, xs:integer | true | Set all colour data points synchronized at the same time. The arguments are for red, green, blue resp. |

Table 5.3.10-2: DataPoints of colour ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| red | xs:integer | true | true | false | The R value of RGB; the range is [0,255] |
| green | xs:integer | true | true | false | The G value of RGB; the range is [0,255] |
| blue | xs:integer | true | true | false | The B value of RGB; the range is [0,255] |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table 6.3.2-3: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activateClockTimer | acCTr |
| deactivateClockTimer | deCTr |
| downChannel | dowCl |
| downVolume | dowVe |
| toggle | togge |
| setColour |  |
| upChannel | uphCl |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 6.4.4	Actions

The containerDefinition attribute of specializations for actions shall have the values specifien in Table 6.4.4-1.

Table 6.4.4-1: containerDefinition values of specializations for actions

| Resource Type Name | containerDefinition value |
| --- | --- |
| activateClockTimer | "org.onem2m.home.moduleclass.timer.activateclocktimer" |
| deactivateClockTimer | "org.onem2m.home.moduleclass.timer.deactivateclocktimer" |
| downChannel | "org.onem2m.home.moduleclass.televisionchannel.downchannel" |
| downVolume | "org.onem2m.home.moduleclass.audiovolume.downvolume" |
| setColour | "org.onem2m.home.moduleclass.colour.setcolour" |
| toggle | "org.onem2m.home.moduleclass.binaryswitch.timer" |
| upChannel | "org.onem2m.home.moduleclass.televisionchannel.upchannel" |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Table 6.5.4-1: XSD definition of Action

| Action | File Name | Note |
| --- | --- | --- |
| activateClockTimer | HD-act-activateClockTimer-v<TS-version><TS-version>.xsd |  |
| deactivateClockTimer | HD-act-deactivateClockTimer-v<TS-version>.xsd |  |
| downChannel | HD-act-downChannel-v<TS-version>.xsd |  |
| downVolume | HD-act-downVolume-v<TS-version>.xsd |  |
| setColour | HD-act-setColour-v<TS-version>.xsd |  |
| toggle | HD-act-toggle-v<TS-version>.xsd |  |
| upChannel | HD-act-upChannel-v<TS-version>.xsd |  |
| upVolume | HD-act-upVolume-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 4---------------------------------------------

# Comments

Short name to be filled in later

Must be verified after generating.