| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de |
| Date:* | 2017-03-20 |
| Reason for Change/s:* | Adding a new ModuleClass for setting and getting binary objects. |
| CR against: Release* | Rel.3 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | New clauses in 5.3. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new ModuleClass for setting and getting binary objects. This internal structure of these binary objects are not defined here. Examples could be images, audio and video files as well as configuration modules and executable code.

### -----------------------Start of change 1-------------------------------------------

### 5.3.x	binaryObject

This new ModuleClass describes the handling of a binary object (blob).

Table 5.3.x-1: DataPoints of binaryObject ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| object | xs:string | true | true | false | This data point contains the base64 encoded binary object. |
| objectType | xs:string | true | true | false | This data point contains the type and subtype of the binary object as a MIME type. |
| size | xs:integer | true | true | true | The size of the decoded binary object. |
| hash | xs:string | true | true | true | The hash code of the blob. If present, it is used to check the decoded content of the “object” data point for integrity. The algorithm used for generating the hash value is SHA-2 [xx]. The data point contains the hash as a hex encoded value. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| oximeter | oximr |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |

### -----------------------End of change 2---------------------------------------------

### ------------------------Start of change 3-------------------------------------------

Table 6.3.3-2: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| channelId | televisionChannel | chaId |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentDate | clock | curDe |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| hash | binaryObject |  |
| height | height | heigt |
| inputSourceID | audioVideoInput | inSId |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keepWarm | brewing |  |
| keyNumber | keypad | keyNr |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| maxValue | audioVolume, temperature | maxVe |
| minValue | temperature | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| object | binaryObject |  |
| type | binaryObject |  |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject |  |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, brewing | stats |
| stepValue | audioVolume, temperature | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedInputSources | audioVideoInput | suISs |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binaryObject | "org.onem2m.home.moduleclass.binaryObject" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runState | "org.onem2m.home.moduleclass.runState" |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |
| bodyCompositionAnalyzer | "org.onem2m.home.moduleclass.bodyCompositionAnalyzer " |
| glucometer | "org.onem2m.home.moduleclass.glucometer " |
| pulsemeter | "org.onem2m.home.moduleclass.pulsemeter " |
| sphygmomanometer | "org.onem2m.home.moduleclass.sphygmomanometer " |
| operationMode | "org.onem2m.home.moduleclass.operationMode" |
| remoteControl | "org.onem2m.home.moduleclass.remoteControl" |
| washingCourse | "org.onem2m.home.moduleclass.washingCourse" |
| washingCourseOption | "org.onem2m.home.moduleclass.washingCourseOption" |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

Table 6.5.3-1: XSD definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binaryObject | HD-mod-binaryObject-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runState | HD-mod-runState-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| bodyCompositionAnalyzer | HD-mod- bodyCompositionAnalyzer -v<TS-version>.xsd |  |
| glucometer | HD-mod- glucometer -v<TS-version>.xsd |  |
| pulsemeter | HD-mod- pulsemeter -v<TS-version>.xsd |  |
| sphygmomanometer | HD-mod- sphygmomanometer -v<TS-version>.xsd |  |
| operationMode | HD-mod- operationMode-v<TS-version>.xsd |  |
| remoteControl | HD-mod- remoteControl-v<TS-version>.xsd |  |
| washingCourse | HD-mod-washingCourse-v<TS-version>.xsd |  |
| washingCourseOption | HD-mod-washingCourseOption-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

## 2.1	Normative references

The following referenced documents are necessary, partially or totally, for the application of the present document. Their use in the context of this TS is specified by the normative statements that are referring back to this clause

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://github.com/Homegateway/SmartDeviceTemplate/tree/7c890b69d9764e341ef1768c5a0e7d53a47cff5c.

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: “Service Layer Core Protocol Specification”

[5]	ISO:80000-1: Quantities and units

[xx]	NIST standard FIPS PUB 180-2

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

### -----------------------End of change 6---------------------------------------------