| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de |
| Date:* | 2017-03-20 |
| Reason for Change/s:* | Adding a new ModuleClass for receiving and initiating phone calls |
| CR against: Release* | Rel.3 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | New clauses in 5.3. |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a new ModuleClass for getting and setting data points receiving and initiating phone calls.

### -----------------------Start of change 1-------------------------------------------

### 5.3.x	phoneCall

This ModuleClass provides the capability get or set the caller and receipient IDs as well as to initate and * terminate a call.

Table 5.3.x-1: Actions of phoneCall ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | call | none | true | Initiate an outgoing call. |
| none | answer | none | true | Answer (pickup) an incoming call. |
| none | hangup | none | true | Hangup an established call. |

Table 5.3.x-2: DataPoints of phoneCall ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| callerID | xs:string | true | true | false | This data point represents the initiating caller identiﬁcation of a call. In case of an outgoing call this would be the local line ID. This data point is optional. When it is empty for an incomming call, then the caller ID is unknown. When it is empty for an outgoing call, then it is exepected that it is set by the PBX or the operator. The format of caller ID is not speciﬁed here. |
| recipientID | xs:string | true | true | false | This data point represents the receiving caller identiﬁcation of a call. In case of an incoming call this would be the local line ID and optionally extension. The format of caller ID is not speciﬁed here. |
| callState | hd:callState | true | false | true | This data point represents the current state of an associated phone device regarding calls. |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

Table 6.4.4-1: containerDefinition values of specializations for actions

| Resource Type Name | containerDefinition value |
| --- | --- |
| activateClockTimer | "org.onem2m.home.moduleclass.timer.activateclocktimer" |
| answer | "org.onem2m.home.moduleclass.phonecall.answer" |
| call | "org.onem2m.home.moduleclass.phonecall.call" |
| deactivateClockTimer | "org.onem2m.home.moduleclass.timer.deactivateclocktimer" |
| downChannel | "org.onem2m.home.moduleclass.televisionchannel.downchannel" |
| downVolume | "org.onem2m.home.moduleclass.audiovolume.downvolume" |
| hangup | "org.onem2m.home.moduleclass.phonecall.hangup" |
| toggle | "org.onem2m.home.moduleclass.binaryswitch.timer" |
| upChannel | "org.onem2m.home.moduleclass.televisionchannel.upchannel" |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.x	hd:callState

Used for the callState data point in the phoneCall ModuleClass.

Table 5.5.x-1: Interpretation of callState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | hangup |  |
| 2 | calling |  |
| 3 | ringing |  |
| 4 | busy |  |
| 5 | answered |  |
| 6 | noline |  |
| NOTE: See clause 5.3.x “phoneCall” |

### -----------------------End of change 3---------------------------------------------

### -----------------------Start of change 4-------------------------------------------

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| oximeter | oximr |
| phoneCall |  |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |

### -----------------------End of change 4---------------------------------------------

### -----------------------Start of change 5-------------------------------------------

Table 6.3.2-3: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activateClockTimer | acCTr |
| answer |  |
| call |  |
| deactivateClockTimer | deCTr |
| downChannel | dowCl |
| downVolume | dowVe |
| hangup |  |
| toggle | togge |
| upChannel | uphCl |

### -----------------------End of change 5---------------------------------------------

### -----------------------Start of change 6-------------------------------------------

Table 6.3.3-2: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| callerID | phoneCall |  |
| callState | phoneCall |  |
| channelId | televisionChannel | chaId |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentDate | clock | curDe |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| height | height | heigt |
| inputSourceID | audioVideoInput | inSId |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keepWarm | brewing |  |
| keyNumber | keypad | keyNr |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| maxValue | audioVolume, temperature | maxVe |
| minValue | temperature | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall |  |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, brewing | stats |
| stepValue | audioVolume, temperature | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedInputSources | audioVideoInput | suISs |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |

### -----------------------End of change 6---------------------------------------------

### -----------------------Start of change 7-------------------------------------------

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| phoneCall | "org.onem2m.home.moduleclass.phoneCall" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runState | "org.onem2m.home.moduleclass.runState" |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |
| bodyCompositionAnalyzer | "org.onem2m.home.moduleclass.bodyCompositionAnalyzer " |
| glucometer | "org.onem2m.home.moduleclass.glucometer " |
| pulsemeter | "org.onem2m.home.moduleclass.pulsemeter " |
| sphygmomanometer | "org.onem2m.home.moduleclass.sphygmomanometer " |
| operationMode | "org.onem2m.home.moduleclass.operationMode" |
| remoteControl | "org.onem2m.home.moduleclass.remoteControl" |
| washingCourse | "org.onem2m.home.moduleclass.washingCourse" |
| washingCourseOption | "org.onem2m.home.moduleclass.washingCourseOption" |

### -----------------------End of change 7---------------------------------------------

### -----------------------Start of change 8-------------------------------------------

Table 6.5.3-1: XSD definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| phoneCall | HD-mod-phoneCall-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runState | HD-mod-runState-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| bodyCompositionAnalyzer | HD-mod- bodyCompositionAnalyzer -v<TS-version>.xsd |  |
| glucometer | HD-mod- glucometer -v<TS-version>.xsd |  |
| pulsemeter | HD-mod- pulsemeter -v<TS-version>.xsd |  |
| sphygmomanometer | HD-mod- sphygmomanometer -v<TS-version>.xsd |  |
| operationMode | HD-mod- operationMode-v<TS-version>.xsd |  |
| remoteControl | HD-mod- remoteControl-v<TS-version>.xsd |  |
| washingCourse | HD-mod-washingCourse-v<TS-version>.xsd |  |
| washingCourseOption | HD-mod-washingCourseOption-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 8---------------------------------------------

### -----------------------Start of change 9-------------------------------------------

Table 6.5.4-1: XSD definition of Action

| Action | File Name | Note |
| --- | --- | --- |
| activateClockTimer | HD-act-activateClockTimer-v<TS-version><TS-version>.xsd |  |
| answer | HD-act-answer-v<TS-version><TS-version>.xsd |  |
| call | HD-act-call-v<TS-version><TS-version>.xsd |  |
| deactivateClockTimer | HD-act-deactivateClockTimer-v<TS-version>.xsd |  |
| downChannel | HD-act-downChannel-v<TS-version>.xsd |  |
| downVolume | HD-act-downVolume-v<TS-version>.xsd |  |
| hangup | HD-act-hangup-v<TS-version><TS-version>.xsd |  |
| toggle | HD-act-toggle-v<TS-version>.xsd |  |
| upChannel | HD-act-upChannel-v<TS-version>.xsd |  |
| upVolume | HD-act-upVolume-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 9---------------------------------------------

# Comments

Add later

Short names later

Filenames must be verified after generating