| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28 |
| Source:* | Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de |
| Date:* | 2017-03-28 |
| Reason for Change/s:* | Clarification on the re-use of ModuleClasses in new Device definitions. |
| CR against: Release* | Rel.3 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.2.0 |
| Clauses * | New explanation in 5.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces a clarification on how to specify and use ModuleClasses.

### -----------------------Start of change 1-------------------------------------------

### 5.2.1	Basic design principle of information modelling

The design principle of the oneM2M abstract information model of home appliance, is to use SDT 3.0 as introduced in oneM2M TR 0017 [i.2]. Note that those terms starting with a capital letter in this clause are SDT terms and are explained in [1].

Domain is a unique name which acts like a namespace (e.g., "org.oneM2M.home.modules"). It is set by the organization creating the SDT, allowing reference to a package of definitions for the contained ModuleClasses and Device models.

ModuleClasses specifies a single service (e.g., audioVolume, powerOn/Off) with one or more Actions, Properties, DataPoints and Events. Each service which is described as a ModuleClass can be re-used in many Devices.

Device model is a physical, addressable, identifiable appliance, sensor and actuator with one or more Modules, Properties and SubDevices.

SubDevice is a device which may be embedded in a Device and/or is addressed via another Device.

Module is an instantiation of a ModuleClass for a specific Device or SubDevice.

Figure 5.2.1-1 depicts the basic structure of SDT 3.0.

Specifications of new Device models and ModuleClasses are encouraged to re-use the definitions specified in this document as much as possible. If re-use is not possible and new Device and/or ModuleClases definitions are necessary, it is strongly adviced to closely follow the guidelines and definition style from this document.

### -----------------------End of change 1---------------------------------------------