| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#28.1 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-4-10 |
| Reason for Change/s:* | Deletion of redundant tables in the clause 6.4 and 6.5. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.3.0 |
| Clauses * | 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present CR requests to delete redundant tables that follow the same rule in the clause 6.4 and 6.5 and write the specific rule and example instead in order to improve manageability of the document

### -----------------------Start of change 1-------------------------------------------

## 6.4	containerDefinition values

### 6.4.1	Introduction

Each specialization has a containerDefinition attribute which can be used as an unique identifier and contains the information of the resource. In this clause, the detailed values of containerDenifition attributes in every specializations for the home appliance information models are given.

### 6.4.2	Device models

The containerDefinition attribute of specializations for device models shall have the values that comply with the following rule.

- Rule: “org.onem2m.home.device.[device name]”

For example, the containerDefinition attribute of specialization for deviceAirConditioner shall be “org.onem2m.home.device.deviceAirConditioner”.

### 6.4.3	ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values that comply with the following rule.

- Rule: “org.onem2m.home.moduleclass.[moduleclass name]”

For example, the containerDefinition attribute of specialization for alarmSpeaker shall be “org.onem2m.home.moduleclass.alarmSpeaker”.

### 6.4.4	Actions

The containerDefinition attribute of specializations for actions shall have the values that comply with the following rule.

- Rule: “org.onem2m.home.moduleclass.[name of moduleclass that the action belongs to].[action name]”

For example, the containerDefinition attribute of specialization for activateClockTimer in the timer ModuleClass shall be “org.onem2m.home.moduleclass.timer.activateclocktimer”.

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 6.5	XSD definitions

### 6.5.1	Introduction

The present clause specifies how to name thefiles which define data types in XSD for Device models, ModuleClasss, and Actions.

Generation process of XSD file is explained in Annex A using some examples.

### 6.5.2	XSD definitions for Device models

The XSD definitions for Device models are specified upon the following rule.

- Rule: HD-[device name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for deviceAirConditioner specified in TS-0023 v3.3.0 shall be “HD-deviceAirConditioner-v3_3_0.xsd”

### 6.5.3	XSD definitions for ModuleClass

The XSD definitions for ModuleClass are specified upon the following rule.

- Rule: HD-mod-[ModuleClass name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for alarmSpeaker specified in TS-0023 v3.3.0 shall be “HD-mod-alarmSpeaker-v3_3_0.xsd”

### 6.5.4	XSD definitions for Action

The XSD definitions for Actions are specified upon the following rule.

- Rule: HD-act-[action name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for activateClockTimer specified in TS-0023 v3.3.0 shall be “HD-act- activateClockTimer -v3_3_0.xsd”.

### -----------------------End of change 2-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?