| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#29 |
| Source:* | NTT, NTT DOCOMO |
| Date:* | 2017-05-12 |
| Contact:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, Hiroyuki Maeomichi(maeomichi.hiroyuki@lab.ntt.co.jp), NTT, Takashi Yoshikawa(yoshikawatak@nttdocomo.com), NTT DOCOMO |
| Reason for Change/s:* | To add the omaDevice module class for OMA DWAPI common properties |
| CR against: Release* | R3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.3.0 |
| Clauses * | 5.3, 5.4, 5.5, 6.3, 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0023 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposed to add the omaDevice module class to collect the OMA DWAPI common property.

### -----------------------Start of change 1-------------------------------------------

### 5.3.xx	omaDevice

This ModuleClasses provides capabilities to collect the OMA DWAPI common property. Devices using OMA DWAPI have omaDevice ModuleClass.

Table 5.3.xx-1: Properties of omaDevice ModuleClass

| Name | Type | Value | Optional | Documentation |
| --- | --- | --- | --- | --- |
| propPartNumber | xs:string | true | false | The number or name of the part of the device. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.4.18	deviceBloodPressureMonitor

A device blood pressure is a device that can be used to monitor the blood  pressure.

Table 5.4.18-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| sphygmomanometer | sphygmomanometer | false | See clause 5.3.47 |
| pulsemeter | pulsemeter | false | See clause 5.3.48 |
| battery | battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### 5.4.19	deviceGlucosemeter

A glucometer is a device that can be used to monitor the blood glucose level.

Table 5.4.19-1: Modules of deviceGlucoseMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| glucometer | glucometer | false | See clause 5.3.49 |
| battery | battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### 5.4.20	devicePulseOximeter

A pulseoximeter is a device that can be used to monitor the blood characteristics.

Table 5.4.20-1: Modules of devicePulseOxiMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | true | See clause 5.3.48. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | oximeter | true | See clause 5.3.21. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### 5.4.21	deviceThermometer

A thermometer is a device that can be used to check the body temperature.

Table 5.4.21-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Temperature | Temperature | false | See clause 5.3.33 |
| Battery | Battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### 5.4.22	deviceWeightScaleAndBodyCompositionAnalyzer

A weight scale & body composition analyzer is a device that can be used to monitor the weight and body composition.

Table 5.4.22-1: Modules of deviceWeightScaleAndBodyCompositionAnalyzer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| Weight | Weight | false | See clause 5.3.40 |
| bodyCompositionAnalyzer | bodyCompositionAnalyzer | false | See clause 5.3.50 |
| bioElectricalImpedanceAnalysis | bioElectricalImpedanceAnalysis | false | See clause 5.3.6 |
| Battery | Battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### 5.4.23	deviceHeartRateMonitor

A heart rate monitor a device that can be used to monitor the heart rate.

Table 5.4.23-1: Modules of deviceHeartRateMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | Pulsemeter | false | See clause 5.3.48 |
| battery | Battery | false | See clause 5.3.4 |
| omaDevice | omaDevice | false | See clause 5.3.xx |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 7.1.2.3  	devicePulseOximeter

DevicePulseOximeter of HAIM shall be mapped to Pulse Oximeter of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.3 Map of devicePulseOximeter of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | modality | spo2 orpulse | See clause 5.3.48. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | oxygenSaturation | spo2 or pulse | See clause 5.3.21. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |

.

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-2

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| geolocation |  |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keepWarm |  |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| numberValue |  |
| oximeter | oximr |
| playerControl |  |
| phoneCall |  |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage |  |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| dimmingLevel |  |
| omaDevice |  |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 6.3.3	Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |
| modelNumber | omaDevice |  |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 6.4.3	ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values specifien in Table 6.4.3-1.

Table 6.4.3-1: containerDefinition values of specializations for module classes

| Resource Type Name | containerDefinition value |
| --- | --- |
| alarmSpeaker | "org.onem2m.home.moduleclass.alarmSpeaker" |
| audioVideoInput | "org.onem2m.home.moduleclass.audioVideoInput" |
| audioVolume | "org.onem2m.home.moduleclass.audioVolume" |
| battery | "org.onem2m.home.moduleclass.battery" |
| binarySwitch | "org.onem2m.home.moduleclass.binarySwitch" |
| bioElectricalImpedanceAnalysis | "org.onem2m.home.moduleclass.bioElectricalImpedanceAnalysis" |
| boiler | "org.onem2m.home.moduleclass.boiler" |
| brewing | "org.onem2m.home.moduleclass.brewing” |
| brightness | "org.onem2m.home.moduleclass.brightness" |
| clock | "org.onem2m.home.moduleclass.clock" |
| colour | "org.onem2m.home.moduleclass.colour" |
| colourSaturation | "org.onem2m.home.moduleclass.colourSaturation" |
| customTemperature | "org.onem2m.home.moduleclass.customTemperature" |
| doorStatus | "org.onem2m.home.moduleclass.doorStatus" |
| electricVehicleConnector | "org.onem2m.home.moduleclass.electricVehicleConnector" |
| energyConsumption | "org.onem2m.home.moduleclass.energyConsumption" |
| energyGeneration | "org.onem2m.home.moduleclass.energyGeneration" |
| faultDetection | "org.onem2m.home.moduleclass.faultDetection" |
| foaming | "org.onem2m.home.moduleclass.foaming” |
| freshTemperature | "org.onem2m.home.moduleclass.freshTemperature" |
| frozenTemperature | "org.onem2m.home.moduleclass.frozenTemperature" |
| grinder | "org.onem2m.home.moduleclass.grinder” |
| height | "org.onem2m.home.moduleclass.height" |
| hotWaterSupply | "org.onem2m.home.moduleclass.hotWaterSupply" |
| keypad | "org.onem2m.home.moduleclass.keypad" |
| liquidLevel | "org.onem2m.home.moduleclass.liquidLevel” |
| liquidRemaining | "org.onem2m.home.moduleclass.liquidRemaining” |
| motionSensor | "org.onem2m.home.moduleclass.motionSensor" |
| oximeter | "org.onem2m.home.moduleclass.oximeter" |
| powerSave | "org.onem2m.home.moduleclass.powerSave" |
| pushButton | "org.onem2m.home.moduleclass.pushButton" |
| recorder | "org.onem2m.home.moduleclass.recorder" |
| refrigeration | "org.onem2m.home.moduleclass.refrigeration" |
| relativeHumidity | "org.onem2m.home.moduleclass.relativeHumidity" |
| rinseLevel | "org.onem2m.home.moduleclass.rinseLevel" |
| runState | "org.onem2m.home.moduleclass.runState" |
| signalStrength | "org.onem2m.home.moduleclass.signalStrength" |
| smokeSensor | "org.onem2m.home.moduleclass.smokeSensor " |
| spinLevel | "org.onem2m.home.moduleclass.spinLevel" |
| televisionChannel | "org.onem2m.home.moduleclass.televisionChannel" |
| temperature | "org.onem2m.home.moduleclass.temperature" |
| temperatureAlarm | "org.onem2m.home.moduleclass.temperatureAlarm" |
| timer | "org.onem2m.home.moduleclass.timer" |
| turbo | "org.onem2m.home.moduleclass.turbo" |
| waterFlow | "org.onem2m.home.moduleclass.waterFlow" |
| waterSensor | "org.onem2m.home.moduleclass.waterSensor" |
| weight | "org.onem2m.home.moduleclass.weight" |
| wind | "org.onem2m.home.moduleclass.wind" |
| bodyCompositionAnalyzer | "org.onem2m.home.moduleclass.bodyCompositionAnalyzer " |
| glucometer | "org.onem2m.home.moduleclass.glucometer " |
| pulsemeter | "org.onem2m.home.moduleclass.pulsemeter " |
| sphygmomanometer | "org.onem2m.home.moduleclass.sphygmomanometer " |
| operationMode | "org.onem2m.home.moduleclass.operationMode" |
| remoteControl | "org.onem2m.home.moduleclass.remoteControl" |
| washingCourse | "org.onem2m.home.moduleclass.washingCourse" |
| washingCourseOption | "org.onem2m.home.moduleclass.washingCourseOption" |
| omaDevice | "org.onem2m.home.moduleclass.omaDevice" |

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 7-------------------------------------------

### 6.5.3	XSD definitions for ModuleClass

The XSD definitions for ModuleClass are listed in Table 6.5.3-1.

Table 6.5.3-1: XSD definition of ModuleClasses

| ModuleClass ID | File Name | Note |
| --- | --- | --- |
| alarmSpeaker | HD-mod-alarmSpeaker-v<TS-version>.xsd |  |
| audioVideoInput | HD-mod-audioVideoInput-v<TS-version>.xsd |  |
| audioVolume | HD-mod-audioVolume-v<TS-version>.xsd |  |
| battery | HD-mod-battery-v<TS-version>.xsd |  |
| binarySwitch | HD-mod-binarySwitch-v<TS-version>.xsd |  |
| bioElectricalImpedanceAnalysis | HD-mod-bioElectricalImpedanceAnalysis-v<TS-version>.xsd |  |
| boiler | HD-mod-boiler-v<TS-version>.xsd |  |
| brewing | HD-mod- brewing -v<TS-version>.xsd |  |
| brightness | HD-mod-brightness-v<TS-version>.xsd |  |
| clock | HD-mod-clock-v<TS-version>.xsd |  |
| colour | HD-mod-colour-v<TS-version>.xsd |  |
| colourSaturation | HD-mod-colourSaturation-v<TS-version>.xsd |  |
| doorStatus | HD-mod-doorStatus-v<TS-version>.xsd |  |
| electricVehicleConnector | HD-mod-electricVehicleConnector-v<TS-version>.xsd |  |
| energyConsumption | HD-mod-energyConsumption-v<TS-version>.xsd |  |
| energyGeneration | HD-mod-energyGeneration-v<TS-version>.xsd |  |
| faultDetection | HD-mod-faultDetection-v<TS-version>.xsd |  |
| foaming | HD-mod- foaming -v<TS-version>.xsd |  |
| grinder | HD-mod- grinder -v<TS-version>.xsd |  |
| height | HD-mod-height-v<TS-version>.xsd |  |
| hotWaterSupply | HD-mod-hotWaterSupply-v<TS-version>.xsd |  |
| keypad | HD-mod-keypad-v<TS-version>.xsd |  |
| liquidLevel | HD-mod- liquidLevel -v<TS-version>.xsd |  |
| liquidRemaining | HD-mod- liquidRemaining -v<TS-version>.xsd |  |
| motionSensor | HD-mod-motionSensor-v<TS-version>.xsd |  |
| oximeter | HD-mod-oximeter-v<TS-version>.xsd |  |
| powerSave | HD-mod-powerSave-v<TS-version>.xsd |  |
| pushButton | HD-mod-pushButton-v<TS-version>.xsd |  |
| recorder | HD-mod-recorder-v<TS-version>.xsd |  |
| refrigeration | HD-mod-refrigeration-v<TS-version>.xsd |  |
| relativeHumidity | HD-mod-relativeHumidity-v<TS-version>.xsd |  |
| rinseLevel | HD-mod-rinseLevel-v<TS-version>.xsd |  |
| runState | HD-mod-runState-v<TS-version>.xsd |  |
| signalStrength | HD-mod-signalStrength-v<TS-version>.xsd |  |
| smokeSensor | HD-mod-smokeSensor-v<TS-version>.xsd |  |
| spinLevel | HD-mod-spinLevel-v<TS-version>.xsd |  |
| televisionChannel | HD-mod- HD-mod--v<TS-version>.xsd |  |
| temperature | HD-mod-temperature-v<TS-version>.xsd |  |
| temperatureAlarm | HD-mod-temperatureAlarm-v<TS-version>.xsd |  |
| timer | HD-mod-timer-v<TS-version>.xsd |  |
| turbo | HD-mod-turbo-v<TS-version>.xsd |  |
| waterFlow | HD-mod-waterFlow-v<TS-version>.xsd |  |
| waterSensor | HD-mod-waterSensor-v<TS-version>.xsd |  |
| weight | HD-mod-weight-v<TS-version>.xsd |  |
| wind | HD-mod-wind-v<TS-version>.xsd |  |
| bodyCompositionAnalyzer | HD-mod- bodyCompositionAnalyzer -v<TS-version>.xsd |  |
| glucometer | HD-mod- glucometer -v<TS-version>.xsd |  |
| pulsemeter | HD-mod- pulsemeter -v<TS-version>.xsd |  |
| sphygmomanometer | HD-mod- sphygmomanometer -v<TS-version>.xsd |  |
| operationMode | HD-mod- operationMode-v<TS-version>.xsd |  |
| remoteControl | HD-mod- remoteControl-v<TS-version>.xsd |  |
| washingCourse | HD-mod-washingCourse-v<TS-version>.xsd |  |
| washingCourseOption | HD-mod-washingCourseOption-v<TS-version>.xsd |  |
| omaDevice | HD-mod-omaDevice-v<TS-version>.xsd |  |
| NOTE: The string '<TS-version>' shall be intepreted as the version of the present document. |

### -----------------------End of change 7-------------------------------------------

-----------------------Start of change 8-------------------------------------------

## 7.1.2.1	 deviceBloodPressureMonitor

DeviceBloodPressureMonitoer of HAIM shall be mapped to Blood Pressure Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.1 Map of deviceBloodPressureMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| sphygmomanometer | diastolicPressure | diastolic | See clause 5.3.47 |
|  | systolicPressure | systolic |  |
|  | meanPressure | mean |  |
| pulsemeter | pulseRate | pulse | See clause 5.3.48 |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

## 7.1.2.2  	deviceGlucosemeter

DeviceGlucometer of HAIM shall be mapped to Glucometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.2 Map of deviceGlucometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| glucometer | concentration | concentration | See clause 5.3.49 |
|  | hba1c | hba1c |  |
|  | contextExercise | contextExercise |  |
|  | contextMedication | contextMedication |  |
|  | contextCarbohydratesAmount | contextCarbohydrates |  |
|  | contextCarbohydratesSource | contextCarbohydrates |  |
|  | contextMeal | contextMeal |  |
|  | contextLocation | contextLocation |  |
|  | contextTester | contextTester |  |
|  | contextHealth | contextHealth |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

## 7.1.2.3  	devicePulseOximeter

DevicePulseOximeter of HAIM shall be mapped to Pulse Oximeter of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.3 Map of devicePulseOximeter of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | modality | spo2, pulse | See clause 5.3.48. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | modality | spo2, pulse | See clause 5.3.21. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

## 7.1.2.4  deviceThermometer

DeviceTermometer of HAIM shall be mapped to Thermometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.4 Map of deviceThermometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | Data Points of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| temperature | unit | temperature | See clause 5.3.33 |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

## 7.1.2.5  deviceWeightScaleAndBodyCompositionAnalyzer

DeviceWeightScaleAdBodyCompositionAnalyzer of HAIM shall be mapped to Weight Scale Body Composition Analyzer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.5 Map of deviceWeightScaleAdBodyCompositionAnalyzer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| bodyCompositionAnalyzer | bodyLength | bodyLength | See clause 5.3.50 |
|  | Bmi | bmi |  |
|  | fatFreeMass | fatFreeMass |  |
|  | softLeanMass | softLeanMass |  |
|  | muscleMass | muscleMass |  |
|  | basalMetabolism | basalMetabolism |  |
|  | impedance | impedance |  |
| weight | weight | bodyMass | See clause 5.3.40 |
| bioElectricalImpedanceAnalysis | water | bodyWater | See clause 5.3.6 |
|  | fat | bodyFat |  |
|  | muscle | musclePercentage |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

## 7.1.2.6  deviceHeartRateMonitor

DeviceHeartRateMonitor of HAIM shall be mapped to Heart Rate Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2.6 Map of deviceHeartRateMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | pulseRate | rate | See clause 5.3.48 |
|  | rr | rr |  |
|  | energy | energy |  |
| battery | level | batteryLevel | See clause 5.3.4. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |
| omaDevice | propPartNumber | part Number | See clause 5.3.xx |

-----------------------End of change 8-------------------------------------------