| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#29.2 |
| Source:* | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2017-06-26 |
| Reason for Change/s:* | This CR requests to add a camera data model. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: STE Small Technical Enhancements / < Work Item number (optional) Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.4.1 |
| Clauses * | 2.1, 5.3.x, 5.4.x, 6.3.2, 6.3.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present CR requests to add a camera device model which does not exist in the current HAIM specification. This model is proposed with only one module class that is mediaType. Other functions could be added in the future if necessary.

### -----------------------Start of change 1-------------------------------------------

### 5.4.x	deviceCamera

A camera is an optical instrument for recording or capturing images, which may be stored locally, transmitted to another locations.

Table 5.4.x-1: Modules of camera model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| mediaType | mediaType | false | See clause 5.3.xx |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |
| deviceAirPurifier |  |
| deviceAirQualityMonitor |  |
| deviceFreezer |  |
| deviceMultiFunctionPrinter |  |
| deviceClothesDryer |  |
| deviceAudioReceiver |  |
| deviceScanner |  |
| deviceCooktop |  |
| deviceFoodProbe |  |
| deviceSetTopBox |  |
| deviceCamera |  |

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-2

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| mediaSelect |  |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| geoLocation |  |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keepWarm |  |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| numberValue |  |
| oximeter | oximr |
| playerControl |  |
| phoneCall |  |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage |  |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| dimmingLevel |  |
| airPurifierJobMode |  |
| dehumidifierJobMode |  |
| autoDocumentFeeder |  |
| clothesDryerJobMode |  |
| heatingZone |  |
| mediaType |  |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 6.3.3 Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-2: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| accuracy | geoLocation |  |
| adfStates | autoDocumentFeeder |  |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation |  |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| callerID | phoneCall |  |
| callState | phoneCall |  |
| channelNumber | televisionChannel | chaId |
| channelName | televisionChannel |  |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentAdfState | autoDocumentFeeder |  |
| currentDate | clock | curDe |
| currentJobMode | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode |  |
| currentJobModeName | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode |  |
| currentPlayerMode | playerControl |  |
| currentPlayerModeName | playerControl |  |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defaultValue | numberValue, textMessage |  |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| heading | geoLocation |  |
| headingAccuracy | geoLocation |  |
| heatingLevel | heatingZone |  |
| hash | binaryObject |  |
| height | height | heigt |
| horizontalAccuracy | geoLocation |  |
| mediaID | mediaSelect |  |
| jobModes | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode |  |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| latitude | geoLocation |  |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| longitude | geoLocation |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| maxLength | textMessage |  |
| MaxHeatingLevel | heatingZone |  |
| maxValue | audioVolume, temperature, numberValue | maxVe |
| mediaName | mediaSelect |  |
| mediaType | mediaSelect |  |
| messageEncoding | textMessage |  |
| minLength | textMessage |  |
| minValue | temperature, numberValue | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| object | binaryObject |  |
| type | binaryObject |  |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall |  |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject |  |
| speedFactor | playerControl | speedFactor |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, mediaSelect | stats |
| stepValue | audioVolume, temperature, numberValue | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedMediaSources | mediaSelect | suISs |
| supportedPlayerModes | playerControl |  |
| supportedTextMessage | textMessage |  |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetAltitude | geoLocation |  |
| targetLatitude | geoLocation |  |
| targetLongitude | geoLocation |  |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| textMessage | textMessage |  |
| time | keepWarm |  |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| verticalAccuracy | geoLocation |  |
| value | numberValue |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |
| currentSecurityMode | securityStatus |  |
| securityMode | securityStatus |  |
| url | mediaType |  |
| sdp | mediaType |  |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.3.xx mediaType

This ModuleClass specifies the media types supported.

Table 5.3.xx-1: DataPoints of mediaType ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| url | xs:string | true | true | true | url for the media instance |
| sdp | xs:string | true | true | true | SDP description syntax as defined in the SDP specification in RFC4566 [xx]. |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

## 2.1 Normative references

The following referenced documents are necessary, partially or totally, for the application of the present document. Their use in the context of this TS is specified by the normative statements that are referring back to this clause

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://github.com/Homegateway/SmartDeviceTemplate/tree/7c890b69d9764e341ef1768c5a0e7d53a47cff5c.

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: “Service Layer Core Protocol Specification”

[5]	oneM2M TS-0005: ”Management Enablement (OMA)”.

[6]	ISO:80000-1: Quantities and units

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

[7]	Open Mobile AllianceTM: “OMA-ER-Device_WebAPIs-V1_0-20160419-C”.

NOTE:	Available at

[8]	Open Mobile AllianceTM: “OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at

[9]	Open Mobile AllianceTM: “OMA-TS-Glucometer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[10]	Open Mobile AllianceTM: “OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at

[11]	Open Mobile AllianceTM: “OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C”.

NOTE:	Available at

[12]	Open Mobile AllianceTM: “OMA-TS-Thermometer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[13]	Open Mobile AllianceTM: “OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C”.

NOTE:	Available at

[14]	W3C Recommendation: “XML Schema Part 2: Datatypes”, 02 May 2001.

NOTE:	Available at http://www.w3.org/XML/Schema/.

[15]	NIST standard FIPS PUB 180-2

[xx]	IETF RFC 4566: "SDP: Session Description Protocol".

### -----------------------End of change 5-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?