| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#29 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-5-22 |
| Reason for Change/s:* | Creation of a new device data model (clothesDryer) |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.3.0 |
| Clauses * | 5, 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present document brings a new device data model for clothes dryer.

### -----------------------Start of change 1-------------------------------------------

### 5.4.x	deviceClothesDryer

A clothes dryer is a home appliance for drying clothes. This clothesDryer information model provides capabilities to control and monitor clothes dryer specific functions and resources.

Table 5.4.x-1: Modules of deviceClothesDryer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| runState | runState | true | See clause 5.3.28 |
| clothesDryerJobMode | clothesDryerJobMode | true | See clause 5.3.x |
| clothesDryerOperationMode | operationMode | true | See clause 5.3.51 This module instance is used to trigger clothesDryer operation. |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.x	clothesDryerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of clothesDryer.

Table 5.3.xx-1: DataPoints of clothesDryerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: clothesDryerJobMode | true | true | false | Currently active job mode. |
| currentJobModeName | xs:string | true | false | true | Name of current job mode in string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd: clothesDryerJobMode | true | false | false | List of possible job states the device supports (see clause 5.5.x) |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.x	hd: clothesDryerJobMode

Used for currentJobMode and jobModes DataPoints of clothesDryerJobMode ModuleClass.

Table 5.5.x-1: Interpretation of hd: clothesDryerJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal | Normal cycle |
| 2 | quick dry | About half the length of a normal cycle, this setting uses high heat to dry a few items. |
| 3 | permanent press | Slow drying with low heat helps wringkle-free garments live up to their name and keeps the hard creases out of thins you typically iron. |
| 4 | heavy duty | Tumbling for an extended period with high heat for sturdy items (towels, sweats, jeans) |
| 5 | delicates | A short, low-heat cycle for delicates and other items such as spandex workout gear, which loses its stretch when too much heat is used. |
| 6 | air dry | A cool-air setting for items that can’t take any heat, such as plastic tablecloths and rubber-backed rugs |
| 7 | extended tumble | Periodically tumbles clothes without heats for a preset amount of time after they’re dry to prevent wrinkles. |
| NOTE: See clause 5.3.xx "clothesDryerJobMode". Negative values are reserved for vendor specific modes. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |
| deviceAirPurifier |  |
| deviceClothesDryer |  |

.

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 6.3.2	Resource types

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| oximeter | oximr |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| airPurifierJobMode |  |
| clothesDryerJobMode |  |

### -----------------------End of change 5-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?