| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#29 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-5-23 |
| Reason for Change/s:* | Enhancement of the TV data model. |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.3.0 |
| Clauses * | 5.3, 5.4, 5.5, 6.3, 6.4, 6.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present document proposes to improve TV data model based on the real product.

R01:

- making audioVolume mandatory as agreed in the group

- movement of the clarifying sentence for maxValue in audioVolume to the maxValue description

- modication of audioVideoInput moduleClass so as to support output as well. (see the changes 6, 7)

R02:

- name change for audioVideoInput to mediaSelect

R03:

- short name modification for mediaSelect

### -----------------------Start of change 1-------------------------------------------

### 5.4.11	deviceTelevision

A television (TV) is a home appliance used to show audio and visual content such as broadcasting programs and network streaming. This TV information model provides capabilities to control and monitor TV specific resources.

Table 5.4.11-1: Modules of deviceTelevision Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| audioVolume | audioVolume | true | See clause 5.3.6 |
| televisionChannel | televisionChannel | true | See clause 5.3.32 |
| playerControl | playerControl | true | See clause 5.3.xx |
| mediaInput | mediaSelect | true | See clause 5.3.2 |
| mediaOutput | mediaSelect | true | See clause 5.3.2 |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.3	audioVolume

This ModuleClass provides capabilities to control and monitor volume

Table 5.3.3-1: Actions of audioVolume

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upVolume | none | true | Increase volume by the amount of the stepValue up to the maxValue. |
| none | downVolume | none | true | Decrease volume by the amount of the stepValue down to 0. |

Table 5.3.3-2: DataPoints of audioVolume

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| volumePercentage | xs:integer | true | true | false | The rounded percentage of the current volume in the range of [0, maxValue]. 0 percentage shall mean no sound produced. |
| stepValue | xs:integer | true | false | true | Step value used by UpVolume and DownVolume Actions. |
| maxValue | xs:integer | true | false | true | Maximum value allowed for Volume. maxValue is 100 by default if “maxValue” is not provided. |
| muteEnabled | xs:boolean | true | true | false | The current status of the mute enablement. "True" indicates enabled, and "False" indicates not enabled. |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.3.32	televisionChannel

This ModuleClass provides capabilities to set and get channels of a device that has a channel list.

Table 5.3.32-1: Actions of televisionChannel ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upChannel | none | true | Change the current channel to the next channel in the stored list of available channels. If the current channel is the last one in the list, the new set channel may be the first one in the list. |
| none | downChannel | none | true | Change the current channel to the previous channel in the stored list of available channels. If the current channel is the first one in the list, the new set channel may be the last one in the list. |

Table 5.3.32-2: DataPoints of televisionChannel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| channelNumber | xs:string | true | true | false | Current channel number. |
| availableChannels | list of xs:integer | true | false | true | The list of available channel numbers which may be build by automatic scan and/or manual selction. |
| previousChannel | xs:integer | true | false | true | The channel number which was selected previously. |
| channelName | xs:string | true | false | true | Current human-friendly channel name in string (e.g., ‘CNN’), |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 5.3.x	playerControl

This ModuleClass provides capabilities to control and monitor the operational modes of a media player functionality.

Table 5.3.x-1: Actions of playerControl ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | nextTrack | none | true | Go forward to a next chapter, section or similar marker in the media. |
| none | previousTrack | none | true | Go back to a previous chapter, section or similar marker in the media. |

Table 5.3.x-2: DataPoints of playerControl ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentPlayerMode | hd:playerMode | true | true | false | The current mode of the player. |
| currentPlayerModeName | xs:string | true | false | true | Name of current player mode in string. This can be used when “currentPlayerMode” is vendor-specific. |
| supportedPlayerModes | list of hd:playerMode | true | false | false | List of supported modes for a player. |
| speedFactor | xs:float | true | true | true | The optional factor of speeding up or slowing down playback, rewind or fast forward. |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 5.5.x	hd:playerMode

Used for currentMode and supportedModes data points in the playerControl ModuleClass.

Table 5.5.x-1: Interpretation of playerMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | stop |  |
| 2 | play |  |
| 3 | pause |  |
| 4 | resume |  |
| 5 | record |  |
| 6 | rewind |  |
| 7 | fast-rewind |  |
| 8 | forward |  |
| 9 | fast-forward |  |
| 10 | searchPrevious |  |
| 11 | searchNext |  |
| NOTE: See clause 5.3.x “playerControl”. Negative values are reserved for vendor specific modes |

### -----------------------End of change 5-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 5.3.2	mediaSelect

This ModuleClass provides capabilities to control and monitor media input and output of device such as TV or SetTopBox.

Table 5.3.2-1: DataPoints of mediaSelect ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| mediaID | xs:integer | true | true | false | Numeric ID of activated media in the supported media list, supportedMediaSources. |
| supportedMediaSources | list of hd:supportedMediaSource | true | false | false | List of supported input or output media for the given device (see clause 5.5.2). |
| mediaName | xs:string | true | false | true | Specifies a pre-defined media input or output |
| status | xs:boolean | true | false | true | Specifies if the specific media instance is selected or not |
| mediaType | hd:supportedMediaSource | true | false | false | Specifies the type of the media |

### -----------------------End of change 6-------------------------------------------

### -----------------------Start of change 6-------------------------------------------

### 5.5.2	hd:supportedMediaSources

Used for supportedMediaSources DataPoint of mediaSelect ModuleClass.

Table 5.5.2-1: Interpretation of supportedMediaSources

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | tuner |  |
| 2 | component |  |
| 3 | composite |  |
| 4 | svideo |  |
| 5 | rgb |  |
| 6 | dvi |  |
| 7 | hdmi |  |
| 8 | displayPort |  |
| 9 | scart |  |
| 10 | externalStorage |  |
| 11 | network |  |
| NOTE: See clause 5.3.2 "mediaSelect". Negative values are reserved for vender specific sources. |

### -----------------------End of change 7-------------------------------------------

### -----------------------Start of change 8-------------------------------------------

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| mediaSelect |  |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |

### -----------------------End of change 8-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?