| Input Contribution |
| --- |
| Meeting ID* | MAS#29 |
| Title:* | New type definitions for Generic Interworking |
| Source:* | Joerg Swetina, NEC, joerg.swetina@neclab.eu |
| Date:* | 2017-05-22 |
| Input related to* | WI 0063, Release 3 Enhancements on Base Ontology & Generic Interworking) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | TS/-0030, v0.2.0 (Generic Interworking), TS-004, TS-0012 (Base Ontology) Note: TS-0001 is not affected! |
| Decision requested or recommendation:* | If MAS agrees to the general principle related CRs would follow in MAS, and PRO. |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Introduction

This contribution proposes a new way how generic interworking can implement communication between a communicating entity and the IPE.

It relies on a new type of structured attributes that allow to include type information in the structure of the attribute. It simplifies data flows considerably by enabling sending a command to the Interworked Device through a simple UPDATE of a corresponding dataPoint attribute. However, such an attribute may need to have a sub-structure (e.g. to contain the X and Y coordinates of the datapoint).

The IPE of the Interworked Device gets notified about this update, reads out the data of the dataPoint, converts it into the format of the technology of the Interworked Device and sends it out.

UPDATEing of single dataPoints is the preferred way, used e.g. in TS-0023, to ensure that sending a command is an atomic action.
For transparent interworking (i.e. sending strings of data that are serialized according to the technology of the Interworked Device) this is no problem, one simply can use containers to implement dataPoints.

However, for semantic interworking the approach taken in e.g. TS-0023 is to specify a new specialization of flexContainer – a new type of datapoint – for each structured data that need to be transmitted.

The use of application-specific flexContainers that are specified in the standard and compiled into the oneM2M system is justified when it helps to harmonize the common data model of a large industry segment, as it is the case for Home Appliances.
However, generic interworking wants to support interworking without the need of pre-compiled datastructures. The IPE relies on an ontology (e.g. provided as “.owl” file) that describes the names and the datatypes of the data-model of the Interworked Device. With this information the IPE constructs oneM2M resources that mimick the data-model of the input- / output parameters of the Interworked Device at runtime.

In release-2 this was accomplished by a system of containers and links to model structured data of these input- / output parameters.

A better way, that uses structured attributes instead of linked resources, is proposed in the current contribution.

The usage of a structured attribute type is not restricted to generic interworking, however, for the time being this type of attribute is only proposed for use in resources of type <genericInterworkingService> and <genericInterworkingOperationInstance> but it could also be made available in <containers> and <flexContainers>.

The following new types are needed:

General types

- anyTypedContent,

- listType,

- structureType, 	structureItem

Types specifically for generic interworking:

- dataPoint

- operation

The basic idea is that the dataPoints of a service are contained in a sequence (0..n occurrances) of attributes with attribute Name: “dataPoint” of the <genericInterworkingService> resource. All these attributes have the same type: m2m:dataPoint.

The real (user-)name of the dataPoint is contained in the ‘name’ element of a m2m:dataPoint type, while the (user-)data are contained in the ‘data’ element of m2m:dataPoint.

To achieve maximum flexibility the ‘data’ element of m2m:dataPoint has a new type: m2m:anyTypedContent, which allows to hold any kinds of data: simple types like integer, sting ..., list types and structure types.
Similarly all operations are contained in a sequence of a single type attribute – attribute Name: “operation”.

The building principle is shown in the figure below:

Noticeable differences to the previous way of implementing dataPoints and operations:

- both, dataPoints and operations, are now modelled as parts of a structured attribute of the <genericInterworkingService>.

- An operation (as part of operations attribute, contains only invocation Data

- The resultData of an operation are part of the resource <genericInterworkingOperationInstance> that is CREATEd for any operation that produces output

- It is proposed that operationState attribute (values: “data_transmitted_to_interworked_device”, “data_received_by_application”,  “operation_ended”, “operation_failed”) is applicable to both:

  - dataPoints (uni-direction transmission of data to / from interworked device)

and

  - operations (data transmission followed by response in the other direction).

- With the help of structured attributes data flows from/to the IPE can be considerably simplified (see below)

- In the reverse direction (IPE => communicating entity) the data flow using a dataPoint is analogous, but in case of transmission failure the IPE generally cannot detect it.

In the reverse direction (IPE => communicating entity) the data flow using an operation is analogous, but in case of transmission failure the IPE generally can only detect failure of sending resultParameters back to the Interworked Device.

# Proposed way forward:

- This work requires substantial changes to

- TS-0012 (Base Ontology) Section 7: on instantiation of classes as oneM2M resources

- TS-0030  (Generic Interworking)  on:

- Section 6: Functional specification of communication with the Generic interworking IPE and Abstraction Application Entity

- Section 7: FlexContainer specializations for Generic interworking

- TS-0004 (Protocol) – see below

- Note that TS-0001 (architecture) is not impacted.

- It is proposed to proceed as follows:

- Agree – together with the new TS-0033 (Proximal interworking) – on a harmonized way for the resource representation of Interworked Devices, e.g. as <AE>s.

- For TS-0012 (Base Ontology)

- Create a new section 7 (instantiation of classes as oneM2M resources) of TS-0012 based on the use of structured attributes in Rel-3 and based on the agreement in step 1

- Move the current section 7 of TS-0012 into a normative Annex, explaining that this is an optional way for instantiation of classes and is included for backward compatibility with Rel-2

- For TS-0030  (Generic Interworking)

- Create a new section 6 (Functional specification of communication with the Generic interworking IPE and Abstraction Application Entity) based on the use of structured attributes in Rel-3 and based on the agreement in step 1

- Move existing section 6 into normative Annex for TS-0030 - as done in step 3

- Modify section 7 (FlexContainer specializations for Generic interworking) to allow both options (backward compatible).

- For TS-0004 (Protocol):

- Create CR with the content below and create related XSDs.

# Proposed new type definitions for TS-0004:

#### 6.3.5.x		m2m: anyTypedContent

Table 6.3.5.23-1: Type Definition of m2m:anyTypedContent

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| String | xs:string | 0..1 |  |
| Boolean | xs:boolean | 0..1 |  |
| Double | xs:double | 0..1 |  |
| hexBinary | xs:hexBinary | 0..1 |  |
| Integer | xs:integer | 0..1 |  |
| unsignedLong | xs:unsignedLong | 0..1 |  |
| list | m2m:listType | 0..1 |  |
| structure | m2m:structureType | 0..1 |  |

This type is an xs:choice. It shall contain exactly one element from a row listed in the table above.

#### 6.3.5.x		m2m:listType

Table 6.3.5.4-1: Type Definition of m2m:listType

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| listItem | m2m:anyTypedContent | 0..n |  |

#### 6.3.5.x		m2m:structureType

Table x.x.x.x-1: Type Definition of m2m:structureType

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| structureItem | m2m:structureItem | 0..n |  |

#### 6.3.5.x		m2m:structureItem

Table x.x.x.x-1: Type Definition of m2m:structureItem

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| itemName | xs:NCName | 1 |  |
| itemContent | m2m:anyTypedContent | 1 |  |

#### 6.3.5.x		m2m:dataPoint

Table x.x.x.x-1: Type Definition of m2m:dataPoint

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName | 1 |  |
| data | m2m:anyTypedContent | 1 |  |

#### 6.3.5.x		m2m:operation

Table x.x.x.x-1: Type Definition of m2m:operation

| Element Path | Element Data Type | Multiplicity | Note |
| --- | --- | --- | --- |
| name | xs:NCName | 1 |  |
| invocationData | m2m:dataPoint | 0..n |  |

(normative): 
Specializations of <flexContainer> resource

  - Introduction

This annex defines each specialization of <flexContainer> resource that are used for generic interworking [35] and AllJoyn interworking [36]. The <flexContainer> resource and procedures are defined in the clause 7.4.37. Since the specialization resources handling procedures are the same as <flexContainer> resource, this annex does not specify them. Also, since all the specialization inherits the universal/common attributes of <flexContainer> resource, this annex does not specify that information.

Resource type [genericInterworkingService]

This resource type is used for grouping Input and/or Output Datapoints and/or OperationInstances of a Service in the context of Ontology based Interworking. The detailed description of the [genericInterworkingService] resource can be found in clause 9.2 of oneM2M TS-0012 [35].

Table J.2-1: Data type definition of [genericInterworkingService] resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| genericInterworkingService | CDT-genericInterworkingService-v3_1_0.xsd | XSD schema for genericInterworkingService resource |

Table J.2-2: Resource Specific Attributes of [genericInterworkingService] resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| containerDefinition | M | NP | xs:anyURI | No default |
| ontologyRef | O | O | xs:anyURI | No default |
| serviceName | M | NP | xs:string | No default. |
| inputDataPointLinks | O | O | m2m:listOfDataLinks | No default |
| outputDataPointLinks | O | O | m2m:listOfDataLinks | No default |
| dataPoint | O | O | m2m:dataPoint | No default |
| operation | O | O | m2m:operation | No default |

How can I indicate multiplicity 0..n of the new attributes ??

Resource type [genericInterworkingOperationInstance]

This resource type and is used for grouping (persistent) Input and/or Output Datapoints and/or (transient) OperationInput / Output of an Operation in the context of Ontology based Interworking. Resources of resource type genericInterworkingOperationInstance are created as child-resources of a genericInterworkingService. The detailed description of the [genericInterworkingService] resource can be found in clause 9.2 of oneM2M TS-0012 [35].

Table J.3-1: Data type definition of [genericInterworkingOperationInstance] resource

| Data Type ID | File Name | Note |
| --- | --- | --- |
| genericInterworkingOperationInstance | CDT-genericInterworkingOperationInstance-v3_1_0.xsd | XSD schema for genericInterworkingOperationInstance resource |

Table J.3-2: Resource Specific Attributes of [genericInterworkingOperationInstance] resource

| Attribute Name | Request Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | Create | Update |  |  |
| containerDefinition | M | NP | xs:anyURI | No default |
| ontologyRef | O | O | xs:anyURI | No default |
| operationName | M | NP | xs:string | No default |
| inputDataPointLinks | O | O | m2m:listOfDataLinks | No default |
| outputDataPointLinks | O | O | m2m:listOfDataLinks | No default |
| inputLinks | O | O | m2m:listOfDataLinks | No default |
| outputLinks | O | O | m2m:listOfDataLinks | No default |
| operationState | O | O | xs:string | No default |
| invocationData | O | O | m2m:dataPoint | No default |
| resultData | O | O | m2m:dataPoint | No default |

How can I indicate multiplicity 0..n of the new attributes ??