| CHANGE REQUEST |
| --- |
| Meeting:* | MAS #29 |
| Source:* | BeiXu, Huawei, echo.xubei@huawei.com Ada, Huawei, xiaoyang.xiao@huawei.com |
| Date:* | 2017-05-10 |
| Contact:* | echo, Huawei, echo.xubei@huawei.com |
| Reason for Change/s:* | A new LwM2M Event Log object can be registered based on 5 LwM2M reusable event log resources which have been registered on the OMA web, and this proposal is provided to add new LwM2M Event Log object definition and the mapping from oneM2M resource [eventLog] to the new LwM2M Event Log object. |
| CR against: Release* | <Release 3> |
| CR against: WI* | Active < Work Item number > MNT maintenace / < Work Item10> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0005 v3.0.0 |
| Clauses/Sub Clauses* | 6.3.11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separated “mirror CR” should be posted at the same time of this CR

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

OMA LwM2M has registered 5 reusable resources (4010 - LogClass, 4011 - LogStart, 4012 – LogStop, 4013 – LogStatus, 4014 - LogData) which are used to record the event log for the device. Based on those resources oneM2M can register a new LwM2M Event Log object in OMA to implement the mapping from oneM2M resource [eventLog] to a LwM2M Object.

This proposal is provided to add a new LwM2M Event Log object definition and the mapping from oneM2M resource [eventLog] to the LwM2M Event Log Object.

A Liaison Statement shall be provided to OMA DM work group and OMNA for registering a new LwM2M Event Log Object.

### -----------------------Start of change 1-------------------------------------------

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. For OMA LwM2M, this Resource shall be mapped to one instance of LwM2M Event Log Object (LwM2M Object: {xx}), which is registered in OMNA as LwM2M objects produced by oneM2M (using ext-lable).

Editor’s Note: The object ID of  LwM2M Event Log Object shall be updated when the object register is finished on OMNA.

Editor’s Note: The mapping currently define in this clause provides a straightforward and generic means to use LwM2M as the underlying event log management tehchnology. It’s foreseen that OMA may further define LwM2M objects for specific log purpose (e.g. by associating re-usable log resources with existing objects). When available, the mapping in this clause will to be updated accordingly.

The context of this Resource is as follows.

# Table 6.3.11-1 Context of resource [eventLog]

| Context | Mapping |
| --- | --- |
| objectIDs | urn:oma:lwm2m:ext:{xx} |
| objectPath | /{xx}/{i} |

The attributes of this Resource shall be mapped to LwM2M Device Object Instance as follows.

# Table 6.3.10-2 Attributes of resource [eventLog]

| Attribute Name of [eventLog] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| logTypeId | 4010 LogClass |
| logData | 4014 LogData |
| logStatus | 4013 LogStatus |
| logStart | 4011 LogStart |
| logStop | 4012 LogStop |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

#### 6.6.1.x	Event Log Object

# This Object defines set of parameters which can be referenced by a specific Instance of the Event Log Object (ID:xx)

# Table 6.6.1.x-1: Object definition

| Name | Object ID | Instances | Mandatory | Object URN |
| --- | --- | --- | --- | --- |
| Event Log | xx | Multiple | Optional | urn:oma:lwm2m:ext:xx |

Table 6.6.1.x-2: Resource definitions

| ID | Name | Operations | Instances | Mandatory | Type | Range or Enumeration | Units | Description |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4010 | LogClass | R | Single | Mandatory | Integer | 0..255 |  | Define the Log Event Class: 0: generic (default) 1: system 2: security 3: event 4: trace 5: panic 6: charging [7-99]: reserved [100-255]: vendor specific |
| 4011 | LogStart | E | Single | Mandatory |  |  |  | a) Start data collection(DC) b) LogStatus is set to 0 (running) c) DC is emptied(default) or extended according to arg'0' value d) DC Period is set according to arg'1' value Arguments '0': DC emptied(=0[default] or extended(=1) '1': set the DC Period (in sec): if=0 or absent[default] DC is stopped by LogStop action only. |
| 4012 | LogStop | E | Single | Mandatory |  |  |  | a) Stop data collection(DC) b) LogStatus is set to 1 (stopped) c) DC is kept(default) or emptied according to arg'0' value Argument: '0': DC kept(=0)[default]or emptied(=1) |
| 4013 | LogStatus | R | Single | Mandatory | Integer | 0..255 |  | Data Collection process status: 0 : running 1 : stopped [2-99] : reserved [100-255] : vendor specific. |
| 4014 | LogData | R | Single | Mandatory | Opaque |  |  | Read Access on that Resource returns the Data Collection associated to the current Object Instance. Data format followed by this Opaque Resource is given by the 1st byte of the opaque sequence: 0 : OMA-LwM2M TLV format 1 : OMA-LwM2M JSON format 2 : OMA-LwM2M CBOR format [3..99] reserved [100..255] vendor specific |

### -----------------------End of change 2---------------------------------------------

CHECK LIST

- Does this change request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror crs been posted?

- Does this change request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable?

- Does this change request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete sections need not show surrounding clauses as long as the proposed section number clearly shows where the new section is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?