## Slide 1: Discussion on updating multiple data points in ModuleClasses
Group Name: MAS
Source: Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de Maciej Goluch, Orange, maciej.goluch@orange.com Meeting Date: 2017-05-22
Notes: 改一改Source和date

## Slide 2: Problem Description
Resources are updated atomically in oneM2M.
Example for a <flexContainer> (pseudo-code):
  PUT <flexContainer>-URL
  <m2m:fcnt>
  <dp1 type="integer">1</dp1>
  <dp2 type="integer">2</dp2>
  </m2m:fcnt>
This sets dp1 and dp2 both at the same time.

## Slide 3: Problem Description
How is this done in a programming language mapping?
  myModuleClass.dp1 = 1 (A)
  myModuleClass.dp2 = 2
Or only
  myModuleClass.dp1 = 1 (B)
Or only
  myModuleClass.dp2 = 2 (C)
How does the internal mapping mechanism of „myModuleClass“ know when the calling code is finished setting data points („dp1“ and „dp2“) and that it now can start to update the oneM2M resource?

## Slide 4: 1: Simple Solution
Update the resource immediately and for each updated data point.
Pros
  No changes needed.
Cons
  The problem is not solved, but only deferred to the device.
  One update request per updated data point.
  May result in wrong behaviour of devices when setting contradictory values.
  May result in superflous network load and unreachable devices (e.g. duty cycle).

## Slide 5: 2a: Leave It Up to the Implementation
Programming language APIs or frameworks define own means to indicate a finished update:
  myModuleClass.dp1 = 1
  myModuleClass.dp2 = 2
  myModuleClass.commit()
Pros
  No changes needed in oneM2M.
Cons
  Bad API design.
  This will result in non-interoperable language and framework bindings.
  Hard to learn, to understand, and error-prone.

## Slide 6: 2b: Leave It Up to the Implementation
Programming language APIs or frameworks define own method for updating multiple Datapoints:
  myModuleClass.setDataPointList(listOfDataPoints)
Pros
  No changes needed in oneM2M.
Cons
  This will result in non-interoperable language and framework bindings.

## Slide 7: 3: Introduce Actions
Add actions to update semantically interconnected datapoints.
  myModuleClass.setSpecificDataPoints(dp1, dp2)
Pros
  Clear indication of a transactional update and semantical intent.
  Better APIs and programming language-dependend frameworks.
  Better self-documentation and less error-prone use.
Cons
  Changes needed in oneM2M for ModuleClasses with interconnected data points (e.g. colour).

## Slide 8: 4: Introduce „common operation”
Add a new common operation to update semantically interconnected datapoints. Similar to 2b), but oneM2M-genericly specified.
  myModuleClass.setDataPoints(listOfDataPoints)
Pros of the „3: Introduce Actions” solution + listed below:
  Common solution: no need for consideration which ModuleClasses have interconnected Datapoints
  Flexibility: developer decides which Datapoints are interconnected
  No problem with optional Datapoints
Cons
  Change needed in oneM2M: each ModuleClass has a common Action

## Slide 9: Backup

## Slide 10: Candidate ModuleClasses
First scan of ModuleClasses that might need additional actions reveal the following set:
alarmSpeaker
clock
colour
runState
timer
wind
grinder
brewing
washingCourse
washingCourseOption
+ new ModuleClasses added

## Slide 11
Thank you for your attention