| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#30 |
| Source:* | NTT, NTT DOCOMO |
| Date:* | 2017-07-10 |
| Contact:* | Kei Harada(harada.kei@lab.ntt.co.jp), NTT, Hiroyuki Maeomichi(maeomichi.hiroyuki@lab.ntt.co.jp), NTT, Takashi Yoshikawa(yoshikawatak@nttdocomo.com), NTT DOCOMO |
| Reason for Change/s:* | To add the SubDevice table on some Device model. |
| CR against: Release* | R3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.4.1 |
| Clauses * | 5.4, 6.3 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0023 |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This contribution proposed to add the SubDevice concept and tables on Device model.

Additionally, I create rooms for Short names, containerDefinition values and XSD definitions for  new SubDevice and property.

R01: Change subDevice name, locate existing property instead of propPartNumber and deleate several subDevice tables.

R02: Add the SubDevice model clause and relocate module classes of device model to SubDevice model.

### -----------------------Start of change 1-------------------------------------------

Contents

Contents	3

1	Scope	7

2	References	7

2.1	Normative references	7

2.2	Informative references	8

3	Definitions	8

4	Conventions	8

5	Home Appliance Information Model	8

5.1	Introduction	8

5.2	Design Principle of the Home Appliance Information Model	9

5.2.1	Basic design principle of information modelling	9

5.2.2	Description rules for Module Classes and Device models	9

5.3	ModuleClasses	11

5.3.1	alarmSpeaker	11

5.3.2	mediaSelect	11

5.3.3	audioVolume	11

5.3.4	battery	12

5.3.5	binarySwitch	12

5.3.6	bioElectricalImpedanceAnalysis	13

5.3.7	boiler	13

5.3.8	brightness	13

5.3.9	clock	13

5.3.10	colour	13

5.3.11	colourSaturation	14

5.3.12	doorStatus	14

5.3.13	electricVehicleConnector	14

5.3.14	energyConsumption	14

5.3.15	energyGeneration	15

5.3.16	faultDetection	15

5.3.17	height	15

5.3.18	hotWaterSupply	16

5.3.19	keypad	16

5.3.20	motionSensor	16

5.3.21	oximeter	16

5.3.22	powerSave	17

5.3.23	pushButton	17

5.3.24	recorder	17

5.3.25	refrigeration	17

5.3.26	relativeHumidity	17

5.3.27	openLevel	18

5.3.28	runState	18

5.3.29	signalStrength	18

5.3.30	smokeSensor	19

5.3.31	spinLevel	19

5.3.32	televisionChannel	19

5.3.33	temperature	20

5.3.34	temperatureAlarm	20

5.3.35	timer	20

5.3.36	turbo	21

5.3.37	waterFlow	21

5.3.38	liquidLevel	22

5.3.39	waterSensor	22

5.3.40	weight	22

5.3.41	wind	22

5.3.42	doorLock	23

5.3.43	liquidRemaining	23

5.3.44	foaming	23

5.3.45	grinder	23

5.3.46	brewing	24

5.3.47	sphygmomanometer	24

5.3.48	pulsemeter	24

5.3.49	glucometer	25

5.3.50	bodyCompositionAnalyzer	25

5.3.51	operationMode	25

5.3.52	remoteControlEnable	26

5.3.53	washingCourse	26

5.3.54	washingCourseOption	26

5.3.55	keepWarm	26

5.3.56	airQualitySensor	27

5.3.57	filterInfo	27

5.3.58	airConJobMode	27

5.3.59	binaryObject	28

5.3.59.1	geoLocation	28

5.3.60	numberValue	29

5.3.61	phoneCall	30

5.3.62	playerControl	30

5.3.63	textMessage	31

5.3.64	securityStatus	31

5.3.65	airPurifierJobMode	32

5.3.66	dehumidifierJobMode	32

5.3.67	autoDocumentFeeder	32

5.3.68	clothesDryerJobMode	32

5.3.69	heatingZone	33

5.4	SubDevice models	33

5.4.1	subDeviceCuff	33

5.5	Device models	33

5.5.1	deviceAirConditioner	33

5.5.2	deviceClothesWasher	34

5.5.3	deviceElectricVehicleCharger	34

5.5.4	deviceLight	35

5.5.5	deviceMicrogeneration	35

5.5.6	deviceOven	35

5.5.7	deviceRefrigerator	35

5.5.8	deviceRobotCleaner	36

5.5.9	deviceSmartElectricMeter	36

5.5.10	deviceStorageBattery	36

5.5.11	deviceTelevision	37

5.5.12	deviceThermostat	37

5.5.13	deviceWaterHeater	37

5.5.14	deviceSwitch	37

5.5.15	deviceWindowShade	38

5.5.16	deviceDoorLock	38

5.5.17	deviceCoffeeMachine	38

5.5.18	deviceBloodPressureMonitor	38

5.5.19	deviceGlucosemeter	38

5.5.20	devicePulseOximeter	39

5.5.21	deviceThermometer	39

5.5.22	deviceWeightScaleAndBodyCompositionAnalyzer	39

5.5.23	deviceHeartRateMonitor	39

5.5.24	deviceKettle	40

5.5.25	deviceHumidifier	40

5.5.26	deviceDehumidifier	40

5.5.27	deviceDishWasher	40

5.5.28	deviceFan	40

5.5.29	devicePrinter	41

5.5.30	deviceWaterValve	41

5.5.31	deviceDoor	41

5.5.32	deviceSmartPlug	41

5.5.33	deviceSecurityPanel	41

5.5.34	devicePurifier	42

5.5.35	deviceAirQualityMonitor	42

5.5.36	deviceFreezer	42

5.5.37	deviceMultiFunctionPrinter	42

5.5.38	deviceClothesDryer	43

5.5.39	deviceAudioReceiver	43

5.5.40	deviceScanner	43

5.5.41	deviceCooktop	43

5.5.42	deviceFoodProbe	44

5.5.43	deviceSetTopBox	44

5.6	Enumeration type definitions	44

5.6.1	hd:deviceType	44

5.6.2	hd:supportedMediaSources	45

5.6.3	hd:liquidLevel	45

5.6.4	hd:spinLevelStrength	46

5.6.5	hd:doorState	46

5.6.6	hd:tone	46

5.6.7	hd:jobStates	46

5.6.8	hd:alertColourCode	47

5.6.9	hd:waterFlowStrength	48

5.6.10	hd:windStrength	48

5.6.11	hd:grainsLevel	48

5.6.12	hd:foamStrength	48

5.6.13	hd:tasteStrength	49

5.6.14	hd:grindCoarseness	49

5.6.15	hd:machineState	49

5.6.16	hd:washingCourse	50

5.6.17	hd:generalTemperature	50

5.6.18	hd:generalLevel	50

5.6.19	hd:generalSpeed	50

5.6.20	hd:airConJobMode	51

5.6.21	hd:callState	51

5.6.22	hd:playerMode	51

5.6.23	hd:securityMode	51

5.6.24	hd:airPurifierJobMode	52

5.6.25	hd:dehumidifierJobMode	52

5.6.26	hd:adfState	52

5.6.27	hd:clothesDryerJobMode	53

5.7	Universal and Common Properties for Device models	53

6	The Principle of Resource Mapping for Home Appliance Information Model	54

6.1	Introduction	54

6.2	The Resource Mapping Rules	54

6.2.1	Introduction	54

6.2.2	Resource mapping for Device model	54

6.2.3	Resource mapping for ModuleClass	54

6.2.4	Resource mapping for Action	55

6.2.5	Resource mapping for Property	55

6.2.6	Resource mapping for DataPoint	55

6.3	Short names	55

6.3.1	Introduction	55

6.3.2	Resource types	56

6.3.3	Resource attributes for properties and data points	58

6.4	containerDefinition values	62

6.4.1	Introduction	62

6.4.2	Device models	62

6.4.3	ModuleClasses	62

6.4.4	Actions	62

6.5	XSD definitions	62

6.5.1	Introduction	62

6.5.2	XSD definitions for Device models	63

6.5.3	XSD definitions for ModuleClass	63

6.5.4	XSD definitions for Action	63

7	Mapping with Other Information Models from External Organizations	63

7.1	OMA GotAPI(DWAPI-PCH)	63

7.1.1	Introduction	63

7.1.2	Device Models	64

7.1.2.1	deviceBloodPressureMonitor	64

7.1.2.2	deviceGlucosemeter	64

7.1.2.3	devicePulseOximeter	65

7.1.2.4	deviceThermometer	66

7.1.2.5	deviceWeightScaleAndBodyCompositionAnalyzer	66

7.1.2.6	deviceHeartRateMonitor	67

7.1.3	Data Types	68

8	Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology	68

A	(informative):  Resource Mapping Examples	69

A.1	Introduction	69

A.2	Example for Device model ‘deviceAirConditioner'	70

A.3	Example of ModuleClass 'binarySwitch'	71

A.4	Example of Action 'toggle'	72

B	(informative):  Introduction of Extarnal Organizations Data Model	73

B.1	OMA Got API(DWAPI-PCH)	73

B.2	OCF	74

B.3	ECHONET	74

C	History	74

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

## 5.4	SubDevice models

### 5.4.1 subDeviceCuff

A  cuff is a subDevice that expresses the attachment device for measuring blood pressure.

Table 5.4.1-1: Modules of subDeviceCuff model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.5 |
| sphygmomanometer | sphygmomanometer | false | See clause 5.3.47 |
| pulsemeter | pulsemeter | false | See clause 5.3.48 |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.18	deviceBloodPressureMonitor

A device blood pressure is a device that can be used to monitor the blood  pressure.

Table 5.5.18-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| battery | battery | false | See clause 5.3.4 |

Table 5.5.18-2: Subdevice of deviceBloodPressureMonitor Device model

| Subdevice Name | Multiplicity | Optional | Description |
| --- | --- | --- | --- |
| cuff | 0..n | false | See clause 5.4.1 |

### -----------------------End of change 3-------------------------------------------

-----------------------Start of change 4-------------------------------------------

## 6.3	Short names

### 6.3.1	Introduction

XML and JSON representations require the explicit encoding of the names of resource attributes, (in the case of XML) and resource types. Whenever a protocol binding transfers such a name over a oneM2M reference point, it shall use a shortened form of that name. Short names enable payload reduction on involved telecommunication interfaces.

The mapping between the full names and their shortened form is given in the clauses that follow.

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |

In protocol bindings resource type names for SubDevice model shall be translated into short names of Table 6.3.2-2.

Table 6.3.2-2: Specialization type short names (SubDevice models)

| Resource Type Name | Short Name |
| --- | --- |
| cuff |  |

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-3

Table 6.3.2-3: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| audioVideoInput | auVIt |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| geolocation |  |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keepWarm |  |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| numberValue |  |
| oximeter | oximr |
| playerControl |  |
| phoneCall |  |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage |  |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| dimmingLevel |  |

In protocol bindings resource type names for actions shall be translated into short names of Table 6.3.2-4.

Table 6.3.2-4: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activateClockTimer | acCTr |
| answer |  |
| call |  |
| deactivateClockTimer | deCTr |
| decrementNumberValue |  |
| downChannel | dowCl |
| downVolume | dowVe |
| nextTrack |  |
| previousTrack |  |
| hangup |  |
| incrementNumberValue |  |
| resetNumberValue |  |
| resetTextMessage |  |
| toggle | togge |
| upChannel | uphCl |

### 6.3.3	Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| accuracy | geoLocation |  |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation |  |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| callerID | phoneCall |  |
| callState | phoneCall |  |
| channelId | televisionChannel | chaId |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentDate | clock | curDe |
| currentPlayerMode | playerControl |  |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defaultValue | numberValue, textMessage |  |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| hash | binaryObject |  |
| height | height | heigt |
| inputSourceID | audioVideoInput | inSId |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| maxLength | textMessage |  |
| maxValue | audioVolume, temperature, numberValue | maxVe |
| messageEncoding | textMessage |  |
| minLength | textMessage |  |
| minValue | temperature, numberValue | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| object | binaryObject |  |
| type | binaryObject |  |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-4: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall |  |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject |  |
| speedFactor | playerControl | speedFactor |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply | stats |
| stepValue | audioVolume, temperature, numberValue | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedInputSources | audioVideoInput | suISs |
| supportedPlayerModes | playerControl |  |
| supportedTextMessage | textMessage |  |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| textMessage | textMessage |  |
| time | keepWarm |  |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| value | numberValue |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |
| currentSecurityMode | securityStatus |  |
| securityMode | securityStatus |  |

-----------------------End of change 4-------------------------------------------