| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#30 |
| Source:* | Andreas Kraft, Deutsche Telekom, a.kraft@telekom.de |
| Date:* | 2017-06-30 |
| Reason for Change/s:* | Adding a new rule when to differentiate between current and target Data Points in TS-0023 ModuleClasses |
| CR against: Release* | Rel.3 |
| CR against: WI* | Active WI-0017 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.4.1 |
| Clauses * | New text in 5.2.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

## Introduction

This CR introduces new text for chapter 5.2.2 of T-0023 (Description rules for Module Classes and Device models). The text adds a new rule and provides guidance when a ModuleClass needs to distinguish between the current and the target value of a data point.

### -----------------------Start of change 1-------------------------------------------

5.2.2	Description rules for Module Classes and Device models

- Rule 11: When to differentiate between current and target Data Points in ModuleClasses:

  - Device operations, which are executed when setting data points to specific values, may take some time to reach the desired result. For example, setting a new temperature to a heater does not immediately change the room temperature, but it may take some time for the heater to increase the temperature. Therefore, it is sometimes necessary to distinguish between current and target data points.

  - A ModuleClass must provide an additional “target” data point when the “current” data point …

    - is writable, and

    - the functionality that is mapped to the data point is an operation, not a configuration function, and

    - the operation may take some time to start and/or to complete, or reach the desired result.

  - When a ModuleClass provides current and target data points then the name for the current data point must have the prefix “current”, and the name for the target data point must have the prefix “target”.

### -----------------------End of change 1---------------------------------------------