| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#30 |
| Source:* | Dongjoo Kim (dongjoo7.kim@lge.com) |
| Date:* | 2017-7-10 |
| Reason for Change/s:* | Addition of the steam closet device model |
| CR against: Release* | Rel-3 |
| CR against: WI* | Active <WI-0056> MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0023 V3.3.1 |
| Clauses * | 5, 6 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | None |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

The present document proposes to add a new device. Its name is steamCloset. This device has functions that reduces odors, steams wrinkles, helps cleaning and dries gently of clothes.

### -----------------------Start of change 1-------------------------------------------

### 5.4.x	deviceSteamCloset

A deviceSteamCloset is a home appliance that de-wrinkles, sanitizes and dries to clean fabrics similar to  a dry cleaner. This information model provides capabilities to interact with specific functions and resources of the steam closet.

Table 5.4.x-1: Modules of deviceSteamCloset Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.5 |
| runState | runState | true | See clause 5.3.28 |
| steamClosetJobMode | steamClosetJobMode | false | See clause 5.3.x |
| steamClosetOperationMode | operationMode | true | See clause 5.3.x |

### -----------------------End of change 1-------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.3.x	steamClosetJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of steamCloset.

Table 5.3.x-1: DataPoints of steamClosetJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd: steamClosetJobMode | true | true | false | Currently active job mode. |
| currentJobModeName | xs:string | true | false | true | Name of current job mode in string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd: steamClosetJobMode | true | false | false | List of possible job states the device supports (see clause 5.5.x) |

### -----------------------End of change 2-------------------------------------------

### -----------------------Start of change 3-------------------------------------------

### 5.5.x	hd:steamClosetJobMode

Used for currentJobMode and jobModes DataPoints of steamClosetJobMode ModuleClass.

Table 5.5.x-1: Interpretation of hd:steamClosetJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | reduceOdor | Using pure water, the machine help remove the smells on clothes |
| 2 | steamWrinkle | The machine steams away wrinkles and also creates pant creases, as well as keep them crisp |
| 3 | helpClean | Using pure water without chemical additives, the machine sanitizes fabrics and items that are difficult to wash |
| 4 | gentleDry | The machine dries fragile garments without worrying about shrinkage or damage |
| NOTE: See clause 5.3.x "steamClosetJobMode". Negative values are reserved for vendor specific modes. |

### -----------------------End of change 3-------------------------------------------

### -----------------------Start of change 4-------------------------------------------

### 6.3.2	Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| deviceAirConditioner | deACr |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |
| deviceAirPurifier |  |
| deviceAirQualityMonitor |  |
| deviceFreezer |  |
| deviceMultiFunctionPrinter |  |
| deviceClothesDryer |  |
| deviceAudioReceiver |  |
| deviceScanner |  |
| deviceCooktop |  |
| deviceFoodProbe |  |
| deviceSetTopBox |  |
| deviceSteamCloset |  |

Table 6.3.2-2: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| alarmSpeaker | alaSr |
| mediaSelect |  |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| geoLocation |  |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| keepWarm |  |
| keypad | keypd |
| liquidLevel |  |
| motionSensor | motSr |
| numberValue |  |
| oximeter | oximr |
| playerControl |  |
| phoneCall |  |
| powerSave | powS0 |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| steamClosetJobMode |  |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage |  |
| timer | timer |
| turbo | turbo |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| wind | wind |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| remoteControl |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| dimmingLevel |  |
| airPurifierJobMode |  |
| dehumidifierJobMode |  |
| autoDocumentFeeder |  |
| clothesDryerJobMode |  |
| heatingZone |  |

### -----------------------End of change 4-------------------------------------------

### -----------------------Start of change 5-------------------------------------------

### 6.3.3	Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-2: Resource attribute short names (ModuleClass data points) (1/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| accuracy | geoLocation |  |
| adfStates | autoDocumentFeeder |  |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation |  |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| callerID | phoneCall |  |
| callState | phoneCall |  |
| channelNumber | televisionChannel | chaId |
| channelName | televisionChannel |  |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentAdfState | autoDocumentFeeder |  |
| currentDate | clock | curDe |
| currentJobMode | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, steamClosetMode |  |
| currentJobModeName | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, steamClosetMode |  |
| currentPlayerMode | playerControl |  |
| currentPlayerModeName | playerControl |  |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defaultValue | numberValue, textMessage |  |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| directionAuto | wind | dirAo |
| directionDown | wind | dirDn |
| directionLeft | wind | dirLt |
| directionRight | wind | dirRt |
| directionUp | wind | dirUp |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | recorder | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | refrigeration | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| heading | geoLocation |  |
| headingAccuracy | geoLocation |  |
| heatingLevel | heatingZone |  |
| hash | binaryObject |  |
| height | height | heigt |
| horizontalAccuracy | geoLocation |  |
| mediaID | mediaSelect |  |
| jobModes | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, steamClosetMode |  |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| latitude | geoLocation |  |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| longitude | geoLocation |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| maxLength | textMessage |  |
| MaxHeatingLevel | heatingZone |  |
| maxValue | audioVolume, temperature, numberValue | maxVe |
| mediaName | mediaSelect |  |
| mediaType | mediaSelect |  |
| messageEncoding | textMessage |  |
| minLength | textMessage |  |
| minValue | temperature, numberValue | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| object | binaryObject |  |
| type | binaryObject |  |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| oxygenSaturation | oximeter | oxySn |

Table 6.3.3-3: Resource attribute short names (ModuleClass data points) (2/2)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall |  |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| rinseLevel | rinseLevel | rinLl |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject |  |
| speedFactor | playerControl | speedFactor |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, mediaSelect | stats |
| stepValue | audioVolume, temperature, numberValue | steVe |
| strength | spinLevel, waterFlow, wind, brewing | streh |
| supportedMediaSources | mediaSelect | suISs |
| supportedPlayerModes | playerControl |  |
| supportedTextMessage | textMessage |  |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetAltitude | geoLocation |  |
| targetLatitude | geoLocation |  |
| targetLongitude | geoLocation |  |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| textMessage | textMessage |  |
| time | keepWarm |  |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| verticalAccuracy | geoLocation |  |
| value | numberValue |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |
| currentSecurityMode | securityStatus |  |
| securityMode | securityStatus |  |

### -----------------------End of change 5-------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?