| CHANGE REQUEST |
| --- |
| Meeting:* | MAS #30 |
| Source:* | Thierry GARNIER, thierry.garnier@gemalto.com BeiXu, Huawei, echo.xubei@huawei.com Ada, Huawei, xiaoyang.xiao@huawei.com |
| Date:* | 2017-07-05 |
| Contact:* | Thierry GARNIER, Gemalto |
| Reason for Change/s:* | A LwM2M Event Log object definition has been endorsed by OMA fully compatible with oneM2M mapping needs. This CR reflects that statement and addresses few fine tuning to fit OMA work |
| CR against: Release* | <Release 3> |
| CR against: WI* | Active < Work Item number > MNT maintenace / < Work Item10> STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0005 v3.1.0 |
| Clauses/Sub Clauses* | 6.3.11, 6.6.2 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO This CR is a mirror CR? YES if YES, please indicate the document number of the original CR: <Document Number) : NO |
| Template Version:27 May 2015 (Dot not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### -----------------------Start of change 1-------------------------------------------

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. For OMA LwM2M, this Resource shall be mapped to one instance of LwM2M Event Log Object (LwM2M Object: {20}), which registration is about to be registered in OMNA. Editor’s Note: The object ID of  LwM2M Event Log Object shall be updated/confirmed when the object will be officially registered on OMNA.

Editor’s Note: The mapping currently defined in this clause provides a straightforward and generic means to use LwM2M as the underlying event log management technology. In case OMAfurther refines the LwM2M object under definition for that  log purpose, the mapping in this clause may have to be refined accordingly before release 3 publication.

# Table 6.3.11-1 Context of resource [eventLog]

| Context | Mapping |
| --- | --- |
| objectIDs | urn:oma:lwm2m:oma:{20} |
| objectPath | /{20}/{i} |

The attributes of this Resource shall be mapped to LwM2M Device Object Instance as follows.

# Table 6.3.10-2 Attributes of resource [eventLog]

| Attribute Name of [eventLog] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| logTypeId | 4010 LogClass 1 (system) if the logTypeId of oneM2M [eventLog] resource is “System”; 2 (security) if the logTypeId of oneM2M [eventLog] resource is “Security”; 3 or 6 (event of charging) if the logTypeId of oneM2M [eventLog] resource is “Event” The charging event shall be mapped to 6; generic events shall be mapped to 3; 4 (trace) if the logTypeId of oneM2M [eventLog] resource is “Trace”; 5 (panic) if the logTypeId of oneM2M [eventLog] resource is “Panic”. |
| logData | 4014 LogData When LogData is used and there are valid Data in it, the 1st Byte is set to 100, meaning the data encoding is vendor specific |
| logStatus | 4013 LogStatusoneM2M logStatus attribute is translated as follows to LwM2M LogStatus Resource 0 : when logging activity is started ( logStatus : 1) 1 : when logging activity is stopped without error (logStatus : 2) 3 : when logData attribute must be ignored (logStatus :4) 5 : when logging activity is stopped with error (logStatus :5) 80 : when the status of the logging activity is unknown (logStatus :3) |
| logStart | 4011 LogStart When oneM2M logStart attribute is set to “True”, CSE shall execute the LogStart command without argument (default) |
| logStop | 4012 LogStop When oneM2M logStop attribute is set to “True”, CSE shall execute the LogStop command without argument (default) |

### -----------------------End of change 1---------------------------------------------

### ----------------------Start of change 2-------------------------------------------

### -----------------------End of change 2---------------------------------------------