| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS-32 |
| Source:* | Wolfgang Granzow, Qualcomm, wgranzow@qti.qualcomm.com |
| Date:* | 2017-11-15 |
| Reason for Change/s:* | Adding Field Device Configuration mgmtObj specializations defined in TS-0022 into TS-0005 for OMA-DM |
| CR against: Release* | 3 |
| CR against: WI* | Active WI-0057 MNT maintenance / < Work Item number(optional)> Is this a companion CR? Yes No Companion CR number: (Note to Rapporteur - use latest agreed revision)Is this a mirror CR? Yes No Mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0005-V3.2.0 |
| Clauses * | 5.3.13 (new), 5.6.2 (new), 2.1 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) |  |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

## Introduction

This CR introduces the <mgmtObj> specializations into TS-0005 which are specified in TS-0022.

Revision R01:  -

- removal of Editor’s Notes (issues have been captured as action items)

- correction in the figure <x+> ( <x>+, completion of co, multiplicity corrections

- corrections in the tabular; multiplicity of mgmtLink of MAFClientRegCfg and MEFClientRegCfg

- generation of a new Device Description Framework (DDF)   XML file

- addition of Excel sheet which includes “DDFcreator” VBA macro to autogenerate oneM2M-MFDCMO.xml from the tabular model description

### -----------------------Start of change 1 (new section)-----------------------------------

### 5.3.13	Resource related to Field Device Configuration

#### 5.3.13.1	Introduction

The Resource Types addressed in the present clause represent <mgmtObj> specializations required to configure ADN, ASN and MN in the field domain. These resource types and the related specific procedures are specified in oneM2M TS-0022 [20]. The subclauses below define the mapping to and from a M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).  which is applicable to both, OMA DM 1.3 and OMA DM 2.0. The root node of the MFDCMO is denoted in the following by the leftmost placeholder node <x>.

#### 5.3.13.2	Resource [registration]

The Resource [registration] is used to convey the service layer configuration information needed to register an AE or CSE with a Registrar CSE, see clause 7.1.2 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [registration] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/registration/<x> node of MFDCMO.

The attributes of an instance of [registration] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.2-1.

The mgmtLink attribute of the [registration] resource points to an [authenticationProfile] resource instance which itself is mapped to a <x>/authenticationProfile/<x> node in MFDCMO.  The original value of this mgmtLink attribute  needs to be translated such that it points to the <x>/authenticationProfile/<x> node  in MFDCMO which corresponds to the linked [authenticationProfile] resource instance. The respective node identifier <x>/authenticationProfile/<x> of this [authenticationProfile] resource instance shall be set as the value of the <x>/dataCollection/<x>/authenticationProfile leaf node.

Table 5.3.13.2-1: Resource [registration]

| Attribute Name of [registration] | Mapping to Nodes in Management Object |
| --- | --- |
| originatorID | <x>/registration/<x>/originatorID |
| poA | <x>/registration/<x>/poA |
| appID | <x>/registration/<x>/appID |
| externalID | <x>/registration/<x>/externalID |
| triggerRecipientID | <x>/registration/<x>/triggerRecipientID |
| mgmtLink [authenticationProfile] | <x>/registration/<x>/authenticationProfile |

#### 5.3.13.3	Resource [dataCollection]

The Resource [dataCollection] is used to convey the application configuration information needed by an AE to collect data and then transmit the data to a Hosting CSE, see clause 7.1.3 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [dataCollection] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/dataCollection/<x> node of MFDCMO.

The attributes of an instance of [dataCollection] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.3-1.

The mgmtLink attribute of the [dataCollection] resource points to an [authenticationProfile] resource instance which itself is mapped to a <x>/authenticationProfile/<x> node in MFDCMO.  The original value of this mgmtLink attribute needs to be translated such that it points to the <x>/authenticationProfile/<x> node in MFDCMO which corresponds to the linked [authenticationProfile] resource instance. The respective node identifier <x>/authenticationProfile/<x> of this [authenticationProfile] resource instance shall be set as the value of the <x>/dataCollection/<x>/authenticationProfile leaf node.

Table 5.3.13.3-1: Resource [dataCollection]

| Attribute Name of [dataCollection] | Mapping to Nodes in Management Object |
| --- | --- |
| containerPath | <x>/dataCollection/<x>/containerPath |
| reportingSchedule | <x>/dataCollection/<x>/reportingSchedule |
| measurementSchedule | <x>/dataCollection/<x>/measurementSchedule |
| mgmtLink [authenticationProfile] | <x>/dataCollection/<x>/authenticationProfile |

#### 5.3.13.4	Resource [authenticationProfile]

The Resource [authenticationProfile] is used to convey the configuration information regarding establishing mutually-authenticated secure communications, see clause 7.1.4 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [authenticationProfile] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/authenticationProfile /<x> node of MFDCMO.

The attributes of an instance of [authenticationProfile] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.4-1.

A mgmtLink attribute of the [authenticationProfile] has one or more instantiations. The value of mgmtLink attribute either points to a [trustAnchorCred] resource, or to a [MAFClientRegCfg] resource. An [authenticationProfile] resource does not include mgmtLink attributes to both [trustAnchorCred] and [MAFClientRegCfg] resources. If there are more than one mgmtLink attribute in the [authenticationProfile] resource, these point all to [trustAnchorCred] resource instances.

For a mgmtLink attribute pointing to a [trustAnchorCred] resource, the linked [trustAnchorCred] resource instance itself is mapped to a <x>/trustAnchorCred/<x> node in MFDCMO. The respective node identifier <x>/trustAnchorCred/<x> of this [trustAnchorCred] resource instance shall be set as the value of the <x>/authenticationProfile/<x>/trustAnchorCred leaf node.

For a mgmtLink attribute pointing to a [MAFClientRegCfg] resource, the linked [MAFClientRegCfg] resource instance itself is mapped to a <x>/MAFClientRegCfg/<x> node in MFDCMO. The respective node identifier <x>/MAFClientRegCfg/<x> of this [MAFClientRegCfg] resource instance shall be set as the value of the <x>/authenticationProfile/<x>/trustAnchorCred leaf node.

Table 5.3.13.4-1: Resource [authenticationProfile]

| Attribute Name of [authenticationProfile] | Mapping to Nodes in Management Object |
| --- | --- |
| SUID | <x>/authenticationProfile/<x>/SUID |
| TLSCiphersuites | <x>/authenticationProfile/<x>/TLSCiphersuites |
| symmKeyID | <x>/authenticationProfile/<x>/symmKeyID |
| symmKeyValue | <x>/authenticationProfile/<x>/symmKeyValue |
| MAFKeyRegLabels | <x>/authenticationProfile/<x>/MAFKeyRegLabels |
| MAFKeyRegDuration | <x>/authenticationProfile/<x>/MAFKeyRegDuration |
| mycertFingerprint | <x>/authenticationProfile/<x>/mycertFingerprint |
| rawPubKeyID | <x>/authenticationProfile/<x>/rawPubKeyID |
| mgmtLink [trustAnchorCred] | <x>/authenticationProfile/<x>/trustAnchorCred |
| mgmtLink [MAFClientRegCfg] | <x>/authenticationProfile/<x>/MAFClientRegCfg |

#### 5.3.13.5	Resource [trustAnchorCred]

The Resource [trustAnchorCred] represents configuration information regarding certificates provided by certificate authorities used be managed entities to authenticate peer endpoints, see clause 7.1.6 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [trustAnchorCred] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/trustAnchorCred/<x> node of MFDCMO.

The attributes of an instance of [trustAnchorCred] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.5-1.

Table 5.3.13.5-1: Resource [trustAnchorCred]

| Attribute Name of [trustAnchorCred] | Mapping to Nodes in Management Object |
| --- | --- |
| certFingerprint | <x>/trustAnchorCred/<x>/certFingerprint |
| URI | <x>/trustAnchorCred/<x>/URI |

#### 5.3.13.6	Resource [myCertFileCred]

The Resource [myCertFileCred] represents configuration information regarding certificates presented by the managed entity to remote entities for the establishment of secure communications, see clause 7.1.5 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [myCertFileCred] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/myCertFileCred/<x> node of MFDCMO.

The attributes of an instance of [myCertFileCred] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.6-1.

Table 5.3.13.6-1: Resource [myCertFileCred]

| Attribute Name of [myCertFileCred] | Mapping to Nodes in Management Object |
| --- | --- |
| SUIDs | <x>/myCertFileCred/<x>/SUIDs |
| myCertFileFormat | <x>/myCertFileCred/<x>/myCertFileFormat |
| myCertFileContent | <x>/myCertFileCred/<x>/myCertFileContent |

#### 5.3.13.7	Resource [MAFClientRegCfg]

The Resource [MAFClientRegCfg] represents configuration information that permits a MAF client to register with a MAF, see clause 7.1.7 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [MAFClientRegCfg] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/MAFClientRegCfg/<x> node of MFDCMO.

The attributes of an instance of [MAFClientRegCfg] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.7-1.

The mgmtLink attribute of the [MAFClientRegCfg] resource points to an [authenticationProfile] resource instance which itself is mapped to a <x>/authenticationProfile/<x> node in MFDCMO.  The original value of this mgmtLink attribute needs to be translated such that it points to the <x>/authenticationProfile/<x> node in MFDCMO which corresponds to the linked [authenticationProfile] resource instance. The respective node identifier <x>/authenticationProfile/<x> of this [authenticationProfile] resource instance shall be set as the value of the <x>/dataCollection/<x>/authenticationProfile leaf node.

Table 5.3.13.7-1: Resource [MAFClientRegCfg]

| Attribute Name of [MAFClientRegCfg] | Mapping to Nodes in Management Object |
| --- | --- |
| fqdn | <x>/MAFClientRegCfg/<x>/fqdn |
| adminFQDN | <x>/MAFClientRegCfg/<x>/adminFQDN |
| httpPort | <x>/MAFClientRegCfg/<x>/httpPort |
| coapPort | <x>/MAFClientRegCfg/<x>/coapPort |
| websocketPort | <x>/MAFClientRegCfg/<x>/websocketPort |
| mgmtLink [authenticationProfile] | <x>/MAFClientRegCfg/<x>/authenticationProfile |

#### 5.3.13.8	Resource [MEFClientRegCfg]

The Resource [MEFClientRegCfg] represents configuration information that permits a MEF client to register with a MEF, see clause 7.1.8 of TS-0022 [20].

Regardless of OMA DM 1.3 and OMA DM 2.0, this resource shall be mapped to M2M FieldDeviceConfig MO (MFDCMO) (urn:oma:mo:ext-onem2m-mfdcmo:1.0).

The Resource [MEFClientRegCfg] is a multi-instance Resource where each instance of the Resource shall map to an instance of the <x>/MEFClientRegCfg/<x> node of MFDCMO.

The attributes of an instance of [MEFClientRegCfg] shall be mapped to nodes of the MFDCMO as shown in Table 5.3.13.7-1.

The mgmtLink attribute of the [MEFClientRegCfg] resource points to an [authenticationProfile] resource instance which itself is mapped to a <x>/authenticationProfile/<x> node in MFDCMO.  The original value of this mgmtLink attribute needs to be translated such that it points to the <x>/authenticationProfile/<x> node in MFDCMO which corresponds to the linked [authenticationProfile] resource instance. The respective node identifier <x>/authenticationProfile/<x> of this [authenticationProfile] resource instance shall be set as the value of the <x>/dataCollection/<x>/authenticationProfile leaf node.

Table 5.3.13.8-1: Resource [MEFClientRegCfg]

| Attribute Name of [MEFClientRegCfg] | Mapping to Nodes in Management Object |
| --- | --- |
| fqdn | <x>/MEFClientRegCfg/<x>/fqdn |
| adminFQDN | <x>/MEFClientRegCfg/<x>/adminFQDN |
| httpPort | <x>/MEFClientRegCfg/<x>/httpPort |
| coapPort | <x>/MEFClientRegCfg/<x>/coapPort |
| websocketPort | <x>/MEFClientRegCfg/<x>/websocketPort |
| mgmtLink [authenticationProfile] | <x>/MEFClientRegCfg/<x>/authenticationProfile |

### -----------------------End of change 1---------------------------------------------

### -----------------------Start of change 2-------------------------------------------

### 5.6.2	M2M FieldDeviceConfig (MFDCMO)

The M2M FieldDeviceConfig MO (MFDCMO) resides in the Management Tree of any ADN, ASN or MN which supports Device Management via OMA DM 1.3 and OMA DM 2.0. This MO corresponds to instances of the Field Device Configuration resources specified in oneM2M TS-0022 [20] which all represent specializations of the mgmtObj resource type.

This MO maintains information required for registration of AEs and CSEs to their registrar CSE,  application configuration parameters which ma be needed by AEs, as well information required to configure security profiles for communication over the Mca and Mcc reference points defined in oneM2M TS-0001 [1], and over the Mmaf and Mmef reference points defined in TS-0032 [20] .

Figure 5.6.1-1 gives the pictorial description of the MFDCMO.

Figure 5.6.1-1: Structure of OMA-DM compatible M2M FieldDeviceConfig MO (MFDCMO)

The various nodes within this MO are described as follows.

| <x> |
| --- |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This placeholder node is the root node for the MFDCMO which includes MOs related to field device configuration. The parent node of this node defines the location of this MO in the Management Tree. The Management Object Identifier for the MFDCMO shall be: "urn:oma:mo:ext-onem2m-mfdcmo:1.0". Detailed information about each of the individual MOs included in the MFDCMO can be found in oneM2M specification TS-0022 "Field Device Configuration". |
| <x>/registration |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of registration MOs. |
| <x>/registration/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder interior node represents the specific instances of registration MOs. |
| <x>/registration/<x>/originatorID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the originatorID attribute of a registration resource instance. |
| <x>/registration/<x>/poA |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the poA attribute of a registration resource instance. |
| <x>/registration/<x>/appID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the appID attribute of a registration resource instance. |
| <x>/registration/<x>/externalID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the externalID attribute of a registration resource instance. |
| <x>/registration/<x>/triggerRecipientID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | This leaf node contains the triggerRecipientID attribute of a registration resource instance. |
| <x>/registration/<x>/authenticationProfile |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of an authenticationProfile node. |
| <x>/dataCollection |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of a dataCollection MO instance. |
| <x>/dataCollection/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder node represents an instance of a dataCollection MO. |
| <x>/dataCollection/<x>/containerPath |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the containerPath attribute of a dataCollection resource instance. |
| <x>/dataCollection/<x>/reportingSchedule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This interior node is the parent node of the reportingSchedule attribute of a dataCollection resource instance. |
| <x>/dataCollection/<x>/reportingSchedule/scheduleEntry |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | Each of these leaf nodes contains a scheduleEntry element of the reportingSchedule attribute of the dataCollection resource instance. |
| <x>/dataCollection/<x>/measurementSchedule |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This interior node is the parent node of the measurementSchedule attribute of a dataCollection resource instance. |
| <x>/dataCollection/<x>/measurementSchedule/scheduleEntry |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | Each of these leaf nodes contains a scheduleEntry element of the measurementSchedule attribute of the dataCollection resource instance. |
| <x>/dataCollection/<x>/authenticationProfile |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of an authenticationProfile node. |
| <x>/authenticationProfile |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of an authenticationProfile MO instance. |
| <x>/authenticationProfile/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder node represents an instance of an authenticationProfile MO. |
| <x>/authenticationProfile/<x>/SUID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | int | Get |  |
|  | This leaf node contains the SUID attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/TLSCiphersuites |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This interior node is the parent node of the TLSCiphersuites attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/TLSCiphersuites/ciphersuite |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | Each of these leaf nodes contains a ciphersuite element in hexchar format of the TLSCiphersuites attribute of the authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/symmKeyID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the symmKeyID attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/symmKeyValue |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the symmKeyValue attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/MAFKeyRegLabels |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | node | Get |  |
|  | This interior node is the parent node of the MAFKeyRegLabels attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/MAFKeyRegLabels/label |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | chr | Get |  |
|  | Each of these leaf nodes contains a label element of the MAFKeyRegLabels attribute of the authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/MAFKeyRegDuration |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the MAFKeyRegDuration attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/myCertFingerprint |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the myCertFingerprint attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/rawPubKeyID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the rawPubKeyID attribute of an authenticationProfile resource instance. |
| <x>/authenticationProfile/<x>/trustAnchorCred |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of a trustAnchorCred node. |
| <x>/authenticationProfile/<x>/MAFClientRegCfg |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of a MAFClientRegCfg node. |
| <x>/trustAnchorCred |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of a trustAnchorCred MO instance. |
| <x>/trustAnchorCred/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder node represents an instance of a trustAnchorCred MO. |
| <x>/trustAnchorCred/<x>/certFingerprint |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the certFingerprint attribute of a trustAnchorCred resource instance. |
| <x>/trustAnchorCred/<x>/URI |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the URI attribute of a trustAnchorCred resource instance. |
| <x>/myCertFileCred |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of a myCertFileCred MO instance. |
| <x>/myCertFileCred/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder node represents an instance of a myCertFileCred MO. |
| <x>/myCertFileCred/<x>/SUIDs |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of the SUIDs attribute of a myCertFileCred resource instance. |
| <x>/myCertFileCred/<x>/SUIDs/SUID |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | OneOrMore | int | Get |  |
|  | Each of these leaf nodes contains a SUID element of the SUIDs attribute of the myCertFileCred resource instance. |
| <x>/myCertFileCred/<x>/myCertFileFormat |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the myCertFileFormat attribute of an authenticationProfile resource instance. |
| <x>/myCertFileCred/<x>/myCertFileContent |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the myCertFileContent attribute of a myCertFileCred resource instance. |
| <x>/MAFClientRegCfg |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of MAFClientRegCfg MOs. |
| <x>/MAFClientRegCfg/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder interior node represents the specific instances of MAFClientRegCfg MOs. |
| <x>/MAFClientRegCfg/<x>/fqdn |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the fqdn attribute of a MAFClientRegCfg resource instance. |
| <x>/MAFClientRegCfg/<x>/adminFQDN |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the adminFQDN attribute of a MAFClientRegCfg resource instance. |
| <x>/MAFClientRegCfg/<x>/httpPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the httpPort attribute of a MAFClientRegCfg resource instance. |
| <x>/MAFClientRegCfg/<x>/coapPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the coapPort attribute of a MAFClientRegCfg resource instance. |
| <x>/MAFClientRegCfg/<x>/websocketPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the websocketPort attribute of a MAFClientRegCfg resource instance. |
| <x>/MAFClientRegCfg/<x>/authenticationProfile |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of an authenticationProfile node. |
| <x>/MEFClientRegCfg |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | node | Get |  |
|  | This interior node is the parent node of instances of MEFClientRegCfg MOs. |
| <x>/MEFClientRegCfg/<x> |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrMore | node | Get |  |
|  | This placeholder interior node represents the specific instances of MEFClientRegCfg MOs. |
| <x>/MEFClientRegCfg/<x>/fqdn |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the fqdn attribute of a MEFClientRegCfg resource instance. |
| <x>/MEFClientRegCfg/<x>/adminFQDN |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node contains the adminFQDN attribute of a MEFClientRegCfg resource instance. |
| <x>/MEFClientRegCfg/<x>/httpPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the httpPort attribute of a MEFClientRegCfg resource instance. |
| <x>/MEFClientRegCfg/<x>/coapPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the coapPort attribute of a MEFClientRegCfg resource instance. |
| <x>/MEFClientRegCfg/<x>/websocketPort |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Optional | ZeroOrOne | chr | Get |  |
|  | This leaf node contains the websocketPort attribute of a MEFClientRegCfg resource instance. |
| <x>/MEFClientRegCfg/<x>/authenticationProfile |
|  | Status | Tree Occurrence | Format | Min. Access Types |  |
|  | Required | One | chr | Get |  |
|  | This leaf node includes a reference (mgmtLink) to an instance of an authenticationProfile node. |

### -----------------------End of change 2---------------------------------------------

### -----------------------Start of change 3-------------------------------------------

## 2.1	Normative references

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the referenced document (including any amendments) applies.

The following referenced documents are necessary for the application of the present document.

[1]	oneM2M TS-0001: "Functional Architecture".

[2]	oneM2M TS-0004: "Service Layer Core Protocol Specification".

[3]	Open Mobile Alliance™: "OMA Device Management Protocol", Version 1.3.

NOTE:	Available at http://openmobilealliance.org/release/DM/

[4]	Open Mobile Alliance™: "OMA Device Management Protocol", Version 2.0.

NOTE:	Available at http://openmobilealliance.org/release/DM/.

[5]	Open Mobile Alliance™: "OMA LightweightM2M", Version 1.0..

NOTE:	Available at http://openmobilealliance.org/release/LightweightM2M/ .

[6]	Open Mobile Alliance™: "OMA Diagnostics and Monitoring Management Object Framework".

NOTE:	Available at http://openmobilealliance.org/release/DiagMon/.

[7]	Open Mobile Alliance™: "OMA Firmware Update Management Object".

NOTE:	Available at http://openmobilealliance.org/release/FUMO/.

[8]	Open Mobile Alliance™: "OMA Software Component Management Object".

NOTE:	Available at http://openmobilealliance.org/release/SCOMO/.

[9]	ETSI TS 103 092: "Machine-to-Machine communications (M2M); OMA DM compatible Management Objects for ETSI M2M".

[10]	Open Mobile Alliance™: "OMA Device Capability Management Object".

NOTE:	Available at http://openmobilealliance.org/release/DCMO/.

[11]	Open Mobile Alliance™: "OMA Management Interface to M2M Requirements".

NOTE:	Available at http://openmobilealliance.org/release/M2Minterface/ .

[12]	ISO 8601:2000: "Data elements and interchange formats -- Information interchange -- Representation of dates and times".

NOTE:	Available at http://www.iso.ch/.

[13]	W3C Recommendation: "XML Schema Part 2: Datatypes", 02 May 2001.

NOTE:	Available at http://www.w3.org/TR/2001/REC-xmlschema-2-20010502/.

[14]	IETF RFC 4122 (July 2005): "A Universally Unique Identifier (UUID) URN Namespace", P. Leach, et al..

NOTE:	Available at http://www.ietf.org/rfc/rfc4122.txt.

[15]	3GPP TS 23.003: "Numbering, addressing and identification".

[16]	BBF TR-069: "CPE WAN Management Protocol", Issue: 1 Amendment 5, November 2013.

[17]	IETF RFC 7252: "The Constrained Application Protocol (CoAP)".

[18]	Open Mobile Alliance™ (Version 1.0): "OMA LightweightM2M - Software Management Object".

NOTE:	Available at http://openmobilealliance.org/release/LWM2M_SWMGMT/

[19]	Open Mobile Alliance™: "OMA LightweightM2M - Device Capability Management Object".

NOTE:	Available at http://openmobilealliance.org/release/LWM2M_DevCapMgmt/

[20]	oneM2M TS-0022: "Field Device Configuration".

### -----------------------End of change 3---------------------------------------------

CHECK LIST

- Does this Change Request include an informative introduction containing the problem(s) being solved, and a summary list of proposals.?

- Does this CR contain changes related to only one particular issue/problem?

- Have any mirror CRs been posted?

- Does this Change Request  make all the changes necessary to address the issue or problem?  E.g. A change impacting 5 tables should not include a proposal to change only 3 tables?Does this Change Request follow the drafting rules?

- Are all pictures editable?

- Have you checked the spelling and grammar?

- Have you used change bars for all modifications?

- Does the change include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change? (Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.)

- Are multiple changes in this CR clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.?