| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#32 |
| Source:* | Yongjing Zhang, Huawei, zhangyongjing@huawei.com |
| Date:* | 2017-11-03 |
| Reason for Change/s:* | This contribution proposes small enhancement to support SPARQL update to <ontology> to improve the efficiency. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0034 v0.4.0 |
| Clauses * | 6.8, 7.5 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | TS-0001 v3.8.0 clause 9.6.51 <ontology> resource type definition. TS-0004 v3.4.0 clause 7.4.47.2.3 Update operation of <ontology> resource |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

# Introduction

This contribution proposes small enhancement to support SPARQL update to <ontology> to improve the efficiency. The mechanism is same as used in the <semanticDescriptor> resource.

It makes sense to support the same level (triple-level) operation on the similar semantic resources like <semanticDescriptor> and <ontology> from the technical consistency perspective.

### -----------------------Start of change 1------------------------------------------

## 6.8 <ontology> Operations

### 6.8.2 Create <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.1-1: <ontology> CREATE

| <ontology> CREATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1] apply with the specific details for: Content: The resource content shall provide the information as defined in clause 9.6.51 in oneM2M TS-0001 [1]. |
| Processing at Originator before sending Request | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Information in Response message | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.2 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.2 in oneM2M TS-0001 [1]. |

### 6.8.3 Retrieve <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.2-1: <<ontology> RETRIEVE

| <ontology> RETRIEVE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc'. |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1]. |
| Processing at Originator before sending Request | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Information in Response message | All parameters defined in table 8.1.3-1 in oneM2M TS-0001 [1] apply. |
| Processing at Originator after receiving Response | According to clause 10.1.3 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.3 in oneM2M TS-0001 [1]. |

### 6.8.3 Update <ontology>

This procedure shall be used for deleting an existing <ontology> resource.

Table 6.8.3-1: <ontology> UPDATE

| <ontology> UPDATE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1] shall apply with the specific details for the Content request parameter which may contain the new ontology information in one of the following ways: the full representation of the new ontology triples in the ontologyContent attribute; or the new IRI of the ontology in the ontologyContent attribute; or the partial representation of the new ontology as described in SPARQL statements [2] in the semanticOpExec attribute in the case that the ontologyFormat is not ‘IRI’. |
| Processing at Originator before sending Request | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.4 in oneM2M TS-0001 [1] with the specific details as follows: Check if both semanticOpExec attribute and ontologyContent attribute exist in the the Content request parameter, if so, return an error code. In the case that the Content request parameter contains partial representation of the new ontology as described in SPARQL statements [2] in the semanticOpExec attribute, and the ontologyFormat is not set to ‘IRI’, the host CSE shall update the ontologyContent attribute according to the execution result of the SPARQL statements [2]. |
| Information in Response message | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.4 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.4 in oneM2M TS-0001 [1]. |

### 6.8.4 Delete <ontology>

Table 6.8.4-1: <ontology> DELETE

| <ontology> DELETE |
| --- |
| Associated Reference Point | Mca, Mcc and Mcc' |
| Information in Request message | All parameters defined in table 8.1.2-2 in oneM2M TS-0001 [1] apply. |
| Processing at Originator before sending Request | According to clause 10.1.5 in oneM2M TS-0001 [1]. |
| Processing at Receiver | According to clause 10.1.5 in oneM2M TS-0001 [1]. |
| Information in Response message | According to clause 10.1.5 in oneM2M TS-0001 [1]. |
| Processing at Originator after receiving Response | According to clause 10.1.5 in oneM2M TS-0001 [1]. |
| Exceptions | According to clause 10.1.5 in oneM2M TS-0001 [1]. |

### -----------------------End of change 1------------------------------------------