| Input Contribution |
| --- |
| Meeting ID* | MAS#32 |
| Title:* | Example for ontology based interworking for annex of TS-0030 |
| Source:* | Joerg Swetina, NEC, Joerg.swetina@neclab.eu |
| Date:* | 2017-11-05 |
| Input related to* | WI 0063, TS-0030 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Decision requested or recommendation:* | As requested at the last meeting an example is provided how SDTs are created for ontology based interworking |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

# Discussion

The following text is proposed for inclusion into TS-0030 as new informative annex A

Annex <A> (Informative): Example for ontology based interworking

## A.1	Overview

This example extends the example - a (simplified) washing machine - of section B.1.3.3 of TS-0012 [3].
However in contrast to TS-0012 we assume that the washing machine is not a 'native' oneM2M application but is interworked with the oneM2M System via ontology based interworking.

In contrast to TS-0012 we are not interested in the semantic description (contained in the descriptor attribute of the <semanticDescriptor>) but in the resources, i.e. the <flexContainer> resources to which these sematic descriptors belong. 
Here we are also not interested in Functions and Commands (which are only described in RDF form in the sematic descriptors) but in Services, Input- / OutputDatapoints and Operations, which are the resources containing data for communication with the washing machine.

The example that was taken from SAREF [i.2] is a (simplified) washing machine:

- The washing machine has been manufactured by manufacturer XYZ.

- XYZ describes this type of washing machine with a Description as "Very cool Washing Machine"

- The model of the type of washing machine is XYZ_Cool

- The state of the washing machine is given by SAREF:state: WashingMachineStatus that can take the values "WASHING" or "STOPPED" or "ERROR".

- This WashingMachineStatus is provided as an the OutputDataPoint of a service MonitorService which exposes the MonitoringFunction to the network .

- The washing machine has an actuating function: StartStopFunction which has three commands:

  - ON_Command

  - OFF_Command

  - Toggle_Command

- The related service of the washing machine that represents that actuating function is of class: SwitchOnService from SAREF. It has

  - an InputDataPoint: BinaryInput (to expose command ON_Command and OFF_Command) and

  - an Operation: ToggleBinary (to expose command Toggle_Command)

- The washing machine has also a metering function: MonitoringFunction that and sets the WashingMachineStatus.

The following figure shows the relationship of the ontology that describes model XYZ_cool of XYZ washingmachines with the oneM2M base ontology. 
We assume that the ontology that describes XYZ washingmachines is identified by the IRI: http://www.XYZ.com/WashingMachines.

Figure 7: relationship of the ontology that describes model XYZ_cool
of XYZ washingmachines with the oneM2M base ontology

## A.2	XSDs created by the IPE

### A.2.1	XSD storage <container>

According to section 7.2.1.1 the IPE creates a <container> resource that acts as a XSD-storage and that is a child resource of the IPE's <AE>.

Derived from the IRI of the ontology: http://www.XYZ.com/WashingMachines, following the rule given in table 1 of  section 7.2.1.2  the resource name for that <container> resource (in the table the placeholder is called &XSDSTORAGE;) will be www.XYZ.com_WashingMachines.

The IPE will also create <contentInstance> resources as child-resources of the XSD-storage <container> resource with the following resource names (see &XSDFILE; in table 1 of 7.2.1.2):

- XYZ_Cool.xsd   … contains the XSD for the <flexContainer> resource of the Interworked Device type XYZ_Cool

- SwitchOnService.xsd  … contains the XSD for the <flexContainer> resource of the Service type SwitchOnService

- MonitorService.xsd  … contains the XSD for the <flexContainer> resource of the Service type MonitorService

- ToggleBinary.xsd  … contains the XSD for the <flexContainer> resource of the Operation type ToggleBinary

When the IPE crates a new <flexContainer> specialization of these types then the attribute containerDefinition will contain the absolute, hierarchical address of the <contentinstance> that contains the related XSD. 
E.g. for the SwitchOnService it could have the value: 
//m2m.service.com/IN-CSE0001/bigFatCse/name_of_IPE_AE/ww.XYZ.com_WashingMachines/SwitchOnService.xsd

### A.2.2	XSD for the Interworked Device type XYZ_Cool

Following the principles of section 7.2.2 an Interworked Device is represented as <flexContainer>.

According to the the convention in table 1 of  section 7.2.1.2 the placeholders and their substitutions that are needed for a <flexContainer>, representing an Interworked Device are:

| &XSDSTORAGE; | is substituted by | www.XYZ.com_WashingMachines |
| --- | --- | --- |
| &DEVICE; | is substituted by | XYZ_Cool |
| &SERVICE_1; | is substituted by | SwitchOnService |
| &SERVICE_2; | is substituted by | MonitorService |
| THINGPROPERTY_1; | is substituted by | Description |
| &TYPENAME_1; | is substituted by | DescriptionType |
| &SIMPLEDATATYPE; | is substituted by | xs:string |

The XSD in the <contentInstance> with resource name XYZ_Cool.xsd will contain:

<?xml version="1.0" encoding="UTF-8"?> <!-- Copyright Notification The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms. This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document. © 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved. Notice of Disclaimer & Limitation of Liability The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied. NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER. --> <xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="www.XYZ.com_WashingMachines" xmlns:xs="http://www.w3.org/2001/XMLSchema" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:obi="www.XYZ.com_WashingMachines" elementFormDefault="unqualified" attributeFormDefault="unqualified"> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-subscription-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-semanticDescriptor-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-commonTypes-v3_0_0.xsd"/> <!-- include XSDs of child resources: (sub-)Devices and Services used in this Device --> <xs:include schemaLocation=" SwitchOnService.xsd" /> <xs:include schemaLocation=" MonitorService.xsd" />´ <xs:element name="XYZ_Cool" substitutionGroup="m2m:sg_flexContainerResource"> <xs:complexType> <xs:complexContent> <!-- Inherit Common Attributes from data type "flexContainerResource" --> <xs:extension base="m2m:flexContainerResource"> <xs:sequence> <!-- Resource Specific Attributes --> <!-- nodeLink as custom attribute --> <xs:element name="nodeLink" type="xs:anyURI" minOccurs="0"/> <!-- all OperationInput- and Outputs are listed here as custom attributes --> <xs:element name="Description" type=" obi:DescriptionType" minOccurs="0"/> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded"/> <xs:choice minOccurs="1" maxOccurs="unbounded"> <!-- Device specific Child Resources (sub-Devices of the Device) --> <!-- Device specific Child Resources (Services of the Device) --> <xs:element ref=" obi:SwitchOnService"/> <xs:element ref=" obi:MonitorService"/> <!-- Common Child Resources --> <xs:element ref="m2m:semanticDescriptor"/> <xs:element ref="m2m:subscription"/> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> <!-- types used for ThingProperties of this Device --> <!-- ********************** --> <!-- Ontology based IWK Simple Types --> <!-- ********************** --> <xs:simpleType name="DescriptionType"> <xs:restriction base="xs:string"/> </xs:simpleType> </xs:schema>

### A.2.3	XSD for the Service type SwitchOnService

Following the principles of section 7.2.3 a Service is represented as <flexContainer>.

According to the the convention in table 1 of  section 7.2.1.2 the placeholders and their substitutions that are needed for a <flexContainer>, representing an Interworked Device are:

| &XSDSTORAGE; | is substituted by | www.XYZ.com_WashingMachines |
| --- | --- | --- |
| &SERVICE; | is substituted by | SwitchOnService |
| &OPERATION_1; | is substituted by | ToggleBinary |
| &INPUTDATAPOINT_1; | is substituted by | BinaryInput |
| &TYPENAME_1; | is substituted by | ToggleBinaryType |
| &SIMPLEDATATYPE; | is substituted by | xs:boolean |

The XSD in the <contentInstance> with resource name SwitchOnService.xsd will contain:

<?xml version="1.0" encoding="UTF-8"?> <!-- Copyright Notification The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms. This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document. © 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved. Notice of Disclaimer & Limitation of Liability The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied. NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER. --> <xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="www.XYZ.com_WashingMachines" xmlns:xs="http://www.w3.org/2001/XMLSchema" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:obi="www.XYZ.com_WashingMachines" elementFormDefault="unqualified" attributeFormDefault="unqualified"> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-subscription-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-semanticDescriptor-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-commonTypes-v3_0_0.xsd"/> <!-- include XSDs of child resources: Operations used in this Service --> <xs:include schemaLocation="ToggleBinary.xsd" /> <xs:element name="SwitchOnService" substitutionGroup="m2m:sg_flexContainerResource"> <xs:complexType> <xs:complexContent> <!-- Inherit Common Attributes from data type "flexContainerResource" --> <xs:extension base="m2m:flexContainerResource"> <xs:sequence> <!-- Resource Specific Attributes --> <!-- all Input- and OutputDatapoints are listed here as custom attributes --> <xs:element name="BinaryInput" type=" obi:BinaryInputType" minOccurs="0"/> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded"/> <xs:choice minOccurs="1" maxOccurs="unbounded"> <!-- Service specific Child Resources (Operations of the Service) --> <xs:element ref=" obi:ToggleBinary"/> <!-- Common Child Resources --> <xs:element ref="m2m:semanticDescriptor"/> <xs:element ref="m2m:subscription"/> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> <!-- types used for Datapoints of this Service --> <!-- ********************** --> <!-- Ontology based IWK Simple Types --> <!-- ********************** --> <xs:simpleType name=" BinaryInputType "> <xs:restriction base="xs:boolean"/> </xs:simpleType> </xs:schema>

### A.2.4	XSD for the Service type MonitorService

Following the principles of section 7.2.3 a Service is represented as <flexContainer>.

According to the the convention in table 1 of  section 7.2.1.2 the placeholders and their substitutions that are needed for a <flexContainer>, representing an Interworked Device are:

| &XSDSTORAGE; | is substituted by | www.XYZ.com_WashingMachines |
| --- | --- | --- |
| &SERVICE; | is substituted by | MonitorService |
| &OUTPUTDATAPOINT_1; | is substituted by | WashingMachineStatus |
| &TYPENAME_1; | is substituted by | WashingMachineStatusType |
| &SIMPLEDATATYPE; | is substituted by | xs:string |
| &RESTRICTIONVALUE; | is substituted by | "WASHING"¦"STOPPED"¦"ERROR" |

The XSD in the <contentInstance> with resource name MonitorService.xsd will contain:

<?xml version="1.0" encoding="UTF-8"?> <!-- Copyright Notification The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms. This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document. © 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved. Notice of Disclaimer & Limitation of Liability The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied. NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER. --> <xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="www.XYZ.com_WashingMachines" xmlns:xs="http://www.w3.org/2001/XMLSchema" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:obi="www.XYZ.com_WashingMachines" elementFormDefault="unqualified" attributeFormDefault="unqualified"> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-subscription-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-semanticDescriptor-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-commonTypes-v3_0_0.xsd"/> <xs:element name="MonitorService" substitutionGroup="m2m:sg_flexContainerResource"> <xs:complexType> <xs:complexContent> <!-- Inherit Common Attributes from data type "flexContainerResource" --> <xs:extension base="m2m:flexContainerResource"> <xs:sequence> <!-- Resource Specific Attributes --> <!-- all Input- and OutputDatapoints are listed here as custom attributes --> <xs:element name="WashingMachineStatus" type=" obi:WashingMachineStatusType" minOccurs="0"/> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded"/> <xs:choice minOccurs="1" maxOccurs="unbounded"> <!-- Service specific Child Resources (Operations of the Service) --> <!-- Common Child Resources --> <xs:element ref="m2m:semanticDescriptor"/> <xs:element ref="m2m:subscription"/> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> <!-- types used for Datapoints of this Service --> <!-- ********************** --> <!-- Ontology based IWK Simple Types --> <!-- ********************** --> <xs:simpleType name="WashingMachineStatusType"> <xs:restriction base="xs:string"/> <!-- next lines for restrictions of the values. Remove not needed ones, Multiple restrictiontypes possible --> <xs:pattern value= "WASHING"¦"STOPPED"¦"ERROR" /> </xs:simpleType> </xs:schema>

### A.2.5	XSD for the Operation type ToggleBinary

Following the principles of section 7.2.3 a Service is represented as <flexContainer>.

According to the the convention in table 1 of  section 7.2.1.2 the placeholders and their substitutions that are needed for a <flexContainer>, representing an Interworked Device are:

| &XSDSTORAGE; | is substituted by | www.XYZ.com_WashingMachines |
| --- | --- | --- |
| &OPERATION; | is substituted by | ToggleBinary |

The XSD in the <contentInstance> with resource name ToggleBinary.xsd will contain:

<?xml version="1.0" encoding="UTF-8"?> <!-- Copyright Notification The oneM2M Partners authorize you to copy this document, provided that you retain all copyright and other proprietary notices contained in the original materials on any copies of the materials and that you comply strictly with these terms. This copyright permission does not constitute an endorsement of the products or services, nor does it encompass the granting of any patent rights. The oneM2M Partners assume no responsibility for errors or omissions in this document. © 2016, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC). All rights reserved. Notice of Disclaimer & Limitation of Liability The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied. NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER. --> <xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="www.XYZ.com_WashingMachines" xmlns:xs="http://www.w3.org/2001/XMLSchema" xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:obi="www.XYZ.com_WashingMachines" elementFormDefault="unqualified" attributeFormDefault="unqualified"> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-subscription-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-semanticDescriptor-v3_0_0.xsd"/> <xs:import namespace="http://www.onem2m.org/xml/protocols" schemaLocation="CDT-commonTypes-v3_0_0.xsd"/> <!-- for operations no includes needed from obi: namespace --> <xs:element name="ToggleBinary" substitutionGroup="m2m:sg_flexContainerResource"> <xs:complexType> <xs:complexContent> <!-- Inherit Common Attributes from data type "flexContainerResource" --> <xs:extension base="m2m:flexContainerResource"> <xs:sequence> <!-- Resource Specific Attributes for operations--> <!-- all OperationInput- and Outputs are listed here as custom attributes --> <!-- Child Resources --> <xs:choice minOccurs="0" maxOccurs="1"> <xs:element name="childResource" type="m2m:childResourceRef" minOccurs="1" maxOccurs="unbounded"/> <xs:choice minOccurs="1" maxOccurs="unbounded"> <!-- Child Resource for Operations that have OperationOutputs is an Operation of the same type --> <!-- Common Child Resources --> <xs:element ref="m2m:semanticDescriptor"/> <xs:element ref="m2m:subscription"/> </xs:choice> </xs:choice> </xs:sequence> </xs:extension> </xs:complexContent> </xs:complexType> </xs:element> <!-- types used for OperationInputs and -Outputs of this Operation --> </xs:schema>