| CHANGE REQUEST |
| --- |
| Meeting ID:* | MAS#32 |
| Source:* | Yongjing Zhang, Huawei, zhangyongjing@huawei.com |
| Date:* | 2017-11-09 |
| Reason for Change/s:* | This contribution proposes changes to the mapping from the [eventLog] resource to the OMA LwM2M Event Log Object (object-id:20) based on the latest update of the OMA LwM2M specification. Editor’s notes are also removed accordingly. |
| CR against: Release* | Release 3 |
| CR against: WI* | Active WI-0053 MNT maintenance / < Work Item number(optional)> Is this a mirror CR? Yes No mirror CR number: (Note to Rapporteur - use latest agreed revision) STE Small Technical Enhancements / < Work Item number (optional)> Only ONE of the above shall be ticked |
| CR against: TS/TR* | TS-0005 v3.2.0 |
| Clauses * | 6.3.11 |
| Type of change: * | Editorial change Bug Fix or Correction Change to existing feature or functionality New feature or functionality Only ONE of the above shall be ticked |
| Impacted other TS/TR(s) | <TS/TR number>, <Version Number>, and <Description on which aspect should be reflected in this TS/TR> |
| Post Freeze checking:* | This CR contains only essential changes and corrections? YES NO This CR may break backwards compatibility with the last approved version of the TS? YES NO |
| Template Version: January 2017 (Do not modify) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

GUIDELINES for Change Requests:

Provide an informative introduction containing the problem(s) being solved, and a summary list of proposals.

Each CR should contain changes related to only one particular issue/problem.

In case of a correction, and the change apply to previous releases, a separate “mirror CR” should be posted at the same time of this CR

Mirror CR: applies only when the text, including clause numbering are exactly the same.

Companion CR: applies when the change means the same but the baselines differ in some way (e.g. clause number).

Follow the principle of completeness, where all changes related to the issue or problem within a deliverable are simultaneously proposed to be made E.g. A change impacting 5 tables should not only include a proposal to change only 3 tables. Includes any changes to references, definitions, and acronyms in the same deliverable.

Follow the drafting rules.

All pictures must be editable.

Check spelling and grammar to the extent practicable.

Use Change bars for modifications.

The change should include the current and surrounding clauses to clearly show where a change is located and to provide technical context of the proposed change. Additions of complete clauses need not show surrounding clauses as long as the proposed clause number clearly shows where the new clause is proposed to be located.

Multiple changes in a single CR shall be clearly separated by horizontal lines with embedded text such as, start of change 1, end of change 1, start of new clause, end of new clause.

When subsequent changes are made to content of a CR, then the accepted version should not show changes over changes. The accepted version of the CR should only show changes relative to the baseline approved text.

# Introduction

This contribution proposes changes to the mapping from the [eventLog] resource to the OMA LwM2M Event Log Object (object-id:20) based on the latest update of the OMA LwM2M specification.

The latest change in LwM2M Event Log (Obj:20) is the following:

- Resource 4014 LogData is simplified by removing the 1st-byte indication for the data format, so the mapping to oneM2M is also simplified as transparent.

- An optional resource 4015 LogDataFormat is introduced to indicate the data format if needed, but it’s not used in the case of mapping to oneM2M since the absence means an unspecified data format and is sufficient.

| 4014 | LogData | R | Single | Mandatory | Opaque |  |  | Read Access on that Resource returns the Data Collection associated to the current Object Instance. |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4015 | LogDataFormat | RW | Single | Optional | Integer | 255 |  | when set by the Server, this Resource indicates to the Client, what is the Server preferred data format to use when the LogData Resource is returned . when retrieved by the Server, this Resource indicates which specific data format is used when the LogData Resource is returned to the Server 0 or Resource not present : no specific data format (sequence of bytes) 1 : OMA-LwM2M TLV format 2 : OMA-LwM2M JSON format 3: OMA-LwM2M CBOR format [4..99] reserved [100..255] vendor specific data format |

Two Editor’s notes are also removed accordingly.

### -----------------------Start of change 1------------------------------------------

### 6.3.11	Resource [eventLog]

The Resource [eventLog] is to record the event log for the device. For OMA LwM2M, this Resource shall be mapped to one instance of LwM2M Event Log Object (LwM2M Object: {20}).

The context of this Resource is as follows.

# Table 6.3.11-1 Context of resource [eventLog]

| Context | Mapping |
| --- | --- |
| objectIDs | urn:oma:lwm2m:oma:{20} |
| objectPath | /{20}/{i} |

The attributes of this Resource shall be mapped to LwM2M Device Object Instance as follows.

# Table 6.3.11-2 Attributes of resource [eventLog]

| Attribute Name of [eventLog] | Mapping to resources in LwM2M Object Instance |
| --- | --- |
| logTypeId | 4010 LogClass: 1 (system) if the logTypeId of oneM2M [eventLog] resource is “System”; 2 (security) if the logTypeId of oneM2M [eventLog] resource is “Security”; 3 or 6 (event of charging) if the logTypeId of oneM2M [eventLog] resource is “Event”. The charging event shall be mapped to 6; generic events shall be mapped to 3; 4 (trace) if the logTypeId of oneM2M [eventLog] resource is “Trace”; 5 (panic) if the logTypeId of oneM2M [eventLog] resource is “Panic”. |
| logData | 4014 LogData The log data is mapped transparently without any transformation. The data format is considered as unspecified opaque (sequence of bytes) in LwM2M. |
| logStatus | 4013 LogStatus: oneM2M logStatus attribute is translated as follows to LwM2M LogStatus Resource 0 : when logging activity is started (oneM2M logStatus : 1) 1 : when logging activity is stopped without error (oneM2M logStatus : 2) 3 : when logData attribute must be ignored (oneM2M logStatus :4) 5 : when logging activity is stopped with error (oneM2M logStatus :5) 128 (0x80) : when the status of the logging activity is unknown (oneM2M logStatus :3) |
| logStart | 4011 LogStart: When oneM2M logStart attribute is set to “True”, CSE shall execute the LogStart command without argument (default) |
| logStop | 4012 LogStop: When oneM2M logStop attribute is set to “True”, CSE shall execute the LogStop command without argument (default) |

### -----------------------End of change 1------------------------------------------