| oneM2M Technical Specification |
| --- |
| Document Number | oneM2M- TS-0023-V3.6.1 |
| Document Name: | Home Appliances Information Model and Mapping |
| Date: | 2017-11-28 |
| Abstract: | This technical specification includes oneM2M defined information model for home appliances and the mapping with other information models from external organization. |
| Template Version: January 2017 (Do not modify) |

The present document is provided for future development work within oneM2M only. The Partners accept no liability for any use of this specification.

The present document has not been subject to any approval process by the oneM2M Partners Type 1.  Published oneM2M specifications and reports for implementation should be obtained via the oneM2M Partners' Publications Offices.

About oneM2M

The purpose and goal of oneM2M is to develop technical specifications which address the need for a common M2M Service Layer that can be readily embedded within various hardware and software, and relied upon to connect the myriad of devices in the field with M2M application servers worldwide.

More information about oneM2M may be found at:  http//www.oneM2M.org

Copyright Notification

© 2017, oneM2M Partners Type 1 (ARIB, ATIS, CCSA, ETSI, TIA, TSDSI, TTA, TTC).

All rights reserved.

The copyright extends to reproduction in all media.

Notice of Disclaimer & Limitation of Liability

The information provided in this document is directed solely to professionals who have the appropriate degree of experience to understand and interpret its contents in accordance with generally accepted engineering or other professional standards and applicable regulations. No recommendation as to products or vendors is made or should be implied.

NO REPRESENTATION OR WARRANTY IS MADE THAT THE INFORMATION IS TECHNICALLY ACCURATE OR SUFFICIENT OR CONFORMS TO ANY STATUTE, GOVERNMENTAL RULE OR REGULATION, AND FURTHER, NO REPRESENTATION OR WARRANTY IS MADE OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE OR AGAINST INFRINGEMENT OF INTELLECTUAL PROPERTY RIGHTS. NO oneM2M PARTNER TYPE 1 SHALL BE LIABLE, BEYOND THE AMOUNT OF ANY SUM RECEIVED IN PAYMENT BY THAT PARTNER FOR THIS DOCUMENT, WITH RESPECT TO ANY CLAIM, AND IN NO EVENT SHALL oneM2M BE LIABLE FOR LOST PROFITS OR OTHER INCIDENTAL OR CONSEQUENTIAL DAMAGES. oneM2M EXPRESSLY ADVISES ANY AND ALL USE OF OR RELIANCE UPON THIS INFORMATION PROVIDED IN THIS DOCUMENT IS AT THE RISK OF THE USER.

Contents

Contents	3

1	Scope	7

2	References	7

2.1	Normative references	7

2.2	Informative references	8

3	Definitions	8

4	Conventions	8

5	Home Appliance Information Model	9

5.1	Introduction	9

5.2	Design Principle of the Home Appliance Information Model	9

5.2.1	Basic design principle of information modelling	9

5.2.2	Description rules for Module Classes and Device models	10

5.3	ModuleClasses	11

5.3.1	3Dprinter	11

5.3.2	acousticSensor	12

5.3.3	airConJobMode	12

5.3.4	airFlow	12

5.3.5	airPurifierJobMode	13

5.3.6	airQualitySensor	13

5.3.7	alarmSpeaker	14

5.3.8	audioVolume	14

5.3.9	autoDocumentFeeder	15

5.3.10	battery	15

5.3.11	binaryObject	16

5.3.12	binarySwitch	16

5.3.13	bioElectricalImpedanceAnalysis	16

5.3.14	bodyCompositionAnalyser	17

5.3.15	boiler	17

5.3.16	brewing	17

5.3.17	brightness	18

5.3.18	clock	18

5.3.19	clothesDryerJobMode	18

5.3.20	colour	18

5.3.21	colourSaturation	18

5.3.22	credentials	19

5.3.23	dehumidifierJobMode	19

5.3.24	doorStatus	19

5.3.25	electricVehicleConnector	20

5.3.26	energyConsumption	20

5.3.27	energyGeneration	20

5.3.28	faultDetection	21

5.3.29	filterInfo	21

5.3.30	foaming	21

5.3.31	geoLocation	21

5.3.32	glucometer	22

5.3.33	grinder	23

5.3.34	heatingZone	23

5.3.35	height	23

5.3.36	hotWaterSupply	23

5.3.37	impactSensor	23

5.3.38	keepWarm	24

5.3.39	keypad	24

5.3.40	liquidLevel	24

5.3.41	liquidRemaining	25

5.3.42	lock	25

5.3.43	mediaSelect	25

5.3.44	motionSensor	25

5.3.45	numberValue	26

5.3.46	openLevel	26

5.3.47	operationMode	27

5.3.48	overcurrentSensor	27

5.3.49	oximeter	27

5.3.50	ozoneMeter	27

5.3.51	phoneCall	28

5.3.52	playerControl	28

5.3.53	powerSave	29

5.3.54	printQueue	29

5.3.55	pulsemeter	29

5.3.56	pushButton	30

5.3.57	recorder	30

5.3.58	refrigeration	30

5.3.59	relativeHumidity	30

5.3.60	remoteControlEnable	31

5.3.61	robotCleanerJobMode	31

5.3.62	runState	31

5.3.63	securityStatus	32

5.3.64	sessionDescription	32

5.3.65	signalStrength	32

5.3.66	smokeSensor	32

5.3.67	sphygmomanometer	33

5.3.68	spinLevel	33

5.3.69	steamClosetJobMode	33

5.3.70	televisionChannel	33

5.3.71	temperature	34

5.3.72	temperatureAlarm	34

5.3.73	textMessage	34

5.3.74	timer	35

5.3.75	turbo	36

5.3.76	uvSensor	36

5.3.77	washingCourse	37

5.3.78	washingCourseOption	37

5.3.79	waterFlow	37

5.3.80	waterSensor	38

5.3.81	weight	38

5.4	SubDevice models	38

5.4.1	subDeviceCuff	38

5.4.2	subDevicePowerOutlet	38

5.5	Device models	39

5.5.1	device3DPrinter	39

5.5.2	deviceAirConditioner	39

5.5.3	deviceAirPurifier	40

5.5.4	deviceAirQualityMonitor	41

5.5.5	deviceAudioReceiver	41

5.5.6	deviceBloodPressureMonitor	41

5.5.7	deviceCamera	41

5.5.8	deviceClothesDryer	41

5.5.9	deviceClothesWasher	42

5.5.10	deviceCoffeeMachine	42

5.5.11	deviceCookerHood	42

5.5.12	deviceCooktop	43

5.5.13	deviceDehumidifier	43

5.5.14	deviceDishWasher	43

5.5.15	deviceDoor	43

5.5.16	deviceDoorLock	43

5.5.17	deviceElectricVehicleCharger	44

5.5.18	deviceFan	44

5.5.19	deviceFoodProbe	44

5.5.20	deviceFreezer	44

5.5.21	deviceGlucosemeter	44

5.5.22	deviceHeartRateMonitor	45

5.5.23	deviceHomeCCTV	45

5.5.24	deviceHumidifier	45

5.5.25	deviceKettle	45

5.5.26	deviceLight	46

5.5.27	deviceMicrogeneration	46

5.5.28	deviceMultiFunctionPrinter	46

5.5.29	deviceOutdoorLamp	46

5.5.30	deviceOven	47

5.5.31	devicePrinter	47

5.5.32	devicePulseOximeter	47

5.5.33	deviceRefrigerator	48

5.5.34	deviceRobotCleaner	48

5.5.35	deviceScanner	48

5.5.36	deviceSecurityPanel	48

5.5.37	deviceSetTopBox	49

5.5.38	deviceSmartElectricMeter	49

5.5.39	deviceSmartPlug	49

5.5.40	deviceSteamCloset	50

5.5.41	deviceStorageBattery	50

5.5.42	deviceSwitch	50

5.5.43	deviceTelevision	50

5.5.44	deviceThermometer	50

5.5.45	deviceThermostat	51

5.5.46	deviceWaterHeater	51

5.5.47	deviceWaterValve	51

5.5.48	deviceWeightScaleAndBodyCompositionAnalyzer	51

5.5.49	deviceWindowShade	52

5.6	Enumeration type definitions	52

5.6.1	hd:3DprinterTechnology	52

5.6.2	hd:adfState	52

5.6.3	hd:airConJobMode	52

5.6.4	hd:airPurifierJobMode	53

5.6.5	hd:alertColourCode	53

5.6.6	hd:callState	53

5.6.7	hd:clothesDryerJobMode	54

5.6.8	hd:dehumidifierJobMode	54

5.6.9	hd:deviceType	54

5.6.10	hd:doorState	55

5.6.11	hd:foamStrength	55

5.6.12	hd:generalLevel	56

5.6.13	hd:generalSpeed	56

5.6.14	hd:generalTemperature	56

5.6.15	hd:grainsLevel	56

5.6.16	hd:grindCoarseness	57

5.6.17	hd:horizontalDirection	57

5.6.18	hd:jobStates	57

5.6.19	hd:liquidLevel	57

5.6.20	hd:machineState	58

5.6.21	hd:ozoneStatus	58

5.6.22	hd:playerMode	58

5.6.23	hd:robotCleanerJobMode	59

5.6.24	hd:securityMode	59

5.6.25	hd:spinLevelStrength	59

5.6.26	hd:steamClosetJobMode	60

5.6.27	hd:supportedMediaSources	60

5.6.28	hd:tasteStrength	60

5.6.29	hd:tone	60

5.6.30	hd:uvStatus	61

5.6.31	hd:verticalDirection	61

5.6.32	hd:washingCourse	61

5.6.33	hd:waterFlowStrength	62

5.7	Universal and Common Properties for Device models	62

6	The Principle of Resource Mapping for Home Appliance Information Model	62

6.1	Introduction	62

6.2	The Resource Mapping Rules	62

6.2.1	Introduction	62

6.2.2	Resource mapping for Device model	62

6.2.3	Resource mapping for ModuleClass	63

6.2.4	Resource mapping for Action	63

6.2.5	Resource mapping for Property	64

6.2.6	Resource mapping for DataPoint	64

6.3	Short names	64

6.3.1	Introduction	64

6.3.2	Resource types	64

6.3.3	Resource attributes for properties and data points	67

6.4	containerDefinition values	71

6.4.1	Introduction	71

6.4.2	Device models	71

6.4.3	ModuleClasses	71

6.4.4	Actions	71

6.5	XSD definitions	71

6.5.1	Introduction	71

6.5.2	XSD definitions for Device models	71

6.5.3	XSD definitions for ModuleClass	72

6.5.4	XSD definitions for Action	72

7	Mapping with Other Information Models from External Organizations	72

7.1	OMA GotAPI(DWAPI-PCH)	72

7.1.1	Introduction	72

7.1.2	Device Models	72

7.1.2.1	deviceBloodPressureMonitor	72

7.1.2.2	deviceGlucosemeter	73

7.1.2.3	devicePulseOximeter	74

7.1.2.4	deviceThermometer	74

7.1.2.5	deviceWeightScaleAndBodyCompositionAnalyzer	75

7.1.2.6	deviceHeartRateMonitor	76

7.1.3	Data Types	76

8	Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology	77

A	(informative):  Resource Mapping Examples	78

A.1	Introduction	78

A.2	Example for Device model ‘deviceAirConditioner'	79

A.3	Example of ModuleClass 'binarySwitch'	81

A.4	Example of Action 'toggle'	82

B	(informative):  Introduction of Extarnal Organizations Data Model	83

B.1	OMA Got API(DWAPI-PCH)	83

B.2	OCF	84

B.3	ECHONET	84

C	History	84

# Scope

The present document describes the oneM2M defined information model for home appliances, including the description of how it is mapped with other information models from external organizations. It also explains the ontology for the home domain information model.

# References

References are either specific (identified by date of publication and/or edition number or version number) or non-specific. For specific references, only the cited version applies. For non-specific references, the latest version of the reference document (including any amendments) applies.

## Normative references

The following referenced documents are necessary, partially or totally, for the application of the present document. Their use in the context of this TS is specified by the normative statements that are referring back to this clause

[1]	Home Gateway Initiative Smart Device Template.

NOTE:	Available at https://github.com/Homegateway/SmartDeviceTemplate/tree/7c890b69d9764e341ef1768c5a0e7d53a47cff5c.

[2]	Java coding rule.

[3]	oneM2M TS-0001: "Functional Architecture".

[4]	oneM2M TS-0004: “Service Layer Core Protocol Specification”

[5]	oneM2M TS-0005: ”Management Enablement (OMA)”.

[6]	ISO:80000-1: Quantities and units

NOTE:	Available at http://www.oracle.com/technetwork/java/codeconventions-135099.html.

[7]	Open Mobile AllianceTM: “OMA-ER-Device_WebAPIs-V1_0-20160419-C”.

NOTE:	Available at  http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-ERELD-DWAPI_V1_0-20160419-C.pdf

[8]	Open Mobile AllianceTM: “OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at  http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Blood_Pressure_Monitor_APIs-V1_0-20160419-C.pdf

[9]	Open Mobile AllianceTM: “OMA-TS-Glucometer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Glucometer_APIs-V1_0-20160419-C.pdf

[10]	Open Mobile AllianceTM: “OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Heart_Rate_Monitor_APIs-V1_0-20160419-C.pdf

[11]	Open Mobile AllianceTM: “OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Pulse_Oximeter_APIs-V1_0-20160419-C.pdf

[12]	Open Mobile AllianceTM: “OMA-TS-Thermometer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Thermometer_APIs-V1_0-20160419-C.pdf

[13]	Open Mobile AllianceTM: “OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C”.

NOTE:	Available at http://www.openmobilealliance.org/release/DWAPI/V1_0-20160419-C/OMA-TS-Weight_Scale_Body_Composition_Analyzer_APIs-V1_0-20160419-C.pdf

[14]	W3C Recommendation: “XML Schema Part 2: Datatypes”, 02 May 2001.

NOTE:	Available at http://www.w3.org/XML/Schema/.

[15]	NIST standard FIPS PUB 180-2

[16]	IETF RFC 4566: "SDP: Session Description Protocol".

[17]	IANA Time Zone Database

NOTE:	Available at https://www.iana.org/time-zones

## Informative references

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.1]	oneM2M Drafting Rules.

NOTE:	Available at http://www.onem2m.org/images/files/oneM2M-Drafting-Rules.pdf.

[i.2]	oneM2M TR-0017: "Home Domain Abstract Information Model".

[i.3]	oneM2M TS-0001: "Functional Architecture".

[i.4]	IEEE 802.15.4: "IEEE Standard for Local and metropolitan area networks--Part 15.4: Low-Rate Wireless Personal Area Networks (LR-WPANs)".

[i.5]	oneM2M TS-0012: "Base Ontology".

[i.6]	https://en.wikipedia.org/wiki/Multiple_inheritance

[i.7]	https://www.me.go.kr/home/web/index.do?menuId=10272&condition.code1=007

# Definitions

For the purposes of the present document, the following terms and definitions apply:

Device Class ID: URN to identify the Device model definition.

ModuleClass ID: URN to identify the ModuleClass model definition

# Conventions

The key words "Shall", "Shall not", "May", "Need not", "Should", "Should not" in the present document are to be interpreted as described in the oneM2M Drafting Rules [i.1].

# Home Appliance Information Model

## Introduction

The present document intends to provide the unified means in the oneM2M system by defining a home appliance information model for the home domain devices such as TV, refrigerator, air conditioner, clothes washer, oven, and robot cleaner. For the reasons of interworking with external technologies and efficiency, the principle of the home appliance information model is designed based on HGI SDT 3.0 [1].

The principle of defining the home appliance information model is introduced in clause 5.2. ModuleClasses which oneM2M systems support are explained in clause 5.3. In the subsequent clause 5.5, Device models are defined.

## Design Principle of the Home Appliance Information Model

### Basic design principle of information modelling

The design principle of the oneM2M abstract information model of home appliance, is to use SDT 3.0 as introduced in oneM2M TR-0017 [i.2]. Note that those terms starting with a capital letter in this clause are SDT terms and are explained in [1].

Domain is a unique name which acts like a namespace (e.g., "org.oneM2M.home.modules"). It is set by the organization creating the SDT, allowing reference to a package of definitions for the contained ModuleClasses and Device models.

ModuleClasses specifies a single service (e.g., audioVolume, powerOn/Off) with one or more Actions, Properties, DataPoints and Events. Each service which is described as a ModuleClass can be re-used in many Devices.

Device model is a physical, addressable, identifiable appliance, sensor and actuator with one or more Modules, Properties and SubDevices.

SubDevice is a device which may be embedded in a Device and/or is addressed via another Device.

Module is an instantiation of a ModuleClass for a specific Device or SubDevice.

Figure 5.2.1-1 depicts the basic structure of SDT 3.0.

Specifications of new Device models and ModuleClasses are encouraged to re-use the definitions specified in this document as much as possible. If re-use is not possible and new Device and/or ModuleClases definitions are necessary, it is strongly advised to closely follow the guidelines and definition style from this document.

Figure 5.2.1-1: Design Structure of the Home Appliance Information Model using SDT 3.0

### Description rules for Module Classes and Device models

When the Home Appliances Information Model is described based on SDT, the following rules shall be applied:

Rule 1: CamelCase rule:

When naming each element, lowerCamelCase shall be used as the Java coding rules [2].

Rule 2: Rule for description of Action, DataPoint:

DataPoint shall be used to represent stateless operations. (e.g. powerState of binarySwitch for on/off operations).

Action shall be used when describing stateful condition, handling unknown internal state conditions (e.g. upVolume/downVolume by increasing/decreasing the audioVolume in steps, handling transactional procedures, or checking integrity using username plus password at the same time).

Rule 3: Rule for description of DataPoint and Property:

Non-functional information shall be described as a Property. Functional information shall be described as a DataPoint. (E.g. non-functional information: version, id; functional information: targetTemperature, targetVolume).

Rule 4: Definition of the Domain:

The Domain, in the case of the Home Appliance Information Model, is specified as "org.onem2m.home".

The sub-domain for Device and ModuleClass shall be specified as "org.onem2m.home.devices" and "org.onem2m.home.moduleclasses" respectively.

Rule 5: Naming rule for the element:

the name of each element should be concise and avoid repeating its parent element name; but

it may include the name of its parent element for readability. (e.g., lightDimmerUp, lightDimmerDown under lightDimmer).

Rule 6: Criteria for marking elements as optional or mandatory:

An element shall only be defined as mandatory if it's foreseen to be universally mandatory to all implementing technologies.

Rule 7: Enumeration type:

When describing the meaning of values for enumeration type elements, they may be described in another clause.

The enumeration types for Home Appliance Information Model are based on <xs:integer>, and the numeric values are interpreted as specified in clause 5.6.

Rule 8: Rule for unit  in documentation :

SI (International Systems of Units in [z]) measurement (e.g. meter, kilogram, second.) should be considered as first candidate.

Otherwise, it may be kept consistency with implementing technologies such as other SDO’s specification..

Editor's note: Popular unit in particular industrial domain should be considered  (e.g. cm for human height, calories for energy consumption in healthcare domain). It should be made coherent in the document, as possible.

Rule 9: Rule for type :

Measured and/or calculated values should be represented in float (without taking care of resolution of values).

Editor’s note: It should be made coherent in the document, as possible. Unit shall not be fixed as a rule but be decided with correspondence to each device or module.

Rule 10: Inheritance of ModuleClasses :

A ModuleClass may inherit from another existing ModuleClass in order to provide additional functionalities based on the existing ModuleClass. However, inheritance from multiple ModuleClasses is not allowed (due to the “diamond problem” [i.6]).

Inheritance of ModuleClass shall only be used in the case that extending an existing ModuleClass is not appropriate, i.e. the functionality to be added is irrelevant to the original design purpose of the existing ModuleClass (e.g. adding a ‘time’ DataPoint to a ‘binarySwitch’ ModuleClass).

Rule 11: When to differentiate between current and target Data Points in ModuleClasses:

Device operations, which are executed when setting data points to specific values, may take some time to reach the desired result. For example, setting a new temperature to a heater does not immediately change the room temperature, but it may take some time for the heater to increase the temperature. Therefore, it is sometimes necessary to distinguish between current and target data points.

A ModuleClass must provide an additional “target” data point when the “current” data point …

  - is writable, and

  - the functionality that is mapped to the data point is an operation, not a configuration function, and

  - the operation may take some time to start and/or to complete, or reach the desired result.

When a ModuleClass provides current and target data points then the name for the current data point must have the prefix “current”, and the name for the target data point must have the prefix “target”. Both data points must have the same suffix, for example “currentTemperature” and “targetTemperature”.

## ModuleClasses

### 3Dprinter

This ModuleClass provides capabilities for a 3D printer.

Table 5.3.1-1: Actions of 3Dprinter

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | start3Dprint | none | true | Start 3D printing. |
| none | stop3Dprint | none | true | Stop 3D printing. |

Table 5.3.1-2: DataPoints of 3Dprinter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| printType | hd:3DprinterTechnology | true | false | false | The type of printing technology (see clause 5.6.1). |
| printSizeX | xs:float | true | false | false | This data pointrepresents the maximum size of a printing object in the direction of X-axis. The unit of measure is “mm”. (1/10cm). |
| printSizeY | xs:float | true | false | false | This data poin represents the maximum size of printing object in the direction of Y-axis. The unit of measure is “mm”. (1/10cm). |
| printSizeZ | xs:float | true | false | false | This data point represents the maximum size of printing object in the direction of Z-axis. The unit of measure is “mm”. (1/10cm). |
| network | xs:boolean | true | false | false | This value indicates the Wide Area Network (WAN) connectivity of the 3D printer, such as Internet or GSM. ”False” indicates that the printer does not have network connectivity to a WAN. “True” indicates that the printer has WAN network connectivity. |
| memorySize | xs:float | true | false | false | This value represents the total memory size of the printer. The unit of measure is MB(Mega Bytes). |

### acousticSensor

This ModuleClass provides capabilities for an acoustic sensor.

Table 5.3.2-1: DataPoints of acousticSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| loudness | xs:float | true | false | false | The unit of measure of the loudness is “dB2”. |
| acousticStatus | xs:integer | true | false | true | The acousticStatus is expressed in percent, whereas a value of 0 means “no sound” and a value of 100 means “most noisy”. |

### airConJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of an air conditioner.

Table 5.3.3-1: DataPoints of airConJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:airConJobMode | true | true | false | Currently active job mode (see clause 5.6.3). |
| currentJobModeName | xs:string | true | false | true | Name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:airConJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.3). |

### airFlow

This ModuleClass provides capabilities for controlling the air flow of a device.

Table 5.3.4-1: DataPoints of airFlow ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| speed | xs:integer | true | true | false | The current speed level in the range of the [minSpeed, maxSpeed] data poins. |
| minSpeed | xs:integer | true | false | true | The minimum value for the speed level. If not present, the default is 0. |
| maxSpeed | xs:integer | true | false | true | The maximum value for the speed level. If not present, the default is 100. |
| verticalDirection | hd:verticalDirection | true | true | true | The vertical direction of the air flow (see clause 5.6.31). |
| supportedVerticalDirection | List of hd:verticalDirection | true | false | true | List of supported vertical directions. |
| horizontalDirection | hd:horizontalDirection | true | true | true | The horizontal direction of the air flow (see clause 5.6.17). |
| supportedHorizontalDirection | List of hd:horizontalDirection | true | false | true | List of supported horizontal directions. |
| automode | xs:boolean | true | true | true | Status of the automode feature. “True” indicates that the speed is set by the device, “False” indicates that the device is not controlling the speed. |

### airPurifierJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of an airPurifier.

Table 5.3.5-1: DataPoints of airPurifierJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:airPurifierJobMode | true | true | false | Currently active job mode (see clause 5.6.4). |
| currentJobModeName | xs:string | true | false | true | Name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:airPurifierJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.4). |

### airQualitySensor

This ModuleClass provides capabilities for a monitoring sensor that measures the air quality.

Table 5.3.6-1: DataPoints of airQualitySense ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| sensorPM1 | xs:integer | true | false | true | The concentration of particle matter under 1㎛.. The minimum value is 0, and the maximum value is 1000. |
| sensorPM2 | xs:integer | true | false | true | The concentration of particle matter under 2.5㎛. The minimum value is 0, and the maximum value is 1000. |
| sensorPM10 | xs:integer | true | false | true | The concentration of particle matter under 10㎛. The minimum value is 0, and the maximum value is 1000. |
| sensorOdor | xs:integer | true | false | true | The concentration of odor that reflects air pollution. The minimum value is 0, and the maximum valu is 1000. |
| sensorHumidity | xs:integer | true | false | true | The measured humidity. The minimum value is 0, and the maximum value is 100. |
| monitoringEnabled | xs:boolean | true | true | true | The current status of monitoring. "True" indicates enabled, and "False" indicates not enabled. |
| co2 | xs:integer | true | false | true | This value indicates the CO2 level in ppm (parts per million). |
| co | xs:integer | true | false | true | This value indicates the CO level in ppm. |
| ch2o | xs:integer | true | false | true | This value indicates the CH2O level in ppm. |
| voc | xs:integer | true | false | true | This value indicates the VOC (Volatile Organic Compounds) value in ppm. |

### alarmSpeaker

This ModuleClass provides the capabilites to initiate and monitor an alarm.

Table 5.3.7-1: DataPoints of alarmSpeaker ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| tone | hd:tone | true | true | true | Representing the tones of the alarm (see clause 5.6.29). |
| light | hd:alertColourCode | true | true | true | Representing the lighting mode of the alarm (see clause 5.6.5). |
| alarmStatus | xs:boolean | true | true | false | "True" indicates the alarm start while "False" indicates the alarm stop. |

### audioVolume

This ModuleClass provides capabilities to control and monitor volume

Table 5.3.8-1: Actions of audioVolume

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upVolume | none | true | Increase the volume by the amount of the stepValue up to the maxValue. |
| none | downVolume | none | true | Decrease the volume by the amount of the stepValue down to 0. |

Table 5.3.8-2: DataPoints of audioVolume

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| volumePercentage | xs:integer | true | true | false | The rounded percentage of the current volume in the range of [0, maxValue]. 0 percentage shall mean no sound produced. |
| stepValue | xs:integer | true | false | true | Step value used by the “UpVolume” and “DownVolume” actions. |
| maxValue | xs:integer | true | false | true | Maximum value allowed for Volume. maxValue is 100 by default if “maxValue” is not provided. |
| muteEnabled | xs:boolean | true | true | false | The current status of the mute enablement. "True" indicates enabled (that is, no sound), and "False" indicates not enabled (that is, sound is played). |

### autoDocumentFeeder

This ModuleClasses provides capabilities to monitor the state of autoDocumentFeeder (ADF). ADF is a feature which takes several pages and feeds the paper one page at a time into a scanner or printer, allowing the user to scan, print or fax, multiple-page documents without having to manually replace each page.

Table 5.3.9-1: DataPoints of autoDocumentFeeder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentAdfState | hd:adfState | true | false | false | Current state of the ADF. |
| adfStates | list of hd:adfState | true | false | false | List of possible ADF states that are supported by the device (see clause 5.6.2). |

### battery

This ModuleClass provides capabilities to indicate the detection of low battery and gives an alarm if the triggering criterion is met. The level data point in the ModuleClass represents the current battery charge level.

Table 5.3.10-1: DataPoints of battery ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| level | xs:integer | true | false | False | The rounded percentage of the current charging level of a battery in the range of [0, 100]. 0 percentage shall mean that no charge remains. |
| capacity | xs:integer | true | false | True | The total capacity of battery in mAh. |
| charging | xs:boolean | true | false | True | The status of charging. "True" indicates enabled, and "False" indicates not enabled. |
| discharging | xs:boolean | true | false | True | The status of discharging. "True" indicates charging, and "False" indicates not charging. |
| lowBattery | xs:boolean | true | false | True | To indicate that the battery is on a low charge level. |
| batteryThreshold | xs:integer | true | true | True | When a battery’s “level” is less than “batteryThreshold” then “lowBattery” is set to “True” (and optionally to generate an alarm, see clause 5.3.7). |
| electricEnergy | xs:integer | true | false | true | Rated electric energy. |
| voltage | xs:integer | true | false | true | Rated voltage. |
| material | xs:string | true | false | true | The material of the cell (for example lithium ion, nickel and lead. |

### binaryObject

This ModuleClass describes the handling of a binary object (blob).

Table 5.3.11-1: DataPoints of binaryObject ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| object | xs:string | true | true | false | This data point contains the base64 encoded binary object. |
| objectType | xs:string | true | true | false | This data point contains the type and subtype of the binary object as a MIME type. |
| size | xs:integer | true | true | true | The size of the decoded binary object. |
| hash | xs:string | true | true | true | The hash code of the blob. If present, it is used to check the decoded content of the “object” data point for integrity. The algorithm used for generating the hash value is SHA-2 [15]. The data point contains the hash as a hex encoded value. |

### binarySwitch

This ModuleClass provides capabilities to control and monitor the state of power.

Table 5.3.12-1: Actions of binarySwitch ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | toggle | none | true | Toggle the switch. |

Table 5.3.12-2: DataPoints of binarySwitch ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerState | xs:boolean | true | true | false | The current status of the binarySwitch. "True" indicates turned-on, and "False" indicates turned-off. |

### bioElectricalImpedanceAnalysis

This ModuleClass provides the analysis of human body tissue based on impedance measurement.

Table 5.3.13-1: DataPoints of bioElectricalImpedanceAnalysis ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| water | xs:float | true | false | false | The water content measurement from the BIA. The unit of measue is percentage. |
| fat | xs:float | true | false | false | The fat content measurement from the BIA. The unit of measure is percentage. |
| muscle | xs:float | true | false | false | The muscle content measurement from the BIA. The unit of measure is percentage. |
| bone | xs:float | true | false | false | The bone content measurement from the BIA. The unit of measure is percentage. |
| visceraFat | xs:float | true | false | false | The viscera fat content measurement from the BIA. The unit of measure is percentage. |
| kcal | xs:float | true | false | false | The kcal (kilocalories) measurement from the BIA. |
| resistance | xs:float | true | false | false | The resistance of human body. The unit of measure is ohm. |

### bodyCompositionAnalyser

This ModuleClass provides the capability to report the measurement of body composition analyser characteristics.

Table 5.3.14-1: DataPoints of body composition analyzer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| bodyLength | xs:float | true | false | true | The measurement of body length by Weight scale and Body composition analyzer. The unit of measure is centimeter(cm). |
| Bmi | xs:float | true | false | true | The measurement of Body Mass Index (BMI) by a weight scale and a body composition analyser. The unit of measure is kg/m2. |
| fatFreeMass | xs:float | true | false | true | The measurement of fat free mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| softLeanMass | xs:float | true | false | true | The measurement of soft lean mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| muscleMass | xs:float | true | false | true | The measurement of muscle mass by a weight scale and a body composition analyser. The unit of measure is kilogram (kg). |
| basalMetabolism | xs:float | true | false | true | The measurement of basal metabolism by a weight scale and a body composition analyser. The unit of measure is kilocalorie (kcal). |
| impedance | xs:float | true | false | true | The measurement of impedance by a weight scale and a body composition analyser. The unit of measure is ohm. |

### boiler

This ModuleClass provides capabilities to control the status of the boiling functionality for water heaters.

Table 5.3.15-1: DataPoints of boiler ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| status | xs:boolean | true | true | false | The status of boiling. “True” indicates boiling, “False” indicates not boiling. |

### brewing

This ModuleClass provides capabilities to control and monitor a brewing process. It is intended to be part of devices that prepare hot drinks such as a coffee or a tea.

Table 5.3.16-1: DataPoints of brewing ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| cupsNumber | xs:integer | true | true | false | The current number of the cups requested to brew. |
| strength | hd:tasteStrength | true | true | true | The current strength of the drink taste (see clause 5.6.28). A higher value indicates a stronger taste. |

### brightness

This ModuleClass provides capabilities to control and monitor the brightness of a light for example from a lamp. Brightness is scaled as a percentage. A lamp or a monitor can be adjusted to a level of light between very dim (0% is the minimum brightness) and very bright (100% is the maximum brightness).

Table 5.3.17-1: DataPoints of brightness ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| brightness | xs:integer | true | true | false | The status of brightness level in percentage. |

### clock

This ModuleClass provides capabilities to control and monitor time and date information.

Table 5.3.18-1: DataPoints of clock ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentTime | xs:time | true | true | false | Information of the current time |
| currentDate | xs:date | true | true | false | Information of the current date |
| currentTimeZone | xs:string | true | true | true | Name of current time zone according to the IANA Timezone data format (TZ) [17], for example, “America/New York”. |

### clothesDryerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a clothes dryer.

Table 5.3.19-1: DataPoints of clothesDryerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:clothesDryerJobMode | true | true | false | Currently active job mode (see clause 5.6.7). |
| currentJobModeName | xs:string | true | false | true | Name of current job mode as a string. This can be used when “currentJobMode” is vendor-specific. |
| jobModes | list of hd:clothesDryerJobMode | true | false | false | List of possible job states the device supports. |

### colour

This ModuleClass provides the capabilities to set the value of the Red, Green, and Blue colour channels for a colour device.

Table 5.3.20-1: DataPoints of colour ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| red | xs:integer | true | true | false | The value of the Red colour channel of RGB. The range is [0,255]. |
| green | xs:integer | true | true | false | The value of the Green colour channel of RGB. The range is [0,255]. |
| blue | xs:integer | true | true | false | The value of the Blue colour channel of RGB. The range is [0,255]. |

### colourSaturation

This ModuleClass provides cababilities to control and monitor a colour saturation value.

Table 5.3.21-1: DataPoints of colourSaturation ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| colourSaturation | xs:integer | true | true | false | The status of colour saturation level. “colourSaturation” has a range of [0,100]. A “colourSaturation” value of 0 means that a device displays or produces black and white images. A “colourSaturation” value of 50 means that a device displays or produces normal colour images. A “colourSaturation” value of 100 means that a device displays or produces very colourfull images. |

### credentials

This ModuleClass provides the capability to manage user credentials which allows a user to authenticate on an appliance or a server that is associated with the appliance. The authentication depends on a user login and password, or on a token. An example appliance which may include this ModuleClass is a camera.

Table 5.3.22-1: DataPoints of credentials ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| loginName | xs:string | false | true | true | The user’s login name. |
| password | xs:string | false | true | true | The user’s password. |
| token | xs:string | false | true | true | An authentication token, for example an OAuth token. |

### dehumidifierJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a dehumidifier device.

Table 5.3.23-1: DataPoints of dehumidifierJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:dehumidifierJobMode | true | true | false | The currently active job mode (see clause 5.6.8). |
| currentJobModeName | xs:string | true | false | true | The name of the current job mode as a string. This can be used when currentJobMode is vendor-specific. |
| jobModes | list of hd:dehumidifierJobMode | true | false | false | List of possible job states the device supports. |

### doorStatus

This ModuleClass provides the status of a door. It is intended to be part of a device such as a refrigerator and an oven that might have multiple doors.

Table 5.3.24-1: DataPoints of doorStatus ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| doorState | hd:doorState | true | false | false | Current state of the door (see clause 5.6.10). |
| openDuration | m2m:timestamp | true | false | true | The time duration the door has been open. |
| openAlarm | xs:boolean | true | true | true | The state of the door open alarm. "True" indicates that the open alarm is active. "False" indicates that the open alarm is not active. |

### electricVehicleConnector

This ModuleClass provides information about charging/discharging devices for electric vehicles.

Table 5.3.25-1: DataPoints of electricVehicleConnector ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| Status | xs:boolean | true | false | false | The status of connection. “True” means connected, “False” means not connected. |
| chargingCapacity | xs:integer | true | false | true | Rated charging capacity. |
| DischargingCapacity | xs:integer | true | false | true | Rated discharging capacity. |

### energyConsumption

This ModuleClass describes the measured energy consumed by the device since power up. One particular use case for the energyConsumption ModuleClass is a smart meter.

Table 5.3.26-1: DataPoints of energyConsumption ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| power | xs:float | true | false | false | The power of the device. The unit of measure is Watt (W). |
| absoluteEnergyConsumption | xs:float | true | false | true | The absolute energy consumption, reflecting the real measurement of accumulative energy. The unit of measure is Watt-hour (Wh). |
| roundingEnergyConsumption | xs: integer | true | false | true | This energy consumption data can be calculated by using significantDigits and multiplyingFactors. |
| significantDigits | xs:integer | true | false | true | The number of effective digits for data. |
| multiplyingFactors | xs:float | true | false | true | The unit for data multiplying factors., for example 1 kWh, 0,1 kWh, 0,01 kWh etc. |
| voltage | xs:float | true | false | true | The voltage of the device. The unit of measure is volts (V). |
| current | xs:float | true | false | true | The current of the device. The unit of measure is ampere (A). |
| frequency | xs:float | true | false | true | The frequency of the device. The unit of measure is hertz (Hz). |

### energyGeneration

This ModuleClass provides information about generation data on electric generator devices such as a photo voltaic power system, fuel cells, or microgeneration.

Table 5.3.27-1: DataPoints of energyGenerationModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerGenerationData | xs:float | true | false | true | Amount of instaneous generation data. |
| roundingEnergyGeneration | xs:integer | true | false | true | This energy generation data can be calculated by using significantFigures and multiplyingFactors. |
| significantDigits | xs:integer | true | false | true | The number of effective digits for data. |
| multiplyingFactors | xs:floatr | true | false | true | The unit for data multiplying factors, for example 1 kWh, 0,1 kWh, 0,01 kWh etc. |

### faultDetection

This ModuleClass provides information about whether a fault has occurred in a device.

Table 5.3.28-1: DataPoints of faultDetection ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| status | xs:boolean | true | false | false | The status of fault detection. |
| code | xs:integer | true | false | true | The numeric representation of the fault. |
| description | xs:string | true | false | true | The message representation of the fault. |

### filterInfo

This ModuleClass is for monitoring filter information of a device.

Table 5.3.29-1: DataPoints of filterInfo ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| usedTime | xs:integer | true | false | false | The cumulative used time in seconds of a filter |
| needsReplacement | xs:boolean | true | false | true | This value indicates that the filter needs to be replaced. |
| filterLifetime | xs:integer | true | false | true | Percentage life time remaining for the water filter. |

### foaming

This ModuleClass provides capabilities to control and monitor desired parameters of foam e.g. for foaming milk. It is initially intended to be part of a device that prepare drinks with milk (for example a coffee machine or hot chocolate machine).

Table 5.3.30-1: DataPoints of foaming ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| foamingStrength | hd:foamStrength | true | true | false | The current strength of foamed milk. A higher value indicates more foamed milk (see clause 5.6.11) |

### geoLocation

This ModuleClass provides the capability to get or set geo-location information.

Table 5.3.31-1: DataPoints of geoLocation ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| latitude | xs:float | true | true | false | The current latitude part of a geo-location. The unit of measures is degrees. |
| longitude | xs:float | true | true | false | The current longitude part of a geo-location. The unit of measures is degrees. |
| altitude | xs:float | true | true | true | The optional current altitude part of a geo-location. The unit of measures is meters. |
| heading | xs:float | true | true | true | The azimuth of a device measured in degrees to true north. North is 0.0 degrees, east is 90.0 degrees, south is 180.0 degrees, west is 270.0 degrees. A negative value indicates an unknown heading. |
| horizontalAccuracy | xs:float | true | false | true | The optional current horizontal accuracy of the geo-location. The unit of measures is meters and describes a radius around the latitude/longitude coordinate. |
| verticalAccuracy | xs:float | true | false | true | The optional current vertical accuracy of the altitude. The unit of measures is meters. |
| headingAccuracy | xs:float | true | false | true | The optional current maximum deviation between the heading and the true geomagnetic heading. The unit of measures is degrees. |
| targetLatitude | xs:float | true | true | true | The optional target latitude part of a geo-location. This can be used to move a device to a new location. The unit of measures is degrees. |
| targetLongitude | xs:float | true | true | true | The optional target longitude part of a geo-location. This can be used to move a device to a new location. The unit of measures is degrees. |
| targetAltitude | xs:float | true | true | true | The optional target altitude part of a geo-location. This can be used to move a device to a new altitude. The unit of measures is meters. |

### glucometer

This ModuleClass provides the capability to report the measurement of glucose characteristics.

Table 5.3.32-1: DataPoints of glucometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| concentration | xs:float | true | false | false | The measurement of concentration by Glucometer. The unit of measure is mg/dl. |
| hba1c | xs:float | true | false | true | The measurement of HbA1c by Glucometer. The unit of measure is percentage. |
| contextExercise | xs:float | true | false | true | The measurement of context exercise by Glucometer. The unit of measure is percentage. |
| contextMedication | xs:float | true | false | true | The measurement of context medication by Glucometer. The unit of measure is mg/dl. |
| contextCarbohydratesAmount | xs:float | true | false | true | The measurement of context carbohydrates by Glucometer. The unit of measure is gram (g). |
| contextCarbohydratesSource | xs:string | true | false | true | The timing of meals (for example “breakfast carbohydrates”). |
| contextMeal | xs:string | true | false | true | The style of meals (for examople “casual”). |
| contextLocation | xs:string | true | false | true | The body location where the Glucometer is worn (for example “finger”). |
| contextTester | xs:string | true | false | true | The test style (for example “self”). |
| contextHealth | xs:string | true | false | true | The severity of symptoms (for example “minor”), |

### grinder

This ModuleClass is for controlling a grinder, for example in a coffee machine.

Table 5.3.33-1: DataPoints of grinder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| useGrinder | xs:boolean | true | true | false | The current status of the grinder enablement. "True" indicates enabled, and "False" indicates disabled. |
| coarseness | hd:grindCoarseness | true | true | true | The wished coarseness of the solid supplies after grinding, for example for coffee beans (see clause 5.6.16). |
| grainsRemaining | hd:grainsLevel | true | false | true | The level of remaining grains in a machine having a grinder, for example for remaining coffee beans in the coffee machine grinder (see clause 5.6.15). |

### heatingZone

This ModuleClass provides the capabilities to monitor the status of the heating zone, for example for a cooktop.

Table 5.3.34-1: DataPoints of heatingZone ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| heatingLevel | xs:integer | true | false | false | The current heating level of the zone. The value range is from 0 (indicating that the zone is not heating) up to the maxHeatingLevel. |
| maxHeatingLevel | xs:integer | true | false | false | The maximum value allowed for the heating level of the zone. |

### height

This ModuleClass provides the capability to report the measurement of height.

Table 5.3.35-1: DataPoints of height ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| height | xs:float | true | false | false | The height measurement. The unit of measure is centimetre (cm). |

### hotWaterSupply

This ModuleClass provides information about the status of supplying hot water into tanks or bath tubs.

Table 5.3.36-1: DataPoints of hotWaterSupply ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| status | xs:boolean | true | false | false | The status of watering operation. |
| bath | xs:boolean | true | true | true | The status of filling bath tub. |

### impactSensor

This ModuleClass describes the capabilities on an impact sensor. The impact is a high force or shock over a short time period and the impactSensor detects this.

Table 5.3.37-1: DataPoints of impactSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| impactStatus | xs:boolean | true | false | false | The “impactStatus” indicates as follows: “True” means that a physical impact is detected, “False” means indicates a normal status (no impact detected). |
| impactLevel | xs:float | true | false | true | The “impactLevel” provides the level of impact. The unit of measure is “g” (G-force). |
| impactDirectionHorizontal | xs:float | true | false | true | The “impactDirection” indicates the horizontal direction where the impact comes from. The value is 0° to 360°. 0 is the front of the sensor and with clockwise increment. |
| impactDirectionVertical | xs:float | true | false | true | The “impactDirection” indicates the vertical direction where the impact comes from. The value is 0° to 360°. 0 is the front of the sensor and with upward increment. |

### keepWarm

This module allows to control the ‘keep warm’ feature in devices like coffe machines, kettles etc. It allows to keep water warm for a desired time. This ModuleClass inherits from binarySwitch (see clause 5.3.12) to store setting for the ‘keep warm’ feature. If the “powerState” data point in a keepWarmSwitch is “True” then the ‘keep warm’ function will be performed just after boiling (or heating) process is finished (otherwise this function will not be applied).

Table 5.3.38-1: DataPoints of keepWarm ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| time | xs:integer | true | true | true | The desired duration of ‘keep water warm’ function. It indicates how long water shall be kept warm, for example after the boiling in a kettle. The value indicates a time expressed in minutes. |

### keypad

This ModuleClass provides the capability to perform a user defined service through the key-in number. For example, a user can define key 1 as "perform a takeout from a restaurant with combo meal 1". The IoT service provider or user can define the services.

Table 5.3.39-1: DataPoints of keypad ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| keyNumber | xs:integer | true | false | false | The number of the pressed key. |

### liquidLevel

This ModuleClass provides the desired level of water (or other liquid)  for an appliance, for example the desired level of milk for a cup of coffee from a coffee machine.

Table 5.3.40-1: DataPoints of liquidLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| liquidLevel | hd:liquidLevel | true | true | false | The desired level of water or other liquid, for example the desired level of milk in a cup of coffee (see clause 5.6.19). |

### liquidRemaining

This ModuleClass provides the status of water level (or other liquid) for an appliance, for example the level of remaining milk in a coffee machine.

Table 5.3.41-1: DataPoints of liquidRemaining ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| liquidRemaining | hd:liquidLevel | true | false | false | The remaining level of water or other liquid in an appliance (see clause 5.6.19). |

### lock

This ModuleClass provides the function to lock and unlock an object.

Table 5.3.42-1: DataPoints of lock ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| lock | xs:boolean | true | true | false | "True" indicates the object is locked, while "False" indicates the object is not locked. |

### mediaSelect

This ModuleClass provides capabilities to control and monitor media input and output of device such as TV or SetTopBox.

Table 5.3.43-1: DataPoints of mediaSelect ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| mediaID | xs:integer | true | true | false | The numeric index of the activated media in the supported media sources list “supportedMediaSources”. |
| supportedMediaSources | list of hd:supportedMediaSource | true | false | false | List of supported input or output media for the given device (see clause 5.6.27). |
| mediaName | xs:string | true | false | true | Specifies a pre-defined media input or output. |
| status | xs:boolean | true | false | true | Specifies whether the specific media instance is selected (“True”) or not (“False”). |
| mediaType | hd:supportedMediaSource | true | false | false | Specifies the type of the media (see clause 5.6.27). |

### motionSensor

This ModuleClass provides the capabilities to indicate the occurrence of motion and raising of an alarm if the triggering criterion is met.

Table 5.3.44-1: DataPoints of motionSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | The detection of the motion occurrence. |
| silentTime | xs:integer | true | true | true | The time that a motionSensor restrains from sending an alarm in case continous motions are detected after one alarm is produced. This data point can be used to avoid repeated alarm reports. The unit of measure is seconds. |
| sensitivity | xs:integer | true | true | true | The level of the detection accuracy of the motion sensor. This data point can be used to control the number of the report. |

### numberValue

This ModuleClass provides the capabilities to represent a number. It also has capabilities for controlled increment and decrement a counter. It can be used to present a number-related functionality in a technology where there is only a weak semantic specification of that functionality.

Table 5.3.45-1: Actions of numberValue ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | decrementNumberValue | none | true | Decrement the “numberValue” by the value of “step”, down to the value of “minimum”. |
| none | incrementNumberValue | none | true | Increment the "numberValue" by the value of "stepValue", up to the value of "maxValue". |
| none | resetNumberValue | none | true | Reset the “numberValue” to its “defaultValue”. |

Table 5.3.45-2: DataPoints of numberValue ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| numberValue | xs:float | true | true | false | The actual value of the number. |
| minValue | xs:float | true | true | true | The optional minimum value of the number. The default is the system-specific minimum value for a float value. |
| maxValue | xs:float | true | true | true | The optional maximum value of the number. The default is the system-specific maximum value for a float value. |
| defaultValue | xs:float | true | true | true | The optional default value for the number. The default is 0.0 . |
| step | xs:float | true | true | true | The optional step size for controlled increment and decrement. The default is 1.0 , even when this data point is not implemeneted. |

### openLevel

This ModuleClass provides the capabilities to control and monitor the open status of an entity, for example a curtain.

Table 5.3.46-1: Actions of openLevel ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | open | None | true | Increase the open level by the amount of the “stepValue” up to the “maxLevel”. |
| none | close | None | true | Decrease the open level by the amount of the “stepValue” down to the “minLevel”. |

Table 5.3.46-2: DataPoints of openLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| openLevel | xs:integer | true | true | false | The rounded percentage of the current open level of entity in the range of [0, 100]. 0 percentage shall mean the entity is closed. |
| stepValue | xs:integer | true | true | true | The step value used by the “open” and “close” actions. |
| minLevel | xs:integer | true | true | true | The minimum value allowed for the “openLevel” status. The default value is 0, which means fully closed. |
| maxLevel | xs:integer | true | true | true | The maximum value allowed for the “openLevel” status. The default value is 100, which means fully opened. |

### operationMode

This ModuleClasses provides capabilities to control or monitor the operation mode of appliances.

Table 5.3.47-1: DataPoints of operationMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| startPause | xs:boolean | true | true | false | A value of “True” triggers or starts an operation, and “False” pauses the operation. |

### overcurrentSensor

This ModuleClass provides capabilities for an over-current sensor.

Table 5.3.48-1: DataPoints of overcurrentSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| overcurrentStatus | xs:boolean | true | false | false | The overcurrentStatus indicates as follows: “True” indicates that an over-current is detected, and “False” indicates a normal status, this means that an over-current is not detected |
| detectedTime | m2m:timestamp | true | false | true | The time when the over-current was detected. |
| duration | xs:float | true | false | true | The duration of the detected over-current. The unit of measure is “ms”. |

### oximeter

This ModuleClass provides the capability to report the measurement of blood oxygen characteristics.

Table 5.3.49-1: DataPoints of oximeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| oxygenSaturation | xs:integer | true | false | false | The measurement of oxygensaturation by Oximeter. The unit of measure is in percentage. |

### ozoneMeter

This ModuleClass provides capabilities for an ozone meter. The “ozoneValue…” attributes are optional, but one of them SHALL be provided.

Table 5.3.50-1: DataPoints of ozoneMeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| ozoneValuePPM | xs:float | true | false | true | The unit of measure of ozone measurement is “ppm”. |
| ozoneValueMG | xs:float | true | false | true | The unit of measure of ozone measurement is “mg/m3“. |
| ozoneStatus | hd:ozoneStatus | true | false | true | The ozoneStatus indicates the level of ozone status. (see clause 5.6.21). |
| maxValue | xs:float | true | false | true | The mazimum value shows the measurement range of the ozone meter (for example maxValue=5 means the range is 0 to 5 ppm). This attribute is only used that the ozoneMeter provides “ppm” value. |

### phoneCall

This ModuleClass provides the capability get or set the caller and receipient IDs as well as to initate and terminate a call.

Table 5.3.51-1: Actions of phoneCall ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | call | none | true | Initiate an outgoing call. |
| none | answer | none | true | Answer (pickup) an incoming call. |
| none | hangup | none | true | Hangup an established call. |

Table 5.3.51-2: DataPoints of phoneCall ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| callerID | xs:string | true | true | false | This data point represents the initiating caller identiﬁcation of a call. In case of an outgoing call this would be the local line ID. This data point is optional. When it is empty for an incomming call, then the caller ID is unknown. When it is empty for an outgoing call, then it is exepected that it is set by the PBX or the operator. The format of caller ID is not speciﬁed here. |
| recipientID | xs:string | true | true | false | This data point represents the receiving caller identiﬁcation of a call. In case of an incoming call this would be the local line ID and optionally extension. The format of caller ID is not speciﬁed here. |
| callState | hd:callState | true | false | true | This data point represents the current state of an associated phone device regarding calls. |

### playerControl

This ModuleClass provides capabilities to control and monitor the operational modes of a media player functionality.

Table 5.3.52-1: Actions of playerControl ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | nextTrack | none | true | Go forward to a next chapter, section or similar marker in the media. |
| none | previousTrack | none | true | Go back to a previous chapter, section or similar marker in the media. |

Table 5.3.52-2: DataPoints of playerControl ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentPlayerMode | hd:playerMode | true | true | false | The current mode of the player. |
| currentPlayerModeName | xs:string | true | false | true | Name of current player mode in string. This can be used when “currentPlayerMode” is vendor-specific. |
| supportedPlayerModes | list of hd:playerMode | true | false | false | List of supported modes for a player. |
| speedFactor | xs:float | true | true | true | The optional factor of speeding up or slowing down playback, rewind or fast forward. |

### powerSave

This ModuleClass provides capabilities to enable the power saving mode of a device and monitor the current status.

Table 5.3.53-1: DataPoints of powerSave ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| powerSaveEnabled | xs:boolean | true | true | false | The current status of the power saving mode. "True" indicates enabled, and "False" indicates not enabled. |

### printQueue

This ModuleClass provides the capabilities for monitoring printing list information.

Table 5.3.54-1: DataPoints of printQueue ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| uri | list of xs:uri | true | false | false | The URI of the printing file. The URI could be “file://www.3dpexcont.com/ex.stl” |
| printingState | list of hd:machineState | true | false | false | The printingState is indicating the status of the printing file. |

### pulsemeter

This ModuleClass provides the capability to report the measurement of pulse characteristics.

Table 5.3.55-1: DataPoints of pulsemeter ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| pulseRate | xs:float | true | false | false | The measurement of pulserate by pulsemeter. The unit of measure is in beats per minute. |
| rr | xs:float | true | false | true | The measurement of RR interval by pulsemeter. The unit of measure is millisecond (ms). |
| energy | xs:float | true | false | true | The measurement of energy by pulsemeter. The unit of mease is kilocalorie per hour. |
| modality | xs:string | true | false | true | The modality of a particular SpO2 measurement. |

### pushButton

This ModuleClass provides the capability to indicate the operation of a push button style switch. A typical application can be an SOS button.

Table 5.3.56-1: DataPoints of pushButton ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| pushed | xs:boolean | true | false | false | This data point indicates the press of the button. |

### recorder

This ModuleClass provides the capability to record video/audio for a defined duration.

Table 5.3.57-1: DataPoints of recorder ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| duration | xs:integer | true | true | false | The duration for video/audio recording. Set to trigger the recorder. The unit of measure is seconds. |

### refrigeration

This ModuleClass provides capabilities for a refrigeration function.

Table 5.3.58-1: DataPoints of refrigeration ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| rapidFreeze | xs:boolean | true | True | true | Controls the rapid freeze capability. “True” indicates active, “False” indicates inactive. |
| rapidCool | xs:boolean | true | True | true | Controls the rapid cool capability. “True” indicates active, “False” indicates inactive. |
| defrost | xs:boolean | true | True | true | Controls the defrost cycle. “True” indicates active, “False” indicates inactive. |

### relativeHumidity

This ModuleClass provides the capability for a device to report the humidity based on a specified rule that is vendor dependent.

Table 5.3.59-1: DataPoints of relativeHumidity ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| relativeHumidity | xs:float | true | false | false | The measurement of the relative humidity value; the unit of measure is percentage. |
| desiredHumidity | xs:float | true | true | true | Desired value for humidity. This data point indicates the desired humidity. |

### remoteControlEnable

This ModuleClasses provides capabilities to monitor the remote controllability of the appliance.

Table 5.3.60-1: DataPoints of remoteControlEnable ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| remoteControlEnabled | xs:boolean | true | false | false | This data point enables or disables remote controllability and is set by a user locally. “True” indicates enabled remote access, and “False” indicates disabled remote access. When set to “False”, however, it still allows to monitor relevant resources. |

### robotCleanerJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of a robotCleaner.

Table 5.3.61-1: DataPoints of robotCleanerJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:robotCleanerJobMode | true | true | false | Currently active job mode (see clause 5.6.23). |
| currentJobModeName | xs:string | true | false | true | Name of current job mode as a string. This can be used when “currentJobMode” is vendor-specific. |
| jobModes | list of hd:robotCleanerJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.23). |

### runState

This ModuleClasses provides capabilities to control and the monitor machine state of appliances.

Table 5.3.62-1: DataPoints of runState ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentMachineState | hd:machineState | true | true | false | The currently active machine state (see clause 5.6.20). |
| machineStates | list of hd:machineState | true | false | false | A list of possible machine states the device supports (see clause 5.6.20). |
| currentJobState | hd:jobState | true | false | true | The currently active job state at the level of some transaction being executed by the device (see clause 5.6.18). |
| jobStates | list of hd:jobState | true | false | true | The list of possible job states that the device supports (see clause 5.6.18). |
| progressPercentage | xs:float | true | false | true | The indication of current job progress in percentage. |

### securityStatus

This ModuleClasses provides capabilities to control and monitor a security mode.

Table 5.3.63-1: DataPoints of securityStatus ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentSecurityMode | hd:securityMode | true | true | false | Current security mode (see clause 5.6.24). |
| securityMode | list of hd:securityMode | true | false | false | List of possible security modes the device supports (see clause 5.6.24). |

### sessionDescription

This ModuleClass provides the capabilities for a sessionDescription containing a URL at twhich the specified media can be accessed and the definition of media using SDP.

Table 5.3.64-1: DataPoints of mediaType ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| url | xs:uri | true | false | true | A URL at which the specified media can be accessed. |
| sdp | xs:string | true | false | true | Media description using SDP. One or more comma separated multiple SDP lines (SDP media or attribute line) can be included using SDP description syntax as defined in the SDP specification in RFC4566 [16]. |

### signalStrength

This ModuleClass provides the capability to monitor the strength of the signal.

Table 5.3.65-1: DataPoints of signalStrength ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| lqi | xs:integer | true | false | false | The current value of link quality indicator, which reflects the scaling of rssi by dividing the received signal strength over reference signal strength. The common unit for lqi is percentage [0,100]. For the detailed definition, please see IEEE 802.15.4 [i.4], clause 6.7.8. |
| rssi | xs:float | true | false | true | The current value of received signal strength indicator, which reflects the raw signal level. |

### smokeSensor

This ModuleClass provides the capabilities to indicate the detection of smoke and raising an alarm if the triggering criterion is met.

Table 5.3.66-1: DataPoints of smokeSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | The alarm is indicated as follows: “True” indicates that smoke has been detected, “False” indicates a normal status, that means that smoke is not detected. |
| detectedTime | m2m:timestamp | true | true | true | The date and time the smoke is detected. |
| smokeThreshhold | xs:integer | true | true | true | The threshhold to trigger the alarm. The unit of measure is ppm. |
| currentValue | xs:integer | true | false | true | The current data value of the smoke sensor. |

### sphygmomanometer

This ModuleClass provides the capability to report the measurement of blood pressure characteristics.

Table 5.3.67-1: DataPoints of sphygmomanometer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| diastolicPressure | xs:float | true | false | false | The measurement of diastolic pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |
| systolicPressure | xs:float | true | false | false | The measurement of systolic pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |
| meanPressure | xs:float | true | false | false | The measurement of mean arterial pressure by sphygmomanometer. The unit of measure is millimetre of mercury (mmHg). |

### spinLevel

This ModuleClass provides capabilities to control and monitor the level of spin. It is intended to be part of devices which use spinning function such as a washing machine and a dryer.

Table 5.3.68-1: DataPoints of spinLevel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| spinLevelStrength | hd:spinLevelStrength | true | true | false | The value of spin-dry level (see clause 5.6.25). A higher value indicates a higher spin level. |

### steamClosetJobMode

This ModuleClasses provides capabilities to control and monitor the job modes of steamCloset.

Table 5.3.69-1: DataPoints of steamClosetJobMode ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentJobMode | hd:steamClosetJobMode | true | true | false | Currently active job mode (see clause 5.6.26). |
| currentJobModeName | xs:string | true | false | true | Name of current job mode as a string. This can be used when “currentJobMode” is vendor-specific. |
| jobModes | list of hd:steamClosetJobMode | true | false | false | List of possible job states the device supports (see clause 5.6.26). |

### televisionChannel

This ModuleClass provides capabilities to set and get channels of a device that has a channel list.

Table 5.3.70-1: Actions of televisionChannel ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | upChannel | None | true | Change the current channel to the next channel in the stored list of available channels. If the current channel is the last one in the list, the new set channel may be the first one in the list. |
| none | downChannel | None | true | Change the current channel to the previous channel in the stored list of available channels. If the current channel is the first one in the list, the new set channel may be the last one in the list. |

Table 5.3.70-2: DataPoints of televisionChannel ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| channelNumber | xs:integer | true | true | false | Current channel number. |
| availableChannels | list of xs:integer | true | false | true | The list of available channel numbers which may be build by automatic scan and/or manual selction. |
| previousChannel | xs:integer | true | false | true | The channel number which was selected previously. |
| channelName | xs:string | true | false | true | Current human-friendly channel name in string, for example ‘CNN’. |

### temperature

This ModuleClass provides capabilities to represent the current temperature and target temperature of devices such as an air conditioner, refrigerator, oven etc.

Table 5.3.71-1: DataPoints of temperature ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentTemperature | xs:float | true | false | false | The current temperature. |
| targetTemperature | xs:float | true | true | true | The desired temperature to reach. |
| unit | xs:string | true | false | true | The unit of measure for the temperature values. The default is celsius (C). |
| minValue | xs:float | true | false | true | Minimum value of “targetTemperature”. |
| maxValue | xs:float | true | false | true | Maximum value of “targetTemperature”. |
| stepValue | xs:float | true | false | true | Step value allowed for “targetTemperature”. |

### temperatureAlarm

This ModuleClass provides the capabilities to indicate the detection of abnormal temperatures and raises an alarm if the triggering criterion is met.

Table 5.3.72-1: DataPoints of temperatureAlarm ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | true | false | false | This data point indicates the status of detection of an abnormal temperature. “True” indicates an abnormal temperature, “False” indicates a normal temperature. |
| temperature | xs:float | true | false | true | To report the value of the temperature. The unit of measure is celsius (C). |
| temperatureThreshhold | xs:integer | true | true | true | The threshhold to trigger the alarm. |

### textMessage

This ModuleClass provides capabilities to set and get a text message.

Table 5.3.73-1: Actions of textMessage ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | resetTextMessage | none | true | Reset the receiver of the message to the “defaultValue”. |

Table 5.3.73-2: DataPoints of textMessage ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| textMessage | xs:string | true | true | false | The current message value. |
| supportedMessageValues | list of xs:string | true | false | true | List of supported values for the message. Each of the values in this list must be URL-encoded. An encoded value must not contain white spaces. |
| minLength | xs:integer | true | false | true | The optional minimum length in characters of the message. The default is 0. |
| maxLength | xs:integer | true | false | true | The optional maximum length in characters of the message. The default is unlimited. |
| messageEncoding | xs:string | true | false | true | The optional expected method for character encoding of the message. The default is "UTF-8". |
| defaultValue | xs:string | true | true | true | The optional default value for “textMessage”. The default is an empty string. |

### timer

This ModuleClass provides capabilities to monitor and control the times when the appliance executes its operations, that means when it starts, when it ends etc.

Table 5.3.74-1: Actions of timer ModuleClass

| Return Type | Name | Argument | Optional | Documentation |
| --- | --- | --- | --- | --- |
| none | activateClockTimer | None | true | Activate current clock timer. |
| none | deactivateClockTimer | None | true | Deactivate current clock timer. |

Table 5.3.74-2: DataPoints of timer ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| referenceTimer | xs:integer | true | false | true | A timer (for example. a time-based value, App Defined Epoch, Progressive) expressed in seconds. The value indicates a time counter to be used as reference for the other time-based data points of this ModuleClass. Usually it is the time since the last event of power-on of the producer (or more in detail the time since the boot of its connectivity node). |
| targetTimeToStart | xs:integer | true | true | true | A time span (for example a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates the time when the appliance is expected to start its operation, starting counting from the last ”referenceTimer”. |
| targetTimeToStop | xs:integer | true | true | true | A time span (for example a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates the time when the appliance is expected to stop its operation, starting counting from the last ”referenceTimer”. |
| estimatedTimeToEnd | xs:integer | true | false | true | A timer (for example a time-based value, App Defined Epoch, Progressive) expressed in seconds. The value indicates the time to the end of an appliance’s operations. It is calculated at runtime by the device itself during the execution of its operation. |
| runningTime | xs:integer | true | false | true | A timer (for example a time-based value, App Defined Epoch, Progressive) expressed in seconds. It indicates the time of the current operation. Usually its value is increasing one value per second. It starts counting from 0 when the operation starts and stops counting when the operation ends. |
| targetDuration | xs:integer | true | false | true | A time span (for a time-based value, App Defined Epoch, Fixed) expressed in seconds. The value indicates a time that represents the target duration of the operation as per user selection. |
| absoluteStartTime | m2m:timestamp | true | true | true | An absolute time to specify the start time. |
| absoluteStopTime | m2m:timestamp | true | true | true | An absolute time to specify the stop time. |

### turbo

This ModuleClass provides capabilities to enable turbo mode and monitor the current status of the turbo function. It is intended to be part of devices which use turbo function such as an air conditioner, a washing machine etc.

Table 5.3.75-1: DataPoints of turbo ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| turboEnabled | xs:boolean | true | true | false | The current status of the turbo mode. "True" indicates enabaled, and "False" indicates not enabled. |

### uvSensor

This ModuleClass describes the capabilities of an ultraviolet sensor.

Table 5.3.76-1: DataPoints of uvSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| uvValue | xs:float | true | false | false | The unit of measure of the UV intensity of radiation is “mW/cm2”. |
| uvStatus | hd:uvStatus | true | false | true | The “uvStatus” indicates the level of the UV radiation status (see clause 5.6.30). |

### washingCourse

This ModuleClasses provides capabilities to control and monitor the washing course of a washer.

Table 5.3.77-1: DataPoints of washingCourse ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| currentWashingCourseName | xs:string | true | true | true | Currently active course name in human readable language. |
| currentWashingCourse | hd:washingCourse | true | true | false | Currently active course (see clause 5.6.32). |
| washingCourses | list of hd:washingCourse | true | false | false | Supported courses by a washer (see clause 5.6.32). |

### washingCourseOption

This ModuleClasses provides capabilities to control and monitor the washing course options of a washer.

Table 5.3.78-1: DataPoints of washingCourseOption ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| washTemp | hd:generalTemperature | true | true | true | This data point represents the water temperature level (see clause 5.6.14). |
| soilLevel | hd:generalLevel | true | true | true | This data point represents the washing level (see clause 5.6.12). |
| spinSpeed | hd:generalSpeed | true | true | true | This data point represents the spin-dry speed level (see clause 5.6.13). |
| preWash | xs:boolean | true | true | true | This data point indicates pre-wash. “True” indicates enabled, “False” indicates disabled. |
| speedWash | xs:boolean | true | true | true | This data point indicates speed wash. “True” indicates enabled, “False” indicates disabled. |
| steamTreat | xs:boolean | true | true | true | This data point indicates steam treat. “True” indicates enabled, “False” indicates disabled. |
| coldWash | xs:boolean | true | true | true | This data point indicates cold wash. “True” indicates enabled, “False” indicates disabled. |
| extraRinse | xs:boolean | true | true | true | This data point indicates extra rinse. “True” indicates enabled, “False” indicates disabled. |

### waterFlow

This ModuleClass provides capabilities for controlling the water strength of a device.

Table 5.3.79-1: DataPoints of waterFlow ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| waterLevelStrength | hd:waterFlowStrength | true | true | false | The desired level of water flow (see clause 5.6.33). A higher value indicates higher water flow. |

### waterSensor

This ModuleClass provides the capabilities to indicate whether or not water has been sensed, and raising an alarm if the triggering criterion is met.

Table 5.3.80-1: DataPoints of waterSensor ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| alarm | xs:boolean | True | false | false | The detection of water. The alarm is indicated as follows: “True” indicates that water has been detected, “False” indicates a normal status, that means that water is not detected. |

### weight

This ModuleClass provides the capability to report the measurement of weight.

Table 5.3.81-1: DataPoints of weight ModuleClass

| Name | Type | Readable | Writable | Optional | Documentation |
| --- | --- | --- | --- | --- | --- |
| weight | xs:float | true | false | false | The weight measurement. The common unit is kilogram (kg). |

## SubDevice models

### subDeviceCuff

A cuff is a subDevice that expresses the attachment device for measuring blood pressure.

Table 5.4.1-1: Modules of subDeviceCuff model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| sphygmomanometer | sphygmomanometer | false | See clause 5.3.67. |
| pulsemeter | pulsemeter | false | See clause 5.3.55. |

### subDevicePowerOutlet

A powerOutlet is a subDevice that specifies the attachment device for deviceSmartPlug.

Table 5.4.2-1: Modules of subDevicePowerOutlet model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| energyConsumption | energyConsumption | true | See clause 5.3.26. |
| overcurrentSensor | overcurrentSensor | true | See clause 5.3.48. |
| dimmingLevel | numberValue | true | See clause 5.3.45. This provides the capability to change the energy. |

## Device models

### device3DPrinter

A 3D printer is a smart home appliance to provide 3D printing capabilities.

Table 5.5.1-1: Modules of device3DPrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| 3Dprinter | 3Dprinter | false | See clause 5.3.1. |
| runState | runState | false | See clause 5.3.62. |
| temperature | temperature | false | See clause 5.3.71. This value of “currentTemperature” in this module instance represents the temperature of the nozzle. This value SHALL be a float number in a range from 0.0 to 1000.0. |
| printQueue | printQueue | false | See clause 5.3.54. |

### deviceAirConditioner

An air conditioner is a home appliance used to alter the properties of air (primarily temperature and humidity) to more comfortable conditions. This air conditioner information model provides capabilities to control and monitor air conditioner specific functions and resources.

Table 5.5.2-1: Modules of deviceAirConditioner Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| airConJobMode | airConJobMode | true | See clause 5.3.1. |
| airConOperationMode | operationMode | true | See clause 5.3.47. This module instance is used to trigger an airCon operation that is pre-set in “airConJobMode”. If this data point is not present, then the air conditioner’s job mode can be triggered by setting the “airConJobMode”. |
| airCleanOperationMode | operationMode | true | See clause 5.3.47. This module instance is used to trigger airClean operation. |
| temperature | temperature | true | See clause 5.3.71. |
| timer | timer | true | See clause 5.3.74. |
| sleepTimer | timer | true | See clause 5.3.74. The sleep function, which is vendor-specific algorithm (for example increasing the remperature by one degree for every 30 minutes), is triggered instantly when “targetDuration” is set, and it indicates the time to the end of appliance operation. It is set at runtime by a user application. |
| turbo | turbo | true | See clause 5.3.75. |
| airFlow | airFlow | true | See clause 5.3.4. |
| powerSave | powerSave | true | See clause 5.3.53. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| filterInfo | filterInfo | true | See clause 5.3.29. |

### deviceAirPurifier

An airPurifieris a home appliance is used to prevent dust and other particles from air by filtering, washing or electrostatic precipitation. This airPurifier information model provides capabilities to control and monitor airPurifier specific functions and resources.

Table 5.5.3-1: Modules of deviceAirPurifier Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| airPurifierJobMode | airPurifierJobMode | true | See clause 5.3.5. |
| airPurifierOperationMode | operationMode | true | See clause 5.3.47. This module instance is used to trigger the airPurifier operation. |
| timer | timer | true | See clause 5.3.74. |
| powerSave | powerSave | true | See clause 5.3.53. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| filterInfo | filterInfo | true | See clause 5.3.29. |

### deviceAirQualityMonitor

An air quality monitor is a home appliance for monitoring the air quality. This airQualityMonitor information model provides capabilities to monitor the airQualityMonitor functions and resources.

Table 5.5.4-1: Modules of deviceAirQualityMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| airQualitySensor | airQualitySensor | false | See clause 5.3.6. |

### deviceAudioReceiver

An audio receiver is a device that receives audio signals from a number of sources, processing them to drive speakers.

Table 5.5.5-1: Modules of deviceAudioReceiver model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | false | See clause 5.3.8. |
| mediaInput | mediaSelect | true | See clause 5.3.43. |
| mediaOutput | mediaSelect | true | See clause 5.3.43. |

### deviceBloodPressureMonitor

A blood pressure monitor is a device that can be used to monitor the blood pressure and is composed of one or more cuffs and a main montor machine.

Table 5.5.6-1: Modules of deviceBloodPressureMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| battery | battery | false | See clause 5.3.10 |
| binarySwitch | binarySwitch | true | See clause 5.3.12 |

Table 5.5.6-2: Subdevice of deviceBloodPressureMonitor Device model

| Subdevice Instance Name | Subdevice Name | Optional | Description |
| --- | --- | --- | --- |
| cuff0 | subDeviceCuff | false | See clause 5.4.1 |
| cuff1 | subDeviceCuff | true | See clause 5.4.1 |
| cuff2 | subDeviceCuff | true | See clause 5.4.1 |
| cuff3 | subDeviceCuff | true | See clause 5.4.1 |
| cuff4 | subDeviceCuff | true | See clause 5.4.1 |
| cuff5 | subDeviceCuff | true | See clause 5.4.1 |

### deviceCamera

A camera is an optical instrument for recording or capturing images, which may be stored locally or transmitted to another locations.

Table 5.5.7-1: Modules of deviceCamera Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| sessionDescription | sessionDescription | false | See clause 5.3.64. |
| playerControl | playerControl | true | See clause 5.3.52. |
| motionSensor | motionSensor | true | See clause 5.3.44. |

### deviceClothesDryer

A clothes dryer is a home appliance for drying clothes. This clothesDryer information model provides capabilities to control and monitor clothes dryer specific functions and resources.

Table 5.5.8-1: Modules of deviceClothesDryer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| clothesDryerJobMode | clothesDryerJobMode | true | See clause 5.3.19. |
| clothesDryerOperationMode | operationMode | true | See clause 5.3.47. This module instance is used to trigger the clothesDryer operation. |

### deviceClothesWasher

A clothes washer is a home appliance that is used to wash laundry, such as clothing and sheets. This information model provides capabilities to interact with specific functions and resources of clothes washers.

Table 5.5.9-1: Modules of deviceClothesWasher Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| operationMode | operationMode | false | See clause 5.3.47. |
| runState | runState | false | See clause 5.3.62. |
| washingCourse | washingCourse | false | See clause 5.3.77. |
| washingCourseOption | washingCourseOption | true | See clause 5.3.78. |
| remoteControlEnable | remoteControlEnable | true | See clause 5.3.60. |
| timer | timer | true | See clause 5.3.74. |

### deviceCoffeeMachine

A coffee machine is a device that is used to brew a coffee, may add foamed milk, and may include some variants, for example a grinder.

Table 5.5.10-1: Modules of deviceCoffeeMachine Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| runState | runState | true | See clause 5.3.62. |
| clock | clock | true | See clause 5.3.18. |
| brewing | brewing | false | See clause 5.3.16. |
| waterStatus | liquidRemaining | true | See clause 5.3.41. |
| milkStatus | liquidRemaining | true | See clause 5.3.41. |
| grinder | grinder | true | See clause 5.3.33. |
| milkFoaming | foaming | true | See clause 5.3.30. |
| milkQuantity | liquidLevel | true | See clause 5.3.40. |
| brewingSwitch | binarySwitch | false | See clause 5.3.12. |
| keepWarm | keepWarm | true | See clause 5.3.38. |

### deviceCookerHood

A cookerHood is a device containing a mechanical fan that hangs above the stove or cooktop in the kitchen.

Table 5.5.11-1: Modules of cookerHood model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| airFlow | airFlow | true | See clause 5.3.4. |

### deviceCooktop

A cooktop is a device that is a kitchen appliance designed for the purpose of cooking food.

Table 5.5.12-1: Modules of deviceCooktop model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| heatingZone0 | heatingZone | false | See clause 5.3.34. |
| heatingZone1 | heatingZone | true | See clause 5.3.34. |
| heatingZone2 | heatingZone | true | See clause 5.3.34. |
| heatingZone3 | heatingZone | true | See clause 5.3.34. |
| heatingZone4 | heatingZone | true | See clause 5.3.34. |
| heatingZone5 | heatingZone | true | See clause 5.3.34. |

### deviceDehumidifier

A dehumidifier is a device that is used to monitor or control the state of a dehumidifying appliance.

Table 5.5.13-1: Modules of deviceDehumidifier Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| relativeHumidity | relativeHumidity | true | See clause 5.3.59. |
| runState | runState | true | See clause 5.3.62. |
| dehumidifierJobMode | dehumidifierJobMode | true | See clause 5.3.23. |
| dehumidifierOperationMode | operationMode | true | See clause 5.3.47. This module instance is used to trigger dehumidifier operation. |
| timer | timer | true | See clause 5.3.74. |
| powerSave | powerSave | true | See clause 5.3.53. |

### deviceDishWasher

A dish washer is a home appliance used to wash dishes. This information model provides capabilities to interact with specific functions and resources of a dish washer.

Table 5.5.14-1: Modules of deviceDishWasher Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |

### deviceDoor

A door is a device that is used to open and close a door.

Table 5.5.15-1: Modules of door model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | true | See clause 5.3.46. |
| doorlock | lock | true | See clause 5.3.42. |
| doorStatus | doorStatus | true | See clause 5.3.24. |

### deviceDoorLock

A door lock is a device that can be used to lock, for example, a door.

Table 5.5.16-1: Modules of deviceDoorLock Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| doorLock | lock | false | See clause 5.3.42. |
| doorStatus | doorStatus | true | See clause 5.3.24. |
| battery | battery | true | See clause 5.3.10. |

### deviceElectricVehicleCharger

An electric vehicle charger is a device that is used for charging or discharging electric vehicles.

Table 5.5.17-1: Modules of deviceElectricVehicleCharger Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | false | See clause 5.3.28. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | false | See clause 5.3.62. |
| battery | battery | false | See clause 5.3.10. |
| electricVehicleConnector | electricVehicleConnector | false | See clause 5.3.25. |

### deviceFan

A fan is a device that is used to monitor or control the state of a fanning device.

Table 5.5.18-1: Modules of deviceFan model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceFoodProbe

A food probe is a device that is used to measure the internal temperature of food.

Table 5.5.19-1: Modules of deviceFoodProbe model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.71. |

### deviceFreezer

A freezer is a large container like a fridge in which the temperature is kept below freezing point, so that food can be storeed inside of it for long periods. This freezer information model provides capabilities to monitor freezer specific functions and resources.

Table 5.5.20-1: Modules of deviceFreezer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.71. |

### deviceGlucosemeter

A glucometer is a device that can be used to monitor the blood glucose level.

Table 5.5.21-1: Modules of deviceGlucoseMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| glucometer | glucometer | false | See clause 5.3.32. |
| battery | battery | false | See clause 5.3.10. |

### deviceHeartRateMonitor

A heart rate monitor is a device that can be used to monitor the heart rate.

Table 5.5.22-1: Modules of deviceHeartRateMonitor Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | false | See clause 5.3.55. |
| battery | battery | false | See clause 5.3.10. |

### deviceHomeCCTV

A home CCTV is a smart home appliance to provide monitoring capabilities when people stay way from their home or a room, or to monitor the environmental status of their home or room.

Table 5.5.23-1: Modules of deviceHomeCCTV Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| sessionDescription | sessionDescription | false | See clause 5.3.64. |
| playerControl | playerControl | true | See clause 5.3.52. |
| runState | runState | true | See clause 5.3.62. |
| motionSensor | motionSensor | true | See clause 5.3.44. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| ozoneMeter | ozoneMeter | true | See clause 5.3.50. |
| smokeSensor | smokeSensor | true | See clause 5.3.66. |
| acousticSensor | acousticSensor | true | See clause 5.3.1. |
| impactSensor | impactSensor | true | See clause 5.3.37. |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| alarmSpeaker | alarmSpeaker | true | See clause 5.3.7. |

### deviceHumidifier

A humidifier is a device that is used to monitor or control the state of a humidifying appliance.

Table 5.5.24-1: Modules of Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceKettle

Kettle is a device used to boil water. It may set a desired temperature for water and may keep water warm for a desired time.

Table 5.5.25-1: Modules of deviceKettle Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| runState | runState | true | See clause 5.3.62. |
| waterStatus | liquidRemaining | true | See clause 5.3.41. |
| boilingSwitch | binarySwitch | false | See clause 5.3.12. |
| temperature | temperature | true | See clause 5.3.71. |
| keepWarm | keepWarm | true | See clause 5.3.38. |

### deviceLight

A light is a device that is used to control the state of an illumination appliance.

Table 5.5.26-1: Modules of deviceLight Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| colour | colour | true | See clause 5.3.20. |
| colourSaturation | colourSaturation | true | See clause 5.3.21. |
| brightness | brightness | true | See clause 5.3.17. |

### deviceMicrogeneration

A microgeneration is a Home Energy Management System (HEMS) device that is used to generate energy. Examples of microgeneration devices are photovoltaics device or fuel cells.

Table 5.5.27-1: Modules of deviceMicrogeneration Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| energyGeneration | energyGeneration | false | See clause 5.3.27. |

Table 5.5.27-2: Device specific properties of deviceMicrogeneration Device model

| Name | Type | Value | Optional | Documentation |
| --- | --- | --- | --- | --- |
| propGenerationSource | xs:string |  | false | The type of generating source. |

### deviceMultiFunctionPrinter

A Multi Function Printer (MFP) is an office machine which incorporates the functionality of multiple devices in one, so as to have a smaller footprint in home or office. A typical MFP may act as a combination of printer, scanner and more. This MFP information model provides capabilities to control and monitor MFP specific functions and resources.

Table 5.5.28-1: Modules of deviceMultiFunctionPrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| printerRunState | runState | false | See clause 5.3.62. |
| scannerRunState | runState | true | See clause 5.3.62. |
| autoDocumentFeeder | autoDocumentFeeder | true | See clause 5.3.9. |
| printQueue | printQueue | true | See clause 5.3.54. |

### deviceOutdoorLamp

An outdoor lamp is a smart home appliance to provide lights and information for outside of home with smart sensing capabilities such as ultraviolet sensing.

Table 5.5.29-1: Modules of deviceOutdoorLamp Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| brightness | brightness | true | See clause 5.3.17. |
| motionSensor | motionSensor | true | See clause 5.3.44. |
| airQualitySensor | airQualitySensor | true | See clause 5.3.6. |
| uvSensor | uvSensor | true | See clause 5.3.76. |
| timer | timer | true | See clause 5.3.74. The timer is used to set duration of giving lights from the moment of triggering by the “brightness” module or “motionSensor” module. |
| faultDetection | faultDetection | true | See clause 5.3.28. |

### deviceOven

An oven is a home appliance used to roast and heat food in a complete stove. This information model is applicable to different types of ovens: gas ovens, electrical ovens, steam ovens, microwave ovens, etc. This information model provides capabilities to interact with specific functions and resources of ovens.

Table 5.5.30-1: Modules of deviceOven Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. Depending on the manufacturer policies or regulations, the binary switch might only be used to turn the device off. |
| runState | runState | true | See clause 5.3.62. |
| timer | timer | true | See clause 5.3.74. |
| temperature | temperature | false | See clause 5.3.71. |

### devicePrinter

A printer is a device that is used to monitor or control the state of a printing appliance.

Table 5.5.31-1: Modules of devicePrinter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| printQueue | printQueue | true | See clause 5.3.54. |

### devicePulseOximeter

A pulseoximeter is a device that can be used to monitor the blood characteristics.

Table 5.5.32-1: Modules of devicePulseOxiMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| pulsemeter | pulsemeter | true | See clause 5.3.55. When the “oximeter” module doesn’t exist, then the “pulsemeter” module is mandatory. |
| oximeter | oximeter | true | See clause 5.3.49. When the “pulsemeter” module doesn’t exist, then the “oximeter” module is mandatory. |
| battery | battery | false | See clause 5.3.10. |

### deviceRefrigerator

A refrigerator is a home appliance used to store food at temperatures which are a few degrees above the freezing point of water. This information model provides capabilities to interact with specific functions and resource of refrigerators.

Table 5.5.33-1: Modules of deviceRefrigerator Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| powerSave | powerSave | true | See clause 5.3.53. |
| doorStatus | doorStatus | true | See clause 5.3.24. |
| frozenTemperature | temperature | true | See clause 5.3.71. |
| fridgeTemperature | temperature | false | See clause 5.3.71. |
| customTemperature | temperature | true | See clause 5.3.71. This module can be configured to fridge temperature or frozen temperature based on its usage by manufacturer |
| refrigeration | refrigeration | true | See clause 5.3.58. |
| controlPanelLock | lock | true | See clause 5.3.42. |
| waterFilterInfo | filterInfo | true | See clause 5.3.29. |

### deviceRobotCleaner

A robot cleaner is an autonomous robotic vacuum cleaner that has intelligent programming and a limited vacuum cleaning system. This robot cleaner information model provides capabilities to control and monitor robot cleaner specific functions and resources.

Table 5.5.34-1: Modules of deviceRobotCleaner Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| robotCleanerJobMode | robotCleanerJobMode | false | See clause 5.3.61. |
| robotCleanerOperationMode | operationMode | true | See clause 5.3.47. |
| battery | battery | true | See clause 5.3.10. |
| timer | timer | true | See clause 5.3.74. |

### deviceScanner

A scanner is a device that optically scans images, printed text, handwriting or an object, and converts it to a digital image.

Table 5.5.35-1: Modules of deviceScanner model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | false | See clause 5.3.62. |
| autoDocumentFeeder | autoDocumentFeeder | true | See clause 5.3.9. |

### deviceSecurityPanel

A security pannel is a device that can change the security mode of, for example, an alarm system.

Table 5.5.36-1: Modules of deviceSecurityPanel model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| securityStatus | securityStatus | false | See clause 5.3.63. |

### deviceSetTopBox

A set top box is a device that in general contains a TV tuner input and displays output to a TV.

Table 5.5.37-1: Modules of setTopBox model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | true | See clause 5.3.8. |
| Channel | televisionChannel | true | See clause 5.3.70. |
| mediaInput | mediaSelect | true | See clause 5.3.43. |
| mediaOutput | mediaSelect | true | See clause 5.3.43. |

### deviceSmartElectricMeter

A smart electric meter is a metering device that is used to measure consumption data for electrictricity.

Table 5.5.38-1: Modules of deviceSmartElectricMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| clock | clock | true | See clause 5.3.18. |
| energyConsumption | energyConsumption | false | See clause 5.3.26. |
| energyGeneration | energyGeneration | true | See clause 5.3.27. |

Table 5.5.38-2: Device specific properties of deviceSmartElectricMeter Device model

| Name | Type | Value | Optional | Documentation |
| --- | --- | --- | --- | --- |
| propMeasuringScope | xs:string |  | true | Measuring scope of the meter (for example a whole house, a room, or an appliance). |

### deviceSmartPlug

A smart plug is a device that can turn on and off a connected appliance.

Table 5.5.39-1: Modules of deviceSmartPlug model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| remoteControlEnable | remoteControlEnable | true | See clause 5.3.60. |

Table 5.5.39-2: Subdevice of deviceSmartPlug Device model

| Subdevice Instance Name | Subdevice Name | Optional | Description |
| --- | --- | --- | --- |
| powerOutlet0 | subDevicePowerOutlet | false | See clause 5.4.2. |
| powerOutlet1 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet2 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet3 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet4 | subDevicePowerOutlet | true | See clause 5.4.2. |
| powerOutlet5 | subDevicePowerOutlet | true | See clause 5.4.2. |

### deviceSteamCloset

A deviceSteamCloset is a home appliance that de-wrinkles, sanitizes and dries to clean fabrics similar to a dry cleaner. This information model provides capabilities to interact with specific functions and resources of the steam closet.

Table 5.5.40-1: Modules of deviceSteamCloset Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| steamClosetJobMode | steamClosetJobMode | false | See clause 5.3.69. |
| steamClosetOperationMode | operationMode | true | See clause 5.3.47. |

### deviceStorageBattery

A storage battery is a Home Energy Management System HEMS device that is used to provide the home with electrical energy.

Table 5.5.41-1: Modules of deviceStorageBattery Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| binarySwitch | binarySwitch | true | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| battery | battery | false | See clause 5.3.10. |

### deviceSwitch

A switch is a device that is used to control and monitor the state of power. Although there is only one module instance in Table 5.5.42-1, the binarySwitch module instance can be extended using different module instance names according to the requirement.

Table 5.5.42-1: Modules of deviceSwitch Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |

### deviceTelevision

A television (TV) is a home appliance used to show audio and visual content such as broadcasting programs and network streaming. This TV information model provides capabilities to control and monitor TV specific resources.

Table 5.5.43-1: Modules of deviceTelevision Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| audioVolume | audioVolume | true | See clause 5.3.8. |
| televisionChannel | televisionChannel | true | See clause 5.3.70. |
| playerControl | playerControl | true | See clause 5.3.52. |
| mediaInput | mediaSelect | true | See clause 5.3.43. |
| mediaOutput | mediaSelect | true | See clause 5.3.43. |

### deviceThermometer

A thermometer is a device that can be used to check, for example, the body or other temperatures.

Table 5.5.44-1: Modules of deviceThermoMeter Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| temperature | temperature | false | See clause 5.3.71. |
| battery | battery | false | See clause 5.3.10. |

### deviceThermostat

A thermostat is used to control the ambient temperature of rooms within, for example, a house. This information model provides capabilities to interact with specific functions of thermostats.

Table 5.5.45-1: Modules of deviceThermostat Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| runState | runState | true | See clause 5.3.62. The possible values of the “supportedModes” datapoint for the thermostat device are included in clause 5.6.18. |
| timer | timer | true | See clause 5.3.74. |
| temperature | temperature | false | See clause 5.3.71. |

### deviceWaterHeater

A water heater is a device that is used to provide hot water through home facilities.

Table 5.5.46-1: Modules of deviceWaterHeater Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| faultDetection | faultDetection | true | See clause 5.3.28. |
| binarySwitch | binarySwitch | false | See clause 5.3.12. |
| runState | runState | true | See clause 5.3.62. |
| clock | clock | true | See clause 5.3.18. |
| boiler | boiler | true | See clause 5.3.15. |
| hotWaterSupply | hotWaterSupply | true | See clause 5.3.36. |

### deviceWaterValve

A water valve is a device that is used to turn the water supply ON or OFF remotely.

Table 5.5.47-1: Modules of waterValve model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | false | See clause 5.3.46. |

### deviceWeightScaleAndBodyCompositionAnalyzer

A weight scale and body composition analyzer is a device that can be used to monitor the weight and body composition.

Table 5.5.48-1: Modules of deviceWeightScaleAndBodyCompositionAnalyzer Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| weight | weight | false | See clause 5.3.81. |
| bodyCompositionAnalyzer | bodyCompositionAnalyzer | false | See clause 5.3.14. |
| bioElectricalImpedanceAnalysis | bioElectricalImpedanceAnalysis | false | See clause 5.3.13. |
| battery | battery | false | See clause 5.3.10. |

### deviceWindowShade

The window shade is an appliance that provides the ability to cover windows. This device type includes but not limited to roller shades, drapes, and tilt-only blinds.

Table 5.5.49-1: Modules of deviceWindowShade Device model

| Module Instance Name | Module Class Name | Optional | Description |
| --- | --- | --- | --- |
| openLevel | openLevel | false | See clause 5.3.46. |
| battery | battery | true | See clause 5.3.10. |

## Enumeration type definitions

### hd:3DprinterTechnology

Used for the “printType” data point of the “3Dprinter” ModuleClass.

Table 5.6.1-1: Interpretation of 3DprinterTechnology

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Fused Filament Fabrication | FFF |
| 2 | Fused Deposition Modeling | FDM |
| 3 | Digital Light Processing | DLP |
| 4 | Powder Bed & inkjet head 3D Printing | PBP |
| 5 | Photopolymer Jetting Technology | PolyJet |
| 6 | Laminated Object Manufacturing | LOM |
| 7 | Stereolithography Apparatus | SLA |
| 8 | Selective Laser Sintering | SLS |
| NOTE: See clause 5.3.1 "3Dprinter". |

### hd:adfState

Used for the “currentAdfState” and “adfStates” data points of the autoDocumentFeeder ModuleClass.

Table 5.6.2-1: Interpretation of hd:adfState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | processing |  |
| 2 | empty |  |
| 3 | jam |  |
| 4 | loaded |  |
| 5 | mispick | The product did not pick up the paper in the document feeder. |
| 6 | hatchOpen | The product hatch is open. |
| 7 | duplexPageTooShort |  |
| 8 | duplexPageTooLong |  |
| 9 | multipickDetected |  |
| 10 | inputTrayFailed |  |
| 11 | inputTrayOverloaded |  |
| NOTE: See clause 5.3.9 "autoDocumentFeeder". Negative values are reserved for vendor specific modes. |

### hd:airConJobMode

Used for the “currentJobMode” and “jobModes” data point of the airConJobMode ModuleClass.

Table 5.6.3-1: Interpretation of hd:airConJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cool | This value is for deviceAirConditioner and indicates cool mode. |
| 2 | airDry | This value is for deviceAirConditioner and indicates air dry mode. |
| 3 | fan | This value is for deviceAirConditioner and indicates fan mode. |
| 4 | AI | This value is for deviceAirConditioner and indicates artificial intelligence mode. |
| 5 | heat | This value is for deviceAirConditioner and indicates heat mode. |
| 6 | airClean | This value is for deviceAirConditioner and indicates air clean mode. |
| 7 | ACO | This value is for deviceAirConditioner and indicates Auto Change Over mode. |
| 8 | aroma | This value is for deviceAirConditioner and indicates aroma mode. |
| NOTE: See clause 5.3.3 "airConJobMode". Negative values are reserved for vendor specific modes. |

### hd:airPurifierJobMode

Used for the “currentJobMode” and “jobModes” data points of the airPurifierJobMode ModuleClass.

Table 5.6.4-1: Interpretation of hd:airPurifierJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normalClean | This indicates the normal mode that operates the basic function. |
| 2 | sleep | This indicates the sleep mode that turns the operating function off at the time set by a timer. |
| 3 | silent | This indicates the silent mode that generates low noise |
| 4 | wet | This indicates the wet mode that passes the air that’s already filtered through water filter once again to provide the humidification effect |
| 5 | circulate | This indicates the circulate mode that circulates the purified air by rotating the fan on top of the air purifier |
| 6 | dual | This indicates the dual mode that operates both the upper and lower parts of the air purifier |
| 7 | auto | This indicates the auto mode that first measures the pollution level (e.g., good, normal, bad, very bad) and then, triggers appropriate modes based on the measured level. In case of bad and very bad condition, the rotating fan on the upper side starts its operation |
| NOTE: See clause 5.3.5 "airPurifierJobMode". Negative values are reserved for vendor specific modes. |

### hd:alertColourCode

Used for the “light” data point of the “alarmSpeaker” ModuleClass.

Table 5.6.5-1: Interpretation of alertColourCode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | red | This colour indicates the alarm status. |
| 2 | green | This colour indicates the alarm has been cleared. |
| NOTE: See clause 5.3.7 "alarmSpeaker". |

### hd:callState

Used for the “callState” data point in the “phoneCall” ModuleClass.

Table 5.6.6-1: Interpretation of callState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | hangup |  |
| 2 | calling |  |
| 3 | ringing |  |
| 4 | busy |  |
| 5 | answered |  |
| 6 | noline |  |
| NOTE: See clause 5.3.51 “phoneCall” |

### hd:clothesDryerJobMode

Used for the “currentJobMode” and “jobModes” d ata points of the “clothesDryerJobMode” ModuleClass.

Table 5.6.7-1: Interpretation of hd:clothesDryerJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal | Normal cycle. |
| 2 | quickDry | About half the length of a normal cycle, this setting uses high heat to dry a few items. |
| 3 | permanentPress | Slow drying with low heat helps wringkle-free garments live up to their name and keeps the hard creases out of thins you typically iron. |
| 4 | heavyDuty | Tumbling for an extended period with high heat for sturdy items (towels, sweats, jeans). |
| 5 | delicates | A short, low-heat cycle for delicates and other items such as spandex workout gear, which loses its stretch when too much heat is used. |
| 6 | airDry | A cool-air setting for items that can’t take any heat, such as plastic tablecloths and rubber-backed rugs. |
| 7 | extendedTumble | Periodically tumbles clothes without heats for a preset amount of time after they’re dry to prevent wrinkles. |
| NOTE: See clause 5.3.19 "clothesDryerJobMode". Negative values are reserved for vendor specific modes. |

### hd:dehumidifierJobMode

Used for “currentJobMode” and “jobModes” data points of the “dehumidifierJobMode” ModuleClass.

Table 5.6.8-1: Interpretation of hd:dehumidifierJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | smart | This indicates the smart mode that first gets the target humidity level from user input, next detects the currect relative humidity, then automatically change the dehumidity level to keep the target humidity level. |
| 2 | fast | This indicates the fast mode that speeds the operating level up to quickly dehumidify when the humidity level is so high. It is a kind of turbo mode. |
| 3 | silent | This indicates the silent mode that can be used when an user sleeps. It reduces the noise. |
| 4 | focus | This indicates the focus mode that dehumidifies focusing on a particular part. |
| 5 | clothes | This indicates the clothes mode that dehumidifies adjusting the wind direction vertically. It is normally used to dehumidify clothes. |
| NOTE: See clause 5.3.23 "dehumidifierJobMode". Negative values are reserved for vendor specific modes. |

### hd:deviceType

Used for the “deviceType” property of device models.

Table 5.6.9-1: Interpretation of deviceType

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | deviceAirConditioner | See clause 5.5.2 |
| 2 | deviceClothesWasher | See clause 5.5.3 |
| 3 | deviceElectricVehicleCharger | See clause 5.5.10 |
| 4 | deviceLight | See clause 5.5.18 |
| 5 | deviceMicrogeneration | See clause 5.5.27 |
| 6 | deviceOven | See clause 5.5.28 |
| 7 | deviceRefrigerator | See clause 5.5.31 |
| 8 | deviceRobotCleaner | See clause 5.5.34 |
| 9 | deviceSmartElectricMeter | See clause 5.5.35 |
| 10 | deviceStorageBattery | See clause 5.5.39 |
| 11 | deviceTelevision | See clause 5.5.42 |
| 12 | deviceThermostat | See clause 5.5.45 |
| 13 | deviceWaterHeater | See clause 5.5.46 |
| 14 | deviceCoffeeMachine | See clause Error! Reference source not found. |
| 15 | deviceBloodPressureMonitor | See clause Error! Reference source not found. |
| 16 | deviceGlucosemeter | See clause Error! Reference source not found. |
| 17 | devicePulseOximeter | See clause Error! Reference source not found. |
| 18 | deviceThermometer | See clause Error! Reference source not found. |
| 19 | deviceWeightScaleAndBodyComposition Analyzer | See clause Error! Reference source not found. |
| 20 | deviceHeartRate Monitor | See clause Error! Reference source not found. |
| 0 | undefinedVendorExt | For vendor specific usage. |
| NOTE: See clause 5.5 "device Models". |

### hd:doorState

Used for the “doorState” DataPoint of doorStatus ModuleClass.

Table 5.6.10-1: Interpretation of doorState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | closed | This indicates that door is closed. |
| 2 | open | This indicates that the door is open, |
| 3 | opening | This indicates that the door is opening, |
| 4 | closing | This indicates that the door is closing, |
| 5 | stopped | This indicates that the door is in stationary state. |
| NOTE: See clause 5.3.24 "doorStatus". |

### hd:foamStrength

Used for data points indicating the strength of a foam, for example, foaming milk from a coffee machine.

Table 5.6.11-1: Interpretation of foamStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.30 “foaming” |

### hd:generalLevel

Used for the “soilLevel” data point of the “washingCourseOption” ModuleClass.

Table 5.6.12-1: Interpretation of generalLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | light |  |
| 2 | normal |  |
| 3 | heavy |  |
| NOTE: See clause 5.3.78“washingCourseOption” |

### hd:generalSpeed

Used for the “spinSpeed” data point of the “washingCourseOption” ModuleClass.

Table 5.6.13-1: Interpretation of generalSpeed

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | low |  |
| 2 | medium |  |
| 3 | high |  |
| 4 | extraHigh |  |
| NOTE: See clause 5.3.78 “washingCourseOption” |

### hd:generalTemperature

Used for the “washTemp” data point of the “washingCourseOption” ModuleClass.

Table 5.6.14-1: Interpretation of generalTemperature

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | cold | The actual temperature is defined by the manufacturer. |
| 2 | warm |  |
| 3 | hot |  |
| NOTE: See clause 5.3.78 “washingCourseOption” |

### hd:grainsLevel

Used for the “grainsRemaining” data point of the “grinder” ModuleClss.  This type specifies a level for supplies that have a grain-aspect, for example.the level of remaining coffee beans in the grinder part of a coffee machine, or the desired level of coffee beans in this machine.

The values for the level of a liquid is covered by “hd:liquidLevel” (see clause 5.6.15).

Table 5.6.15-1: Interpretation of grainsLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.33 "grinder". |

### hd:grindCoarseness

Used for the coarseness data points of the “grinder” ModuleClass. This type specifies the level of coarseness of a solid after grinding, for example grinded coffee beans.

Table 5.6.16-1: Interpretation of grindCoarseness

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | ultrafine |  |
| 2 | fine |  |
| 3 | medium |  |
| 4 | coarse |  |
| 5 | coarsest |  |
| NOTE: See clause 5.3.33 “grinder” |

### hd:horizontalDirection

Used for the “horizontalDirection” and “supportedHorizontalDirection” of the “airflow” ModuleClass, indicating horizontal directions.

Table 5.6.17-1: Interpretation of horizontalDirection

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | auto |  |
| 2 | center |  |
| 3 | left |  |
| 4 | right |  |
| NOTE: See clause 5.3.4 "airFlow". |

### hd:jobStates

Used for the “currentJobState” and “jobStates” data points of the “runState” ModuleClass.

Table 5.6.18-1: Interpretation of jobState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | aborted |  |
| 2 | cancelled |  |
| 3 | completed |  |
| 4 | paused |  |
| 5 | pending |  |
| 6 | processing |  |
| NOTE: See clause 5.3.62 "runstate". |

### hd:liquidLevel

Used for data points indicating the desired level or the remaining level of liquid.

Table 5.6.19-1: Interpretation of liquidLevel

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | low |  |
| 3 | medium |  |
| 4 | high |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.40 "liquidLevel" and clause 5.3.41 “liquidRemaining”. |

### hd:machineState

Used for the “currentMachineState” and “machineStates” data points of the “runState” ModuleClass.

Table 5.6.20-1: Interpretation of machineState

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | idle | Machine is ready to operate |
| 2 | preActive | Machine is operating its pre-functions (ex. pre-heat) |
| 3 | active | Machine is operating its functions |
| 4 | reserved | Reservation is made by user |
| 5 | stopped | Operation is stopped/aborted by some other reasons |
| 6 | error | Error has occurred |
| 7 | diagnostic | Machine reports diagnostic information to the server |
| 8 | test | Particular functions run for test |
| 9 | maintenance | Machine is needed to maintain |
| 10 | clear | The result is not removed yet |
| 11 | charging | Machine is being charged |
| NOTE: See clause 5.3.62 "runState". |

### hd:ozoneStatus

Used for the “ozoneStatus” property of the “ozoneMeter” ModuleClass.

Table 5.6.21-1: Interpretation of ozoneStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Good | For example, 0 to 0.030 ppm. |
| 2 | Normal | For example, 0.031 to 0.090 ppm. |
| 3 | Bad | For example, 0.091 to 0.150ppm. |
| 4 | Very bad | For example, 0.151 ppm or above. |
| NOTE: See clause 5.3.50 "ozoneMeter". The examples in the notes are references from Korean Environmental Standard[i.7]. |

### hd:playerMode

Used for the “currentMode” and “supportedModes” data points in the “playerControl” ModuleClass.

Table 5.6.22-1: Interpretation of playerMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | stop |  |
| 2 | play |  |
| 3 | pause |  |
| 4 | resume |  |
| 5 | record |  |
| 6 | rewind |  |
| 7 | fast-rewind |  |
| 8 | forward |  |
| 9 | fast-forward |  |
| 10 | searchPrevious |  |
| 11 | searchNext |  |
| NOTE: See clause 5.3.52 “playerControl” |

### hd:robotCleanerJobMode

Used for the “currentJobMode” and “jobModes” data points of the “robotCleanerJobMode” ModuleClass.

Table 5.6.23-1: Interpretation of robotCleanerJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zigzag | The machine moves forward by going at an angle first to one side then to the other |
| 2 | sectorBase | The machine first cleans a specific sector (fo example, 1x1m), then moves to another sector. |
| 3 | spot | The machine cleans a targeted area of about specific spot |
| NOTE: See clause 5.3.61 "robotCleanerJobMode". Negative values are reserved for vendor specific modes. |

### hd:securityMode

Used for the “currentSecurityMode” and “securityMode” data points of the “securityStatus” ModuleClass.

Table 5.6.24-1: Interpretation of securityMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | active | Unit is active |
| 2 | armedAway | Unit is armed for away |
| 3 | armedInstant | Unit is armed instantly |
| 4 | armedMaximum | Unit is armed at maximum level |
| 5 | armedNightStay | Unit is armed in night stay |
| 6 | armedStay | Unit is armed in stay mode |
| NOTE: See clause 5.3.63 “securityStatus” |

### hd:spinLevelStrength

Used for the “spinLevelStrength” data points of the “spinLevel” ModuleClass, indicating the strength of a spinLevel.

Table 5.6.25-1: Interpretation of strength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | weak |  |
| 4 | medium |  |
| 5 | strong |  |
| 6 | maximum |  |
| NOTE: See clause 5.3.68 "spinLevel". |

### hd:steamClosetJobMode

Used for “currentJobMode” and “jobModes” data points of the “steamClosetJobMode” ModuleClass.

Table 5.6.26-1: Interpretation of steamClosetJobMode

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | reduceOdor | Using pure water, the machine help remove the smells on clothes. |
| 2 | steamWrinkle | The machine steams away wrinkles and also creates pant creases, as well as keep them crisp. |
| 3 | helpClean | Using pure water without chemical additives, the machine sanitizes fabrics and items that are difficult to wash. |
| 4 | gentleDry | The machine dries fragile garments without worrying about shrinkage or damage. |
| NOTE: See clause 5.3.69 "steamClosetJobMode". Negative values are reserved for vendor specific modes. |

### hd:supportedMediaSources

Used for the “supportedMediaSources” data point of the “mediaSelect” ModuleClass.

Table 5.6.27-1: Interpretation of supportedMediaSources

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | tuner |  |
| 2 | component |  |
| 3 | composite |  |
| 4 | svideo |  |
| 5 | rgb |  |
| 6 | dvi |  |
| 7 | hdmi |  |
| 8 | displayPort |  |
| 9 | scart |  |
| 10 | externalStorage |  |
| 11 | network |  |
| NOTE: See clause 5.3.43"mediaSelect". Negative values are reserved for vender specific sources. |

### hd:tasteStrength

Used for the “strength” data point of the “brewing” ModuleClass, indicating strength of a drink taste, for example coffee strength.

Table 5.6.28-1: Interpretation of tasteStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | medium |  |
| 4 | strong |  |
| 5 | maximum |  |
| NOTE: See clause 5.3.16 “brewing” |

### hd:tone

Used for the “tone” data point of the “alarmSpeaker” ModuleClass.

Table 5.6.29-1: Interpretation of tone

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | fire |  |
| 2 | theft |  |
| 3 | emergency |  |
| 4 | doorbell |  |
| 5 | deviceFail |  |
| NOTE: See clause 5.3.7 "alarmSpeaker". |

### hd:uvStatus

Used for the “uvStatus” data point of the “uvSensor” ModuleClass.

Table 5.6.30-1: Interpretation of uvStatus

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | Good |  |
| 2 | Normal |  |
| 3 | Bad |  |
| 4 | Very Bad |  |
| 5 | Danger |  |
| NOTE: See clause 5.3.76 "uvSensor". |

### hd:verticalDirection

Used for the “verticalDirection” and “supportedVerticalDirection” data points of the “airFlow" ModuleClass, indicating vertical direction.

Table 5.6.31-1: Interpretation of verticalDirection

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | auto |  |
| 2 | center |  |
| 3 | up |  |
| 4 | down |  |
| NOTE: See clause 5.3.4 "airFlow". |

### hd:washingCourse

Used for the “currentWashingCourse” and “washingCourses” data points of the “washingCourse” ModuleClass. Washing options such as water temperature and spin speed are decided to pre-set values upon selected washing course. Manufacturers can define their own courses by setting this value to 0.

Table 5.6.32-1: Interpretation of washingCourse

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | normal |  |
| 2 | smallLoad |  |
| 3 | delicate |  |
| 4 | comforter |  |
| 5 | expressWash |  |
| 6 | cleanWash |  |
| 7 | kidsWear |  |
| 8 | workoutWears |  |
| 0 | vendorSpecific |  |
| NOTE: See clause 5.3.77 “washingCourse” |

### hd:waterFlowStrength

Used for the “waterLevelStrength” data point of the “waterFlow” ModuleClass,  indicating the strength of a waterflow.

Table 5.6.33-1: Interpretation of waterFlowStrength

| Value | Interpretation | Note |
| --- | --- | --- |
| 1 | zero |  |
| 2 | sensitive |  |
| 3 | weak |  |
| 4 | medium |  |
| 5 | strong |  |
| 6 | maximum |  |
| NOTE: See clause 5.3.79 "waterFlow". |

## Universal and Common Properties for Device models

Universal and common properties are defined as the specialized [objectAttibute]s of the [deviceInfo] resource in annex D.8 of TS-0001[3]. Some properties are mandatory for all device models and called "Univeral Properties", since they are universally seen in typical device types and carry necessary information to identify each device instance. Others are optional for all device models and called "Common Properties", since they are commonly used in many device types but not always. The multiplicity of properties shall follow the the definition in Table 8-2 in TS-0001 [3].

Universal and common properties are applicable to all device models. They are not repeated in the property table of each device model in clause 5.5, where only device specific properties shall be specified.

NOTE:	The instantiated values of the universal properties might be empty in case of exceptional scenarios, e.g. interworking with non-oneM2M device models.

# The Principle of Resource Mapping for Home Appliance Information Model

## Introduction

Home appliance information models which are defined in clause 5 need to be represented as resources in the oneM2M system. This clause defines the principle of resource mapping based on <flexContainer>. The individual information mapping is provided in annexes A, B, C and D.

## The Resource Mapping Rules

### Introduction

The present clause specifies the rule to map the "Home Appliance Information Model" in clause 5, to oneM2M resources.

### Resource mapping for Device model

When the AE exposes a controling interface for a home domain device which is specified as an information model in clause 5.5, a specialization of the <flexContainer> resource shall be created as the mapping of the model following conversion rules:

Rule 1-1: Each Device model defined in clause 5.5 shall be mapped to a specialization of <flexContainer> resource with associated 'DeviceClass ID' (e.g. "org.onem2m.home.device.tv") on containerDefinition attributes.

Rule 1-2: Each entry of 'Module' table shall be mapped to child resource(s) which is mapped as a specialised <flexContainer> following the rule in clause 6.2.3 'Resource mapping for ModuleClass'.

Rule 1-3: Each ‘Property’ of a Device model shall be mapped to a specialized [objectAttribute] of a [deviceInfo] resource that is defined in Annex D.8 of TS-0001[3]. The specialized <flexContainer> resource of the Device model shall contain a specialized mandatory [customAttribute] as a ‘nodeLink’ attribute (as defined in TS-0001[3] and in TS-0004[4]), which links to a <node> resource that is hosted on the same hosting CSE of the <flexContainer>. That <node> resource shall contain as child-resource the [deviceInfo] resource of the Device model instance.  The <node> resource contains all the management information as specialized <mgmtObj> resources (e.g. [firmware]) about the Device model instance for different management purposes.

Rule 1-4: XSD file for each Device model shall be named following naming convension:
'HD-<name of Device model>-v<version of TS>.xsd'
For example, XSD file for ‘deviceAirConditioner' is named as ‘HD-deviceAirConditioner-v1_0_0.xsd'.

### Resource mapping for ModuleClass

The ModuleClass models (in clause 5.3) shall be mapped to the specializations of <flexContainer> resource. The following rules shall be applied:

When the Device model in clause 5.5 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with a ModuleClass in the model, a <flexContainer> resource which is mapped from ModuleClass definitions shall be created as a child resource:

Rule 2-1: The ModuleClass ID shall be specified on the containerDefinition attribute (e.g. "org.onem2m.home.moduleclass. audiovolume").

Rule 2-2: Each entry of 'Action', 'Property', and 'DataPoint' in ModuleClass definitions shall be mapped following the resource mapping rules for them.

Rule 2-3: XSD file for each ModuleClass shall be named following naming convension:
'HD-mod-<name of ModuleClass>-v<version of TS>.xsd'
For example, XSD file for ‘binarySwith' is named as ‘HD-mod-binarySwitch-v1_0_0.xsd. The Device model which refer any ModuleClass shall include the XSD of the ModuleClasses.

### Resource mapping for Action

When the Device model in clause 5.5 or the ModuleClass model in clause 5.3 is mapped to the <flexContainer> resource, and if the device supports the functionality associated with the Action in the model, a <flexContainer> resource which is mapped from the Action definition shall be created as a child resource:

Rule 3-1: The Action ID shall be specified on the containerDefinition attribute (e.g. "org.onem2m.home.moduleclass.audiovolume.upvolume").

Rule 3-2: When the Action supports any 'Arguments' or 'Return Type', they are mapped to [customizedAttribute] with its variable names.

Rule 3-3: XSD file for each Action shall be named following naming convesion:
'HD-act-<name of Action>-v<version of TS>.xsd'. 
For example, XSD file for 'toggle' is named as 'HD-act-toggle-v1_0_0.xsd'. The device or ModuleClass which refers any Action shall include the XSD of the Action.

Rule 3-4: When the Action does not support any ‘Argument' or ‘Return Type', the Action shall be triggered by updating with null Content parameter.

### Resource mapping for Property

When the Device model (in clause 5.5) or the ModuleClass model (in clause 5.3) is mapped to the <flexContainer> resource, and if the device supports a Property, the following rules shall be applied:

Rule 4-1: Each entry of ‘Property’ table in ModuleClass model, shall be mapped to the [customAttribute] of <flexContainer> resource which is mapped from associated ModuleClass model, with its Property name with prefix 'prop'.

Rule 4-2: Each ‘Property’ of a Device model is mapped to a specialized [objectAttribute] of a [deviceInfo] resource following Rule 1-3.

### Resource mapping for DataPoint

When the ModuleClass model (in clause 5.3) is mapped to the <flexContainer> resouce, and if the ModuleClass supports a DataPoint, the following rules shall be applied:

Rule 5-1: Each entry of DataPoint table in ModuleClass model, shall be mapped to [customAttribute] of <flexContainer> resource which is mapped from associated ModuleClass model, with its DataPoint name.

## Short names

### Introduction

XML and JSON representations require the explicit encoding of the names of resource attributes, (in the case of XML) and resource types. Whenever a protocol binding transfers such a name over a oneM2M reference point, it shall use a shortened form of that name. Short names enable payload reduction on involved telecommunication interfaces.

The mapping between the full names and their shortened form is given in the clauses that follow.

### Resource types

In protocol bindings resource type names for device models shall be translated into short names of Table 6.3.2-1.

Table 6.3.2-1: Specialization type short names (Device models)

| Resource Type Name | Short Name |
| --- | --- |
| device3Dprinter |  |
| deviceAirConditioner | deACr |
| deviceCamera |  |
| deviceClothesWasher | deCWr |
| deviceCoffeeMachine |  |
| deviceCookerHood |  |
| deviceElectricVehicleCharger | dEVCr |
| deviceKettle |  |
| deviceLight | devLt |
| deviceMicrogeneration | devMn |
| deviceOutdoorLamp |  |
| deviceOven | devOn |
| deviceRefrigerator | devRr |
| deviceRobotCleaner | deRCr |
| deviceSmartElectricMeter | dSEMr |
| deviceSteamCloset |  |
| deviceStorageBattery | deSBy |
| deviceTelevision | devTn |
| deviceThermostat | devTt |
| deviceWaterHeater | deWHr |
| devicePulseOximeter |  |
| deviceGlucosemeter |  |
| deviceHeartRateMonitor |  |
| deviceHomeCCTV |  |
| deviceWeightScaleAndBodyCompositionAnalyzer |  |
| devicePulseOximeter |  |
| deviceThermoMeter |  |
| deviceHumidifier |  |
| deviceDehumidifier |  |
| deviceDishWasher |  |
| deviceFan |  |
| devicePrinter |  |
| deviceWaterValve |  |
| deviceDoor |  |
| deviceSmartPlug |  |
| deviceSecurityPanel |  |
| deviceAirPurifier |  |
| deviceAirQualityMonitor |  |
| deviceFreezer |  |
| deviceMultiFunctionPrinter |  |
| deviceClothesDryer |  |
| deviceAudioReceiver |  |
| deviceScanner |  |
| deviceCooktop |  |
| deviceFoodProbe |  |
| deviceSetTopBox |  |

In protocol bindings resource type names for SubDevice model shall be translated into short names of Table 6.3.2-3.

Table 6.3.2-3: Specialization type short names (SubDevice models)

| Resource Type Name | Short Name |
| --- | --- |
| subDevicePowerCuff |  |
| subDevicePowerOutlet |  |

In protocol bindings resource type names for module classes shall be translated into short names of Table 6.3.2-5.

Table 6.3.2-5: Specialization type short names (ModuleClasses and Module Instances)

| Resource Type Name | Short Name |
| --- | --- |
| 3Dprinter |  |
| acousticSensor |  |
| alarmSpeaker | alaSr |
| mediaSelect |  |
| audioVolume | audVe |
| battery | batty |
| binaryObject |  |
| binarySwitch | binSh |
| bioElectricalImpedanceAnalysis | bEIAs |
| boiler | boilr |
| brewing |  |
| brightness | brigs |
| clock | clock |
| colour | color |
| colourSaturation | colSn |
| customTemperature | cusTe |
| doorStatus | dooSe |
| electricVehicleConnector | elVCr |
| energyConsumption | eneCn |
| energyGeneration | eneGn |
| faultDetection | fauDn |
| foaming |  |
| freshTemperature | freTe |
| frozenTemperature | froTe |
| geoLocation |  |
| grinder |  |
| height | heigt |
| hotWaterSupply | hoWSy |
| impactSensor |  |
| keepWarm |  |
| keypad | keypd |
| liquidLevel |  |
| lock |  |
| motionSensor | motSr |
| numberValue |  |
| oximeter | oximr |
| ozoneMeter |  |
| playerControl |  |
| phoneCall |  |
| powerSave | powS0 |
| printQueue |  |
| pushButton | pusBn |
| recorder | recor |
| refrigeration | refrn |
| relativeHumidity | relHy |
| liquidRemaining |  |
| runState |  |
| sessionDescription |  |
| signalStrength | sigSh |
| smokeSensor | smoSr |
| spinLevel | spiLl |
| steamClosetJobMode |  |
| televisionChannel | telCl |
| temperature | tempe |
| temperatureAlarm | temAm |
| textMessage |  |
| timer | timer |
| turbo | turbo |
| uvSensor |  |
| waterFlow | watFw |
| waterSensor | watSr |
| weight | weigt |
| bodyCompositionAnalyzer |  |
| glucometer |  |
| pulsemeter |  |
| sphygmomanometer |  |
| operationMode |  |
| overcurrentSensor |  |
| remoteControl |  |
| robotCleanerJobMode |  |
| washingCourse |  |
| washingCourseOption |  |
| airQualitySensor |  |
| filterInfo |  |
| dimmingLevel |  |
| airPurifierJobMode |  |
| dehumidifierJobMode |  |
| autoDocumentFeeder |  |
| clothesDryerJobMode |  |
| heatingZone |  |

In protocol bindings resource type names for actions shall be translated into short names of Table 6.3.2-7.

Table 6.3.2-7: Specialization type short names (Actions)

| Resource Type Name | Short Name |
| --- | --- |
| activateClockTimer | acCTr |
| answer |  |
| call |  |
| deactivateClockTimer | deCTr |
| decrementNumberValue |  |
| downChannel | dowCl |
| downVolume | dowVe |
| nextTrack |  |
| previousTrack |  |
| hangup |  |
| incrementNumberValue |  |
| resetNumberValue |  |
| resetTextMessage |  |
| toggle | togge |
| upChannel | uphCl |

### Resource attributes for properties and data points

In protocol bindings resource attributes names for properties of module classes shall be translated into short names of Table 6.3.3-1.

Table 6.3.3-1: Resource attribute short names (ModuleClass properties)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| chargingCapacity | electricVehicleConnector | chaCy |
| dischargingCapacity | electricVehicleConnector | disCy |
| electricEnergy | battery | eleEy |
| material | battery | matel |
| voltage | battery | volte |

In protocol bindings resource attributes names for data points of module classes shall be translated into short names of Table 6.3.3-2.

Table 6.3.3-2: Resource attribute short names (ModuleClass data points)

| Attribute Name | Occurs in | Short Name |
| --- | --- | --- |
| absoluteEnergyConsumption | energyConsumption | abECn |
| absoluteStartTime | timer | abSTe |
| absoluteStopTime | timer | abST0 |
| accuracy | geoLocation |  |
| acousticStatus | acousticSensor |  |
| adfStates | autoDocumentFeeder |  |
| alarm | motionSensor, smokeSensor, temperatureAlarm, waterSensor | alarm |
| alarmStatus | alarmSpeaker | alaSs |
| altitude | geoLocation |  |
| availableChannels | televisionChannel | avaCs |
| bath | hotWaterSupply | bath |
| batteryThreshold | battery | batTd |
| blue | colour | blue |
| bone | bioelectricalImpedanceAnalysis | bone |
| brightness | brightness | brigs |
| capacity | battery | capay |
| callerID | phoneCall |  |
| callState | phoneCall |  |
| channelNumber | televisionChannel | chaId |
| channelName | televisionChannel |  |
| charging | battery | charg |
| coarseness | grinder |  |
| code | faultDetection | code |
| colourSaturation | colourSaturation | colSn |
| cupsNumber | brewing |  |
| current | energyConsumption | currt |
| currentAdfState | autoDocumentFeeder |  |
| currentDate | clock | curDe |
| currentJobMode | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, robotCleanerJobMode, steamClosetJobMode |  |
| currentJobModeName | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, robotCleanerJobMode, steamClosetJobMode |  |
| currentPlayerMode | playerControl |  |
| currentPlayerModeName | playerControl |  |
| currentTemperature | temperature | curT0 |
| currentTime | clock | curTe |
| defaultValue | numberValue, textMessage |  |
| defrost | refrigeration | defrt |
| description | faultDetection | descn |
| desiredHumidity | relativeHumidity | desHy |
| detectedTime | smokeSensor, overcurrentSensor | detTe |
| diastolicPressure | oximeter | diaPe |
| discharging | battery | discg |
| doorState | doorStatus | dooSe |
| duration | Recorder, overcurrentSensor | duran |
| estimatedTimeToEnd | timer | eTTEd |
| fat | bioElectricalImpedanceAnalysis | fat |
| filterLifetime | filterInfo | filLe |
| frequency | energyConsumption | freqy |
| foamingStrength | foaming |  |
| grainsRemaining | grinder |  |
| green | colour | green |
| heading | geoLocation |  |
| headingAccuracy | geoLocation |  |
| heatingLevel | heatingZone |  |
| hash | binaryObject |  |
| height | height | heigt |
| horizontalAccuracy | geoLocation |  |
| horizontalDirection | airFlow |  |
| impactStatus | impactSensor |  |
| impactLevel | impactSensor |  |
| impactDirectionHorizontal | impactSensor |  |
| impactDirectionVertical | impactSensor |  |
| mediaID | mediaSelect |  |
| jobModes | airConJobMode, airPurifierJobMode, dehumidifierJobMode, clothesDryerJobMode, robotCleanerJobMode, steamClosetJobMode |  |
| kcal | bioElectricalImpedanceAnalysis | kcal |
| keyNumber | keypad | keyNr |
| latitude | geoLocation |  |
| level | battery | level |
| light | alarmSpeaker | light |
| liquidLevel | liquidLevel | liqLl |
| liquidRemaining | liquidRemaining |  |
| longitude | geoLocation |  |
| loudness | acousticSensor |  |
| lowBattery | battery | lowBy |
| lqi | signalStrength | lqi |
| network | 3Dprinter |  |
| maxLength | textMessage |  |
| maxHeatingLevel | heatingZone |  |
| maxSpeed | airFlow |  |
| maxValue | audioVolume, temperature, numberValue, ozoneMeter | maxVe |
| mediaName | mediaSelect |  |
| mediaType | mediaSelect |  |
| memorySize | 3Dprinter |  |
| messageEncoding | textMessage |  |
| minLength | textMessage |  |
| minSpeed | airFlow |  |
| minValue | temperature, numberValue | minVe |
| multiplyingFactors | energyConsumption, energyGeneration | mulFs |
| muscle | bioElectricalImpedanceAnalysis | musce |
| muteEnabled | audioVolume | mutEd |
| object | binaryObject |  |
| type | binaryObject |  |
| openAlarm | doorStatus | opeAm |
| openDuration | doorStatus | opeDn |
| overcurrentStatus | overcurrentSensor |  |
| oxygenSaturation | oximeter | oxySn |
| ozoneStatus | ozoneMeter |  |
| ozoneValueMG | ozoneMeter |  |
| ozoneValuePPM | ozoneMeter |  |
| power | energyConsumption | power |
| powerGenerationData | energyGeneration | poGDa |
| powerSaveEnabled | powerSave | poSEd |
| powerState | binarySwitch | powSe |
| previousChannel | televisionChannel | preCl |
| printSizeX | 3Dprinter |  |
| printSizeY | 3Dprinter |  |
| printSizeZ | 3Dprinter |  |
| printType | 3Dprinter |  |
| printingState | printQueue |  |
| pulseRate | oximeter | pulRe |
| pushed | pushButton | pusBn |
| rapidCool | refrigeration | rapCl |
| rapidFreeze | refrigeration | rapFe |
| recipientID | phoneCall |  |
| red | colour | red |
| referenceTimer | timer | refTr |
| relativeHumidity | relativeHumidity | relHy |
| resistance | bioElectricalImpedanceAnalysis | resie |
| roundingEnergyConsumption | energyConsumption | roECn |
| roundingEnergyGeneration | energyGeneration | roEGn |
| rssi | signalStrength | rssi |
| runningTime | timer | runTe |
| sdp | sessionDescription |  |
| sensitivity | motionSensor | sensy |
| significantDigits | energyConsumption, energyGeneration | sigDs |
| silentTime | motionSensor | silTe |
| size | binaryObject |  |
| speed | airFlow |  |
| speedFactor | playerControl | speedFactor |
| status | boiler, electricVehicleConnector, faultDetection, hotWaterSupply, mediaSelect | stats |
| stepValue | audioVolume, temperature, numberValue | steVe |
| strength | spinLevel, waterFlow, brewing | streh |
| supportedHorizontalDirection | airFlow |  |
| supportedMediaSources | mediaSelect | suISs |
| supportedPlayerModes | playerControl |  |
| supportedTextMessage | textMessage |  |
| supportedVerticalDirection | airFlow |  |
| systolicPressure | oximeter | sysPe |
| targetDuration | timer | tarDn |
| targetAltitude | geoLocation |  |
| targetLatitude | geoLocation |  |
| targetLongitude | geoLocation |  |
| targetTemperature | temperature | tarTe |
| targetTimeToStart | timer | tTTSt |
| targetTimeToStop | timer | tTTSp |
| temperature | temperatureAlarm | tempe |
| temperatureThreshhold | temperatureAlarm | temTd |
| textMessage | textMessage |  |
| time | keepWarm |  |
| tone | alarmSpeaker | tone |
| turboEnabled | turbo | turEd |
| unit | temperature | unit |
| useGrinder | grinder |  |
| uri | printQueue |  |
| verticalAccuracy | geoLocation |  |
| verticalDirection | airFlow |  |
| value | numberValue |  |
| visceraFat | bioElectricalImpedanceAnalysis | visFt |
| voltage | energyConsumption | volte |
| volumePercentage | audioVolume | volPe |
| water | bioElectricalImpedanceAnalysis | water |
| weight | weight | weigt |
| coldWash | washingCourceOption |  |
| currentJobState | runState |  |
| currentMachingState | runState |  |
| currentWashingCourse | washingCource |  |
| extraRinse | washingCourceOption |  |
| jobStates | runState |  |
| machineStates | runState |  |
| preWash | washingCourceOption |  |
| progressPercentage | runState |  |
| remoteControlEnabled | remoteControl |  |
| soilLevel | washingCourceOption |  |
| speedWash | washingCourceOption |  |
| spinSpeed | washingCourceOption |  |
| startPause | operationMode |  |
| steamTreat | washingCourceOption |  |
| url | sessionDescription |  |
| uvValue | uvSensor |  |
| uvStatus | uvSensor |  |
| washingCourses | washingCourse |  |
| washTemp | washingCourceOption |  |
| currentSecurityMode | securityStatus |  |
| securityMode | securityStatus |  |

## containerDefinition values

### Introduction

Each specialization has a containerDefinition attribute which can be used as an unique identifier and contains the information of the resource. In this clause, the detailed values of containerDenifition attributes in every specializations for the home appliance information models are given.

### Device models

The containerDefinition attribute of specializations for device models shall have the values that comply with the following rule.

- Rule: “org.onem2m.home.device.[device name]”

For example, the containerDefinition attribute of specialization for deviceAirConditioner shall be “org.onem2m.home.device.deviceAirConditioner”.

### ModuleClasses

The containerDefinition attribute of specializations for module classes shall have the values that comply with the following rule.

- Rule: “org.onem2m.home.moduleclass.[moduleclass name]”

For example, the containerDefinition attribute of specialization for alarmSpeaker shall be “org.onem2m.home.moduleclass.alarmSpeaker”.

### Actions

The containerDefinition attribute of specializations for actions shall have the values

that comply with the following rule.

- Rule: “org.onem2m.home.moduleclass.[name of moduleclass that the action belongs to].[action name]”

For example, the containerDefinition attribute of specialization for activateClockTimer in the timer ModuleClass shall be “org.onem2m.home.moduleclass.timer.activateclocktimer”.

## XSD definitions

### Introduction

The present clause specifies how to name the files which define data types in XSD for Device models, ModuleClasss, and Actions.

Generation process of XSD file is explained in Annex A using some examples.

### XSD definitions for Device models

The XSD definitions for Device models are specified upon the following rule.

- Rule: HD-[device name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for deviceAirConditioner specified in TS-0023 v3.3.0 shall be “HD-deviceAirConditioner-v3_3_0.xsd”

### XSD definitions for ModuleClass

The XSD definitions for ModuleClass are specified upon the following rule.

- Rule: HD-mod-[ModuleClass name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for alarmSpeaker specified in TS-0023 v3.3.0 shall be “HD-mod-alarmSpeaker-v3_3_0.xsd”

### XSD definitions for Action

The XSD definitions for Actions are specified upon the following rule.

- Rule: HD-act-[action name]-v<TS-version>.xsd where the string '<TS-version>' shall be intepreted as the version of the present document

For example, the XSD definition for activateClockTimer specified in TS-0023 v3.3.0 shall be “HD-act- activateClockTimer -v3_3_0.xsd”.

# Mapping with Other Information Models from External Organizations

This clause specifies how the Home Appliance Information Model (HAIM) defined in the clause 5of the present document can be mapped with existing external models from , OCF, ECHONET, OMA GotAPI etc. and introduction of these models is written in annex B. The mapping shall be  to enable the interworking between the oneM2M system and external technologies at the information model level. This means a oneM2M native application which understand only oneM2M standardized HAIM shall be able to  interact with non-oneM2M home appliances of different technologies in a consistent way without knowing the technology specific details. An IPE shall be  responsible for translating the HAIM to/from technology specific information model bidirectionally following the mapping specification in this clause. Using HAIM as a bridge, home appliances and applications of different technologies shall be able to  also interact with each other via the oneM2M system (with IPEs).

## OMA GotAPI(DWAPI-PCH)

### Introduction

This section is intended to specify the mapping relationship between HAIM and OMA DWAPI-PCH with tables.

OMA DWAPI-PCH have no concept  that corresponds to ModuleClass in oneM2M. The mappings of DataPoints to data objects of OMA DWAPI-PCH are expressed in following tables.

### Device Models

#### deviceBloodPressureMonitor

DeviceBloodPressureMonitoer of HAIM shall be mapped to Blood Pressure Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-1: Map of deviceBloodPressureMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| sphygmomanometer | diastolicPressure | diastolic | See clause 5.3.67 |
|  | systolicPressure | systolic |  |
|  | meanPressure | mean |  |
| pulsemeter | pulseRate | pulse | See clause 5.3.55 |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

#### deviceGlucosemeter

DeviceGlucometer of HAIM shall be mapped to Glucometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-2: Map of deviceGlucometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| glucometer | concentration | concentration | See clause 5.3.32 |
|  | hba1c | hba1c |  |
|  | contextExercise | contextExercise |  |
|  | contextMedication | contextMedication |  |
|  | contextCarbohydratesAmount | contextCarbohydrates |  |
|  | contextCarbohydratesSource | contextCarbohydrates |  |
|  | contextMeal | contextMeal |  |
|  | contextLocation | contextLocation |  |
|  | contextTester | contextTester |  |
|  | contextHealth | contextHealth |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

#### devicePulseOximeter

DevicePulseOximeter of HAIM shall be mapped to Pulse Oximeter of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-3: Map of devicePulseOximeter of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | modality | spo2, pulse | See clause 5.3.55. When oximeter module doesn’t exist, pulsemeter module is mandatory. |
| oximeter | modality | spo2, pulse | See clause 5.3.49. When pulsemeter module doesn’t exist, oximeter module is mandatory. |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

#### deviceThermometer

DeviceTermometer of HAIM shall be mapped to Thermometer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-4: Map of deviceThermometer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | Data Points of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| temperature | unit | temperature | See clause 5.3.71 |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

#### deviceWeightScaleAndBodyCompositionAnalyzer

DeviceWeightScaleAdBodyCompositionAnalyzer of HAIM shall be mapped to Weight Scale Body Composition Analyzer of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-5: Map of deviceWeightScaleAdBodyCompositionAnalyzer of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| bodyCompositionAnalyzer | bodyLength | bodyLength | See clause 5.3.14 |
|  | Bmi | bmi |  |
|  | fatFreeMass | fatFreeMass |  |
|  | softLeanMass | softLeanMass |  |
|  | muscleMass | muscleMass |  |
|  | basalMetabolism | basalMetabolism |  |
|  | impedance | impedance |  |
| weight | weight | bodyMass | See clause 5.3.81 |
| bioElectricalImpedanceAnalysis | water | bodyWater | See clause 5.3.13 |
|  | fat | bodyFat |  |
|  | muscle | musclePercentage |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

#### deviceHeartRateMonitor

DeviceHeartRateMonitor of HAIM shall be mapped to Heart Rate Monitor of OMA DWAPI-PCH on the basis of the following table.

Table 7.1.2-6: Map of deviceHeartRateMonitor of oneM2M HAIM to OMA DWAPI-PCH

| ModuleClass | DataPoints of oneM2M HAIM | data objects of OMA DWAPI-PCH | Description |
| --- | --- | --- | --- |
| pulsemeter | pulseRate | rate | See clause 5.3.55 |
|  | rr | rr |  |
|  | energy | energy |  |
| battery | level | batteryLevel | See clause 5.3.10. It shall be the integer type at HAIM, but shall be the float type at OMA DWAPI-PCH. It shall be the rounded percentage of the current level of battery in the range of [0, 100] at HAIM, but shall be a float number in the range of [0.0, 1.0] atOMA DWAPI-PCH. |

### Data Types

Data types of oneM2M HAIM and OMA DWAPI-PCH shall be mapped each other on the basis of the following table.

Table 7.1.3-1: Map of data types between oneM2M and OMA DWAPI-PCH

| oneM2M data type | Mapping to data type in OMA DWAPI-PCH | Description |
| --- | --- | --- |
| xs:integer | int, Number | Data type for 32-bit signed integer. |
| xs:string | String, Array | Data type for text. The length limitation should be considered for the mapping. |
| xs:float | Float | Data type for a single precision 32-bit floating point type as defined in XML Schema 1.0 [14] as the float primitive type. |
| xs:Boolean | Boolean | Data type for Boolean. |

Editor’s note: The mapping between string and Array and between integer and Number needs clarification.

# Ontology for the Home Appliance Information Model aligned with oneM2M Base Ontology

The following table shows a mapping of  the Home Appliance Information Model to the oneM2M Base Ontology in oneM2M TS-0012 [i.5].

The table only shows mapping of  SDT concepts that are used to classify all concepts in the Home Appliance Information Model. Therefore, since any concept in the Home Appliance Information Model can be classified according to a specific SDT concept it also (transitively) maps to the related class of the oneM2M Base Ontology.

Table 7.1.3-1: Mapping between SDT concepts in the Home Appliance Information Model 
and the oneM2M Base Ontology

| SDT Concept in the Home Appliance Information Model | Mapping relationship | Class in Base Ontology | Property in Base Ontology | Comment |
| --- | --- | --- | --- | --- |
| SDT: Device | sub-class of | Device |  |  |
| SDT: SubDevice | sub-class of | Device |  | The base ontology allows a Device to consist of (sub-) Devices |
| SDT: Action | sub-class of | Operation |  |  |
| SDT: Args (of an Action) | sub-class of | OperationInput |  |  |
| SDT: ReturnType (of an Action) | sub-class of | OperationOutput |  |  |
| SDT: Event | sub-class of | Operation |  |  |
| SDT: Data (of an Event) | sub-class of | OutputDataPoint |  |  |
| SDT: Module | sub-class of | Service |  | The base ontology allows a Service to have subServices. Each SDT:Module implements one SDT:ModuleClass. Therfore SDT:Module can be considered a subclass of SDT:ModuleClass and therefore subclass of oneM2M:Service. See note. |
| SDT: ModuleClass | sub-class of | Service |  | See note |
| SDT: UnitOfMeasure | sub-class of | MetaData |  |  |
| SDT: DataPoint | sub-class of | InputDataPoint |  | If SDT:DataPoint is writable |
| SDT: DataPoint | sub-class of | OutputDataPoint |  | If SDT:DataPoint is readable |
| SDT: Property (of a Device) | sub-class of | ThingProperty |  |  |
| SDT: Property (of a ModuleClass) | sub-class of | Aspect |  | Aspect (of the Functionality) |
| SDT: SimpleType | sub-property of |  | hasDataType | The base ontology's SimpleTypeVariable class has data properties: hasDataType hasDataRestriction |
| SDT: Constraint | sub-property of |  | hasDataRestriction |  |
| NOTE: In RESTful technologies the Service (i.e. the electronic representation of a Functionality in a network) is implicitly bound to its Functionality by the naming of the used resources (e.g. the Functionality of ModuleClass "AudioVolume" is implemented as a Service through CRUD operations on a [audioVolume] <flexContainer> specialization). |

(informative): 
Resource Mapping Examples

Introduction

The AE may construct oneM2M resource tree on hosting CSE as the mapping of associated device, and each XSD definition for the device information models is generated following ‘Resource Mapping Rule' in clause 6.2.

The present clause explains how to use the oneM2M resource tree to map Device model for each device (see clause 5.5).

Example for Device model ‘deviceAirConditioner'

The present clause explains the creation process for the device typed 'deviceAirConditioner' (see clause 5.5.1 for device model definition of ‘deviceAirConditioner').

Using the definition, 'deviceAirConditioner' model is mapped to [deviceAirConditioner] resource which is a specialization of <flexContainer> resource (See Figure 7.1.3-1).

Figure 7.1.3-1: Structure of [deviceAirConditioner] resource

The AE creates the [deviceAirConditioner] specialization of <flexContainer> resource for the Device model [deviceAirConditioner] resource.

The [deviceAirConditioner] resource contains the child resource specified in Table 7.1.3-2.

Table 7.1.3-2: Child resources of [deviceAirConditioner] resource

| Child Resources of [deviceAirConditioner] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [binarySwitch] | 0..1 | This resource is used to map 'binarySwith' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [runState] | 0..1 | This resource is used to map 'runState' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airConJobMode] | 0..1 | This resource is used to map ‘airConJobMode’ ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airConOperationMode] | 0..1 | This resource is used to map ‘airConOperationMode’ ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airCleanOperationMode] | 0..1 | This resource is used to map ‘airCleanOperationMode’ ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [temperature] | 0..1 | This resource is used to map ‘temperature’ ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [timer] | 0..1 | This resource is used to map 'timer' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [sleepTimer] | 0..1 | This resource is used to map 'sleepTimer' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [turbo] | 0..1 | This resource is used to map 'turbo' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airFlow] | 0..1 | This resource is used to map 'airFlow' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [powerSave] | 0..1 | This resource is used to map 'powerSave' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [airQualitySensor] | 0..1 | This resource is used to map 'airQualitySensor' ModuleClass defined in clause 5. |
| [variable] | <flexContainer> as defined in the specialization [filterInfo] | 0..1 | This resource is used to map 'filterInfo' ModuleClass defined in clause 5. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [i.3] |

The [deviceAirConditioner] resource contains the attributes specified in Table 7.1.3-4.

Table 7.1.3-4: Attributes of [deviceAirConditioner] resource

| Attributes of [deviceAirConditioner] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3]. |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.device.airconditioner" |
| creator | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3]. |
| ontologyRef | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3]. |
| nodeLink | 1 | RO | nodeLink attribute links to a <node> resource that is hosted on the same hosting CSE of the <flexContainer>. See clause 6.2.2 and 6.2.5 for more details. |

Example of ModuleClass 'binarySwitch'

The [binarySwitch] resource is used to share information regarding the modeled binary switch module as a ModuleClass. The [binarySwitch] resource is a specialization of the <flexContainer> resource.

Figure 7.1.3-3: Structure of [binarySwitch] resource

The [binarySwitch] resource contains the child resource specified in Table 7.1.3-6.

Table 7.1.3-6: Child resources of [binarySwitch] resource

| Child Resources of [binarySwitch] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <flexContainer> as defined in the specialization [toggle] | 0..1 | This resource is used to map 'toggle' Action defined in Clause 5.3.12. |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [i.3] |

The [binarySwitch] resource contains the attributes specified in Table 7.1.3-8.

Table 7.1.3-8: Attributes of [binarySwitch] resource

| Attributes of [binarySwitch] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch" |
| creator | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3] |
| ontologyRef | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3] |
| powerState | 1 | RW | See clause 5.3.12 |

Example of Action 'toggle'

The [toggle] resource is used to share information regarding the modeled toggle as an Action. The [toggle] resource is a specialization of the <flexContainer> resource.

Figure 7.1.3-4: Structure of [toggle] resource

The [toggle] resource contains the child resource specified in Table 7.1.3-10.

Table 7.1.3-10: Child resources of [toggle] resource

| Child Resources of [toggle] | Child Resource Type | Multiplicity | Description |
| --- | --- | --- | --- |
| [variable] | <subscription> | 0..n | See clause 9.6.8 in oneM2M TS-0001 [i.3] |

The [toggle] resource contains the attributes specified in Table 7.1.3-12.

Table 7.1.3-12: Attributes of [toggle] resource

| Attributes of [toggle] | Multiplicity | RW/ RO/ WO | Description |
| --- | --- | --- | --- |
| resourceType | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| resourceID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| resourceName | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| parentID | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| expirationTime | 1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| accessControlPolicyIDs | 0..1 (L) | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| creationTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| lastModifiedTime | 1 | RO | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| labels | 0..1 | RW | See clause 9.6.1.3 in oneM2M TS-0001 [i.3] |
| containerDefinition | 1 | WO | The value is "org.onem2m.home.moduleclass.binaryswitch.toggle" |
| creator | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3] |
| ontologyRef | 0..1 (L) | RW | See clause 9.6.35 in oneM2M TS-0001 [i.3] |

(informative): 
Introduction of Extarnal Organizations Data Model

OMA Got API(DWAPI-PCH)

OMA GotAPI(OMA Generic Open Terminal API Framework) provides the framework to enable applications and multitype devices through GotAPI Servers and Extension Plug-Ins [6]. When APIs are implemented in Extension Plug-Ins under the GotAPI framework, these APIs are called as OMA Device WebAPIs Enabler. In case of healthcare devices, these APIs are called as OMA DWAPI-PCH(Device WebAPIs for Personal Connected Healthcare).

Healthcare devices can be a one of the smart home devices so OMA DWWAPI-PCH can have relationship with oneM2M SDT.

OCF

ECHONET

History

| Publication history |
| --- |
| V2.0.0 | 2016-08-30 | Release 2 - Publication |

| Draft history (to be removed on publication) |
| --- |
| V3.0.0 | 2016-11-07 | Incorporating agreed contributions in TP#25 MAS-2016-0232-HAIM_enhancement MAS-2016-0213R03-add_coffee_machine_in_TS-0023 |
| V3.1.0 | 2016-12-16 | Incorporating agreed contributions in TP#26 MAS-2016-0276R02-Align_HAIM_device_property_with_deviceInfo_TS0023 MAS-2016-0279R01-TS-0023-Section6-Coffee MAS-2016-0284-TS-0023_section5_5_1_for_coffee_machine The caption numbers of tables in secsion 6.2 have been corrected |
| V3.2.0 | 2017-02-27 | Incorporating agreed contributions in TP#26.2 and TP#27 MAS-2017-0007-TS0023 mgmtLink for HAIM resource mapping R3 MAS-2017-0009R04-Adding healthcare device model of OMA CDWG to TS-0023 MAS-2017-0015R02-HAIM_modification_for_Washer_model |
| V3.3.0 | 2017-04-05 | Incorporating agreed contributions in TP#27.2 and TP#28 MAS-2017-0032-runState_revival_for_Washer MAS-2017-0039R05-Mapping_with_OMA GotAPI MAS-2017-0040R03-Add kettle in TS-0023 MAS-2017-0046R03-HAIM_modification_for_airConditioner_model MAS-2017-0047-HAIM_modification_for_humidifier_model MAS-2017-0048-HAIM_modification_for_dehumidifier_model MAS-2017-0049-HAIM_modification_for_dishWasher_model MAS-2017-0050R01-HAIM_modification_for_fan_model MAS-2017-0052-HAIM_modification_for_printer_model MAS-2017-0057R03-Adding binaryObject to TS-0023 MAS-2017-0058R02-Adding geoLocation to TS-0023 MAS-2017-0059R01-Adding numberValue to TS-0023 MAS-2017-0060-Adding phoneCall to TS-0023 MAS-2017-0061-Adding playerControl to TS-0023 MAS-2017-0062R03-Adding textMessage to TS-0023 MAS-2017-0064-HAIM modification for waterValve model MAS-2017-0065R01-HAIM modification for door model MAS-2017-0066R02-HAIM modification for smartPlug model MAS-2017-0067-HAIM modification for securityPanel model MAS-2017-0068R01-HAIM modification for openLevel moduleClass MAS-2017-0069-Editorial to TS-0023 §6.4.4 MAS-2017-0072R02-Clarification on the re-use of ModuleClasses |
| V3.4.0 | 2017-05-29 | Incorporating agreed contributions in TP#28.1 and TP#29 MAS-2017-0058R03-Adding_geoLocation_to_TS-0023 MAS-2017-0079-sleepTimer MAS-2017-0081-TS0023_ch6_reorganization MAS-2017-0102-HAIM_modification_for_airPurifier_model MAS-2017-0103-HAIM_modification_for_airQualityMon_model MAS-2017-0104R01-HAIM_modification_for_dehumidifier_model MAS-2017-0106-HAIM_modification_for_freezer_model MAS-2017-0107R01-HAIM_modification_for_printMultiFunction_model MAS-2017-0108-HAIM_modification_for_clothesDryer_model MAS-2017-0109R03-HAIM_modification_for_TV_model MAS-2017-0110R03-HAIM_modification_for_receiver_model MAS-2017-0111R01-HAIM_modification_for_scanner_model MAS-2017-0113R01-HAIM_modification_for_cooktop_model MAS-2017-0114R01-HAIM_modification_for_food_prove_model MAS-2017-0115R02-HAIM_modification_for_set_top_box_model |
| V3.4.1 | 2017-05-29 | The new baseline(V3.4.1) for TS-0023 includes the modification of enumeration names done by the repporteur in order to write them in consistency way. |
| V3.4.2 | 2017-07-03 | (Editorial change) Cross-references are enabled |
| V3.4.3 | 2017-07-04 | (Editorial change) Devices, ModuleClasses and Enumeration are relocated in alphabetical order |
| V3.5.0 | 2017-07-17 | Incorporating agreed contributions in TP#30 MAS-2017-0062R04 Adding textMessage to TS-0023 MAS-2017-0105R04 HAIM modification for camera model MAS-2017-0112R03 HAIM modification for cookerHood model MAS-2017-0131R03 Adding_SubDevice_table MAS-2017-0155R04 HAIM_propose_impactSensor MAS-2017-0156R02 HAIM_propose_overcurrentSensor MAS-2017-0157R03 HAIM_propose_ozonemeter MAS-2017-0158R03 HAIM_propose_smokeSensor MAS-2017-0159R03 HAIM_propose_uvSensor MAS-2017-0160R03 Adding a new rule when to differentiate between current and target Data Points in TS-0023 ModuleClasses MAS-2017-0161R01 HAIM_propose_acousticSensor MAS-2017-0162R02 HAIM_propose_devicePowerOutlet MAS-2017-0163R02 HAIM_propose_deviceMultiwayOutlet MAS-2017-0164R02 HAIM_propose_deviceGardenLamp MAS-2017-0165R02 HAIM_propose_deviceHomeCCTV MAS-2017-0167R03 HAIM_propose_printQueue MAS-2017-0168R01 HAIM_propose_3DprintAttribute MAS-2017-0169R01 HAIM_propose_3DprintStatus MAS-2017-0170R01 HAIM_propose_device3DPrinter MAS-2017-0171 HAIM_modify_devicePrinter MAS-2017-0172 HAIM_modify_deviceMultiFunctionPrinter MAS-2017-0173 HAIM_modification_for_robotCleaner MAS-2017-0174R01 HAIM_modification_for_refrigerator MAS-2017-0175R01 HAIM_modification_for_oven MAS-2017-0176R01 HAIM_modification_for_steamCloset MAS-2017-0178R02 Adding_a_new_element_for_dataPoints_of_clock_ModuleClas MAS-2017-0179R01 Adding_a_new_element_for_DataPoints_of_smokeSensor_ModuleClas MAS-2017-0188 jobStates_in_runState MAS-2017-0191R01 CR to TS-0023 changing mgmtLink into nodeLink of a Device model flexContainer MAS-2017-0192R01 HAIM credentials |
| V3.6.0 | 2017-11-20 | (Editorial changes) Corrected spelling errors. Alligned language, formatting, etc. |
| V3.6.1 |  |  |

# Comments

DataPoints start with lower case.

I would like to remove this note. This is defining a behaviour, which is up to a device, if it supports this functionality

What is the unit of measure here?

Changed from US to British English

Editor’s note: discussion with SEC regarding completeness and methods is expected.

Unit of measure?

All data points start lower case

I still have no idea what this means.

What is the uom?

Why not meter?

Still no idea what this actualy means. What is the resp. meaning of true or false for this data points?

Is this correct?

What is the unit of measure?

I would remove the example. We don’t give them in this columnt

Actually, we need a “remoteMonitorEnable” MC here as well in order to distinguish this functionality as well.

The name of ModuleClass doesn’t fully align with the functionality. “status” is different from a “mode”.

Changed this from string to uri since this data point contains a URL.

What does this mean? We don’t have this kind of flexibility in the other devices. Such a new device would not be compliant.

Rule for sub-devices is missing.

A rule for sub-devices is missing.

This is still the old text.

Be careful when inserting new refernces here! Only do this by copying fields. Don’t change the levels when inserting new fields for tables

Reason: The numbering is different for the different levels in the document. Word cannot do this automatically

What to do with the empty chapters in this Annex?