| Input contribution INITIAL REQUIREMENTS SUBSET |
| --- |
| Title:* | General Requirements on Lightweight Communication Protocols between Intranet M2M Device and Back-end System |
| Group Name:* | WG3 |
| Source:* | <China Telecom>, <CCSA> |
| Contact: | Tang Jianjun, <China Telecom><tangjj@ctbri.com.cn> Zhou Kaiyu, <China Telecom>, zhouky@ctbri.com.cn Mao Tong, <China Telecom>, Maotong@ctbri.com.cn |
| Date:* | <2013-06-04> |
| Abstract:* | Requirements for Lightweight Communication Protocols between Intranet M2M Device and Back-end System. |
| Agenda Item:* |  |
| Work item(s): |  |
| Document(s) Impacted* |  |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approval |

oneM2M IPR STATEMENT

“Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of an agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

## Title

### General Requirements on Lightweight Communication Protocols between Intranet M2M Device and back-end system

## Description

### Due to the exhaustion of IPv4 address and limited IPv6 deployment, a large number of M2M end devices will be deployed inside the Intranet. The M2M device is generally resource-constrained equipment, so if the standard Network Address Translation (NAT) traversal technology is used to access the device in the intranet, the high requirement for the device processing ability will cause an increase in cost. To solve this problem, the M2M system shall provide a general lightweight remote control protocol adapt to the application case that M2M device is in the intranet, instead of the complex NAT traversal technology, to efficiently control these M2M devices.

## Source (as applicable)

### China Telecom

## Actors

### Equipment Provider （EP）
Vendors who make equipments with built-in communication protocol capability, sell and install equipment, and provide equipment remote maintenance service

### Equipment User (EU)

### Customers who use equipment

### M2M Device Provider (M2M DP)

### Vendors who make M2M Device with built-in communication protocol and other M2M service capability

### M2M Service Provider (M2M SP)

### Service provider who provide M2M service which including network service

### Mobile Network Operator (MNO)

### Service provider who provide mobile network service

### Equipment Provider Back-end Application (EPBA)

### One kind of M2M Applications by which EPs can be monitor, controls, and collect data from their equipment. It is normally located in EP’s office.

### M2M Service Platform (MSP)

### Platform which is operated by M2M SP and provides M2M Service

### Equipment

### It is made by EP, which can do some specific work in some specific areas, such as concrete machinery, hoisting machinery and air compressor.

### M2M Device

### Device embedded into equipment, which serves the function of communication between equipment and EPBA. It also talks with MSP to use M2M service.

## Pre-conditions (if any)

### M2M backend system is deployed in the public network.

### M2M devices are deployed in the public network, or inside the intranet.

### M2M devices need be remote managed and controlled.

### Reference to “High Level Illustration”

## Triggers (if any)

### When M2M device is deployed and connected to network, it can initiate to send message to backend system

### If need, backend system can send management and control message to device.

## Normal Flow (as applicable)

## Post-conditions (if any)

## High Level Illustration (as applicable)

### <Relevant diagram or picture>

## Potential requirements (as applicable)

### M2M Device inside the intranet needs interactive application.

### The requirement of uniform communication protocol is needed.