| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | X Interface Protocol Implementation |
| Source:* | ILS Technology LLC |
| Contact: | Mihai Voicu, ILS Technology LLC, mvoicu@ilstechnology.com Mitch Tseng, Tseng InfoServ LLC, mitch@t-infoserv.com |
| Date:* | <2013-08-07> |
| Abstract:* | This document outlines the specifications for possible implementation of the X Interface for an CSE |
| Agenda Item:* | X |
| Work item(s): |  |
| Document(s) Impacted* | PROT TR |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To agree on inclusion of the proposed text into the Protocol Study TR (Work Item 08) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Scope

The scope of this document is to propose a possible implementation of the X Interface based on the current TIA TR-50 TIA-4940-020 document available in the OneM2M pool.

This document proposes some text for inclusion into the Protocol Analysis Technical Report.

- Proposed text for inclusion into the TR:

The following text is proposed for inclusion into the TR, into section 5.1. “M2M Specific Protocols”.

--- START OF ADDED TEXT ---

5.1.x. TIA TR-50 Protocol

5.1.x.1. Background to the protocol

- The protocol is based on a frame that is flexible to provide extensions for further enhancements / improvements.

- The communication on the X Interface assumes a reliable network connection.

5.1.x.2. Detailed technical description: frame details

The communication is based on:

- Requests

- Responses

5.1.x.3. Detailed technical description: request frame details

The M2M request frames are based on a JSON structure and consist of two major sections:

- Authentication – this is the place where the entire authentication items are placed.

- Command(s) – this is the place where the commands items are placed

Below is the structure of the OneM2M frame:

{

"auth": {

"applicationToken": "<application token>",

"sessionId": "<session token>"

},

"ref": {

"command": "<command keyword>",

"params": []

}

}

In order to minimize the traffic, it is possible to have M2M frames with multiple commands:

"ref1": {

"command": "<first command>",

"params": []

},

"ref2": {

"command": "<second command>",

"params": []

}

The description of the fields is presented below:

| Name | Description | Type | Mandatory |
| --- | --- | --- | --- |
| auth | Keyword. Identifies the authentication stanza in the M2M request frame | String | Yes |
| applicationToken | Keyword. Identifies the application making the request | String | Yes |
| sessionId | Keyword. Unique ID received after the use of the authentication services. Identifies the current session between the two entities | String | Yes |
| ref1, ref2, ref3 | Identifies the commands that are in the request. Can be simple identifiers. They are not keyword. It is expected that the response will contain them. | String | Yes |
| command | Keyword. Identifies a known command that can be executed | String | Yes |
| params | Keyword. Identifies the parameters required by the command. The field must exist, but it can be empty. | String | Yes |

Note: The “authentication, deauthentication, authorization and deauthorization” are suggested actions to complete the diagram.

5.1.x.4. Detailed technical description: response frame details

The response frame is based on the JSON format and it has the following structure:

{

"ref1": {

"success": true,

"params": []

},

"ref2": {

"success": false,

"errorCodes":

[

<errorCode1>,

<errorCode2>

]

"errorMessages":

[

<errorMessage>,

<errorMessage>

]

},

}

- “ref1” response is an example for a positive return of a request

- “ref2” response is an example for an negative or error return of a request

The description of the fields is presented below:

| Name | Description | Type | Mandatory |
| --- | --- | --- | --- |
| ref1,ref2, ref3 | Identifies the request commands. | String | Yes |
| success | Keyword. Identifies the response. Can be true or false | String | Yes |
| errorCodes | Keyword. Identifies the error codes . |  |  |
| errorMessages | Keyword. Identifies the error message. | String | No |
| params | Keyword. Identifies the response parameters. Can be empty. | String | Yes |

--- END OF ADDED TEXT ---

The following diagram depicts a possible interaction between an application and a CSE on the X Interface:

- Example of encapsulation with regards to stage 2:

Based on the ARCH TS-0001 v.0.0.5, where the request is defined as:

Send request from an Issuer to a Receiver could includes the following information:

op:  operation to be executed: Create (C), Retrieve (R), Update (U), Delete (D),

to:  address of target resource, e.g. /m2m.provider1.com/netBase/temp1,

fr:  address of the resource representing the Issuer. Used for access control, e.g., /m2m.provider2.com/remBase/app1,

hd:  headers containing meta-information about the Send request,

cn:  resource content to be transferred.

An example of a request might be:

{

"auth": {

"applicationToken": "<application token>",

"sessionId": "<session token>"

},

"ref": {

{

"command": "create",

"params":

[

{	"to":"/m2m.provider1.com/netBase/temp1",

"fr":"/m2m.provider2.com/remBase/app1",

"hd":"…",

"cn":"…"

}

]

}

}