| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 (PRO) |
| Title:* | Protocol Analysis on WebSocket |
| Source:* | FUJITSU(TTC) |
| Contact: | Shingo Fujimoto, FUJITSU(TTC), shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2013-09-29 |
| Abstract:* | Proposal to add analysis on WebSocket |
| Agenda Item:* | Protocol Analysis |
| Work item(s): | WI-0008 |
| Document(s) Impacted* | TR-000 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG3 member should agree on inclusion of proposed text. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Introduction

WebSocket is getting popular as alternatives of TCP in Web Applications.

This contribution explains basic characteristics of WebSocket.

=== Proposed Text start from Here ===

7.x	WebSocket Protocol

7.x.1	Description

HTTP protocol is widely used for Web Services in different ways . One of those usages is standardized as WebSocket Protocol.

WebSocket Protocol provides an alternative way to ‘HTTP polling’  for two-way communication, which transmits data with upgrading established HTTP connection with remote host.

WebSocket Protocol was originally introduced as part of HTML5 specification, but later the transport protocol specification is standardized as the extension for HTTP in IETF.

7.x.2 	Status

WebSocket Protocol specification is published as RFC6455 (PROPOSED STANDARD) by IETF in 2011.

7.x.3	Intended Use

WebSocket Protocol provides relatively simple transport for two-way communication with remote host, which can coexist with HTTP and deployed HTTP infrastructure.

7.x.4	Deployment Trend

Since WebSocket can use form javascript in HTML5, there are many implementations.

Following are some of implementation which includes WebSocket support:

[Server-Side]

- Apache Tomcat

- Jetty

- Node.js + Socket.IO

[Client-Side]

- Google Chrome Browser

- Cordova (AKA PhoneGap)

7.x.5	Key Features

(cited from Section “1.5 Design Philosophy” of RFC6455 )

The WebSocket Protocol is designed on the principle that there should  be minimal framing (the only framing that exists is to make the protocol frame-based instead of stream-based and to support a distinction between Unicode text and binary frames).  It is expected  that metadata would be layered on top of WebSocket by the application layer, in the same way that metadata is layered on top of TCP by the application layer (e.g., HTTP).

Conceptually, WebSocket is really just a layer on top of TCP that does the following:

o  adds a web origin-based security model for browsers

o  adds an addressing and protocol naming mechanism to support  multiple services on one port and multiple host names on one IP  address

o  layers a framing mechanism on top of TCP to get back to the IP packet mechanism that TCP is built on, but without length limits

o  includes an additional closing handshake in-band that is designed  to work in the presence of proxies and other intermediaries

Other than that, WebSocket adds nothing.  Basically it is intended to be as close to just exposing raw TCP to script as possible given the constraints of the Web.  It's also designed in such a way that its servers can share a port with HTTP servers, by having its handshake  be a valid HTTP Upgrade request.  One could conceptually use other protocols to establish client-server messaging, but the intent of WebSockets is to provide a relatively simple protocol that can coexist with HTTP and deployed HTTP infrastructure (such as proxies)   and that is as close to TCP as is safe for use with such infrastructure given security considerations, with targeted additions  to simplify usage and keep simple things simple (such as the addition  of message semantics).

The protocol is intended to be extensible; future versions will  likely introduce additional concepts such as multiplexing.

7.x.6	Security

Security feature on WebSocket can be independent, but HTTP can provide necessary protections in  transport layer.

7.x.7	Dependency

WebSocket Protocol  depends on HTTP (1.1 or later) protocol.

7.x.8	Benefits and Constrains

[Benefits]

- Allowing co-exist with existing Web infrastructures

- Reuse security solutions which is applied on HTTP Servers

- HTML5 browser can supports WebSocket natively (seamless integration on HTTP based application)

[Constrains]

- Leaving  WebSocket connection opened for long time periods may cause DoS attack risk

- Server-side WebSocket  implementation can host limited number of connections