| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 - Protocols |
| Title:* | XMPP Analysis |
| Source:* | Cisco Systems: Mukesh Taneja |
| Contact: |  |
| Date:* | <2013-09-29> |
| Abstract:* | XMPP Analysis for Section 7 of the Protocol Analysis document |
| Agenda Item:* | Protocol Analysis |
| Work item(s): |  |
| Document(s) Impacted* | M2M Protocol Analysis Technical Report |
| Intended purpose of document:* | xx Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Addition of XMPP section in the M2M Protocol Analysis Technical Report |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

We propose addition to Section 7 as highlighted below.

## 7.x	XMPP: eXtensible Messaging and Presence Protocol

The following clauses describe the eXtensible Messaging and Presence Protocol (XMPP). [i.4]

### 7.x.1	Background

XMPP was first proposed by Jabber open source community and later formalized by IETF in RFC3920.  It is an open XML based protocol for near real-time messaging, presence and request – response services.  Several extensions have been added to achieve other capabilities.

### 7.x.2	Status

IETF RFCs and drafts:

- RFC6120: XMPP: Core (Standards Track RFC. Obsoleted RFC3920). It defines the base XMPP protocol along with RFC6121.

- RFC6121: XMPP: Instant Messaging and Presence. Standards track RFC (obsoletes RFC 3921)

- RFC6122: XMPP Address Format (Standards Track).  Updates RFC3920

XEP (XMPP Extension Protocol) documents specify extensions to XMPP and are standardized by XSF (XMPP Standards Foundation, http://xmpp.org/extensions/).

### 7.x.3	Category and Architectural Style

- XMPP uses a federated client-server model with multiple interconnected servers as shown in Figure 1.  Each server is responsible for managing its own domain and works cooperatively with servers of other domains as peers.  An example is shown in Figure 1.

- XMPP supports Availability for Concurrent Transactions (ACT) style where asynchronous end-to-end exchange of structured data is carried out using direct and persistent XML streams among a distributed network of globally addressable, presence aware clients and servers (RFC6120)

Figure 1: XMPP Federated Client – Server Model

### 7.x.4	Intended use

It is intended to be used for P2P, P2M and IoT purposes.

### 7.x.5	Deployment Trend

- Millions of users world-wide use XMPP for instant messaging and presence based applications.

- List of some servers that support XMPP is given at http://xmpp.org/xmpp-software/servers/.  These servers provide basic messaging, presence and XML routing features.  These servers are available for different platforms such as Linux, Solaris, Windows and Mac OS X.

- A list of XMPP clients is available at http://xmpp.org/xmpp-software/clients/. These clients are available for different platforms such as Linux, Windows, Android, Blackberry, iOS, Mac OS X, J2ME, Palm OS and Browser.

- List of XMPP software libraries is available at http://xmpp.org/xmpp-software/libraries/. These libraries are implemented in various languages such as C, C++, Java, Perl, Ruby, PHP, Python, JavaScript, Tcl, Objective C, Flash / Action Script and C # /.Net/Mono.

- It is used by Jabber client. First instant messaging service based on  XMPP was Jabber.org.

- Jabber is used for text conferencing of IETF meetings.

- Cisco / WebEx uses XMPP.

- Google Talk uses XMPP protocol for instant messaging and presence.   It uses extensions of XMPP for VoIP, video and peer-to-peer communication.

- Microsoft provides XMPP interface to its Microsoft Messenger Service and have XMPP gateways integrated in their messaging systems.

- Facebook presents an XMPP interface to its clients for its chart feature

### 7.x.6	Key Features

- XMPP supports Availability for Concurrent Transactions (ACT) style (RFC6120).

- It supports distributed client server architecture where a client needs to connect with a server to gain access to network. Only after that, it is allowed to exchange XML stanzas with other entities in the network (e.g. in a different domain). End-to-end communication is logically peer-to-peer but physically client-to-server, server-to-server and server-to-client.

- TLS (RFC 4492) is supported for encryption purposes (between client – server and server – server).

- SASL (Simple Authentication and Security Layer, RFC 4422) is used for authentication of initiating entity (e.g. an XMPP client) with the receiving entity (e.g. XMPP server) before the initiating entity is allowed to send XML stanzas to receiving entity.

- Server to server model allows authenticated and secure inter-domain communication.

- Each domain is controlled by a server in a decentralized architecture. Each domain owner can define level of security needed, QoS and policies that are needed for that domain.

- XEP-0016 Privacy Lists: It can be used to block communication from some XMPP users. It can be potentially used for M2M applications as well. In some sense, it allows to implement simple policies to allow or block access to an M2M device from another M2M device.

- XEP-0030 Service Discovery: Allows to discover XMPP entities and features supported by these entities.

- XEP-0045 Multi-user conferencing service.

- XEP-0060 Publish-Subscribe service. It enables to generate notifications and deliver those to multiple subscribers. It is more generalized than the special form of publish-subscribe model supported by presence service. Personal Event Profile (XEP-0163) specifies a stripped down profile of pubSub.

- XEP-0079 Advanced-Message Processing. Allows including message expiration feature. It can be useful to indicate expiration time for M2M data that is cached.

- XEP-0080: Allows publishing location information.

- XEP-0136 Message Archiving: In addition to P2P applications, this can be potentially used for caching M2M data at an XMPP server.

- XEP-0138 – Supports application layer compression.

- XEP-0149 – Allows XMPP entities to specify time period for state, event or activity.

- Jingle specifications (XEP-0166, XEP-0167, XEP-0177, ….) extend XMPP for initiating and managing peer-to-peer media sessions between two XMPP entities.  It uses XMPP for signaling purposes and uses different transport methods (such as TCP, UDP, ….) for data plane packets.  It uses IQ stanzas to negotiate a session between two XMPP end points.  XMPP is used to set up and manage sessions, to negotiate the audio / video codecs to be used, to negotiate the transport to be used for data plane etc.

- XEP-0198 Reliability, Stream Management Protocol

- XEP-0199 : Provides support for application level pings

- XEP-0124 and XEP-0206 Use of HTTP as transport for XML streams

- XEP-0203:  In addition to P2P applications, this can potentially be also used for M2M applications. It allows an XMPP server to store a message if corresponding XMPP client (e.g. an M2M device) is in offline (e.g. sleep) state and send message as soon as it gets to know that the client / device is available. It gets to know the status via presence notification as the client / device moves from offline (sleep) state to available state.

- XEP-0322 Efficient XML Interchange (EXI) Format for XMPP. Useful for M2M applications.

- XEP-0323 Sensor data:  It provides architecture, data structures and basic operations for sensor (M2M) data communication over XMPP networks. This is designed for implementation in sensors that may have limited amount of memory or processing power.

- XEP-0325 Internet of Things – Control: It provides mechanism to control actuators in XMPP based sensor networks.

- XEP-0326 Internet of Things – Concentrators

### 7.x.7	Protocol Stack

As described in RFC6120, XMPP is an application profile of XML that enables near real-time exchange of structured yet extensible data between any two or more network aware entities.  An XMPP address (called a Jabber Identifier or JID) is represented as localpart@domainpart/resourcepart. Here, “domainpart” is required and other elements are optional. “domainpart” could identify a home server to which clients connect for XML routing and data management functionality (RFC6122). It typically maps to a Fully Qualified Domain Name (FQDN).  “localpart” uniquely identifies the entity requesting and using the network access provided by a server. “resourcepart” could identify an object (e.g. a participant in a chat room) or a specific connection (such as a device).  An entity can maintain multiple connected resources simultaneously with each resource differentiated from other resources by different resourcepart and each resource associated with a distinct XML stream. localpart@domainpart is called bare JID and a full JID is formed by adding resourcepart. Some example of JIDs are: <tom@jabber.org/Laptop> , <room@conference.example.com/joe>.

For client-to-server communication, client resolves FQDN of the receiving entity to an IP address and opens a TCP connection to the advertised port at receiver’s IP address. Channel encryption is optionally supported using TLS and authentication is done using SASL. After a client authenticates with a server, it binds a specific resource to the stream so that server can properly address the client. Address for use over that stream is a full Jabber ID of the form <localpart@domainpart/resource>. Client opens an XML stream over TCP with a server (of its domain) and exchanges XML stanzas.

Here, an XML stream is a container for carrying XML elements between two elements in a network. XML elements in an XML stream carry XML stanzas (i.e. actual payload message in XML format) or the elements that are used to negotiate the stream (e.g. for TLS and SASL purposes).  Each stream is unidirectional and thus two streams are needed between an initiating entity and a receiving entity for bidirectional transfer of XML stanzas. An XML stanza is a basic unit of meaning in XMPP.  An XML stream begins with an open tag <stream> and ends with a close tag </stream>. Each direction of conversation is represented as a streaming XML document that ends when that connection is terminated. Root node of that streaming document is the <stream/> element.

For server-to-server communication, a server opens an XML stream over TCP with a server of different domain for inter-server (or inter-domain) communication. Server-to-server streams are typically negotiated in the initialization phase.

Figure 2: XMPP

An example where a client initiates a stream (session) to its server is shown below. A TCP connection is first established between client (Initiator) and server.  Next, client opens an XML stream with the server.

I: <?xml version=’1.0’ ?>

<stream:stream

from=”tom@gmail.com”

to=”mike@jabber.org”

version=”1.0”

xml:lang=”en”

xmlns=”jabber:client”

xmlns:stream=”http://etherx.jabber.org/streams”>

R: <?xml version=’1.0’ ?>

<stream:stream

from=”mike@jabber.org”

id=”h7dssJu+xw79Anik…….=”

to=”tom@gmail.com”

version=”1.0”

xml:lang=”en”

xmlns=”jabber:client”

xmlns:stream=”http://etherx.jabber.org/streams”>

“id” in the message sent by receiving entity above is called stream id and it specifies a unique identifier for the stream. It is generated by the receiving entity when it sends a response stream header to initiating entity.

Following steps are performed after above initial exchange:

- “Stream feature” of XMPP is used at this stage to negotiate TLS for data encryption.

- Client is authenticated with the server (using SASL).

- Resource binding is performed. This makes complete JID from bare JID.

Once above is successful, client can send XML stanzas to server. Client ends communication with  </stream: stream>.

There are three core stanza types, <presence/>, <message/> and <iq/>,  each with its own semantics and they use following five common attributes:

- “to”: It specifies JID of the recipient for the XML stanza

- “from”: This identifies JID of the sender.

- “id”: Requests and responses are matched using this id when IQ stanza is used.

- “type”: It specifies purpose or context of these stanzas. An example of “type” for message stanza is “chat”.

- “xml:lang”: It specifies default language of any human-readable XML character data.

These three core stanzas are briefly described below:

- presence stanza: It is a basic publish-subscribe mechanism that allows several entities to receive information (about presence or availability) of a specific entity to which they have subscribed. In an IM application, presence information of a user’s (or client’s) contacts is displayed in user’s contact list or roster. When a user gets online, XMPP software announces user’s current status to server of user’s domain and that server informs user’s contacts about its online status. It is a simple broadcast mechanism in that sense. That server also informs the presence status of user’s contacts to user. An example of presence notification using presence stanza is given below:

<presence from=”tom@gmail.com/resourcepart”>

<show> do not disturb </show>

<status> working on oneM2M contribution </status>

</presence>

Allowed values of “show” element include: dnd (do not disturb), xa (extended away), away and chat.  An M2M device if not available for processing some action can use “dnd” to indicate that it is not available.

- message stanza: This supports push mechanism where one entity pushes information to another entity. It supports real-time as well as delayed (i.e. store and push) delivery of messages. In IM scenario, message typically encapsulates chat data.  Messages are also used for group chat, event delivery and notifications. Message type includes the following: normal, chat, groupchat, headline and error. Message type “headline” is used to send alert and notifications.  Type “chat” is used for Instant Messaging.  An example of message XML stanza is given below:

I: <message

from=”tom@gmail.com/resourcepart”

to=”mike@jabber.org”

type=”chat”

id=”msg7”>

<subject>  subject text </subject>

<body>  body text    </body>

</message>

For IM, XMPP servers are optimized to handle large number of small messages. As an XMPP server knows about the availability (or presence) status of XMPP clients, it can quickly take an appropriate decision. It can either send message to that client quickly if that client is available or can store it in buffer and send as soon as it gets to know that the client is available.

- IQ (Info/Query) stanza: It is a request-response mechanism that allows structured exchange of data between an initiating entity and a requesting entity in somewhat reliable way.  Values of type attribute used with IQ stanza are get, result, set and error. An iq-result (i.e. iq with type=result) or iq-error type of message is received in response to iq-get or iq-set type of message. <query> tag is used to query from an entity.  Requesting entity also includes an id for tracking the request / response operation. An example of a query using IQ stanza is given below:

I: <iq

From=”tom@gmail.com/laptop”

to=”tom@gmail.com”

type=”get”

id=”query8”>

<query xmlns=”jabber:iq:roster”/>

</iq>

An <error/> stanza is sent by an entity that detected an error. Value of type attribute is set to “error” for this purpose.

Editor’s Note: To add more about IoT related extensions.

### 7.x.8	Data Model

- XMPP is based on XML.

- EXI is also supported for M2M applications.

### 7.x.9	Security

- TLS is supported for encryption of client-to-server and server-to-server communication. It is optional to use. Receiving entity (such as a client or a peer server) can mandate initiating entity to use TLS for data encryption.

- Initiating entity needs to authenticate with receiving entity before sending XML stanzas. If TLS is used, it is used before negotiating for SASL (Simple Authentication and Security Layer Protocol). It helps protect the authentication information exchanged during SASL negotiation.

### 7.x.10	Dependencies

- XMPP streams as defined in RFC6120 use TCP as transport

- Use of HTTP as transport is allowed as per XEP-0124 and XEP-0206

- Uses TLS and SASL for security.

- Jingle extensions use XMPP for signalling but data plane packets are sent over other transport mechanisms such as TCP, UDP, ….

### 7.x.11	Benefits and Constraints

#### 7.x.11.1  Benefits

- It is an open standard. IETF has approved XMPP RFCs for core methods (RFC6121), instant messaging and presence technology (RFC6121) and address format (RFC6122). XMPP standard foundation and IETF continue to extend this.

- XMPP is easily extensible. It provides basic set of features that can be expanded by protocol extensions (XEPs) to provide new set of features.

- Resource location is specified in the address itself and that makes it easy to identify different resources of an XMPP user.

- XMPP is already used by some devices for IM applications.  In that sense, it improves Person-to-Machine  (P2M) communication as user is able to directly interact with smart object running XMPP. It does not necessarily require use of protocol gateways as may be needed with CoAP (e.g. for HTTP to CoAP conversion) and MQTT.

- It supports a federated client-server architecture where no (global) centralized server is needed. Anyone with a domain name can run an XMPP server on its own domain. Public XMPP servers are available for everyone.

- Support of message, presence and IQ stanza types helps meet needs of several IoT applications.

- As it uses “store and push” mechanism to transfer data, it can store contents if the receiving entity is offline (e.g. if IoT device is in sleep mode).

- <xml:lang> common attribute enables internationalization.

- An XMPP address (or JID) can include any Unicode character and is not restricted to ASCII characters.

- Some of the existing mechanisms (such as publish-subscribe, caching, delayed delivery, support for EXI, etc.) are applicable for IoT use cases as well. Work continuing to standardize some IoT related extensions.

#### 7.x.11.2 Constraints

- Uses of TCP may not be desirable for some IoT segments.

- Overhead may be high if XML data is used but EXI extensions available for IoT applications.

### 7.x.12	Support of oneM2M requirements

Support of oneM2M Requirements [i.2] by XMPP  is shown in the following clauses:

#### 7.1.12.1  Fully Supported Requirements

Editor’s Note: To be completed

#### 7.1.12.2   Partially Supported Requirements

Editor’s Note: To be completed

#### 7.1.12.3	Disallowed Requirements

Editor’s Note: To be completed