| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#7(TP#6.6) PRO WG |
| Title:* | Bluetooth description |
| Source:* | LM Ericsson |
| Contact: | raymond.forbes@ericsson.com |
| Date:* | 2013-10-02 |
| Abstract:* | This contribution provides some comparion Bluetooth & other wireless Technologies for the Stage 3 report. |
| Agenda Item:* | <Agenda item reference> |
| Work item(s): | WI0008 |
| Document(s) Impacted* | TR-0009-Protocols |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | If approved. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

- Introduction

In PRO #6.6 (web conference), it was discussed that the description of uniform interface needed to include other protocols since the description was not complete. Thus, in this contribution the comparison  of Bluetooth Wireless Metrics to other well know radion access sytems proposed.

====START of Proposed text ====

# Annex B
Definitions of Radio metrics for Technologies used above for M2M releated Protocols (Informative)

NOTE:  The following definitions are quoted for reference from publicly-available sources, and no representation is made regarding the accuracy or timeliness of the information it contains. In addition, the appearance or omission of any M2M-related information in this list does not imply either the intention, or lack of intention, to undertake any normative or other work within oneM2M.

Table B-1: Table of Wreless access technologies in the M2M landscape

|  |  | ZigBee | Bluetooth | 802.11b | 802.11g | 802.11a | 802.11n | UWB |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Throughput | Mbps | 0.03 | 1-3 | 11 | 54 | 54 | 200 | 200 |
| Max range | ft | 75 | 30 | 200 | 200 | 150 | 150 | 30 |
| Sweet spot | Mbps-ft | .03@75 | 1-3@10 | 2@200 | 2@200 | 36@100 | 100@100 | 200@10 |
| Service | bps-ft2 | 530 | 314M | 251G | 251G | 1.13T | 3.14T | 62G |
| Power | mW | 30 | 100 | 750 | 1000 | 1500 | 2000 | 400 |
| Bandwidth | MHz | 0.6 | 1 | 22 | 20 | 20 | 40 | 500 |
| Spectral efficiency | b/Hz | 0.05 | 1 | 0.5 | 2.7 | 2.7 | 5 | 0.4 |
| Power efficiency1 | mW/Mbps | 1000 | 100 | 68 | 19 | 27 | 10 | 2 |
| Power efficiency2 | mAh/GB | 2211 | 67 | 46 | 12 | 18 | 7 | 1.3 |
| TTGB | Time | 3.1 day | 2.2 hr | 12 min | 2.5 min | 2.5 min | 40 sec | 40 sec |
| Price | US$ | $2 | $3 | $5 | $9 | $12 | $20 | $7 |
| Note: TTGB: Time To Gene (the time to live for a security session key). |

Bluetooth Wireless Technology

Bluetooth wireless technology is geared towards voice and data applications

Bluetooth wireless technology operates in the unlicensed 2.4 GHz spectrum

The range of Bluetooth wireless technology is application specific. The Bluetooth Specification mandates operation over a minimum distance of 10 meters or 100 meters depending on the Bluetooth device class, but there is not a range limit for the technology. Manufacturers may tune their implementations to support the distance required by the use case they are enabling.

The peak data rate with EDR is 3 Mbps

Bluetooth wireless technology is able to penetrate solid objects

Bluetooth technology is omni-directional and does not require line-of-sight positioning of connected devices

Security has always been and continues to be a priority in the development of the Bluetooth specification. The Bluetooth specification allows for three modes of security

Ultra-Wideband (UWB)

UWB technology for Personal Area Networks offers a unique combination of low power consumption (~1mW/Mbps) and high data throughput (up to 480 Mbps).

WiMedia UWB is an internationally recognized standard (ECMA-368, ISO/IEC 26970 and ECMA-369, ISO/IEC 26908) and has regulatory approval in major markets worldwide, including US, EU, Korea and Japan. Additional regions, e.g. China and Canada are expecting regulatory approval in the near future.

Ideally, it will have low power consumption, low price, high speed, use a wide swath of radio spectrum, carry signals through obstacles (doors, etc.) and apply to a wide range of applications (defense, industry, home, etc.)

WiMedia UWB takes a "Common Radio Platform" approach allowing the same radio to be used for a variety of applications.

WiMedia UWB allows for data rates up to 480Mbps at ranges of several meters and a data rate of approximately 110 Mbps at a range of up to 10 meters

While Wireless USB has initially utilized UWB technology, it is expected that the Bluetooth high speed solution will not suffer the same performance and interoperability issues due to the specification development and qualification process employed by the Bluetooth SIG.

The Bluetooth SIG announced in May 2005 its intentions to work with UWB to develop a high rate Bluetooth specification on the UWB radio

Certified Wireless USB

Speed: Wireless USB is projected to be 480 Mbps up to 2 meters and 110 Mbps for up to 10 meters. Wireless USB hub can host up to 127 wireless USB devices

Wireless USB will be based on and run over the UWB radio promoted by the WiMedia Alliance.

Allows point-to-point connectivity between devices and the Wireless USB hub

Intel established the Wireless USB Promoter Group in February 2004

The USB Implementers Forum, Inc. (USB-IF) tests and certifies the "certified Wireless USB" based wireless equipment

Wi-Fi (IEEE 802.11)

Bluetooth technology uses a fifth of the power of Wi-Fi

The Wi-Fi Alliance tests and certifies 802.11 based wireless equipment

802.11a: This uses OFDM, operates in the 5 GHz range, and has a maximum data rate of 54 Mbps

802.11b: Operates in the 2.4 GHz range, has a maximum data rate of 11 Mbps and uses DSSS. 802.11b is the original Wi-Fi standard

802.11g: Operates in the 2.4 GHz range, uses OFDM and has a maximum data rate of 54 Mbps. This is backwards compatible with 802.11b

802.11e: This standard will improve quality of service

802.11h: This standard is a supplement to 802.11a in Europe and will provide spectrum and power control management. Under this standard, dynamic frequency selection (FS) and transmit power control (TPC) are added to the 802.11a specification

802.11i: This standard is for enhanced security. It includes the advanced encryption standard (AES). This standard is not completely backwards compatible and some users will have to upgrade their hardware. The full 802.11i support is also referred to as WPA2

802.11k: Under development, this amendment to the standard should allow for increased radio resource management on 802.11 networks

802.11n: This standard is expected to operate in the 5 GHz range and offer a maximum data rate of over 100 Mbps (though some proposals are seeking upwards of 500 Mbps). 802.11n will handle wireless multimedia applications better than the other 802.11 standards

802.11p: This standard will operate in the automotive-allocated 5.9 GHz spectrum. It will be the basis for the dedicated short range communications (DSRC) in North America. The DSRC will allow vehicle to vehicle and vehicle to roadside infrastructure communication

802.11r: This amendment to the standard will improve users' ability to roam between access points or base stations. The task group developing this form in spring/summer 2004

802.11s: Under development, this amendment to the standard will allow for mesh networking on 802.11 networks. The task group developing this formed in spring/summer 2004

WiMAX (Worldwide Interoperability for Microwave Access and IEEE 802.16)

WiMax is a wireless metropolitan area network (MAN) technology

WiMax has a range of 50 km with data rates of 70 Mbps. Typical cell has a shorter range

The original 802.16 standard operated in the 10-66 GHz frequency bands with line of sight environments

The newly completed 802.16a standard operates between 2 and 11 GHz and does not need line of sight

Delays in regulatory approval in Europe due to issues regarding the use of the spectrums in the 2.8 GHz and 3.4 GHz range

Supports vehicle mobility for between 20 to 100 km/hr. The 802.16e standard will allow nomadic portability

The IEEE 802.16a and the ETSI HIPERMAN (High Performance Radio Metropolitan Area Network) share the same PHY and MAC. 802.16 has been designed from the beginning to be compatible with the European standard

Created to compete with DSL and cable modem access, the technology is considered ideal for rural, hard to wire areas

WiBro (Wireless Broadband)

Portable Internet Service (WiBro) is to provide a high data rate wireless internet access with PSS (Personal Subscriber Station) under the stationary or mobile environment, anytime and anywhere. Primarily based in South Korea based on TTA specifications

2300-2400 MHz, TDD, OFDMA, channel bandwidth 10 MHz, etc

System shall support mobile users at a velocity of up to 60km/h

Throughput (per user) Max. DL / UL = 3 / 1 [Mbps], Min. DL / UL = 512 / 128 [Kbps]

Will come online Q1 2006

Infrared (IrDA)

IrDA is used to provide wireless connectivity for devices that would normally use cables to connect. IrDA is a point-to-point, narrow angle (30° cone), ad-hoc data transmission standard designed to operate over a distance of 0 to 1 meter and at speeds of 9600 bps to 16 Mbps

IrDA is not able to penetrate solid objects and has limited data exchange applications compared to other wireless technologies

IrDA is mainly used in payment systems, in remote control scenarios or when synchronizing two PDAs with each other

Radio Frequency Identification (RFID)

There are over 140 different ISO standards for RFID for a broad range of applications

With RFID, a passive or unpowered tag can be powered at a distance by a reader device. The receiver, which must be within a few feet, pulls information off the 'tag,' and then looks up more information from a database. Alternatively, some tags are self-powered, 'active' tags that can be read from a greater distance

RFID can operate in low frequency (less than 100 MHz), high frequency (more than 100 MHz), and UHF (868 to 954 MHz)

Uses include tracking inventory both in shipment and on retail shelves

Near Field Communication (NFC)

The NFC Forum is involved in the development and promotion of NFC. The 12 sponsor members of the NFC Forum include MasterCard International, Microsoft, Motorola, NEC, Nokia, Panasonic, Philips, Renesas, Samsung Electronics, Sony, Texas Instruments and Visa

Capacity: 212 kbps over a distance from 0 to 20 centimeters over the 13.56 Mhz frequency range

The NFC standard is based on RFID technology

Applications suggested for NFC include ticketing, payment and gaming.

Support for a passive mode of communication leads to savings on battery power

Near-Field Magnetic Communication

Proprietary wireless technology developed, patented and licensed by Aura Communications.

Range: 1.5 to 2 meters; Power: about 100 nanowatts; and frequency: 10 to 15 MHz. Creates a weak magnetic bubble of 4 to 6 feet in diameter in which it works

Currently this technology is only used for wireless headsets. An adapter must be attached to the phone since it is not integrated in any handset

Only available in the U.S. to-date

HiperLAN

Speed: HiperLAN 2 = 54 Mbps, and has a 50 to 100 m capacity

No present killer application

HIPERMAN

Fixed wireless access standard developed by the European Telecommunications Standards Institute (ETSI)

Operates in the spectrum between 2 GHz and 11 GHz and is compatible/interoperable with the IEEE 802.16a-2003 standard

802.20

Considered to be mobile wireless broadband wireless access.

Maximum data rate expected to be 1 Mbps, operating in licensed bands below 3.5 GHz

Supports vehicle mobility up to 250 km/hr

ZigBee (IEEE 802.15.4)

The promoter companies of the ZigBee Alliance include Philips, Honeywell, Mitsubishi Electric, Motorola, Samsung, BM Group, Chipcon, Freescale and Ember; more than 70 members

Capacity of 250 Kbits at 2.4 GHz, 40 Kpbs at 915 Mhz, and 20 Kpbs at 868 Mhz with a range of 10-100 M

Its purpose is to become a wireless standard for remote control in the industrial field

The ZigBee technology is targeting the control applications industry, which does not require high data rates, but must have low power, low cost and ease of use (remote controls, home automation, etc.)

The specification was formally adopted in December 2004

Security was not considered in the initial development of the specification. Currently there are three levels of security

# Annex Z
Bibliography

Note: It shall contain a list of standards, books, articles, or other sources on a particular subject which are not mentioned in the document itself.

<Publication>: "<Title>".

<Publication>: "<Title>".

<Publication>: "<Title>".