| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | Delivery-related ptimitives |
| Source:* | QUALCOMM Japan Inc., |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2013-12-02 |
| Abstract:* | This contribution proposes delivery-related primitives. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes primitives in line with the <delivery> related flows as defined in 10.3.1 of the Architecture TS.

--------------------- Start of proposed modified text -------------------

### Delivery resource and management procedure

#### This section describes each of the primitives applied to <delivery> resource.

##### deliveryCreate

- deliveryCreateRequest

This procedure is used for requesting a CSE to take responsibility to deliver the provided data to a target CSE. The originating CSE will use default values for optional parameters that are not specified.

# Table x-1: Applicability of the primitive

| Primitive applicability |
| --- |
| Applicable interfaces | Mca | Mcc | Mcn |
| Originator | - | CSE | - |
| Receiver | - | Target CSE | - |

# Table x-2: deliveryCreateRequest

| Primitive: deliveryCreateRequest |
| --- |
| Primitive attribute | M/O | Description |
| originatorID (fr) | M | ID of the Originator |
| targetID (to) | M | URI of the target resource or the parent of the target resource |
| resourceType (ty) | M | Type of the resource to be created |
| primitiveType | M | DELIVERY_CREATE_REQUEST |
| requestID (ri) | M | Identifier of the request |
| lifespan (ls) | M | Time limit for the delivery |
| expirationTime (et) | M | Expiration timestamp |
| responseTypeFlag (rt) | M | Indication of the type of the response expected |
| eventCategory (ec) | M | different possible event categories that delivery handling can process |
| resultContent (rc) | M | Indication of the components of the result of the requested operation |
| responsePersistence (rp) | M | Duration which the address containing the response is to persist |
| deliveryAggregationFlag (da) | M | Indication of forwarding one or more original requests to the same target CSEs. This shall be set to ‘ON’. |
| Resource | M/O | Description |
| delivery | M | The application resource representation of the resource to be created |

    - deliveryCreateResponse (successful case)

This response is triggered by the deliveryCreateRequest. The primitive shall comply with table x-3.

# Table x-3: deliveryCreateResponse, successful case

| Primitive: deliveryCreateResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_CREATE_RESPONSE |
| statusCode (rs) | M | Result of the requested delivery |
| resourceURI | M | The URI of the created delivery resource |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |
| Resource | M/O | Description |
| delivery | O | The delivery resource representation. Only present if any of the provided attributes were modified by the target CSE. |

##### deliveryCreateResponse (unsuccessful case)

This response is triggered by the deliveryCreateRequest. The primitive shall comply with table x-4.

# Table x-4: deliveryCreateResponse, unsuccessful case

| Primitive: deliveryCreateResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_CREATE_RESPONSE |
| errorInfo (rs + ai) | M | Additional information about the error that occurred |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |

#### deliveryRetrieve

##### deliveryRetrieveRequest

This procedure is used for requesting a CSE to provide information on a previously created <delivery> resource which represents delivery of data to a target CSE. The originating CSE will use default values for optional parameters that are not specified.

# Table x-5: Applicability of the primitive

| Primitive applicability |
| --- |
| Applicable interfaces | Mca | Mcc | Mcn |
| Originator | - | CSE | - |
| Receiver | - | Target CSE | - |

# Table x-6: deliveryRetrieveRequest

| Primitive: deliveryRetrieveRequest |
| --- |
| Primitive attribute | M/O | Description |
| originatorID (fr) | M | ID of the Originator |
| targetID (to) | M | URI of the target resource or the parent of the target resource |
| primitiveType | M | DELIVERY_RETRIEVE_REQUEST |
| requestID (ri) | M | Identifier of the request |
| lifespan (ls) | M | Time limit for the delivery |
| expirationTime (et) | M | Expiration timestamp |
| responseTypeFlag (rt) | M | Indication of the type of the response expected |
| eventCategory (ec) | M | different possible event categories that delivery handling can process |
| resultContent (rc) | M | Indication of the components of the result of the requested operation |
| responsePersistence (rp) | M | Duration which the address containing the response is to persist |
| deliveryAggregationFlag (da) | M | Indication of forwarding one or more original requests to the same target CSEs. This shall be set to ‘ON’. |

##### deliveryRetrieveResponse (successful case)

This response is triggered by the deliveryRetrieveRequest. The primitive shall comply with table x-7.

# Table x-7: deliveryRetrieveResponse, successful case

| Primitive: deliveryRetrieveResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_RETRIEVE_RESPONSE |
| statusCode (rs) | M | Result of the requested delivery |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |
| Resource | M/O | Description |
| delivery | M | The delivery resource representation. |

##### deliveryRetrieveResponse (unsuccessful case)

This response is triggered by the deliveryRetrieveRequest. The primitive shall comply with table x-8.

# Table x-8: deliveryRetrieveResponse, unsuccessful case

| Primitive: deliveryRetrieveResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_RETRIEVE_RESPONSE |
| errorInfo (rs + ai) | M | Additional information about the error that occurred |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |

#### deliveryUpdate

##### deliveryUpdateRequest

This procedure is used for requesting a CSE to update information on a previously created <delivery> resource which represents a pending delivery of data to a target CSE. The update may have impact on further processing of the delivery.

# Table x-9: Applicability of the primitive

| Primitive applicability |
| --- |
| Applicable interfaces | Mca | Mcc | Mcn |
| Originator | - | CSE | - |
| Receiver | - | Target CSE | - |

# Table x-10: deliveryUpdateRequest

| Primitive: deliveryUpdateRequest |
| --- |
| Primitive attribute | M/O | Description |
| originatorID (fr) | M | ID of the Originator |
| targetID (to) | M | URI of the target resource or the parent of the target resource |
| primitiveType | M | DELIVERY_UPDATE_REQUEST |
| requestID (ri) | M | Identifier of the request |
| lifespan (ls) | M | Time limit for the delivery |
| expirationTime (et) | M | Expiration timestamp |
| responseTypeFlag (rt) | M | Indication of the type of the response expected |
| eventCategory (ec) | M | different possible event categories that delivery handling can process |
| resultContent (rc) | M | Indication of the components of the result of the requested operation |
| responsePersistence (rp) | M | Duration which the address containing the response is to persist |
| deliveryAggregationFlag (da) | M | Indication of forwarding one or more original requests to the same target CSEs. This shall be set to ‘ON’. |

##### deliveryUpdateResponse (successful case)

This response is triggered by the deliveryUpdateRequest. The primitive shall comply with table x-11.

# Table x-11: deliveryUpdateResponse, successful case

| Primitive: deliveryUpdateResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_UPDATE_RESPONSE |
| statusCode (rs) | M | Result of the requested delivery |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |
| Resource | M/O | Description |
| delivery | O | The delivery resource representation. Only present if any of the provided attributes were modified by the target CSE. |

##### deliveryUpdateResponse (unsuccessful case)

This response is triggered by the deliveryUpdateRequest. The primitive shall comply with table x-12.

# Table x-12: deliveryUpdateResponse, unsuccessful case

| Primitive: deliveryUpdateResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_UPDATE_RESPONSE |
| errorInfo (rs + ai) | M | Additional information about the error that occurred |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |

#### deliveryDelete

##### deliveryDeleteRequest

This procedure is used for requesting a CSE to cancel a pending delivery of data to a target CSE or to delete the <delivery> resource of an already executed delivery.

# Table x-13: Applicability of the primitive

| Primitive applicability |
| --- |
| Applicable interfaces | Mca | Mcc | Mcn |
| Originator | - | CSE | - |
| Receiver | - | Target CSE | - |

# Table x-14: deliveryDeleteRequest

| Primitive: deliveryUpdateRequest |
| --- |
| Primitive attribute | M/O | Description |
| originatorID (fr) | M | ID of the Originator |
| targetID (to) | M | URI of the target resource or the parent of the target resource |
| primitiveType | M | DELIVERY_DELETE_REQUEST |
| requestID (ri) | M | Identifier of the request |
| lifespan (ls) | M | Time limit for the delivery |
| expirationTime (et) | M | Expiration timestamp |
| responseTypeFlag (rt) | M | Indication of the type of the response expected |
| eventCategory (ec) | M | different possible event categories that delivery handling can process |
| resultContent (rc) | M | Indication of the components of the result of the requested operation |
| responsePersistence (rp) | M | Duration which the address containing the response is to persist |
| deliveryAggregationFlag (da) | M | Indication of forwarding one or more original requests to the same target CSEs. This shall be set to ‘ON’. |

##### deliveryDeleteResponse (successful case)

This response is triggered by the deliveryDeleteRequest. The primitive shall comply with table x-15.

# Table x-15: deliveryDeleteResponse, successful case

| Primitive: deliveryDeleteResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_DELETE_RESPONSE |
| statusCode (rs) | M | Result of the requested delivery |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |

##### deliveryDeleteResponse (unsuccessful case)

This response is triggered by the deliveryDeleteRequest. The primitive shall comply with table x-16.

# Table x-16: deliveryDeleteResponse, unsuccessful case

| Primitive: deliveryDeleteResponse |
| --- |
| Primitive Attribute | M/O | Description |
| primitiveType | M | DELIVERY_DELETE_RESPONSE |
| errorInfo (rs + ai) | M | Additional information about the error that occurred |
| requestID (ri) | M | Identifier of the request |
| originatingTimestamp (ot) | O | Originating timestamp when the message was built |
| exprirationTimestamp (et) | O | Expiration timestamp |

--------------------- End of proposed modified text ---------------------