| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | CoAP Protocol Binding |
| Source:* | Hitachi (China) R&D Corp. |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-01-22 |
| Abstract:* | This contribution proposes CoAP protocol binding details. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

# 5	Overview

## 5.1 CoAP Overview

### 5.1.1 CoAP Message Model

CoAP provides four message types for message correlation, including CON, NON, ACK, and RST. CoAP request and response semantics are carried in CoAP messages.

| Messaging Model | CON (Confirmable) | Reliable message transmission |
| --- | --- | --- |
|  | NON (Non-confirmable) | Non-reliable message transmission |
|  | ACK (Acknowledgement) | Acknowledge sender the reception of CON message |
|  | RST (Reset) | Used for replying sender that recipient is not at all able a CON or NON message, or used in “coap ping” as an inexpensive check of the liveness of an endpoint |
| Request/ Response Model | Request | Carried by CON or NON message |
|  | Response | Carried by CON, NON, ACK, or RST message |

### 5.1.2 CoAP Method

CoAP makes use of GET, PUT, POST and DELETE request methods in a similar manner to HTTP as following.

| GET | Retrieve a representation for the information that currently corresponds to the resource identified by the request URI |
| --- | --- |
| POST | Request that the representation enclosed in the request be processed |
| PUT | Request that the resource identified by the request URI be updated or created with the enclosed representation |
| DELETE | Request that the resource identified by the request URI be deleted |

Each response code is described below:

| Success 2.xx | 2.01 Created | In response to POST and PUT requests |
| --- | --- | --- |
|  | 2.02 Deleted | In response to requests that cause the resource to cease being available, DELETE and POST requests |
|  | 2.03 Valid | Indicate that the response identified by the entity-tag identified by the included ETag Option is valid |
|  | 2.04 Changed | In response to POST and PUT requests |
|  | 2.05 Content | In response to GET requests |
| Client Error 4.xx | 4.00 Bad Request | Request could not be understood by server due to malformed syntax |
|  | 4.01 Unauthorized | The client is not authorized to perform the requested action |
|  | 4.02 Bad Option | The request could not be understood by the server due to one or more unrecognized or malformed options |
|  | 4.03 Forbidden | The server understood the request, but is refusing to fulfill it |
|  | 4.04 Not Found | The server has not found anything matching the request URI |
|  | 4.05 Method Not Allowed | The request method is not allowed for the resource identified by the request URI |
|  | 4.06 Not Acceptable | The response could not be acceptable |
|  | 4.12 Precondition Failed | The precondition given in one or more request fields evaluated to false when it was tested on the server |
|  | 4.13 Request Entity Too Large | The server is refusing to process a request because the request entity is larger than the server is willing or able to process |
|  | 4.15 Unsupported Content-Format | The server is refusing to service the request because the entity of the request is in a format not supported by the requested resource for the requested method |
| Server Error 5.xx | 5.00 Internal Server Error | The server encountered an unexpected condition which prevented it from fulfilling the request |
|  | 5.01 Not Implemented | The server does not support the functionality required to fulfill the request |
|  | 5.02 Bad Gateway | The server, while acting as a gateway or proxy, received an invalid response from the upstream server it accessed in attempting to fulfill the request |
|  | 5.03 Service Unavailable | The server is currently unable to handle the request due to a temporary overloading or maintenance of the server |
|  | 5.04 Gateway Timeout | The server, while acting as a gateway or proxy, did not receive a timely response from the upstream server specified by the URI it needs to access in attempting to complete the request |
|  | 5.05 Proxying Not Supported | The server is unable or unwilling to act as a forward-proxy for the URI specified in the Proxy-Uri Option |

### 5.1.3 Options

CoAP defines a single set of options that are used in both requests and responses:

| Uri-Host, Uri-Port, Uri-Path and Uri-Query | Uri-Host | Specify the Internet host of the resource being requested |
| --- | --- | --- |
|  | Uri-Port | Specify the transport layer port number of the resource |
|  | Uri-Path | Specify one segment of the absolute path to the resource |
|  | Uri-Query | Specify one argument parameterizing the resource |
| Proxy-Uri and Proxy-Scheme | Proxy-Uri | Used to make a request to a forward-proxy |
|  | Proxy-Scheme | Used to construct the absolute-URI |
| Content-Format | Content-Format | Indicate the representation format of the message payload |
| Accept | Accept | Indicate which Content-Format is acceptable to the client |
| Max-Age | Max-Age | Indicate the maximum time a response may be cached before it is considered not fresh |
| ETag | ETag | As a resource-local identifier for differentiating between representation of the same resource that vary over time |
| Location-Path and Location-Query | Location-Path | Indicate a relative URI that consists of an absolute path |
|  | Location-Query | Indicate a relative URI that consists of a query string |
| Conditional Request Options | If-Match | Used to make a request conditional on the current existence or value of an ETag for one or more representations of the target resource |
|  | If-None-Match | Used to make a request conditional on the non-existence of the target resource |
| Size Option | Size1 | Provide size information about the resource representation in a request |

## 5.2 oneM2M Protocol Mapping

### 5.2.1 Primitive Types Mapping

The CoAP request method shall be mapped into oneM2M primitive types as following:

| CoAP Methods | oneM2M Primitive Types |
| --- | --- |
| POST | DELIVERY_CREATE_REQUEST |
| GET | DELIVERY_RETRIEVE_REQUEST |
| PUT | DELIVERY_UPDATE_REQUEST |
| DELETE | DELIVERY_DELETE_REQUEST |

### 5.2.2 Response Codes Mapping

If the CoAP response code is in the range 2.01 to 2.05, then the response shall be considered as a successful case.

| CoAP Response Code | oneM2M Primitive Types |
| --- | --- |
| Success 2.xx | 2.01 Created | DELIVERY_CREATE_RESPONSE |
|  | 2.02 Deleted | DELIVERY_DELETE_RESPONSE |
|  | 2.03 Valid | DELIVERY_RETRIEVE_RESPONSE DELIVERY_UPDATE_RESPONSE |
|  | 2.04 Changed | DELIVERY_UPDATE_RESPONSE |
|  | Content | DELIVERY_RETRIEVE_RESPONSE |

If the CoAP response code is in the range of 4.00 to 4.15 or 5.00 to 5.05, then the response shall be considered as unsuccessful case. Additional information about the error should be included.

| CoAP Response Code | oneM2M Primitive Types | errorinfo |
| --- | --- | --- |
| Client Error 4.xx | DELIVERY_CREATE_RESPONSE DELIVERY_DELETE_RESPONSE DELIVERY_RETRIEVE_RESPONSE DELIVERY_UPDATE_RESPONSE | Additional information about the error |
| Server Error 5.xx | DELIVERY_CREATE_RESPONSE DELIVERY_DELETE_RESPONSE DELIVERY_RETRIEVE_RESPONSE DELIVERY_UPDATE_RESPONSE | Additional information about the error |

--------------------- End of proposed modified text ---------------------