| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 - Protocols |
| Title:* | IoT Protocols – Summary (PRO-2014-0209-IoT_Protocols_-_Summary) |
| Source:* | Cisco Systems |
| Contact: | Mukesh Taneja, mutaneja@cisco.com |
| Date:* | <2014-03-24> |
| Abstract:* | “IoT Protocols - Summary” for Section 7 of the Protocol Analysis document (TR-0009) |
| Agenda Item:* | Protocol Analysis |
| Work item(s): |  |
| Document(s) Impacted* | oneM2M Protocol Analysis Technical Report |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Text to complete Table 8 in section 7 of the Protocol Analysis Technical Report (TR-0009) |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

We propose two existing tables in section 7 of the TR-0009 to be replaced with tables given here:

## 7	Summary

| Protocol / Traits | Architecture Style | Intended or Actual Deployment | Above RS-485 or above TCP/UDP or above XMPP/HTTP | Data Model / Data Representation | Messaging (only a subset of features indicated here) | Security (only a subset of mechanisms listed here) |
| --- | --- | --- | --- | --- | --- | --- |
| CoAP | Client / server model. P2P. RESTful | IoT networks with low power constrained sensors such as smart metering | Above UDP (or DTLS/ UDP) | Plain text, XML, JSON, EXI, octet-stream, ….. Support for content negotiation | Request / Response, Pub-Sub | Largely depends on lower layers (DTLS, ….) |
| MQTT | Client / Server model. Brokered style. | Low bandwidth, high latency networks (e.g. HealthCare, Energy) | MQTT runs above TCP (or TLS/TCP). (MQTT-SN runs over UDP) | No formal data model | Publish-Subscribe | Authentication: Userid / password can be passed in a packet. SSL / TLS can be used. |
| HTTP as RESTful API | RESTful | WWW | Above TCP (or TLS/TCP) | XML, JSON, etc. Support for Content negotiation | Request - Response | Largely depends on lower layers (SSL / TLS, ….) |
| XMPP | Availability for Concurrent Transactions (ACT) style for carrying out asynchronous end-to-end exchange of structured data | Instant Messaging and Presence Applications, Jabber | Above TCP (or TLS/TCP) | XML, EXI | Publish- Subscribe | SASL, TLS, lower layer security |
| WebSockets | Full duplex communication over TCP | Low latency, high performance web applications | Above TCP. Uses HTTP for initial handshake | JSON, etc. | Full duplex communication same over TCP socket. | TLS |
| DDS | Data centric model. (Virtual) Global Data space and broker-less Peer-to-Peer model | Several segments such as health care, UAVs, asset tracking, etc. | Can run over UDP, TCP, shared memory and other transport types | DSSI defines a standard data format based on extension of Common Data Representation. Named topics, user defined data types | Real-time Publish-Subscribe | TLS and some OMG specific security methods. Vendor specific extensions also available. |
| Modbus | Message passing. Client-Server model. | Process Automation Industry, Power substation applications | Over serial interfaces (RS-232 / 485), over TCP/IP/ Ethernet, …. | bit-addressable and 16-bit word addressable, …. | Request / Response mode | Depends on other security mechanisms. |
| DNP3 | Client-Server model. | Electric (Power System) and water utility companies | Over serial interfaces (RS-232 / 485) and over TCP/IP/ Ethernet | Binary input / output, Analog input / output, Counter input | Request-Response model, Report-by-exception. | Mutual authentication using challenge response mechanisms |
| UPnP Cloud | Client-Server model | Home Automation | Above TCP (such as over XMPP/TCP or over HTTP (extensions) / TCP) | State variables of complex type expressed in XML. | Publish Subscribe | Uses SASL for authentication, TLS |
| ISA100.11a | Client Server model for ISA100.11a application layer | Process automation | Layer 2+ stacks over IEEE 802.15.4 type of networks | Analog, binary, block data (such as for waveform and firmware image) | Publish – Subscribe, Alert | Authentication, Confidentiality, Integrity |
| Wireless HART | Mater-Slave mode for IEEE802.15.4 based networks | Process automation | Layer 2+ stacks over IEEE 802.15.4 type of mesh / star networks | Fix and floating point numbers, bit and byte arrays, enumerations, time and text. | Command based application layer used in HART systems. Master-Slave mode and data publishing | Hop-by-hop (Layer 2) and end-to-end (network) layer security |

Table 1: IoT Protocols – Summary (I of II)

| Protocol / Traits | Synchronization mechanisms | QoS | Discovery | Multicast | SDOs |
| --- | --- | --- | --- | --- | --- |
| CoAP | No internal mechanism. (Could use NTP, IEEE 1588v2 and other mechanisms.) | Confirmable or non-confirmable message modes | Support for discovery. Uses concept of resource directory | Supports IP multicast | IETF |
| MQTT | Relies on external mechanisms | Three assurance levels for message delivery (deliver message at most once, exactly once, at least once) | No automatic discovery. | -- (Depends on external protocols) | OASIS |
| HTTP as RESTful API | No | Reliability via TCP | No | -- | It is an architecture style. Protocol part: W3C and IETF. |
| XMPP | No | Reliability over TCP | Service discovery | Syntax for sending messages to multiple recipients is supported | IETF, XEP |
| WebSockets | No | Reliability over TCP | No | -- | IETF, W3C |
| DDS | Relies on external mechanisms | 20+ QoS policies in terms of latency budget, reliability etc. Reliability provided by DDSI protocol. | Automatic discovery of publishers and subscribers | If DDS over UDP, one could use IP multicast | OMG |
| Modbus | For Modbus / TCP, NTP or some other protocol can be used. For Modbus over serial interfaces, mechanisms can be built on top of Modbus protocol. | TCP can provide reliability for Modbus-TCP. | No | No | Modbus.org |
| DNP3 | In-built time synchronization mechanism as part of DNP3 standard | Reliable data transfer through the use of timestamping | No | If using over UDP, one could use IP multicast | IEEE, DNP user group |
| UPnP Cloud | DCP level (like synchronized video playout) | Reliability via TCP or other protocols | Yes | Multicast events mapped to XMPP Pub-Sub | UPnP Forum |
| ISA100.11a | ISA networks need time synchronization mechanisms | Can be supported by different layers of the stack | Neighbor discovery | Depends on other layers of the stack | ISA, Uses components such as 6LoWPAN from IETF |
| Wireless HART | Time Synchronization needed | Can be supported | Neighbor discovery | Depends on other layers of the stack | IEC |

Table 2: IoT Protocols – Summary (II of II)

Performance:  Following should be noted:

- Some of these protocols (and associated systems) such as Modbus, DNP3, Wireless HART and ISA100.11a are optimized for industrial applications.

- CoAP and MQTT-SN  are simple and efficient protocols for IoT applications. Though MQTT runs over TCP, MQTT-SN (MQTT for Sensor Networks) runs over UDP.

- DDS offers good capabilities for the scenarios when there are several applications running on a node.

Note to Editor: It could be useful to do an extensive performance evaluation of some of these protocols though that does not appear to be in oneM2M agenda at present.  We could potentially cite references from public domain if we find extensive performance studies of these protocols.