| NPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | CSEBase Resource Type |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-06-11 |
| Abstract:* | This contribution proposed resource definition for CSEBase in Core Protocol TS. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed Resource Type definition of Resource Type CSEBase.

R03: Reflects given feedbacks at first  presentation in TP11 .

Checked CSEBase is  always a root of  path (see Table 9.6-1 in  Arch TS)

Additionally CSEBase is always nessesary to make any resource being uniquely addressable (See 9.1 General Principal in ArchTS).

All resource and associated attributes shall be uniquely addressable via their associated Universal Resource Identifiers (URI), consisting of:

a hierarchical URI based on the chain of child-parent relations;

a non-hierarchical URI made of a unique identifier addressable via the CSEBase.

Description for CRUD Operations are updated with reference of Generic Procedures 7.2.1.2.x.

---Change 1 STARTS---

### 7.3.1	Resource Type CSEBase

#### 7.3.1.1	Introduction

A <CSEBase> resource shall represent a CSE. This <CSEBase> resource shall be the root for all the resources that are residing on the CSE.

The detailed description can be found in clause 9.6.3 in Architecture TS([ref-Arch-TS]).

Table 7.3.1.1.1 Data Type Definition of cseBase

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Editor’s Note: Data Type definition should be posted after general agreement on technical issues

Table 7.3.1.1.2 Optionality of operations by reference point

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | N/A | N/A | N/A |
| Retrieve | M | M | M |
| Update | N/A | N/A | N/A |
| Delete | N/A | N/A | N/A |

Table 7.3.1.1.3 Data Types for resource specific attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| supportedResourceType | m2m:commaList | (TBD) | Read-Only |

Table 7.3.1.1.4 Reference of child resources

| Child Resource Type Name |  | Multiplicity | Ref . to in Resource Type Definition |  |
| --- | --- | --- | --- | --- |
| remoteCse(variable) |  | 0..n | 7.3.1 |  |
| node(variable) |  | 0..n |  |  |
| AE (variable) |  | 0..n | 7.3.3 |  |
| container(variable) |  | 0..n | 7.3.4 |  |
| group(variable) |  | 0..n | 7.3.11 |  |
| accessControlPolicy |  | 0..n |  |  |
| subscription(variable) |  | 0..n | 7.3.6 |  |
| mgmtCmd(variable) |  | 0..n | 7.3.13 | 9.6.16 |
| locationPolicy(variable) |  | 0..n | 7.3.8 | 9.6.10 |
| statsConfig(variable) |  | 0..n | 7.3.29 | 9.6.22 |
| statsCollect(variable) |  | 0..n | 7.3.31 | 9.6.24 |

7.3.1.2	Operations

This sub-clause describes cseBase  resource’s specific behaviour for CRUD operations.

7.3.1.2.1	Create

The <cseBase > resource shall not be created via API.

Receiver:  The Receiver shall execute the following steps in order.

Rcv-C-Rq-1.0		“Create an unsuccessful Response” with responseCode TBD (Method not allowed).

Rcv-C-Rq-2.0		“Send Response primitive”.

7.3.1.2.2	Retrieve

This procedure follows the Generic Resource RetrieveRequest Procedure specified in clause 7.2.1.2.2.

7.3.1.2.3	Update

The <cseBase > resource shall not be UPDATEed via API.

Receiver:  The Receiver shall execute the following steps in order.

Rcv-U-Rq-1.0		“Create an unsuccessful Response” with responseCode TBD (Method not allowed).

Rcv-U-Rq-2.0		“Send Response primitive”.

#### 7.3.1.2.4	Delete

The <cseBase > resource shall not be DELETEed via API.

Receiver:  The Receiver shall execute the following steps in order.

Rcv-D-Rq-1.0		“Create an unsuccessful Response” with responseCode TBD (Method not allowed).

Rcv-D-Rq-2.0		“Send Response primitive”.

--- Change 1 ENDS--

# Comments

Need to harmonize External ID Data Type (see also Table 6.2-1).

Which document shall be refered ?

reference to Arch TS should be highlighted to check its consistency

How we can describe  on appearance ( full data , name only, some other form of representation)

Reference info should be filled.

It seems no meaning to have, consider to remove this field from template