| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO 11.0 |
| Title:* | Response Status Clause |
| Source:* | Philip Jacobs, Cisco Systems, phjacobs@cisco.com, Josef Blanz, Qualcomm, jblanz@qti.qualcomm.com |
| Contact: |  |
| Date:* | 2014-05-30 |
| Abstract:* | This contribution proposes initial text and structure of a new Response Status clause, Ro1 reflects discussions during PRO 10.8 Ad hoc. |
| Agenda Item:* | TS-0004 contributions |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M Protocol Technical Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | To accept this text as a starting point for a new Response Status clause. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction: Following the concepts presented in PRO-2014-0208-Response_Status_Codes_Concepts during PRO 10.7, the following text is proposed to be added as a template/starting point for a new Response Status Codes (RSC) clause in TS-0004.

Suggested points for further discussion

- Classification enables the Originator to process the responses by first looking at the class. It is proposed to broadly classify responses per oneM2M “successful”, “unsuccessful” and “acknowledgement”, is this the best classification? An alternative could be to map them to a small set of actions that the Originator would take upon receiving the RSC.

- The use of ranges within each broad classification can be implemented in many ways. In the examples below, there are 2 ranges defined for the first release:

    - Current Release, which includes

      - Native oneM2M codes (inferred by TS0001)

      - Mapped Security codes (TS0003)

      - Mapped DM codes (TS0005, TS0006)

      - Mapped Underlying transport codes (TS0008, TS0009, TS0010)

    - Reserved for future use

However, this could be done differently, such as allocating vendor extension RSCs for the initial release, or by allocating a larger range for native oneM2M codes so it would be for all releases (first and subsequent).

- Exemplary RSCs have been included from the ARC TS to stimulate discussion, it is not clear from the ARC TS when additional resource-specific RSCs are needed relative to the generic flow RSCs. WG3 to determine the need for distinct or unique RSCs.

- It is not clear whether to keep protocol-specific RSCs, or to map them when possible to a single RSC. E.g. common underlying transport RSCs, common DM RSCs, or common across all RSCs.

# X	Response Status Codes

## X.1	Introduction

This clause specifies the allocated and reserved Response Status Codes (RSC) for a oneM2M System. This clause defines the framework for RSCs to support current and future oneM2M messages and transactions, current and future security procedures, external device management protocols, underlying transport protocols, interworking protocols, and vendor extensions.. The detailed mappings between the oneM2M message RSCs and security procedures and other protocols are specified in the oneM2M TS of each other protocol. These include:

- RSCs for security procedures in [TS0003]

- RSCs for OMA device management [TS0005]

- RSCs for BBF device management [TS0006]

- RSCs for CoAP underlying transport protocol [TS0008]

- RSCs for HTTP underlying transport protocol [TS0009]

- RSCs for MQTT underlying transport protocol [TS0010]

## X.2	RSC Data Type

## An RSC data type consists of a constrained integer and a list of strings. Each instance of an RSC is defined to include the constrained integer (numeric code) and mandatory list of zero or more strings (arguments) dependent upon the constrained integer. A single RSC instance is supported in each Response message. An error is a condition, which prevents the requested operation from being completed. The first error detected during validation procedures during an unsuccessful operation shall be reported via this single RSC instance. A warning is a condition that is associated with, but does not prevent the requested operation from being completed. The first warning detected during validation procedures during a successful operation shall be reported via this single RSC instance.

## X.3	RSC Framework Overview

## All RSCs are categorised as one of three classes: successful, unsuccessful or as an acknowledgement. For each response class as indicated in Table X.3-1, the framework includes two RSC Source partitions: “current” and “reserved for future”. RSCs are permanently and un-mutably allocated in the “current” partition. The order of allocation of RSCs from various sources within a partition is not specified. New RSCs shall be allocated by adding them to the “current” partition while reducing the “reserved for future” partition.  RSCs within the “current” partition are associated with a oneM2M release. For each subsequent oneM2M release, a new set of RSCs shall be allocated and added to the “current” partition.

## The term “native” is used to indicate that the RSC source originated as a result of a resource operation validation procedure before protocol mapping is applied.

Table X.3-1 - RSC Framework Overview

| Response Class | RSC Source | Numeric Code Range |
| --- | --- | --- |
| Successful | Current native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | 0000 - aaaa |
|  | Reserved for future native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | hhhh - iiii |
| Un-successful | Current native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | jjjj - kkkk |
|  | Reserved for future native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped Interworking codes mapped vendor extensions | rrrr - ssss |
| Acknowledgements | Current native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | tttt - uuuu |
|  | Reserved for future native oneM2M codes mapped security codes mapped device management codes mapped transport codes mapped interworking codes mapped vendor extensions | eeff - gghh |

## Editor’s Note: Other terms rather than “current” and “reserved for future” may be preferred e.g. first release and subsequent release.

## Editor’s Note: The alphanumeric bounds of the Numeric Code Range will be determined and updated just before the first release.

## X.4	Current Response Status Codes

## The tables in the following clauses specify the RSCs for oneM2M releases. Each RSC includes: a response status description, a numeric code, arguments, and applicable APIs (indicated by reference points). The response status description shall be unique within the set of response status descriptions for a release. Response status descriptions may be re-used among RSCs associated with different releases.

### X.4.1	Successful Responses

### The following tables specify the RSCs for successful responses for each release.

Table X.4.1-1 – RSCs for Successful Responses for Release 1

| Response Status Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
|  | 0000 |  |  |  |  |  |  |  |
|  | 0001 |  |  |  |  |  |  |  |
|  | 0002 |  |  |  |  |  |  |  |
|  | 0003 |  |  |  |  |  |  |  |
|  | 0004 |  |  |  |  |  |  |  |
|  | 0005 |  |  |  |  |  |  |  |
|  | 0006 |  |  |  |  |  |  |  |
|  | 0007 |  |  |  |  |  |  |  |
|  | 0008 |  |  |  |  |  |  |  |
|  | 0009 |  |  |  |  |  |  |  |

## Editor’s Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

### X.4.2	Un-successful Responses

### The following tables specify the RSCs for un-successful responses for each release.

Table X.4.2-1 – RSCs for Un-successful Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
| Location info not authorized | 0010 |  |  |  |  |  | X |  |
| Unsupported resource | 0011 | Resource URI |  |  | X | X |  |  |
| Unsupported attribute | 0012 | Attribute URI |  |  | X | X |  |  |
| Cannot forward, target not reachable | 0013 | Resource URI |  |  | X | X |  |  |
| Cannot forward, other reason TBD | 0014 | Resource URI |  |  | X | X |  |  |
| Create error - no privilege | 0015 | Resource URI |  |  | X | X |  |  |
| Create error – already exists | 0016 | Resource URI |  |  | X | X |  |  |
| Create error – missing mandatory parameter | 0017 | Missing parameter |  |  | X | X |  |  |
| Retrieve error - no privilege | 0018 | Resource URI |  |  | X | X |  |  |
| Retrieve error – does not exist | 0019 | Target URI |  |  | X | X |  |  |
| Update error - no privilege | 0020 | Resource URI |  |  | X | X |  |  |
| Update error – does not exist | 0021 | Resource URI |  |  | X | X |  |  |
| Update error – unacceptable contents | 0022 | Attribute URI |  |  | X | X |  |  |
| Delete error – does not exist | 0023 | Target URI |  |  | X | X |  |  |
| Delete error – no privilege | 0024 | Resource URI |  |  | X | X |  |  |
| Create delivery – not able to take on responsibility | 0025 |  |  |  | X | X |  |  |
| Create fanoutpoint – group request identifier exists | 0026 |  |  |  | X | X |  |  |
| Retrieve fanoutpoint – group request identifier exists | 0027 |  |  |  | X | X |  |  |
| Update fanoutpoint – group request identifier exists | 0028 |  |  |  | X | X |  |  |
| Delete fanoutpoint – group request identifier exists | 0029 |  |  |  | X | X |  |  |
| Create mgmtObj – not allowed | 0030 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj – already exists | 0031 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj – not reachable | 0032 | CSEBase URI |  |  | X | X |  |  |
| Create mgmtObj – memory shortage | 0033 | CSEBase URI |  |  | X | X |  |  |
| Retrieve mgmtObj – not found | 0034 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj – not reachable | 0035 | MgmtObj URI |  |  | X | X |  |  |
| Update mgmtObj – not found | 0036 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj – not reachable | 0037 | MgmtObj URI |  |  | X | X |  |  |
| Delete mgmtObj – not found | 0038 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj – not reachable | 0039 | MgmtObj URI |  |  | X | X |  |  |
| Execute mgmtObj – not found | 0040 | MgmtObj URI |  |  | X | X |  |  |
| Cancel execInstance – not cancellable | 0041 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Cancel execInstance – already complete | 0042 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance – not cancellable | 0043 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Delete execInstance – already complete | 0044 | Name of mgmtCmd resource |  |  | X | X |  |  |
| Retrieve CSEBase – format error | 0045 | CSEBase URI |  |  | X | X |  |  |
| CMDH rules –non compliant | 0046 |  |  |  |  |  |  |  |
|  | 0047 |  |  |  |  |  |  |  |
|  | 0048 |  |  |  |  |  |  |  |
|  | 0049 |  |  |  |  |  |  |  |

## Editor’s Note: The contents of this table are exemplary and are expected to be revised. In particular ARC discussions regarding UPDATE and attributes may impact argument1. Some of the exemplary RSCs may be equivalent and can be collapsed to fewer RSCs.

## Editor’s Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

### X.4.3	Acknowledgement Responses

### The following tables specify the RSCs for acknowledgement responses for each release.

Table X.4.3-1 - RSCs for Acknowledgement Responses for Release 1

| Description | Numeric Code | Argument1 | Argument2 | Argument 3 | Applicability |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  |  | Mca | Mcc | Mcn | Mcc' |
|  | 0140 |  |  |  |  |  |  |  |
|  | 0141 |  |  |  |  |  |  |  |
|  | 0142 |  |  |  |  |  |  |  |
|  | 0143 |  |  |  |  |  |  |  |
|  | 0144 |  |  |  |  |  |  |  |
|  | 0145 |  |  |  |  |  |  |  |
|  | 0146 |  |  |  |  |  |  |  |

## Editor’s Note: Since more RSCs may be added until the first release, the Numeric Codes will be finalized just before the first release.

# Comments

ARC 8.5.2

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 9.5.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.1

ARC 10.1.1.2.1

ARC 10.1.2

ARC 10.1.3

ARC 10.1.3

ARC 10.1.3

ARC 10.4

ARC 10.1.4

10.2.4.2

10.2.6.6

ARC 10.2.6.7

ARC 10.2.6.8

ARC 10.2.6.9

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.2

ARC 10.2.7.3

ARC 10.2.7.4

ARC 10.2.7.4

ARC 10.2.7.5

ARC 10.2.7.5

ARC 10.2.7.6

ARC 10.2.7.6

ARC 10.2.8.7

ARC 10.2.8.7

ARC 10.2.8.

ARC 10.2.8.9

ARC 10.2.9.2