| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO |
| Title:* | Resource Discovery Procedure |
| Source:* | LG Electronics |
| Contact: | Seongyoon Kim, LG Electronics, seongyoon.kim@lge.com |
| Date:* | 2014-05-31 |
| Abstract:* | Proposes resource discovery procedure |
| Agenda Item:* | PRO |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | Technical Specification – Core Protocol |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Approve the proposed change and integrate it into the TS document |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1	Rationale

This contribution proposes new clause for Access Control Mechanism

========================Start of 1st Change==========================

X.X.X.X.X Resource Discovery Request Procedure

A resource discovery is used to discover resources in a CSE. A Resource discovery request is done by sending RETRIEVE request with filterUsage, one of the filterCriteria parameters, configured as “discovery” and the request may include other filterCriteria prameters as well. A resource discovery request procedure shall be comprised of the following actions.

Originator: The Originator shall execute the following steps in order:

Orig-R-1.0	"Compose Request primitive".

•	The to parameter in the RETRIEVE Request indicates the root of where the discovery begins.

•	The RETRIEVE Request shall include filterUsage parameter in cn.

•	The RETRIEVE Request may include other parameters of filterCriteria in cn.

Orig-R-2.0	"Send a Request to the receiver CSE".

Orig-R-3.0	"Wait for Response primitive".

Receiver: the procedure of the Receiver written in the clause 7.2.1.2.2 (from Rcv-R-1.0 to Rcv-R-5.0) shall be the same as initial steps. The following steps are for the resource discovery specific procedure.

Rcv-R-6.0	"Find resources, which match all the configured filterCriteria in cn and which the Originator has “Discover” access right, under the addressed resource".

Rcv-R-7.0	"Create a successful Response".

Rcv-R-8.0	"Send Response primitive".