| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP11 |
| Title:* | Primitive templates and procedure outlines modification |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-05-31 |
| Abstract:* | This contribution proposes to modify the current general procedure in a more readable way by distinguishing communication modes by blockingSync, Non-blockingSync, Non-blockingAsync |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 The contribution only provides the general procedure for Create, the procedure for the other operation can be modified based on this in a similar way. A decision is asked to accept the other general procedure based on the consensus had on this contribution. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

7.2.1.2 Description of Generic Procedures

7.2.1.2.1 Generic Resource Create Request Procedure

A Generic Resource Create Request Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing these actions and providing additional steps.

The Originator shall execute the following steps in order:

BlockingSync:

Orig-C-1.0	"Compose Request primitive".

Orig-C-2.0	"Send a Request to the receiver CSE".

Orig-C-3.0	"Wait for Response primitive".

Non-BlockingSync:

Orig-C-1.0	"Compose Request primitive"

Orig-C-2.0	"Send a Request to the receiver CSE".

Orig-C-3.0	"Wait for Response primitive".

Orig-C-4.0	“Retrieve the result”

Non-BlockingAsync:

Orig-C-1.0	"Compose Request primitive"

Orig-C-2.0	"Send a Request to the receiver CSE".

Orig-C-3.0	"Wait for Response primitive".

Orig-C-4.0	“Wait for the Notify of the result”

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

The Receiver is the Hosting CSE of the targeted resource:

BlockingSync:

Rcv-C-1.0	“Check the syntax of received message”.

Rcv-C-1.1	“Check existence of the addressed resource”

Rcv-C-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-C-7.0	"Check validity of resource representation for the given resource type

Rcv-C-8.0	"Create the resource".

Rcv-C-9.0	If the resource is the announce-able resource type and the announceTo attribute is included, then the Receiver shall “Announce the resource”.

Rcv-C-10.0	"Create a successful Response".

Rcv-C-11.0	"Send Response primitive".

Non-blockingSync:

Rcv-C-1.0	“Check the syntax of received message”.

Rcv-C-1.1	“Check existence of the addressed resource”

Rcv-C-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-C-2.0	" Response primitive (ack) with the information of <request> resource”

Rcv-C-7.0	"Check validity of resource representation for the given resource type

Rcv-C-8.0	"Create the resource".

Rcv-C-9.0	If the resource is the announce-able resource type and the announceTo attribute is included, then the Receiver shall “Announce the resource”.

Rcv-C-12.0	“Update the result to the <request> resource”

Non-blockingAsync:

Rcv-C-1.0	“Check the syntax of received message”.

Rcv-C-1.1	“Check existence of the addressed resource”

Rcv-C-6.0	"Check authorization of the requesting entity based on accessControlPolicyID".

Rcv-C-2.0	"Response primitive (ack)”

Rcv-C-7.0	"Check validity of resource representation for the given resource type

Rcv-C-8.0	"Create the resource".

Rcv-C-9.0	If the resource is the announce-able resource type and the announceTo attribute is included, then the Receiver shall “Announce the resource”.

Rcv-C-12.0	“Notify the originator with the result of the operation”

The Receiver is not the Hosting CSE of the targeted resource:

Rcv-C-4.1 	“Re-targeting”

Rcv-C-4.2 	“Create and Send a Response primitive (ack)”.

Rcv-C-4.5 	“Wait for operational result”.

Rcv-C-4.6 	“Provide the received operational result to the Originator”.

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

Editor’s Note: BlockingSync, Non-blockingSync, Non-blockingAsync need to be further clarified.