| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP11 |
| Title:* | Primitive templates and procedure outlines modification |
| Source:* | Huawei Technologies Co., Ltd. |
| Contact: | Jiaxin Yin, Yinjiaxin@huawei.com |
| Date:* | 2014-05-31 |
| Abstract:* | This contribution proposes to modify the current general procedure in a more readable way by distinguishing communication modes by blockingSync, Non-blockingSync, Non-blockingAsync |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 The contribution only provides the general procedure for Create, the procedure for the other operation can be modified based on this in a similar way. A decision is asked to accept the other general procedure based on the consensus had on this contribution. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

7.2.1.2 Description of Generic Procedures

7.2.1.2.1 Generic Resource Create Request Procedure

A Generic Resource Create Request Procedure shall be comprised of the following actions. Additional actions specific to individual procedures may be listed in the respective sections by referencing these actions and providing additional steps.

The Originator shall execute the following steps in order:

BlockingSync:

- "Compose Request primitive".

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

Non-BlockingSync:

- "Compose Request primitive"

- "Send a Request to the receiver CSE".

- "Wait for Response primitive". The Response contains information about the <request> resource.

- “Compose Request primitive”, the Request shall be addressing the <request> resource responded from the Response in the former step 3.

- “Send a Request to the receiver CSE”. The Request is addressing the <request> resource.

- "Wait for Response primitive".

Non-BlockingAsync:

- "Compose Request primitive"

- "Send a Request to the receiver CSE".

- "Wait for Response primitive".

- “Receive the Notify of the result”

The Receiver shall execute the following steps in order. In case of error in any of the steps below, the Receiver shall execute "Create an unsuccessful Response" and then "Send Response primitive". The corresponding Response Code shall be included in the Response primitive.

Hosting CSE of the targeted resource for blocking requests:

  - “Check the syntax of received message”.

  - “Check existence of the addressed resource”

  - "Check authorization of the requesting entity based on accessControlPolicyID".

  - "Check validity of resource representation for the given resource type

  - "Create the resource".

  - “Announce the resource”.

  - "Create a successful Response".

  - "Send Response primitive".

Transit CSE of the targeted resource for blocking requests:

- “Check the syntax of received message”.

- “Re-targeting”

Hosting CSE for non-blocking synchronous requests:

- “Check the syntax of received message”.

- “Check existence of the addressed resource”

- "Check authorization of the requesting entity based on accessControlPolicyID".

- " Response primitive (ack) with the information of <request> resource”

- "Check validity of resource representation for the given resource type

- "Create the resource".

- “Announce the resource”.

- “Update the result to the <request> resource”

Hosting CSE for non-blocking asynchronous requests:

  - “Check the syntax of received message”.

  - “Check existence of the addressed resource”

  - "Check authorization of the requesting entity based on accessControlPolicyID".

  - "Response primitive (ack) with the information of <request> resource”

  - "Check validity of resource representation for the given resource type

  - "Create the resource".

  - “Announce the resource”.

  - “Notify the originator with the result of the operation”

Transit CSE for non-blocking synchronous requests:

- “Check the syntax of received message”.

- “Generate <request> resource based on the Request”

- " Response primitive (ack) with the information of <request> resource”

- “Re-targeting”

Transit CSE for non-blocking asynchronous requests:

- “Check the syntax of received message”.

- " Response primitive (ack)”

- “Re-targeting”

- “Notify the originator with the result of the Request”

Editor’s Note: These procedures and steps are FFS. Steps are pointer to the common operation section in TS-0004.

Editor’s Note: BlockingSync, Non-blockingSync, Non-blockingAsync need to be further clarified.