| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | More mapping of HTTP status codes |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-06-02 |
| Abstract:* | This contribution proposed to describe common operation mapping on HTTP binding |
| Agenda Item:* | HTTP Binding TS |
| Work item(s): | WI-0013 |
| Document(s) Impacted* | TS-0009 (HTTP Binding TS) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed change on TS-0009.

Reason for change

Common Operations should be specified in each protocol bindings. This contribution aimed to add some specification for HTTP-REST protocol binding.

—Change 1 STARTS—

Editor’s Note: following sections  are added after clause 6.2

## Common Operation Mapping

### Compose Request Primitive (Originator AE/CSE)

The originator AE or CSE, shall compose a Request message for HTTP-REST protocol mapping.

#### Setting Standard Headers and Parameters

The Originator shall compose Request message as specified in HTTP/1.1(RFC2616)[(ref-RFC2616)] unless further requirements in use of oneM2M compliant M2M System described below.

##### Request-URI

The Request-URI parameter shall be set with the equivalent of the address for to parameter.

##### From

The From parameter shall be set with the Originator’s either AE-ID or CSE-ID which is applicable.

##### Query String

The use of query string is described in clause (TBD).

Editor’s Note: Actual use of query string is FFS

##### Media Type

The Media Type shall be set with ‘application/onem2m-resource+xml’ or ‘application/onem2m-resource+json’ when oneM2M Resource Type is transferred.

#### Setting Private Extended Headers and Parameters

Editor’s Note: This clause shall be added if needed.

#### Setting Resource Content

Editor’s Note: detailed specification is FFS.

### Send a Request to the Receiver CSE (Originator AE/CSE)

The originator AE or CSE, shall send a composed Request message for HTTP-REST protocol mapping following section 6 of HTTP/1.1(see details in section 6 ‘Connections’ of RFC2616[(ref-rfc2616)]) .

—Change 1 ENDS—