| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#11 |
| Title:* | <locationPolicy> Resource-Type Specific Procedures |
| Source:* | LG Electronics, AT&T, LG U+ |
| Contact: | Hongbeom Ahn, Hongbeom.ahn@lge.com WANG, JIANRONG, jw8065@att.com Micheal HS Yang, hsyang@lguplus.com |
| Date:* | 2014-06-01 |
| Abstract:* | Description of <locationPolicy> resource-type specific procedure |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Core Protocol TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

This input contribution describes the specific procedure for <locationPolicy> resource type and relevant attributes definition.

### ----------------------- Start of text 1 -----------------------

## Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.X]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: “RESTful Network API for Terminal Location”, Version 1.0

[i.Y]	OMA-TS-MLP-V3_4-20130226-C: “Mobile Location Protocol”, Version 3.4

### ----------------------- End of text 1 -----------------------

### ----------------------- Start of text 2 -----------------------

### 7.3.8	Resource Type locationPolicy

#### 7.3.8.1		Introduction

The <locationPolicy> resource represents the method for obtaining and managing geographical location information of an M2M Node.

The detailed description can be found in the clause 9.6.10 in [6].

The resource specific attributes information is defined in the Annex A.

Table 7.3.20.1 Data Type Definition of locationPolicy

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Editor’s Note: Data Type definition should be posted after general agreement on technical issues

Table 7.3.20.1.2 Optionality of operations by reference point

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | O | O | O |
| Retrieve | O | O | O |
| Update | O | O | O |
| Delete | O | O | O |
| Notify | O | O | O |

#### 7.3.8.2	Operations

This sub-clause describes <locationPolicy> resource specific primitive behaviour for CRUD operations.

#### 7.3.8.2.1	Create

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.1.

Receiver: the procedure of the Receiver written in the clause 7.2.1.2.1 (from Rcv-C-1.0 to Rcv-C-11.0) shall be the same as initial steps. The following steps are the <locationPolicy> resource type specific procedure for CREATE operation.

Rcv-C-LP-1.0	After the successful creation of <locationPolicy> resource, the Hosting CSE shall create <container> resource where the actual location information will be stored and the resource shall contain cross-references for the both resources, locationContainerID attribute for the <locationPolicy> resource and locationID attribute for the <container> resource. The name of the created <container> resource shall be determined by the locationContainerID attribute if it is applicable.

Rcv-C-LP-2.0	Check the locationSource and locationUpdatePeriod attributes:

- If the locationSource attribute is set by ‘Network Based’ and locationUpdatePeriod attribute is set by any duration value (higher than 0 second), then continue with the next step (Rcv-C-LP-3.0)

- If the locationSource attribute is set by ‘Device Based’ and locationUpdatePeriod attribute is set by any duration value (higher than 0 second), then continue with the next step (Rcv-C-LP-4.0)

- If the locationSource attribute is set by ‘Sharing Based’ and locationUpdatePeriod attribute is set by any duration value (higher than 0 second), then continue with the next step (Rcv-C-LP-5.0)

Rcv-C-LP-3.0	The Hosting CSE shall retrieve the locationTargetID and locationServer attributes from the stored <location Policy> resource.

In case either the locationTargetID or locationServer attribute cannot be obtained, the hosting CSE shall reject the request with the error code.

Editor’s Note: The ‘Error code’ should be posted after general agreement.

Then, the Hosting CSE shall transform the location-acquisition request into Location Server request [i.X], using the attributes stored in <locationPolicy> resource. The Hosting CSE shall also provide default values for other required parameters (e.g., quality of position) in the Location Server request according to local policies.

The Hosting CSE shall send this Location Server request to the location server using, for example, OMA Mobile Location Protocol [i.Y] and OMA RESTful NetAPI for Terminal Location [i.X]. The location server performs positioning procedure based upon the Location Server request. Then continue with the step Rcv-C-LP-6.0.

Based on the period information, locationUpdatePeriod attribute, this step can be periodically repeated or the location server can only notify the Hosting CSE of location information that performs periodically.

Note: the location server performs the privacy control and only responds successfully if the positioning procedure is permitted.

Note: the detail information on how the Location Server request message is converted into OMA RESTful NetAPI for Terminal Location message is described in Annex X.

Rcv-C-LP-4.0	The Hosting CSE shall perform positioning procedure using location determination modules and technologies (e.g., GPS). Then continue with the step Rcv-C-LP-6.0.

Based on the period information, locationUpdatePeriod attribute, this step can be periodically repeated.

Note: the Hosting CSE can utilize the internal interface (e.g., System Call) to communicate with the modules and technologies. The detail procedure is out-of-scope.

Rcv-C-LP-5.0	The Hosting CSE shall collect information of topology of M2M Area Network using <node> resource and find the closest Node from the Originator that has registered with the Hosting CSE and has location information. The closest Node can be determined by the minimum hop based on the collected topology information.

- If the Hosting CSE can find the closest Node from the Originator, the location information of the closest Node shall be stored as the location information of the Hosting CSE into a <contentInstance> resource under the created <container> resource.

- If the Hosting CSE cannot find the closest Node from the Originator, the location information of the Hosting CSE shall be stored as the location information of the Hosting CSE into a <contentInstance> resource under the created <container> resource.

Rcv-C-LP-6.0	The Hosting CSE shall receive the corresponding response and transform it into a Response primitive.

- If the positioning procedure is failed, the Hosting CSE shall store a statusCode based on the error code in the locationStatus attribute in the created <locationPolicy> resource.

- If the positioning procedure is successfully complete which means that the Hosting CSE acquires the location information, The Hosting CSE shall store the acquired location information into a <contentInstance> resource under the created <container> resource.

Editor’s Note: The ‘Error code’ should be posted after general agreement.

#### 7.3.8.2.2	Retrieve

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.2.

Receiver: the procedure of the Receiver is the same as the clause 7.2.1.2.2.

#### 7.3.8.2.3	Update

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.3.

Receiver: the procedure of the Receiver is the same as the clause 7.2.1.2.3.

#### 7.3.8.2.4	Delete

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.4.

Receiver: the procedure of the Receiver written in the clause 7.2.1.2.4 (from Rcv-D-1.0 to Rcv-D-10.0) shall be the same as initial steps. A following step is the  <locationPolicy> resource type specific procedure for DELETE operation.

Rcv-D-LP-1.0	Once the <locationPolicy> resource is deleted, the Receiver shall delete the associated resources (e.g., <container>, <contentInstance> resources). If the locationSource attribute and the locationUpdatePeriod attribute of the <locationPolicy> resource has been set with appropriate value, the Receiver shall tear down the session. The specific mechanism used to tear down the session depends on the support of the Underlying Network and other factors.

### ----------------------- End of text 2 -----------------------

### ----------------------- Start of text 3 -----------------------

Editor’s Note: This input shall be included in the table A-1 in the annex A.

Annex A (Normative): Resource attributes

| ResourceType | Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| <locationPolicy> | locationSource | - | xs:nonNegativeInteger | 0 | 0=”Network Based”, 1=”Device Based” 2=”Sharing Based” |  |
| <locationPolicy> | locationUpdatePeriod | - | xs:duration | PT0S |  |  |
| <locationPolicy> | locationTargetId | - | m2m:nodeId | - |  |  |
| <locationPolicy> | locationServer | - | xs:anyURI | - |  |  |
| <locationPolicy> | locationContainerID | - | xs:anyURI | - |  |  |
| <locationPolicy> | locationContainerName | - | xs:string | - |  |  |

### ----------------------- End of text 3 -----------------------