| INPUT CONTRIBUTION |
| --- |
| Group Name:* | TP#11 |
| Title:* | Location Request on Mcn Reference Point |
| Source:* | LG Electronics, AT&T |
| Contact: | Hongbeom Ahn, Hongbeom.ahn@lge.com WANG, JIANRONG, jw8065@att.com |
| Date:* | 2014-06-01 |
| Abstract:* | This input contribution describes the information on location request by means of OMA-REST-NetAPI for Location Terminal when location request is used between CSE and NSE for network-based location acquisition. |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Core Protocol TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Introduction

This input contribution describes the information on location request by means of OMA-REST-NetAPI for Location Terminal when location request is used between CSE and NSE for network-based location acquisition.

### ----------------------- Start of text 1 -----------------------

## Informative references

Clause 2.2 shall only contain informative references which are cited in the document itself.

The following referenced documents are not necessary for the application of the present document but they assist the user with regard to a particular subject area.

[i.X]	OMA-TS-REST-NetAPI_TerminalLocation-V1_0-20130924-A: “RESTful Network API for Terminal Location”, Version 1.0

[i.Y]	“RESTful Network API for Notification Channel”, Open Mobile Alliance™, OMA-TS-REST_NetAPI_NotificationChannel-V1_0

### ----------------------- End of text 1 -----------------------

Annex X (Normative): Location Request

## Location Request is a means by which a CSE requests the geographical or physical location information of a target Node to the location server located in the Underlying Network over Mcn reference point. This annex describes only the case of location request when the attribute locationSource of <locationPolicy> resource type is set to Network Based. Please see the clause 7.3.8.

## The specific interface used for this request depends on the capabilities of the Underlying Network and other factors. This annex provides the interfaces for location request used for the communication between the CSE and the location server. The interfaces are following:

## X.1 - OMA-REST-NetAPI-Terminal Location Interface

# Editor’ Note: more interfaces for location request can be described in this annex.X.1	Location Request by means of OMA-REST-NetAPI-TerminalLocation Interface

## X.1.1	Introduction

## This OMA REST Network API for Terminal Location specification v1.0 [i.X] is generally used to open up service capabilities, especially location capability, in the underlying network toward applications. This clause introduces the resources types and procedures defined in [X] and used for the oneM2M-specified location request.

## X.1.2	Resource Structure of OMA NetAPI for Terminal Location

## When a CSE needs to request the geographical or physical location information of a target CSE or AE hosted in a M2M Node toward a location server located in the Underlying Network over Mcn reference point. The CSE shall request Terminal Location Query (see [X]).

The OMA REST NetAPI for Terminal Location allows applications to obtain information about geographical location of a terminal. In order to obtain location information, the it is proposed to use following two services of the Terminal Location API:  request in a single query toward a Location Server to get the current Terminal Location or  subscribe to notifications for periodic  location updates for this terminal.

## Since oneM2M system utilizes the two services mentioned above, this clause introduces the capabilities that is related to the services from OMA REST NetAPI for Terminal Location [X].

## Note: A CSE and a Node shall act as an application and a terminal respectively as described in [X].

The two capability used for oneM2M system location request are ‘Terminal location’ and ‘Periodic location notification subscriptions’. The table below describes the URL structure, data structure and mapping with CRUD operation of each resource.

| Capability | URL Base URL: | Resource Type | Operations |
| --- | --- | --- | --- |
|  |  |  | C | R | U | D |
| Terminal location | /location | TerminalLocation | no | return current location of the terminal | no | no |
| Periodic location notification subscriptions | /periodic | PeriodicNotificationSubscription (used for CREATE) | create new subscription | return all subscriptions | no | no |

## Based on the table above, two resource types, TerminalLocation and PeriodicNotificationSubscription, shall be used for the location request specified oneM2M system. The information of the resource types are described in the tables below. The table also contains the relevant attributes column that is correlated with <locationPolicy> resource type defined [6]. Only attributes that may be utilized by oneM2M system are described. For the detailed information, see the [X]

Table B.1.2-2	Resource Type Definition – TerminalLocation

| Attributes | OMA NetAPI Defined Type | Description | Relevant Attribute defined by oneM2M |
| --- | --- | --- | --- |
| Address | xsd:anyURI | Address of the terminal to which the location information applies | locationTargetID in the <locationPolicy> resource type |
| locationRetrievalStatus | common:RetrievalStatus | Status of retrieval for this terminal address. | locationStatus in the <locationPolicy> resource type |
| currentLocation | LocationInfo | Location of terminal. | Content in the <contentInstance> resource type |

Table B.1.2-3	Resource Type Definition – PeriodicNotificationSubscription

| Attributes | OMA NetAPI Defined Type | Description | Relevant Attribute defined by oneM2M |
| --- | --- | --- | --- |
| address | xsd:anyURI | Addresses of terminals to monitor | locationTargetID in the <locationPolicy> resource type |
| frequency | xsd:int | Maximum frequency (in seconds) of notifications (can also be considered minimum time between notifications) per subscription. | locationUpdatePeriod in the <locationPolicy> resource type |
| duration | xsd:int | Period of time (in seconds) notifications are provided for. If set to “0” (zero), a default duration time, which is specified by the service policy, will be used. If the parameter is omitted, the notifications will continue until the maximum duration time, which is specified by the service policy, unless the notifications are stopped by deletion of subscription for notifications. | locationUpdatePeriod in the <locationPolicy> resource type |

## X.1.3	Procedures for Terminal Location

## X.1.3.1		Request in a Single Query toward a Location Server

## This procedure shows how to request and return location for a M2M Node.

Figure B.1.2-1	Location Query

- A Hosting CSE requests location for a single terminal (Node) by means of OMA REST NetAPI for terminal location API. This request message shall contain terminal address and Request URL with the address of Location Server using RETRIEVE operation.

In this step, the TerminalLocation resource type described in the table-B.1.2-2 shall be used with RETRIEVE operation.

NOTE: GET operation shall be used for this RETRIEVE operation.

- The Location Server shall retrieve the location information of the terminal.

- After the successful retrieve, the Hosting CSE shall receive the location information.

## X.1.3.2		Subscribe to Notifications for Periodic Location Updates

## This procedure shows how to control subscriptions for periodic notifications about terminal location.

- A Hosting CSE creates a new periodic notification subscription for obtaining location information of a terminal periodically.

In this step, the PeriodicNotificationSubscription resource type described in the table-B.1.2-3 shall be used with UPDATE operation.

NOTE: POST operation shall be used for this CREATE operation.

- After the successful creation of subscription, the Hosting CSE shall receive the response.

- When the set up timer is expires, the location server shall notify the application of current location information.

In this step, the notification message shall be used as NOTIFY operation.

NOTE: Alternatively, the hosting CSE obtains the notifications using a Notification Channel [Y]. This is repeated at specific frequency (periodic information) when the CSE is not reachable.

NOTE: POST operation shall be used for this NOTIFY operation

- After the successful receiver of notification, the Hosting CSE shall send a response to the location server.

- Based upon the location configuration change by the Hosting CSE, it updates an individual subscription for periodic location notification.

In this step, the PeriodicNotificationSubscription resource type described in the table-B.1.2-3 shall be used with UPDATE operation.

NOTE: PUT operation shall be used for this UPDATE operation.