| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Stage 3 text for <mgmtCmd> |
| Source:* | InterDigital Communications |
| Contact: | catalina.mladin@interdigital.com |
| Date:* | 2014-05-31 |
| Abstract:* | Contribution proposes Stage 3 resource, primitive and procedure definitions for <mgmtCmd> |
| Agenda Item:* | 6. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### 7.3.15	<mgmtCmd> Resource

#### 7.3.15.1	Introduction

The <mgmtCmd> resource shall contain the following child resource and attributes.

Table 7.3.15.1.1 Data Type Definition of <mgmtCmd>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.15.1.2 Data Types for resource specific attributes

| Attribute Name | Data Type |
| --- | --- |
| description | xs:string |
| execReqArgs | m2m: AnyArgType |
| cmdType | m2m:cmdType |
| execEnable | xs: anyURI |

Table 7.3.15.1.3 Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <execInstance> | xs:anyURI | 9.6.17 |

#### 7.3.15.2	Resource Specific Procedures

This sub-clause describes <mgmtCmd> resource specific procedures for CRUD operations.

#### 7.3.15.2.1	Create

Primitive specific operation before Orig-C-1.0:

1: If the Originator is an ASN/MN-CSE (i.e. a remote entity), the Originator shall generate the <mgmtCmd> resource representation based on the information of management commands available on the remote entity.

#### 7.3.15.2.2	Retrieve

This procedure uses the Retrieve common operations detailed in section 7.2.2, without primitive specific actions.

#### 7.3.15.2.3	Update

If the Update primitive does not address the execEnable attribute of the <mgmtCmd> or the URI provided as the value of the execEnable , it results in update of all or part of the information of an existing <mgmtCmd> resource with the new attribute values. The procedure uses the common Update operations detailed in section 7.2.2, without primitive specific actions.

If the Update primitive for <mgmtCmd> does address the execEnable attribute of the <mgmtCmd>, it effectively triggers an Execute <mgmtCmd> procedure, see section 7.3.15.5.

#### 7.3.15.2.4	Delete

This procedure uses the Delete common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-D-3.0 and before Rcv-D-4.0:

- If the originator is IN-AE and the requested <mgmtCmd> resource includes pending management commands previously initiated on the remote entity and the pending command is cancellable, the Receiver shall perform the following steps, otherwise it shall continue to step Rcv-D-4.

- It shall identify the managed remote entity and the management protocol

- It shall establish a management session with the remote entity.

- It shall perform management command conversion and execution resulting in cancellation of the pending management commands.

- It shall delete the addressed resource.

#### 7.3.15.2.5	Execute

The execute operation is triggered by an Update primitive, if the primitive addresses the execEnable attribute of the <mgmtCmd> or the URI provided as the value of the execEnable. The procedure uses the Update common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-U-4.0 and before Rcv-D-5.0:

- The receiver shall identify the managed remote entity and the management protocol

- The receiver shall establish a management session with the remote entity.

- The receiver shall perform management command conversion and execution.

If the Update primitive for <mgmtCmd> does not address the execEnable attribute of the <mgmtCmd>, it effectively triggers an Update <mgmtCmd> procedure, see section 7.3.15.3.

### 7.3.16	<execInstance> Resource

#### 7.3.16.1	Introduction

The <execInstance> resource shall contain the following child resource and attributes.

Table 7.3.16.1.1 Data Type Definition of <execInstance>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.16.1.2 Data Types for resource specific attributes

| Attribute Name | Data Type |
| --- | --- |
| execStatus | m2m:execStatusType |
| execResult | xs:string |
| execDisable | xs:string |
| execTarget | xs:int |
| execMode | m2m:execModeType |
| execFrequency | xs:int |
| execDelay | xs:int |
| execNumber | xs:int |
| execReqArgs | m2m:execReqArgsListType |

#### 7.3.16.2	Resource Specific Procedures

This sub-clause describes <execInstance> resource specific procedures for CRUD operations.

#### 7.3.16.2.1	Cancel

The <execInstance> Cancel operation is triggered by an Update primitive, if the primitive addresses the execDisable attribute or the URI provided as the value of the execDisable. The procedure uses the Update common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-U-1.0 and before Rcv-U-2.0:

- It shall identify the managed remote entity and the management protocol and determine if the management operations associated with the <execInstance> are pending and cancellable.

- If the management operations are cancellable, it shall determine the management operations resulting in cancellation of the pending management commands.

- It shall establish a management session with the remote entity.

- It shall perform the management operations for cancelling the pending management commands

#### 7.3.16.2.2	Retrieve

This procedure uses the Retrieve common operations detailed in section 7.2.2, without primitive specific actions.

#### 7.3.16.2.3	Delete

This procedure uses the Delete common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-D-3.0 and before Rcv-D-4.0:

- If the originator is IN-AE and the addressed<execInstance> resource initiated management commands still pending on the remote entity and the pending command is cancellable, the Receiver shall perform the following steps, otherwise it shall continue to step Rcv-D-4.

- It shall identify the managed remote entity and the management protocol

- It shall establish a management session with the remote entity.

- It shall perform management command conversion and execution resulting in cancellation of the pending management commands.

- It shall delete the addressed <execInstance> resource.

### ----------------------- End of proposed text 1 -------------------------------------------

### -----------------------Start of proposed text 2 -------------------------------------------

##### x.x.x.	Types

<?xml version="1.0" encoding="UTF-8"?>

<schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://uri.etsi.org/m2m"

xmlns:tns="http://uri.etsi.org/m2m" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<element name="execReqArgs" type="tns:ExecReqArgsListType"/>

<complexType name="ExecReqArgsListType">

<sequence>

<element name="execReqArg" type="tns:ExecReqArgsType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ExecReqArgsType">

<choice>

<element name="Download" type="tns:DownloadArgsType"/>

<element name="SoftwareInstall" type="tns:SoftwareInstall ArgsType"/>

<element name="SoftwareUninstall" type="tns:SoftwareUninstallArgsType"/>

<element name="CancelTransfer" type="tns:CancelTransferArgsType"/>

<element name="Upload" type="tns:UploadArgsType"/>

<element name="Reboot" type="tns:RebootArgsType"/>

<element name="Reset" type="tns:ResetArgsType"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</choice>

</complexType>

<complexType name="DownloadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="Filesize" type="string"/>

<element name="TargetFile" type="string"/>

<element name="DelaySeconds" type="int"/>

<element name="SuccessURL" type="anyURI"/>

<element name="StartTime" type="dateTime"/>

<element name="StartTime" type="dateTime"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareInstallArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="UUID" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareUninstallArgsType">

<sequence>

<element name="UUID" type="string"/>

<element name="Version" type="string"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="CancelTransferType">

<sequence>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="UploadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="RebootArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ResetArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgsListType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgType">

<sequence>

<element name="name" type="string"/>

<element name="type" type="string"/>

<element name="value" type="anyType"/>

</sequence>

</complexType>

</schema>

### -----------------------End of proposed text 2  -------------------------------------------