| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Stage 3 text for <mgmtCmd> |
| Source:* | InterDigital Communications |
| Contact: | catalina.mladin@interdigital.com chonggang.wang@interdigital.com |
| Date:* | 2014-05-31 |
| Abstract:* | Contribution proposes Stage 3 resource, primitive and procedure definitions for <mgmtCmd> |
| Agenda Item:* | 6. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

### Major Updates in PRO-2014-0230R01

### Defined a few status code

### Updated Data Type table according to the latest TS-0004 draft v.0.4.3

### Completed two .xsd files for <mgmtCmd> and <execInstance>, respectively.

### Updated and clarified the description of operations for <mgmtCmd> and <execInstance>

### ----------------------- End of proposed text 1 -------------------------------------------

### 7.3.15	<mgmtCmd> Resource

#### 7.3.15.1	Introduction

The <mgmtCmd> resource shall contain the following attributes and child resource as illustrated in Table 7.3.15.1.2 and Table 7.3.15.1.3. The data type and default value of these attributes and child resources are included in the Tables.

Table 7.3.15.1.1 Data Type Definition of <mgmtCmd>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.15.1.2 Data Types for resource specific attributes

| Attribute Name | Data Type | Default | Value Restrictions | Notes |
| --- | --- | --- | --- | --- |
| description | xs:string | Not applicable | size: 256 |  |
| execReqArgs | m2m: execReqArgsListType | Not applicable | It depends on the value of cmdType |  |
| cmdType | m2m:cmdType | Not applicable | RESET, REBOOT, UPLOAD, DOWNLOAD, SOFTWAREINSTALL, SOFTWAREUNINSTALL |  |
| execEnable | xs: anyURI | Not applicable |  |  |
| execTarget | m2m:nodeID | Not applicable |  |  |
| execMode | m2m:execModeType | IMMEDIATEONCE | IMMEDIATEONCE, IMMEDIATEREPEAT, RANDOMONCE, RANDOMREPEAT |  |
| execFrequency | xs:duration | Not applicable |  |  |
| execDelay | xs:duration | 0 |  |  |
| execNumber | xs: nonNegativeInteger | 1 |  |  |

Table 7.3.15.1.3 Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| <execInstance> | xs:anyURI | 9.6.17 |

#### 7.3.15.2	Resource Specific Procedures

This sub-clause describes <mgmtCmd> resource specific procedures for CRUD operations.

#### 7.3.15.2.1	Create

This procedure uses the Create common operations detailed in section 7.2.2, without primitive specific actions. The Originator shall provide the <mgmtCmd> resource representation to the Receiver (e.g. IN-CSE). The Receiver may generate one of the following status codes and send it to the Originator.

- If the Originator provides an invalid cmdType value in the Create primitive, the Receiver shall generate the status code STATUS_INVALID_CMDTYPE.

- If the name/value entry in execReqArgs does not match the value of cmdType in the Create primitive, the Receiver shall generate the status code STATUS_UNMATCHED_ARGUMENTS.

- If name/value entries in execReqArgs do not contain mandatory arguments as required by cmdType, the Receiver shall generate the status code STATUS_INSUFFICIENT_ARGUMENTS

#### 7.3.15.2.2	Retrieve

This procedure uses the Retrieve common operations detailed in section 7.2.2, without primitive specific actions.

#### 7.3.15.2.3	Update

If the Update primitive does not address the execEnable attribute of the <mgmtCmd> or the URI provided as the value of the execEnable , it results in update of all or part of the information of an existing <mgmtCmd> resource with the new attribute values. The procedure uses the common Update operations detailed in section 7.2.2, without primitive specific actions.

- If the Originator attempts to update any attribute which is not allowed as described in Table 7.3.15.2.1, the Receiver shall generate the status code STATUS_REQUEST_DENIED.

- If the Originator attempts to update any attribute which is allowed as described in Table 7.3.15.2.1 but gives a not allowed value, the Receiver shall generate the status code STATUS_WRONG_VALUE.

If the Update primitive for <mgmtCmd> does address the execEnable attribute of the <mgmtCmd>, it effectively triggers an Execute <mgmtCmd> procedure, see section 7.3.15.2.5.

Table 7.3.15.2.1 Update operation for attributes of <mgmtCmd>

| Attributes | <mgmtCmd> State | Allowed Update Operation |
| --- | --- | --- |
| cmdType | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execReqArgs | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execTarget | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execMode | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execFrequency | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execDelay | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| execNumber | <mgmtCmd> is not enabled or it has no any <execInstance> child resource created. | Yes |
| cmdType | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execReqArgs | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execTarget | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execMode | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execFrequency | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execDelay | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |
| execNumber | <mgmtCmd> is enabled or it has <execInstance> child resource created. | No |

#### 7.3.15.2.4	Delete

This procedure uses the Delete common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-D-3.0 and before Rcv-D-4.0:

- If the Originator is IN-AE and the requested <mgmtCmd> resource includes pending management commands previously initiated on the managed entity (i.e. <mgmtCmd> resource has instantiated <execInstance> child resources and their execStatus is INITIATED or STARTED) and the pending command is cancellable, the Receiver shall perform the following steps, otherwise it shall continue to step Rcv-D-4.0.

- It shall identify the managed entity associated with each <execInstance> child resource which execStatus is INITIATED or STARTED and the management protocol. The execTarget attribute of the pending management command resource (i.e. <execInstance>) indicates the managed entity.

- It shall establish a management session with the identified managed entity.

- It shall perform management command conversion and execution resulting in cancellation of the pending management commands which were previously initiated on the managed entity. The Receiver shall convert the received Delete primitive to corresponding management operation for cancellation and execute it on the managed entity.

- The managed entity may report the following status codes to the Receiver: STATUS_REQUEST_UNSUPPORTED (cancellation operation is not supported at the managed entity), STATUS_REQUEST_DENIED (cancellation request as a general request is denied at the managed entity), STATUS_CANCEL_DENIED (cancellation request is not permitted at the managed entity in its current transfer state)._

- The Receiver shall delete the addressed resource and send the received status codes in the response to the Originator.

#### 7.3.15.2.5	Execute

The execute operation is triggered by an Update primitive, if the primitive addresses the execEnable attribute of the <mgmtCmd> or the URI provided as the value of the execEnable. The procedure uses the Update common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-U-4.0 and before Rcv-D-5.0:

- The Receiver shall identify the managed entity and the management protocol. The parentID or execTarget attribute of <mgmtCmd> indicates the managed entity.

- The Receiver shall automatically create an <execInstance> based on the <mgmtCmd> resource. The Receiver shall copy the following attributes from <mgmtCmd> to <execInstance>: execTarget, execMode, execFrequency, execDelay, execNumber, and execReqArgs. The execStatus of <execInstance> is set as INITIATED.

- The Receiver shall determine if the <mgmtCmd> shall be executed immediately or postponed according to the combination of execMode, execFrequency, execDelay, and execNumber. If the <mgmtCmd> shall be executed immediately (e.g. execMode is IMMEDIATEONCE), the following steps shall be performed; otherwise the following steps shall be postponed and skipped until the delay is expired (e.g. as indicated by execDelay).

- The Receiver shall establish a management session with the identified managed entity.

- The Receiver shall perform management command conversion and execution and set the execStatus attribute of <execInstance> to STARTED. If the Receiver cannot perform the command conversion successfully (e.g. execReqArgs does not have sufficient name/value pairs), the Receiver shall generate status code STATUS_CONVERSION_FAILURE.

- After receiving completion response from the managed entity, the Receiver shall set execStatus attribute of corresponding <execInstance> to FINISHED.

If the Update primitive for <mgmtCmd> does not address the execEnable attribute of the <mgmtCmd>, it effectively triggers an Update <mgmtCmd> procedure, see section 7.3.15.2.3.

### 7.3.16	<execInstance> Resource

#### 7.3.16.1	Introduction

The <execInstance> resource shall contain the following child resource and attributes.

Table 7.3.16.1.1 Data Type Definition of <execInstance>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.16.1.2 Data Types for resource specific attributes

| Attribute Name | Data Type | Default | Value Restrictions | Notes |
| --- | --- | --- | --- | --- |
| execStatus | m2m:execStatusType | INITIATED | INITATED, STARTED, FINISHED, CANCELLING, CANCELLED |  |
| execResult | xs:execResultType | Not applicable |  |  |
| execDisable | xs:anyURI | Not applicable |  |  |
| execTarget | m2m:nodeID | Not applicable |  |  |
| execMode | m2m:execModeType | IMMEDIATEONCE | IMMEDIATEONCE, IMMEDIATEREPEAT, RANDOMONCE, RANDOMREPEAT |  |
| execFrequency | xs:duration | Not applicable |  |  |
| execDelay | xs:duration | 0 |  |  |
| execNumber | xs:nonNegativeInteger | 1 |  |  |
| execReqArgs | m2m:execReqArgsListType | Not applicable |  |  |

#### 7.3.16.2	Resource Specific Procedures

This sub-clause describes <execInstance> resource specific procedures for CRUD operations.

#### 7.3.16.2.1	Update (Cancel)

The <execInstance> Cancel operation is triggered by an Update primitive, if the primitive addresses the execDisable attribute or the URI provided as the value of the execDisable. The procedure uses the Update common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-U-1.0 and before Rcv-U-2.0:

- The Receiver of this primitive shall identify the managed entity and the management protocol. The <execTarget> attribute indicates the managed entity.

- The Receiver shall check the cmdType attribute of <execInstance>’s parent resource (i.e. <mgmtCmd>) and the execStatus attribute of <execInstance> to determine if the management operation associated with the <execInstance> are pending (i.e. only if its execStatus attribute is INITIATED or STARTED) and/or cancellable. If the management operation is pending or not cancellable, the following steps shall be skipped.

- If the management operation associated with the <execInstance> is pending, the Receiver shall return the status code STATUS_CANCEL_DENIED.

- If the management operation associated with the <execInstance> is not cancellable, the Receiver shall return the status code STATUS_NON_CANCELLABLE.

- If the management operations are cancellable, the Receiver shall determine the management operations resulting in cancellation of the pending management commands which were previously initiated on the managed entity. The Receiver shall convert the received Update primitive to the corresponding command for cancellation and execute it on the managed entity. The execStatus attribute of <execInstance> is set as CANCELLING.

- The Receiver shall establish a management session with the remote entity.

- The Receiver shall perform the corresponding command for cancelling the pending management commands as denoted by the cmdType attribute on the managed entity.

  - The managed entity may report the following status codes to the Receiver: STATUS_REQUEST_UNSUPPORTED (cancellation request is not supported at the managed entity), STATUS_REQUEST_DENIED (cancellation request as a general request is denied at the managed entity), STATUS_CANCEL_DENIED (cancellation request is not permitted at the managed entity in its current transfer state).

- If the cancelling is successfully executed on the managed entity, the Receiver shall set execStatus of <execInstance> as CANCELLED.

#### 7.3.16.2.2	Retrieve

This procedure uses the Retrieve common operations detailed in section 7.2.2, without primitive specific actions.

#### 7.3.16.2.3	Delete

This procedure uses the Delete common operations detailed in section 7.2.2, with the following primitive specific operation after Rcv-D-3.0 and before Rcv-D-4.0:

- If the Originator is IN-AE and the addressed<execInstance> resource initiated management commands is still pending on the remote entity and the pending command is cancellable, the Receiver shall perform the following steps, otherwise it shall continue to step Rcv-D-4.

- The Receiver shall identify the managed entity and the management protocol. The execTarget attribute indicates the managed entity.

- The Receiver shall establish a management session with the managed entity.

- The Receiver shall perform management command conversion and execution resulting in cancellation of the pending and cancellable management commands which were previously initiated on the managed entity.

- The managed entity may report the following status codes to the Receiver: STATUS_REQUEST_UNSUPPORTED (cancellation REQUEST is not supported at the managed entity), STATUS_REQUEST_DENIED (cancellation request as a general request is denied at the managed entity), STATUS_CANCEL_DENIED (cancellation request is not permitted at the managed entity in its current transfer state).

- It shall delete the addressed <execInstance> resource and send the received status codes in the response to the Originator.

### ----------------------- End of proposed text 1 -------------------------------------------

### -----------------------Start of proposed text 2 -------------------------------------------

CDT-<<mgmtCmd>>-v1_0_0-<<20140610>>.xsd

##### x.x.x.	Types

<?xml version="1.0" encoding="UTF-8"?>

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<element name=”cmdType” type=”m2m:CmdType”>

<simpleType name="CmdType">

<restriction base="string">

<enumeration value="RESET"/>

<enumeration value="REBOOT"/>

<enumeration value="UPLOAD"/>

<enumeration value="DOWNLOAD"/>

<enumeration value="SOFTWAREUNINSTALL"/>

<enumeration value="SOFTWAREINSTALL"/>

</restriction>

</simpleType>

<element name=”execMode” type=”m2m:ExecModeType”>

<simpleType name="ExecNodeType">

<restriction base="string">

<enumeration value="IMMEDIATEONCE"/>

<enumeration value="IMMEDIATEREPEAT"/>

<enumeration value="RANDOMONCE"/>

<enumeration value="RANDOMREPEAT"/>

</restriction>

</simpleType>

<element name="execReqArgs" type="m2m:ExecReqArgsListType"/>

<complexType name="ExecReqArgsListType">

<sequence>

<element name="execReqArg" type="tns:ExecReqArgsType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ExecReqArgsType">

<choice>

<element name="Download" type="tns:DownloadArgsType"/>

<element name="SoftwareInstall" type="tns:SoftwareInstallArgsType"/>

<element name="SoftwareUninstall" type="tns:SoftwareUninstallArgsType"/>

<element name="Upload" type="tns:UploadArgsType"/>

<element name="Reboot" type="tns:RebootArgsType"/>

<element name="Reset" type="tns:ResetArgsType"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</choice>

</complexType>

<complexType name="DownloadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="Filesize" type="string"/>

<element name="TargetFile" type="string"/>

<element name="DelaySeconds" type="int"/>

<element name="SuccessURL" type="anyURI"/>

<element name="StartTime" type="dateTime"/>

<element name="StartTime" type="dateTime"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareInstallArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="UUID" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareUninstallArgsType">

<sequence>

<element name="UUID" type="string"/>

<element name="Version" type="string"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="UploadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="RebootArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ResetArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgsListType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgType">

<sequence>

<element name="name" type="string"/>

<element name="type" type="string"/>

<element name="value" type="anyType"/>

</sequence>

</complexType>

</schema>

### -----------------------End of proposed text 2  -------------------------------------------

### -----------------------Start of proposed text 3 -------------------------------------------

CDT-<<execInstance>>-v1_0_0-<<20140610>>.xsd

##### x.x.x.	Types

<?xml version="1.0" encoding="UTF-8"?>

<xs:schema xmlns="http://www.w3.org/2001/XMLSchema" targetNamespace="http://www.onem2m.org/xml/protocols"

xmlns:m2m="http://www.onem2m.org/xml/protocols" xmlns:xsi="http://www.w3.org/2001/XMLSchema-instance">

<element name=”execMode” type=”m2m:ExecModeType”>

<simpleType name="ExecNodeType">

<restriction base="string">

<enumeration value="IMMEDIATEONCE"/>

<enumeration value="IMMEDIATEREPEAT"/>

<enumeration value="RANDOMONCE"/>

<enumeration value="RANDOMREPEAT"/>

</restriction>

</simpleType>

<element name=”execStatus” type=”m2m:ExecStatusType”>

<simpleType name="ExecStatusType">

<restriction base="string">

<enumeration value="INITIATED"/>

<enumeration value="STARTED"/>

<enumeration value="FINISHED"/>

<enumeration value="CANCELLING"/>

<enumeration value="CANCELLED"/>

</restriction>

</simpleType>

<element name="execResult" type="m2m:ExecResultList"/>

<complexType name="ExecResultList">

<sequence>

<element name="execResultItem" type="tns:ExecResultItem" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ExecResultItem">

<sequence>

<element name="name" type="string"/>

<element name="value" type="anyType"/>

</sequence>

</complexType>

<element name="execReqArgs" type="m2m:ExecReqArgsListType"/>

<complexType name="ExecReqArgsListType">

<sequence>

<element name="execReqArg" type="tns:ExecReqArgsType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ExecReqArgsType">

<choice>

<element name="Download" type="tns:DownloadArgsType"/>

<element name="SoftwareInstall" type="tns:SoftwareInstallArgsType"/>

<element name="SoftwareUninstall" type="tns:SoftwareUninstallArgsType"/>

<element name="Upload" type="tns:UploadArgsType"/>

<element name="Reboot" type="tns:RebootArgsType"/>

<element name="Reset" type="tns:ResetArgsType"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</choice>

</complexType>

<complexType name="DownloadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="Filesize" type="string"/>

<element name="TargetFile" type="string"/>

<element name="DelaySeconds" type="int"/>

<element name="SuccessURL" type="anyURI"/>

<element name="StartTime" type="dateTime"/>

<element name="StartTime" type="dateTime"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareInstallArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="UUID" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="SoftwareUninstallArgsType">

<sequence>

<element name="UUID" type="string"/>

<element name="Version" type="string"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="ExecEnvRef" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="UploadArgsType">

<sequence>

<element name="FileType" type="string"/>

<element name="URL" type="anyURI"/>

<element name="Username" type="string"/>

<element name="Password" type="string"/>

<element name="AnyArg" type="tns:AnyArgsListType" minOccurs="0"/>

</sequence>

</complexType>

<complexType name="RebootArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="ResetArgsType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgsListType">

<sequence>

<element name="anyArg" type="tns:AnyArgType" minOccurs="0" maxOccurs="unbounded"/>

</sequence>

</complexType>

<complexType name="AnyArgType">

<sequence>

<element name="name" type="string"/>

<element name="type" type="string"/>

<element name="value" type="anyType"/>

</sequence>

</complexType>

</schema>

### -----------------------End of proposed text 3  -------------------------------------------