| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Request resource type definition |
| Source:* | QUALCOMM Incorporated (TIA) |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2014-06-02 |
| Abstract:* | This contribution proposes text for Resource Type request. |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

--------------------- Start of proposed modified text -------------------

### 7.3.10	Resource Type request

#### 7.3.10.1	Introduction

The <request> resource is used to represent information on locally issued requests (i.e. issued by an AE or CSE internal). This allows for robust synchronous and asynchronous request processing coping with various constraints on maximum blocking time. The use of this resource type is optional depending on the configuration. The detailed description can be found in clause 9.6.12 in Architecture TS.

Table 7.3.10.1.1 Data Type Definition of request

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.10.1.2 Optionality of operations by reference point

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | N/A | N/A | N/A |
| Retrieve | O | O | N/A |
| Update | N/A | N/A | N/A |
| Delete | O | O | N/A |

Table 7.3.10.1.3 Data Types for resource specific attributes

| Attribute Name | Data Type |
| --- | --- |
| operation | m2m:operation |
| target | xs:anyURI |
| originator | xs:anyURI |
| requestIdentifier | m2m:requestId |
| metaInformation | m2m:metaInformation |
| content | m2m:content |
| requestStatus | m2m:requestStatus |
| operationResult | m2m:operationResult |

Table 7.3.10.1.4 Reference of child resources

| Child Resource Type Name | Data Type ID | Ref. in ArchTS |
| --- | --- | --- |
| subscription (variable) | TBD | 9.6.8 |

#### 7.3.10.2	Resource Specific Procedure on CRUD Operations

This sub-clause describes request resource specific procedure on Resource Hosting CSE  for CRUD operations.

#### 7.3.10.2.1	Create

The <request> resource shall not be created via API.

Instead the <request> resource is created by the Registrar CSE as a result of any request issued by a Registree CSE or Registree AE of a Registrar CSE which contains the rt parameter in the request message and where rt is set to 'nonBlockingReqeustSynch' or 'nonBlockingRequestAsynch'. The Registrar CSE is the Hosing CSE for that <request> resource.

Receiver:  The Receiver shall execute the following steps in order.

Rcv-C-Rq-1.0		“Create an unsuccessful Response” with responseCode TBD (Method not allowed).

Rcv-C-Rq-2.0		“Send Response primitive”.

#### 7.3.10.2.2	Retrieve

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.2.

Receiver: the procedure of the Receiver is the same as the clause 7.2.1.2.2.

#### 7.3.10.2.3	Update

The <request> resource shall not be updated via API.

For a <request> resource explicit update requests shall not be supported. Changes in the attributes of a <request> resources can only be done by the Hosting CSE due to changes of the status of the associated non-blocking request that implied the creation of this <request> resource or due to reception of an operation result in response to the associated non-blocking request that implied the creation of this <request> resource.

Receiver: the Receiver shall execute the ollowing steps in order.

Rcv-U-Rq-1.0		“Create an unsuccessful Response” with responseCode TBD (Method not allowed).

Rcv-U-Rq-2.0		“Send Response primitive”.

#### 7.3.10.2.4	Delete

Originator: the procedure of the Originator is the same as the clause 7.2.1.2.4.

Receiver: the procedure of the Receiver is the same as the clause 7.2.1.2.4.