| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Stage 3 text for Resource Type <statsConfig> |
| Source:* | InterDigital |
| Contact: | Guang Lu, InterDigital, guang.lu@interdigital.com |
| Date:* | 2014-06-09 |
| Abstract:* | Contribution proposes Stage 3 resource, primitive and procedure definitions for <statsConfig> |
| Agenda Item:* | 7. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

––– Begin proposed text –––

### 7.3.29	Resource Type <statsConfig>

#### 7.3.29.1	Introduction

The <statsConfig> resource is used to store configuration data for collecting statistics for AEs. The <eventConfig> child resource is a mechanism for defining events that trigger statistics collection activity. Additional description of the <statsConfig> resource is contained in clauses 9.6.22 and 10.2.15 of oneM2M TS-0001 [6].

Table 7.3.29.1-1: Data Type definition of <statsConfig>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-statsConfig-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.29.1-2: Optionality of operations by reference point for <statsConfig>

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | M | N/A | N/A |
| Retrieve | M | N/A | N/A |
| Update | M | N/A | N/A |
| Delete | M | N/A | N/A |

Table 7.3.29.1-3: Data Types for resource specific attributes of <statsConfig>

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| None |

Table 7.3.29.1-4: Reference of child resources of <statsConfig>

| Child Resource Type Name | Data Type ID | Ref. to in Resource Type Definition |
| --- | --- | --- |
| <eventConfig> | list of xs:anyURI | 7.3.30 |
| <subscription> | list of xs:anyURI | 7.3.6 |

Editor’s note: How to represent multiplicity need to clarify.

#### 7.3.29.2	<statsConfig> resource-specific procedure on CRUD operations

##### 7.3.29.2.1	Create

This procedure follows the Generic Resource Create Request Procedure specified in clause 7.2.1.2.1, with the following <statsConfig> resource-specific updates.

Resource-specific operation before Orig-C-1.0:

- If event-based statistics collection will be used, the Originator shall generate the necessary number of representations of the <eventConfig> child resource to produce the desired combination of trigger conditions for the intended event. For example, one representation of <eventConfig> could have eventType set to “DATA OPERATION” and transactionType set to “RETRIEVE” and a second representation could have eventType set to “TIMER-BASED”, eventStart set to midnight tomorrow and eventEnd set to midnight of the day after tomorrow; the resulting configuration would be an event that would record all RETRIEVE operations for tomorrow’s calendar date for the collected entity specified in a <statsCollect> resource. See Table A-1 for value restrictions and default settings pertaining to the attributes of <eventConfig>.

Resource-specific operation before Rcv-C-5.0:

- If the To primitive parameter addresses a receiver CSE that is not an IN-CSE, then the request shall be rejected with a “STATUS_BAD_REQUEST”.

##### 7.3.29.2.2	Retrieve

This procedure follows the Generic Resource Retrieve Request Procedure specified in clause 7.2.1.2.2.

##### 7.3.29.2.3	Update

This procedure follows the Generic Resource Update Request Procedure specified in clause 7.2.1.2.3.

##### 7.3.29.2.4	Delete

This procedure follows the Generic Resource Delete Request Procedure specified in clause 7.2.1.2.4.

––– End proposed text –––