| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Stage 3 text for Resource Type <eventConfig> |
| Source:* | InterDigital |
| Contact: | Guang Lu, InterDigital, guang.lu@interdigital.com |
| Date:* | 2014-06-09 |
| Abstract:* | Contribution proposes Stage 3 resource definitions for <eventConfig> |
| Agenda Item:* | 7. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

––– Begin #1: New text proposal –––

### 7.3.30	Resource Type <eventConfig>

#### 7.3.30.1	Introduction

The <eventConfig> resource defines events that trigger statistics collection activity on an IN-CSE. Additional description of the <eventConfig> resource is contained in clauses 9.6.23 and 10.2.15 of oneM2M TS-0001 [6].

Table 7.3.30.1-1: Data Type definition of <eventConfig>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-eventConfig-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.30.1-2: Optionality of operations by reference point for <eventConfig>

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | M | N/A | N/A |
| Retrieve | M | N/A | N/A |
| Update | M | N/A | N/A |
| Delete | M | N/A | N/A |

Table 7.3.30.1-3: Resource-specific attributes of <eventConfig>

| Attribute Name | Presence in CREATE request | Presence in UPDATE request | Presence in Response | Description |
| --- | --- | --- | --- | --- |
| eventID | O | NP | M | see Table A-1 |
| eventType | M | M | M | see Table A-1 |
| eventStart | O | O | O | see Table A-1 |
| eventEnd | O | O | O | see Table A-1 |
| transactionType | O | O | O | see Table A-1 |
| dataSize | O | O | O | see Table A-1 |

Editor’s Note: Optionality of Attributes should be referred in Arch-TS or self-contained?

Table 7.3.30.1-4: Reference of child resources of <eventConfig>

| Child Resource Type Name | Data Type ID | Ref. to in Resource Type Definition |
| --- | --- | --- |
| <subscription> | list of xs:anyURI | 7.3.6 |

Editor’s note: How to represent multiplicity need to clarify.

#### 7.3.30.2	<eventConfig> resource-specific procedure on CRUD operations

##### 7.3.30.2.1	Create

This procedure follows the Generic Resource Create Request Procedure specified in clause 7.2.1.2.1.

##### 7.3.30.2.2	Retrieve

This procedure follows the Generic Resource Retrieve Request Procedure specified in clause 7.2.1.2.2.

##### 7.3.30.2.3	Update

This procedure follows the Generic Resource Update Request Procedure specified in clause 7.2.1.2.3.

##### 7.3.30.2.4	Delete

This procedure follows the Generic Resource Delete Request Procedure specified in clause 7.2.1.2.4.

––– End #1: New text proposal –––

––– Begin #2: Existing text change –––

Table A-1: Resource attributes

| ResourceType | Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| <eventConfig> | dataSize |  | xs:positiveInteger | None | TBD | Optional attribute. Provided only when eventType is set to “SIZE-BASED”. Sets a threshold for stored data size above which collection activity is triggered. |
| <eventConfig> | eventEnd |  | xs:dateTime | None | None | Optional attribute. Provided only when eventType is set to “TIMER-BASED”. |
| <eventConfig> | eventID |  | xs:string | None | None | Mandatory attribute. Uniquely identifies an event. |
| <eventConfig> | eventStart |  | xs:dateTime | None | None | Optional attribute. Provided only when eventType is set to “TIMER-BASED”. |
| <eventConfig> | eventType |  | xs:string | None | “DATA OPERATION”, “SIZE-BASED”, “TIMER-BASED” | Mandatory attribute. Defines a type of event that triggers collection activity. |
| <eventConfig> | transactionType |  | xs:string | None | “CREATE”, “RETRIEVE”, “UPDATE”, “DELETE”, “NOTIFY” | Optional attribute. Provided only when eventType is set to “DATA OPERATION”. |

––– End #2: Existing text change –––

# Comments

Unit for dataSize (e.g., byte, KB, MB)?