| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.0 |
| Title:* | Stage 3 text for Resource Type <statsCollect> |
| Source:* | InterDigital |
| Contact: | Guang Lu, InterDigital, guang.lu@interdigital.com |
| Date:* | 2014-06-09 |
| Abstract:* | Contribution proposes Stage 3 resource, primitive and procedure definitions for <statsCollect> |
| Agenda Item:* | 7. Contributions |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

––– Begin #1: text proposal –––

### 7.3.31	Resource Type <statsCollect>

#### 7.3.31.1	Introduction

The <statsCollect> resource controls the collection of statistics information on an IN-CSE. Information in an associated <eventConfig> resource shall be used by the IN-CSE or IN-AE to define specific event-related triggers. Additional description of the <statsCollect> resource is contained in clauses 9.6.24 and 10.2.15 of oneM2M TS-0001 [6].

Table 7.3.31.1-1: Data Type definition of <statsCollect>

| Data Type ID | File Name | Note |
| --- | --- | --- |
| Actual Data Type ID | CDT-statsCollect-v1_0_0-<<date of published>>.xsd | some note texts can be added here |

Table 7.3.31.1-2: Optionality of operations by reference point for <statsCollect>

| Operations | Mca | Mcc | Mcc’ |
| --- | --- | --- | --- |
| Create | M | N/A | N/A |
| Retrieve | M | N/A | N/A |
| Update | M | N/A | N/A |
| Delete | M | N/A | N/A |

Table 7.3.31.1-3: Data Types for resource specific attributes of <statsCollect>

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| statsCollectID | see Table A-1 | see Table A-1 |  |
| collectingEntityID | see Table A-1 | see Table A-1 |  |
| collectedEntityID | see Table A-1 | see Table A-1 |  |
| status | see Table A-1 | see Table A-1 |  |
| statModel | see Table A-1 | see Table A-1 |  |
| subscriberID | see Table A-1 | see Table A-1 |  |
| collectPeriod | see Table A-1 | see Table A-1 |  |
| eventID | see Table A-1 | see Table A-1 |  |

Table 7.3.31.1-4: Reference of child resources of <statsCollect>

| Child Resource Type Name | Data Type ID | Ref. to in Resource Type Definition |
| --- | --- | --- |
| <subscription> | list of xs:anyURI | 7.3.6 |

Editor’s note: How to represent multiplicity need to clarify.

#### 7.3.31.2	<statsCollect> resource-specific procedure on CRUD operations

##### 7.3.31.2.1	Create

This procedure follows the Generic Resource Create Request Procedure specified in clause 7.2.1.2.1, with the following <statsCollect> resource-specific updates.

Resource-specific operation before Orig-C-1.0:

- The Originator shall generate and populate a representation of the <statsCollect> resource to produce the desired collection scenario, with the exception of statsCollectID (which is populated by the IN-CSE). If statsModel is set to “EVENT-BASED” then the Originator shall provide a value for eventID that corresponds to an eventID value stored in a <statsConfig> resource (which defines the event triggers to be used). See Table A-1 for value restrictions and default settings pertaining to the attributes of <statsCollect>.

Resource-specific operation before Rcv-C-5.0:

- If the To primitive parameter addresses a receiver CSE that is not an IN-CSE, then the request shall be rejected with a “STATUS_BAD_REQUEST”.

Resource-specific operation before Rcv-C-9.0 and after Rcv-C-8.0:

- The receiver IN-CSE shall generate and store a unique (within the Service Provider domain) value for statsCollectID.

- If the status attribute is set to “ACTIVE”, the IN-CSE shall begin monitoring the conditions defined by the <statsCollect> resource and generating Service Statistics Collection Records as the conditions are met.

##### 7.3.31.2.2	Retrieve

This procedure follows the Generic Resource Retrieve Request Procedure specified in clause 7.2.1.2.2.

##### 7.3.31.2.3	Update

This procedure follows the Generic Resource Update Request Procedure specified in clause 7.2.1.2.3.

Resource-specific operation before Rcv-U-9.0 and after Rcv-U-8.0:

- If the status attribute is set to “ACTIVE”, the IN-CSE shall begin monitoring the conditions defined by the <statsCollect> resource and generating Service Statistics Collection Records as the conditions are met.

- If the status attribute is set to “INACTIVE”, the IN-CSE shall stop monitoring the conditions defined by the <statsCollect> resource.

##### 7.3.31.2.4	Delete

This procedure follows the Generic Resource Delete Request Procedure specified in clause 7.2.1.2.4.

––– End #1: text proposal –––

––– Begin #2: text change –––

Table A-1: Resource attributes

| ResourceType | Attribute Name | Short Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- | --- | --- |
| <statsCollect> | collectedEntityID |  | m2m:id | None | Valid entity ID | Mandatory attribute. Unique ID of entity whose statistics will be collected (e.g., AE-ID, CSE-ID) |
| <statsCollect> | collectingEntityID |  | m2m:id | None | Valid entity ID | Mandatory attribute. Unique ID of entity requesting the collection of statistics (e.g., AE-ID, CSE-ID) |
| <statsCollect> | collectPeriod |  | xs:string | None | “ANNUAL”, “MONTHLY”, “WEEKLY”, “DAILY | Optional attribute; mandatory if statsModel is set to “SUBSCRIBER-BASED”. Defines the statistics collection period. |
| <statsCollect> | eventID |  | xs:string | None | see entry for <eventConfig> | Optional attribute; mandatory if statsModel is set to “EVENT-BASED”. Corresponds to an eventID attribute in an <eventConfig> resource that defines a specific event for collection. |
| <statsCollect> | statModel |  | xs:string | None | “EVENT-BASED”, “SUBSCRIBER-BASED” | Mandatory attribute. Identifies a collection model. |
| <statsCollect> | statsCollectID |  | m2m:id | None | TBD | Mandatory attribute. Unique ID (within SP domain) for each instance of collected statistics |
| <statsCollect> | status | ?? | xs:string | None | “ACTIVE”, “INACTIVE” | Mandatory attribute. Indicates the status of the current rule. |
| <statsCollect> | subscriberID |  | m2m:id | None | Valid M2M-Sub-ID | Mandatory attribute. Set to M2M-Sub-ID for collected entity. |

––– End #2: text change –––

# Comments

Unclear what is being asked for in this column.

Unclear if this type is appropriate or if new/different type is needed.