| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | MQTT Binding Basic Procedure for request-response messages |
| Source:* | KETI, IBM |
| Contact: | Jaeho Kim, Yong-Suk Park, Sung-Chan Choi, JaeSeung Song ({jhkim, yspark, csc}@keti.re.kr, jssong@sejong.ac.kr) Peter Niblett (peter_niblett@uk.ibm.com) |
| Date:* | 2014-06-11 |
| 31Abstract:* | This document proposes MQTT binding basic procedure for the request-response message with oneM2M architecture. |
| Agenda Item:* | MQTT Binding TS |
| Work item(s): | WI-0014 |
| Document(s) Impacted* | TS-0010 (MQTT Protocol Binding) |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG3 members should agree on proposal |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

1. Introduction

This document proposes MQTT binding basic procedure for the request-response messages in oneM2M architecture. This is related to the Protocol Binding in section 6 of TS-0010.

### -----------------------------Start of change 1---------------------------------

## Connecting to MQTT

- In order to communicate, the two client parties (AE and CSE or CSE and CSE) shall connect to a common MQTT server. The MQTT server shall be hosted in one of the two nodes or shall exist as an independent external entity, following one of the configuration patterns shown in clause 5.2

NOTE: Other configuration patterns are FFS.

Once each party has located the address of the MQTT server, it then connects to it using the standard MQTT CONNECT protocol packet. The following additional considerations apply:

- The CONNECT packet contains a Client Id as described in section A.3.2. The Client Ids have to be unique at least among all clients that connect to a given MQTT server instance (this is a requirement imposed by the MQTT protocol). This condition will be satisfied if an AE uses its AE-ID and a CSE uses its CSE-ID. See Clause 7 of TS-0001 [2] for a discussion of these Identifiers. The prefix A:: or C:: shall be added to the ID to show whether it is an AE-ID or a CSE-ID as these ID spaces are not distinct.

- A client shall set the “Clean Session” flag in the CONNECT packet to false. This means that MQTT Session state related to that client will be retained by the MQTT Server in the event of a disconnection (deliberate or otherwise) of that client.

- A client shall not set the “Will Flag”, so Will Messages are not enabled

- A client may choose to provide a non-zero MQTT KeepAlive value or to provide a KeepAlive of 0 (this disables the MQTT KeepAlive)

NOTE: An Infrastructure Provider might wish to specify and enforce a policy that sets a lower bound on the KeepAlive that can be used on portions of its network. The mechanisms for this are FFS.

- The MQTT server may require that a client provides a User Name and a password (or other credential). For more information see Clause 7.

NOTE: We might want to use the Will Message to allow a client’s connection status to be tracked. This is FFS.

NOTE: Also FFS is a discussion of connection strategy, for example a client might choose to keep the MQTT connection open permanently (restarting it as soon as possible after any unforeseen connection loss), it might choose to connect only when it wants to act as an Originator, or it might choose to connect on some kind of schedule.

Once a client has connected to the MQTT server it can then communicate (subject to authorisation policies) with any other client connected to its server. There is no need for it to create another connection if it wants to communicate with a different counter-party.

When a client determines that it no longer wishes to participate in an MQTT Session with its MQTT Server it shall perform the following steps:

- Disconnect from that server, if it is currently connected

- Reconnect with the cleanSession flag set to true

- Disconnect again

These steps delete any state that the MQTT server might be holding on behalf of the client.

## Sending and Receiving Messages

### 6.2.1 	Request and Response Messages

An MQTT Control Packet consists of up to three parts: a fixed header, a variable header, a payload. The control packet format is depicted in Figure 6.2.1-1. Since MQTT does not have a data model to describe or constrain the content of its Application Message payloads (to that extent it is similar to a TCP socket), Mca and Mcc request messages shall be serialized into XML or JSON following the serialization process defined in the Core Protocol specification [3].

Figure 6.2.1-1 Message format of MQTT Control Packet

The fixed header includes information about the packet type, flags specific to packet type and the packet length. Figure 6.2.1-2 shows the fixed header’s structure.

Figure 6.2.1-2 Fixed header structure

The packet type field in Figure 6.2.1-2 is used to define the MQTT Control packet type. It is a 4-bit field which possible values are listed in the Table 6.2.1-1. When oneM2M Request/Response message is bound to MQTT payload, its packet type shall have value 3 i.e. the Request/Response message is delivered in an MQTT PUBLISH packet.

# Table 6.2.1-1: MQTT Control Packet Types

| Reserved | 0 | Reserved for future use |
| --- | --- | --- |
| CONNECT | 1 | Client request to connect to server |
| CONNACK | 2 | Connect acknowledgement |
| PUBLISH | 3 | Publish message |
| PUBACK | 4 | Publish message acknowledgement |
| PUBREC | 5 | Publish received (QoS=2) |
| PUBREL | 6 | Publish release (QoS=2) |
| PUBCOMP | 7 | Publish complete (QoS=2) |
| SUBSCRIBE | 8 | Client subscribe request |
| SUBACK | 9 | Subscribe acknowledgement |
| UNSUBSCRIBE | 10 | Client unsubscribe request |
| UNSUBACK | 11 | Unsubscribe acknowledgement |
| PINGREQ | 12 | Ping request |
| PINGRESP | 13 | Ping response |
| DISCONNECT | 14 | Client disconnection request |
| Reserved | 15 | Reserved for future use |

Figure 6.2.1-3 Flags for PUBLISH packet

Figure 6.2.1-3 shows the flags specific to MQTT PUBLISH packet. The QoS field represents the QoS level of the PUBLISH packet with possible values of 1,2, and 3. However, since oneM2M messages are idempotent, they should be sent with MQTT QoS 1.

Note: MQTT packet are subjected to a theoretical maximum size of 256M, but it is good practice not to send packets that are bigger than a few Megabytes. If a larger amount of data needs to be sent, it should be segmented into multiple packets.

NOTE: This is FFS and is something that might need to be addressed in the Core Protocol specification

### 6.2.2 	Sending a Request

A request is transmitted by sending it as an MQTT PUBLISH protocol packet to the MQTT Server. It uses a Topic that identifies the Receiver of the request. The precise structure of this Topic is FFS, but an initial suggestion is:

/oneM2M/req/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the target resource (it is assumed that this includes the AE or CSE id)

- “req” is a literal string identifying this as a request.

As described in 6.2.1, MQTT payload is used to bind oneM2M Request message over Mca/Mcc with MQTT protocol. An example payload configuration for a request message in JSON may have the following values.

{“op”: “RETRIEVE”, “fr”: “AE-ID”, “to”: “CSE-ID/resource”, “ri”: “xxx”, “cn”: “xxx”, “ty”: “xxx”}

- op: operation (CRUDN)

- fr: ID of the Originator (either the AE or CSE)

- to: URI of the target resource

- ri: request identifier

- cn: attributes of the resource / information(data, reference) to be provided by Originator

- ty: type of resource to be created

Figure 6.2.2-1 Request message structure

NOTE: It might be useful to include some other components in the topic name, such as the Operation type. In particular it might be useful to include a <fr> field for security purposes. This is FFS

### 6.2.3 	Listening for and responding to a Request

A Receiver listens for requests arriving via MQTT by subscribing to its Topic (as described in the previous section).

When it receives a request, the receiver shall check the request expiration timestamp (if any) contained in the request, since it is possible that that time might have passed while the message was being stored by MQTT.

It then transmits a response by sending an MQTT PUBLISH packet to a response topic. This takes the form

/oneM2M/resp/<to>

- “oneM2M” is a literal string identifying the topic as being used by oneM2M

- <to> is the URI of the originator of the request (or the rd information from the request)

- “resp” is a literal string identifying this as a response.

The originator (or other interested party) must subscribe to this topic if it is to see the response.

As described in 6.2.1, MQTT payload is used to bind oneM2M Request message over Mca/Mcc with MQTT protocol. An example payload configuration for a response message in JSON may have the following values.

{“fr”: “CSE-ID”, “to”: “AE-ID”, “ri”: “xxx”, “cn”: “xxx”, “rs”:“Success”}

- rs: operation response

- ri: request identifier

- cn: contents to be transferred

Figure 6.2.3-1 Response message structure

### 6.2.4 	Request/Response Message Flow

6.2.4.1 Subscription to resource based case

Figure 6.2.4.1-1 Initiating Process in MQTT binding

In MQTT protocol, each client shall subscribe to the MQTT server to receive messages. As shown in Figure 6.2.4.1-1, the AE or CSE initiates MQTT binding process by passing the URI of its resources to the MQTT client. After the MQTT client receives the message, it tries to connect to the MQTT server. In this process, the URI of the resources are used as client identifiers within the MQTT CONNECT packet.

After the MQTT client successfully connects to the server, each MQTT client shall subscribe to the MQTT server. In this process, the URI of the resource is used as the topic name within the MQTT SUBSCRIBE packet. The full topic names subscribed to are “oneM2M/req/ID/resource” and “oneM2M/resp/ID/resource”. Therefore, AE or CSE receives messages if the request/response messages are published with oneM2M/req/ID/resource and oneM2M/resp/ID/resource as topic name.

Figure 6.2.4.1-2 Request/Response message delivery over MQTT

Figure 6.2.4.1-2 illustrates the request/response message delivery over MQTT protocol between AE and CSE via Mca reference point in oneM2M. The message flow is as follows.

In this scenario, AE wants to send a Request message to the registered CSE. After that, the MQTT client of the AE send MQTT PUBLISH packet to the MQTT server with “oneM2M/req/CSE-ID/resource” as the topic name. The MQTT PUBLISH packet includes {“op”, “fr”, “to”, “ri”, “cn”, “ty”} and any other optional message parameters in its payload.

After the MQTT server receives the MQTT PUBLISH packet from the MQTT client, the server refers to the topic name and delivers the message to the intended MQTT client. Finally, the MQTT client delivers the message to the CSE.

Regarding the Response message, the MQTT messages are sent using CSE-ID/AE-ID as topic. In order to send a Response message to the requestor, the CSE uses the “fr” information from the received request message and sends an MQTT PUBLISH packet to the MQTT server with “oneM2M/resp/AE-ID” as the topic name in this scenario. The MQTT PUBLISH packet includes {“rs”, “ri”, “cn”} and any other optional message parameters in its payload.

Similar to the request message delivery from AE to CSE, the MQTT server delivers the published packet to the intended MQTT client by referring to the topic name. Finally, AE receives the response message from the MQTT client.

6.2.4.2 Subscription to AE/CSE based case

Figure 6.2.4.2-1 Initiating Process in MQTT binding

In MQTT protocol, each client shall subscribe to the MQTT server to receive messages. As shown in Figure 6.2.4.2-1, AE or CSE initiates MQTT binding process by passing its AE-ID/CSE-ID to the MQTT client. After the MQTT client receives the message, it tries to connect to the MQTT server. In this process, the AE-ID/CSE-ID is used as client identifier within the MQTT CONNECT packet.

After the MQTT client successfully connects to the server, each MQTT client subscribes to the MQTT server. In this process, AE-ID/CSE-ID is used as topic name within the MQTT SUBSCRIBE packet. The full topic names subscribed to are “oneM2M/req/ID” and “oneM2M/resp/ID”. Therefore, AE or CSE receives messages if the request/response messages are published with oneM2M/req/ID and oneM2M/resp/ID as topic name.

Figure 6.2.4.2-2 Request/Response message delivery over MQTT

Figure 6.2.4.2-2 illustrates the request/response message delivery over MQTT protocol between AE and CSE via Mca reference point in oneM2M. The message flow is as follows.

In this scenario, the AE wants to send a Request primitive to the Registrar CSE. After that, the MQTT client of the AE sends a Publish message to the MQTT server with “oneM2M/req/CSE-ID” as the topic name. The MQTT Publish packet includes {“op”, “fr”, “to”,”ri”, “cn”, “ty”} and any other optional message parameters in its payload.

After the MQTT server receives the MQTT PUBLISH packet from the MQTT client, the server refers to the topic name and delivers the packet to the intended MQTT client. Finally, the MQTT client delivers the packet to the CSE.

Regarding the Response message, the message flow is backwards compared to the Request message flow. In order to send a Response message to the requestor, the CSE uses the “fr” information from the received Request message and sends an MQTT PUBLISH packet to the MQTT server with “oneM2M/resp/AE-ID” as the topic name. The MQTT PUBLISH packet includes {“rs”, “ri”, “cn”}and any other optional message parameters in its payload.

Similar to the Request message delivery from AE to CSE, the MQTT server delivers the published message to the intended MQTT client by referring to the topic name. Finally, AE receives the Response message from the MQTT client.

### -----------------------------End of change 1---------------------------------