| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | Response Code Mapping |
| Source:* | Hitachi, |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-06-12 |
| Abstract:* | This contribution proposes CoAP protocol binding details about Response code mapping. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

## 6.3	Response Codes Mapping

6.3.1 CoAP Response Code to ResponseConfirm PrimitiveIf the CoAP response code is in the range 2.01 to 2.05, then the response shall be considered as a successful case.

| CoAP Response Code | Description | Note |
| --- | --- | --- |
| Success 2.xx | 2.01 Created |  |  |
|  | 2.02 Deleted |  |  |
|  | 2.03 Valid |  |  |
|  | Changed |  |  |
|  | 2.05 Content |  |  |

If the CoAP response code is in the range of 4.00 to 4.15 or 5.00 to 5.05, then the response shall be considered as unsuccessful. Additional information about the error should be included.

| CoAP Response Code | Description | Note |
| --- | --- | --- |
| Client Error 4.xx |  | Additional information about the error |
| Server Error 5.xx |  | Additional information about the error |

## 6.3.2 Response Primitive to CoAP Response

The response primitive shall be correlated to the corresponding request primitive and the following rules shall be followed:

- The CoAP response shall be correlated to the CoAP request corresponding to the request primitive.

- The statusCode shall be the status code from the primitive.

- If the response primitive has any resource representation, this shall be transported in the payload of theCoAP response.

- The CoAP message shall be sent to issuer over the data transfer function.

- The statusCode of the response for successful and unsuccessful responseConfirm shall be set according to thetable below. For the successful operations, STATUS_OK shall be mapped to the CoAP statusCode corresponding to the specific operation.

Table x.x Successful Cases

| Status Code | Status Code of CoAP |
| --- | --- |
| "STATUS_OK" | 2.02. 2.03, 2.04, 2.05 |
| "STATUS_CREATED" | 2.01 |
| "STATUS_ACCEPTED" | ACK |

Table x.x Unsuccessful Cases

| Status Code | Status Code of CoAP |
| --- | --- |
| "STATUS_NOT_FOUND" |  |

--------------------- End of proposed modified text ---------------------