| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO#11.8 |
| Title:* | TS-0004 Annex.D Cleanup |
| Source:* | QUALCOMM Incorporated (TIA) |
| Contact: | Nobu Uchida, nuchida@qti.qualcomm.com |
| Date:* | 2014-07-14 |
| Abstract:* | This contribution proposes changes to Annex.D to address Editor’s Notes for chdm-related management instances and alignment with the latest TS-0001 v0.8.0. |
| Agenda Item:* | Contribution |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Protocol Specification |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Agree for inclusion in TS-0004 |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposes moditications to Annex D. The modifications are;

- Changed the Annex title based on the TS-0001 Annex D

- References to Arc TS are corrected

- Missing <mgmtObj> resource instances are added

  - firmware

  - software

  - memory

  - areaNwkInfo

  - areNwkDeviceInfo

  - battery

  - deviceInfo

  - deviceCapability

  - reboot

  - eventLog

- Common attribute table based on the new template is added

- Resource-specific attributes tables based on the new template are added

- Data types, defaults values have been filled

- Removed Editor’s Notes from the old template.

--------------------- Start of proposed modified text -------------------

(Normative): <mgmtObj> Resource Instances

## Void

## Resource firmware

## Editor’s Note: This section needs to be assigned.

## Resource software

Editor’s Note: This section needs to be assigned.

## Resource memory

Editor’s Note: This section needs to be assigned.

## Resource areaNwkInfo

Editor’s Note: This section needs to be assigned.

## Resource areaNwkDeviceInfo

Editor’s Note: This section needs to be assigned.

## Resource Type battery

Editor’s Note: This section needs to be assigned.

## Resource Type deviceInfo

Editor’s Note: This section needs to be assigned.

## Resource Type deviceCapability

Editor’s Note: This section needs to be assigned.

## Resource Type reboot

Editor’s Note: This section needs to be assigned.

## Resource Type eventLog

Editor’s Note: This section needs to be assigned.

## Resource cmdhPolicy

The Resource [cmdhPolicy] represents a set of rules defining which CMDH parameters will be used by default when a request issued by a local originator contains the ec (event category) parameter but not all other CMDH parameters.

The detailed description can be found in clause D.12 of Architecture TS-0001 [6].

Table D.12-1: Data Type Definition of [cmdhPolicy]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhPolicyType | CDT-cmdhPolicy-v1_0_0-<<date of published>>.xsd |  |

Table D.12-2: Applicable Common Attributes on [cmdhPolicy]

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| resourceType | M | O | O | NP | “mgmtObj” |  |
| resourceID | NP | O | NP | NP | None |  |
| parentID | NP | O | NP | NP | None |  |
| expirationTime | O | O | O | NP | Default is determined by Hosting CSE policy |  |
| accessControlPolicyIDs | O | O | O | NP | Default is determined by Hosting CSE policy |  |
| creationTime | NP | O | NP | NP | None |  |
| lastModifiedTime | NP | O | NP | NP | None |  |
| labels | O | O | O | NP | Empty |  |

NOTE: this table is applied to sub-clauses D.12.1 to D.12.8.

Table D.12-3: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhPolicy” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| name | M | O | O | NP | xs:string | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | None |

The Resource Specific Procedure on CRUD Operations as specified in clause 7.3.14 for the generic <mgmtObj> resource type apply.

### Resource activeCmdhPolicy

The resource [activeCmdhPolicy] provides a link to the currently active set of CMDH policies.

The detailed description can be found in clause D.12.1 of Architecture TS-0001 [6].

Table D.12.1-1: Data Type Definition of [activeCmdhPolicy]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| activeCmdPolicyType | CDT-activeCmdhPolicy-v1_0_0-<<date of published>>.xsd | At most one Policy instance shall be enabled at a time. |

Table D.12.1-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “activeCmdhPolicy” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | None |

### Resource cmdhDefaults

The resource [cmdhDefaults] defines default CMDH policy values. The detailed description can be found in clause D.12.2 of Architecture TS-0001 [6].

Table D.12.2-1: Data Type Definition of [cmdhDefaults]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhDefaultsType | CDT-cmdhDefaults-v1_0_0-<<date of published>>.xsd |  |

Table D.12.2-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhDefaults” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | None |

### Resource cmdhDefEcValue

The resource [cmdhDefEcValue] represents a value for the ec (event category) parameter of an incoming request. The detailed description can be found in clause D.12.3 of Architecture TS-0001 [6].

Table D.12.3-1: Data Type Definition of [cmdhDefEcValue]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhDefEcValueType | CDT-cmdhDefEcValue-v1_0_0-<<date of published>>.xsd |  |

Table D.12.3-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhDefEcValue” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| defEcValue | M | O | O | NP | m2m:eventCat | None |
| requestOrigin | M | O | O | NP | xs:string | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |

### Resource cmdhEcDefParamValues

The resource [cmdhEcDefParamValues] represents a specific set of default values for the CMDH related parameters rqet (request expiration timestamp), rset (result expiration timestamp), oet (operational execution time), rp (response persistence) and da (delivery aggregation) that are applicable for a given ec (event category) if these parameters are not specified in the request. The detailed description can be found in clause D.12.4 of Architecture TS-0001 [6].

Table D.12.4-1: Data Type Definition of [cmdhEcDefParamValues]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhEcDefParamValuesType | CDT-cmdhEcDefParamValues-v1_0_0-<<date of published>>.xsd |  |

Table D.12.4-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhEcDefParamValues” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| applicableEventCategory | M | O | O | NP | m2m:eventCat | None |
| defaultRequestExpTime | M | O | O | NP | xs:dateTime | None |
| defaultResultExpTime | M | O | O | NP | xs:dateTime | None |
| defaultOpExecTime | M | O | O | NP | xs:dateTime | None |
| defaultRespPersistence | M | O | O | NP | xs:duration | None |
| defaultDelAggregation | M | O | O | NP | xs:boolean | None |

### Resource cmdhLimits

The Resource [cmdhLimits] represents limits for CMDH related parameter values. The detailed description can be found in clause D.12.5 of Architecture TS-0001 [6].

Table D.12.5-1: Data Type Definition of [cmdhLimits]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhLimitsType | CDT-cmdhLimits-v1_0_0-<<date of published>>.xsd |  |

Table D.12.5-2: Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhLimits” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| order | M | O | O | NP | xs:positiveInteger | None |
| requestOrigin | M | O | O | NP | xs:string | None |
| requestContext | O | O | O | NP | xs:string | None |
| requestContextNotification | O | O | O | NP | xs:boolean | None |
| requestCharacteristics | O | O | O | NP | xs:string | None |
| limitsEventCategory | M | O | O | NP | m2m:eventCat | None |
| limitsRequestExpTime | M | O | O | NP | xs:dateTime | None |
| limitsResultExpTime | M | O | O | NP | xs:dateTime | None |
| limitsOpExecTime | M | O | O | NP | xs:dateTime | None |
| limitsRespPersistence | M | O | O | NP | xs:duration | None |
| limitsDelAggregation | M | O | O | NP | xs:boolean | None |

### Resource cmdhNetworkAccessRules

The resource [cmdhNetworkAccessRules] defines the usage of underlying networks for forwarding information to other CSEs during processing of CMDH-related requests in a CSE. The detailed description can be found in clause D.12.6 of Architecture TS-0001 [6].

Tabla D.12.6-1:Type Definition of [cmdhNetworkAccessRules]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhNetworkAccessRulesType | CDT-cmdhNetworkAccessRules-v1_0_0-<<date of published>>.xsd |  |

Table D.12.6-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhNetworkAccessRules” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| applicableEventCategories | M | O | O | NP | m2m:eventCat | None |
| cmdhNwAccessRule | O | O | O | NP | m2m:mgmtLink | None |

### Resource cmdhNwAccessRule

The resource [cmdhNwAccessRule] defines limits in usage of specific underlying networks for forwarding information to other CSEs during processing of CMDH-related requests. The detailed description can be found in clause D.12.7 of Architecture TS-0001 [6].

Table D.12.7-1 Data Type Definition of [cmdhNwAccessRule]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhNwAccessRuleType | CDT-cmdhNwAccessRule-v1_0_0-<<date of published>>.xsd |  |

Table D.12.7-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhNwAccessRule” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| targetNetwork | M | O | O | NP | xs:string | None |
| minReqVolume | M | O | O | NP | xs:nonNegativeInteger | None |
| backOffParameters | M | O | O | NP | m2m: backOffParameters | None |
| otherConditions | O | O | O | NP | TBD | None |
| mgmtLink | M | O | O | NP | m2m:mgmtLink | None |

Editor’s Note: The otherConditions attribute needs to be clarified  in TS-0001 before we can determine the data type.

## Resource cmdhBuffer

The resource [cmdhBuffer] represents limits in usage of buffers for temporarily storing information that needs to be forwarded to other CSEs during processing of CMDH-related requests in a CSE. The detailed description can be found in clause D.12.8 of Architecture TS-0001 [6].

Table D.12.8-1: Data Type Definition of [cmdhBuffer]

| Data Type ID | File Name | Note |
| --- | --- | --- |
| cmdhBufferType | CDT-cmdhBuffer-v1_0_0-<<date of published>>.xsd |  |

Table D.12.8-2:  Data Types for resource specific attributes

| Attribute Name | Optionality | Data Type | Default Value and Constraints |
| --- | --- | --- | --- |
|  | C | R | U | D |  |  |
| mgmtDefinition | M | O | O | NP | m2m:mgmtDefinition | “cmdhBuffer” |
| objectID | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| objectPath | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| description | O | O | O | NP | xs:string | See Table 7.3.14.1.2 |
| applicableEventCategory | M | O | O | NP | m2m:eventCat | None |
| maxBufferSize | M | O | O | NP | xs:nonNegativeInteger | None |
| storagePriority | M | O | O | NP | xs:positiveInteger | None. The range of storage priority is from 1 to 10. |