| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 Protocols |
| Title:* | DTLS related mapping |
| Source:* | Hitachi, |
| Contact: | He Xuan, xhe@hitachi.cn |
| Date:* | 2014-07-08 |
| Abstract:* | This contribution proposes CoAP protocol binding details. |
| Agenda Item:* | Contributions |
| Work item(s): | WI 0012 |
| Document(s) Impacted* | oneM2M-TS-0008-CoAP Protocol Binding |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | <A concise statement of the decision required or the recommended action to be taken> |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

- Introduction

This contribution proposes CoAP protocol binding related part to TS-0008.

--------------------- Start of proposed modified text -------------------

7. Security

CoAP itself does not provide protocol primitives for authentication or authorization; where this is required, it shall be provided by DTLS.

Just as HTTP is secured using Transport Layer Security (TLS) over TCP, CoAP shall be secured using Datagram TLS (DTLS) [DTLS 1.2].

All CoAP messages shall be sent as DTLS “application data”. For matching an ACK or RST to a CON message or a RST to a NON message: The DTLS session shall be the same and the epoch shall be the same.

For matching a response to a request, the DTLS session shall be the same and the epoch shall be the same. The response to a DTLS secured request shall always be DTLS secured using the same security session and epoch.

Editor’s note: WG4 will provide detailed clause numbers WG3 can refer to.

--------------------- End of proposed modified text ---------------------

# Comments

I hope we can move these kind of details to the Security TS-0003, and this section can direct the reader to that section of TS-0008.

Move to TS-0003

The other bindings will have similar constrains. These details should be in TS-0003, since they will not be specific to CoAP.

Move to TS-0003

Related reference should be moved to TS-0003