| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | MIME_type_for_oneM2M_resource_representation |
| Source:* | FUJITSU |
| Contact: | Shingo Fujimoto,FUJITSU,shingo_fujimoto@jp.fujitsu.com |
| Date:* | 2014-07-12 |
| Abstract:* | This contribution proposed to define oneM2M specific MIME types |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004 |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | WG members should agree on proposed texts. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

This contribution proposed to define oneM2M specific MIME types

---New TEXTs STARTS---

## 6.x MIME Types for oneM2M protocols

The present sub-clause explains the use of oneM2M specific MIME-Type which shall be used in one of protocol bindings.

Those MIME-Types are registered with the prefix ‘application/vnd.onem2m-‘ on IANA registry.

Editor’s Note: actual request of assignment in IANA is FFS.

### 6.x.1 application/vnd.onem2m-resource-data+xml

This data type is used for XML-based data to represent the oneM2M resource.

NOTE: Actual data structure is defined as part of CDT-mimeTypes-v1_0_0-YYYYMMDD.xsd.

### 6.x.2 application/vnd.onem2m-response-data+xml

This data type is used for XML-based data to represent the response status.

NOTE: Actual data structure is defined as part of CDT-mimeTypes-v1_0_0-YYYYMMDD.xsd.

### 6.x.3 application/vnd.onem2m-partial-updates+xml

This data type is used for XML-based data to represent the instruction to perform partial update.

NOTE: Actual data structure is defined as part of CDT-mimeTypes-v1_0_0-YYYYMMDD.xsd.

---New TEXTS ENDS---

---Change 1 STARTS---

### 6.4.4 responseData Type

#### 6.4.4.1 Description

This type defines data structure used as MIME-Type ‘application/vnd.onem2m-resource-data +xml’. It is included  in CDT-mimeTypes-v1_0_0-<date>.xsd.

#### 6.4.4.2 Reference

(TBD)

#### 6.4.4.3 Usage Example

---Change 1 ENDS ---

---Change 2 STARTS ---

### 6.4.5 responseData Type

#### 6.4.5.1 Description

This type defines data structure used as MIME-Type ‘application/vnd.onem2m-response-data+xml’. It is included  in CDT-mimeTypes-v1_0_0-<date>.xsd.

#### 6.4.5.2 Reference

(TBD)

#### 6.4.5.3 Usage Example

(TBD)

---Change 2 ENDS ---

---Change 3 STARTS ---

### 6.4.6 partialUpdates Type

#### 6.4.6.1 Description

This type defines data structure used as MIME-Type ‘application/vnd.onem2m-partial-updates +xml’. It is included  in CDT-mimeTypes-v1_0_0-<date>.xsd.

#### 6.4.6.2 Reference

(TBD)

#### 6.4.6.3 Usage Example

(TBD)

---Change 3 ENDS ---

# Comments

After “Resource Data Types” 6.5 ?

# Text boxes

<?xml version="1.0"?>

<m2m:resourceData xmlns:m2m="http://www.onem2m.org/xml/protocols">

<m2m:resourceTypeId>containerType</m2m:resourceTypeId>

<m2m:container>

<m2m:name>container1</m2m:name>

</m2m:container>

</m2m:resourceData>