| INPUT CONTRIBUTION |
| --- |
| Group Name:* | PRO # 11.9 |
| Title:* | notification definition and procedures |
| Source:* | LG Electronics |
| Contact: | Seungmyeong Jeong, seungmyeong.jeong@lge.com |
| Date:* | 2014-07-16 |
| Abstract:* | notification definition and procedures |
| Agenda Item:* | TBD |
| Work item(s): | WI 0009 |
| Document(s) Impacted* | oneM2M-TS-0004 Core Protocol TS |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Incorporate the text into the TS. |

oneM2M IPR STATEMENT

Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by all provisions of IPR policy of the admitting Partner Type 1 and permission that all communications and statements, oral or written, or other information disclosed or presented, and any translation or derivative thereof, may without compensation, and to the extent such participant or attendee may legally and freely grant such copyright rights, be distributed, published, and posted on oneM2M’s web site, in whole or in part, on a non-exclusive basis by oneM2M or oneM2M Partners Type 1 or their licensees or assignees, or as oneM2M SC directs.

Introduction

Since Notify operation has no corresponding resource type definition in stage2, in stage3 we need a definition for Notify request/response primitive definition with existing attribute data types.

This contribution proposes the primitive definitions, which are to be included under clause 7.3

### ----------------------- Start of change 1 -----------------------

### 7.3.x	Definition of Notification

#### 7.3.x.1	Introduction

Notification has no resource type representation in the Architecture TS. Rather, Notify request and response primitive formats are defined in clause 7.2.1.1.

Table 7.3.x.1-1 Data Type Definition of notification

| Data Type ID | File Name | Note |
| --- | --- | --- |
| notificationType | CDT-<<resource name>>-v1_0_0-<<date of published>>.xsd |  |

Table 7.3.x.1-2 Applicable Common Attributes on notification

| Attribute Name | Optionality | Default Value | Resource Specific Note |
| --- | --- | --- | --- |
|  | N |  |  |
| resourceType | O |  |  |
| resourceID | O |  |  |
| parentID | O |  |  |
| accessControlPolicyIDs | O |  |  |
| creationTime | O |  |  |
| expirationTime | O |  |  |
| lastModifiedTime | O |  |  |
| stateTag | O |  |  |
| labels | O |  |  |
| link | O |  |  |
| announceTo | O |  |  |
| announcedAttribute | O |  |  |

Table 7.3.7.1-3 Data Types for notification attributes

| Attribute Name | Data Type | Default Value and Constraints | Entity which allows operation |
| --- | --- | --- | --- |
| notificationEvent | list of m2m:notificationEvent |  |  |
| creator | m2m:id |  |  |
| verificationRequest | xs:boolean |  |  |
| subscriptionDeletion | xs:boolean | TRUE |  |
| subscriptionRef | xs:anyURI |  |  |

#### 7.3.x.2	Notification Procedures

Notification is sent as Notify Request primitive as defined in clause 7.3.x.2. The procedures for Notify request and response primitive shall be happen in the following cases.

#### 7.3.x.2.1	Notification for Subscription

TBD

#### 7.3.x.2.2	Subscription Verification during Subscription Creation

Originator:

When the Originator is triggered to perform subscription verification (clause 7.3.7.2.1) during <subscription> creation procedure, it performs the following in order.

- Add verificationRequest parameter set as TRUE into the Notify request primitive.

- Add creator attribute set as the Originator ID of the <subscription> creation into the primitive.

- Add to parameter set as notificationURI into the primitive. If the notificationURI contains more than one URI, then set each URI to the different primitives.

- Send the primitive(s).

Receiver:

When the Hosting CSE receives a Notify request primitive including verificationRequest parameter set as TRUE, the Hosting CSE shall check if the creator and the Originator have NOTIFY privilege to the notificationURI.

If it fails, the Hosting CSE shall return “Subscription verification failed” error with the Notify response primitive. Otherwise, it shall return successful response primitive.

#### 7.3.7.x.3	Notification for Subscribed-to Resource Deletion

Originator:

When the <subscription> resource is deleted, the Originator shall send a Notify request primitive with subscriptionDeletion attribute set as TRUE and subscriptionRef attribute set as URI of the <subscription> resource.

#### 7.3.7.x.4	Notification for Asynchronous Non-blocking Request

Editor’s Note: Qualcomm would bring a contribution for this clause.

### ----------------------- End of change 1 -----------------------

### ----------------------- Start of change 2 -----------------------

#### 6.3.2.3		Complex Data Types

Table 6.3.2.3-1 describes oneM2M-specific complex data type definitions.

Table 6.3.2.3-1: oneM2M Complex Data Types

| XSD type name | Element | Element Data Type | Description |
| --- | --- | --- | --- |
| m2m:notificationEvent | all resource specific attributes of subscribable resource types. | data type of each attribute (This is defined in sub-clauses of clause 7.3) | used to indicate the date and time when the event occurs |

NOTE: List of subscriable resource types are <accessControlPolicy>, <CSEBase>, <remoteCSE>, <AE>, <container>, <contentInstance>, <schedule>, <locationPolicy>, <delivery>, <request>, <group>, <mgmtObj>, <mgmtCmd>, <execInstance>, <node>, <m2mServiceSubscription>, <nodeInfo>, <statsConfig>, <eventConfig> and <statsCollect>.

### ----------------------- End of change 2 -----------------------

### ----------------------- Start of change 3 -----------------------

### Request/Response Parameters

Request/Response parameters are specified in clause 8.1.2 and 8.1.3 [6]. The data types and values shall be supported according to the description given in table 6.3.4-1.

Table 6.3.4-1: Request/Response Parameters

| Parameter Name | Data Type | Default | Value restrictions | Notes |
| --- | --- | --- | --- | --- |
| notificationStoragePriority | xs:nonNegativeInteger |  |  | Used in Notify request primitive |

### ----------------------- End of change 3 -----------------------