| INPUT CONTRIBUTION |
| --- |
| Group Name:* | WG3 |
| Title:* | Clarify the Device Triggering |
| Source:* | Qi Yu, Huawei, yuqi@huawei.com |
| Contact: | <name>, <company>, <contact info> (if different to the source) |
| Date:* | 2014-07-15 |
| Abstract:* | Before the CSE initiates the device triggering, the CSE and MTC-IWF shall first execute the following steps: Mutual Authentication Advertise support of the Diameter Tsp application by the Capabilities-Exchange-Request and Capabilities-Exchange-Answer commands The current TS does not cover this part. |
| Agenda Item:* | Core Protocol TS |
| Work item(s): | WI-0009 |
| Document(s) Impacted* | TS-0004v0.5.3 Annex B |
| Intended purpose of document:* | Decision Discussion Information Other <specify> |
| Decision requested or recommendation:* | Member should agree on proposed changes. |

oneM2M Notice

The document to which this cover statement is attached is submitted to oneM2M.  Participation in, or attendance at, any activity of oneM2M, constitutes acceptance of and agreement to be bound by terms of the Working Procedures and the Partnership Agreement, including the Intellectual Property Rights (IPR) Principles Governing oneM2M Work found in Annex 1 of the Partnership Agreement.

Before the CSE initiates the device triggering, the CSE and MTC-IWF shall first execute the following steps:

Mutual Authentication

Advertise support of the Diameter Tsp application by the Capabilities-Exchange-Request  and Capabilities-Exchange-Answer commands

The current TS does not cover this part. This contribution intends to add the corresponding text to Annex B.

----- Start of change 1----

Annex B (normative):
Device Triggering

B.1 Providing Device Triggering service by means of 3GPP networks

B.1.1 Introduction

3GPP Underlying Network has defined a dedicated interface for requesting device triggering. The normative references for applicable interfaces are as follows: 3GPP TS 23.682 [15]. The specification for the interface Tsp is described in 3GPP TS 29.368 [16]. Tsp interface uses Diameter Base Protocol as specified in IETF RFC 3588 [13], in order to use such an interface the CSE shall act as a Diameter client as described in IETF RFC 6733 [14].

Before the CSE initiates the device triggering, the CSE and MTC-IWF shall first execute the following steps as specified in 3GPP TS29.368 [16]:

  - Mutual Authentication

  - Advertise support of the Diameter Tsp application by the Capabilities-Exchange-Request  and Capabilities-Exchange-Answer commands

B.1.2 Device Action Request command

When a CSE needs to issue a device triggering request from MTC-IWF, the CSE shall send a Device-Action-Request (DAR) command (see [16]). The following tables provide an overview of the parameters and the parameter values needed for the DAR command.

NOTE:	The values of the parameters indicated in the "Value" column need to be mapped to the specific 3GPP data type.

Table B.1.2-1: AVPs in Device Action Request (DAR) command

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Value |
| --- | --- | --- | --- | --- |
| Session-Id | It is used to identify a specific session (see [13]) | UTF8String | 263 | CSE implementation specific |
| Auth-Application-Id | This parameter transport the Tsp application identifier as specified in [16], clause 6.1.3 | Enumerated | 274 | 16777309 |
| Auth-Session-State | The Tsp session is terminated after each request/answer pair and in accordance with [16] the parameter shall indicate that the session state shall not be maintained | Enumerated | 277 | NO_STATE_MAINTAINED (see [16]) |
| Origin-Host | It identifies the endpoint that originated the Diameter message (see [13]) | DiamIdent | 264 | CSE implementation specific |
| Origin-Realm | It identifies the Realm of the originator of theDiameter message (see [13]) | DiamIdent | 296 | CSE implementation specific |
| Destination-Realm | It identifies the realm the message is to be routed to. (see [13]) | DiamIdent | 283 | Domain Identifier part from M2M-Ext-ID |
| Destination-Host | The absence of the Destination-Host causes the message to be sent to any Diameter server supporting the application within the specified realm. (see [13]) | DiamIdent | 293 | NULL |
| Origin-State-Id | It is an increasing value that is advanced whenever a Diameter entity restarts with loss of previous state, for example upon reboot (see [13]) | Unsigned32 | 278 | CSE implementation specific |
| Device-Action | It contains the specific action for the device (see [16]) | Grouped | 3001 | Specific format described in table B.1.2-2 |
| Proxy-Info | It's a grouped AVP which provides the proxy state and host (see [13]) | Grouped | 284 | CSE implementation specific |
| Route-Record | The identity added in this AVP is be the same as the one received in the Origin-Host (see [13]) | DiamIdent | 282 | Not applicable |

Table B.1.2-2: AVPs in Device Action AVP (Grouped AVP)

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Value |
| --- | --- | --- | --- | --- |
| External-Id | It is the identifier of the device as specified in [TS 29.336] | UTF8String | 3111 | M2M-Ext-ID |
| MSISDN | It is the identifier of the device as specified in [TS 29.329] | OctetString | 701 | M2M-Ext-ID |
| SCS-Identifier | It identifies the CSE issuing the request (see [16]) | OctetString | 3104 | CSE-ID |
| Reference-number | It uniquely identifies a transaction (see [16]) | Unsigned32 | 3007 | CSE implementation specific Editor's note: possibility to maybe use M2M-Request-ID is FFS |
| Action-Type | It informs the MTC-IWF of the required action | Enumerated | 3005 | 1 (Device Trigger Request) |
| Trigger-Data |  | Grouped | 3003 | See table B.1.2-3 |
| Validity-Time | The validity time in seconds for the specific action requested. (see [16]) | Unsigned32 | 448 | CSE implementation specific |
| NOTE: Tither external-Id or MSISDN shall be used, not both. |

Table B.1.2-1: AVPs in Trigger Data AVP (Grouped AVP)

| Attribute Value Pair (AVP) name | AVP description | 3GPP Data Type | AVP Code | Value |
| --- | --- | --- | --- | --- |
| Payload | It contains the payload to be transferred to the addressed device. (see [16]) | OctetString | 3004 | NULL Furhter values can be defined (FFS) Editor's Note: in the current TS-0001 does not specify how to use payload. |
| Priority-Indication | It identifies priority of the device trigger. (see [16]) | Enumerated | 3006 | CSE implementation specific (possible values are 0 or 1) |
| Application-Port-Identifier | It uniquely identifies the triggering entity addressed in the device. (see [16]) | Unsigned32 | 3010 | Trigger-Recipient-ID |

Editor's Note: Removal of Editor's Note in the Value file for Payload should be considered.

B.1.3 Device Action Answer command

As a result of device triggering request to MTC-IWF, the CSE receives a Device-Action-Answer (DAA) command (see [16]). The relevant parameters for a CSE are the following ones:

Result-Code AVP: see [13] for detail;

Session-Id AVP: see [13] for detail;

Other AVPs for Diameter Base Protocol: see [13] for detail.

Following AVPs are set in Device-Notification AVP (Grouped AVP):

Either MSISDN or External-Id: the CSE shall check that the identifier of the target CSE is correct;

SCS-Identifier: the CSE shall check that the value corresponds to its CSE-ID;

Reference-Number: the CSE can use this value for correlating the DAA with the corresponding Device-Action-Request command issued previously by the CSE;

Action-Type: the CSE shall check that the value is se to 1 (Trigger Request) as same value of DAR command;

Request-Status: see table B.1.3-1 for the list of possible value.

Table B.1.3-1: Result Status

| Result-Status value | Name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that device action requested is confirmed. |
| 201 | TEMPORARYERROR | See [16] for detail. |
| 101 | INVALIDPAYLOAD | See [16] for detail. |
| 102 | INVEXTID | See [16] for detail. |
| 103 | INVSCSID | See [16] for detail. |
| 104 | INVPERIOD | See [16] for detail. |
| 105 | NOTAUTHORIZED | See [16] for detail. |
| 106 | SERVICEUNAVAILABLE | See [16] for detail. |
| 107 | PERMANENTERROR | See [16] for detail. |
| 108 | QUOTAEXCEEDED | See [16] for detail. |
| 109 | RATEEXCEEDED | See [16] for detail. |

B.1.4 Device Notification Request command

As a report of the result for device triggering delivery by 3GPP network, the CSE receives a Device-Notification-Request (DNR) command (see [16]). The relevant parameters for a CSE are the following ones:

Result-Code AVP: see [13] for detail;

Session-Id AVP: see [13] for detail;

Other AVPs for Diameter Base Protocol: see [13] for detail.

Following AVPs are set in Device-Notification AVP (Grouped AVP):

Either MSISDN or External-Id: the CSE shall check that the identifier of the target CSE is correct;

SCS-Identifier: the CSE shall check that the value corresponds to its CSE-ID;

Reference-Number: the CSE can use this value for correlating the DAA with the corresponding Device-Action-Request command issued previously by the CSE;

Action-Type: the CSE shall check that the value is set to 2 (Delivery Report);

Delivery-Outcome: see tableB.1.4-1 for the list of possible value

Table B.1.4-1:: Delivery-Outcome

| Delivery-Outcome value | Name | Parameter description |
| --- | --- | --- |
| 0 | SUCCESS | This value indicates that the device action request was successfully completed. |
| 1 | EXPIRED | See [16] for detail. |
| 2 | TEMPORARYERROR | See [16] for detail. |
| 3 | UNDELIVERABLE | See [16] for detail. |
| 4 | UNCONFIRMED | See [16] for detail. |

B.1.5 Device Notification Answer command

As a result of device notification request to MTC-IWF, the CSE sends a Device-Notification-Answer (DNA) command (see [16]). The relevant parameters for a CSE are the following ones:

Auth-Application-ID: set to 16777309 as indicated in in [16]);

Auth-Session-State: set to NO_STATE_MAINTAINED as indicated in [16];

Other AVPs for Diameter Base Protocol: see [13] for detail, the value of such AVP is CSE implementation specific.

----- End of change 1----

# Comments

Is this reference, which is to an obsolete version of the RFC, correct?

Reference to be added in the reference clause.

Reference to be added in the reference clause.